## Slide 1: Designing a Motion Control System

## Slide 2: Agenda
Elements of a motion control system
Motion Control Software
Motion Controllers
Motor Drives
Motors
Feedback devices
Example Application
Notes: The things we will cover in this tutorial are the elements of a motion control system, motion control software, motion controllers, motor drives, motors, feedback devices, integration, and an example application.

## Slide 3: Elements of a Motion System
App
Software
Motion
Controller
Amp/Drive
Motor
Position
Voltage
Current
Position Feedback
Mechanical
Feedback
Device
Notes: <number>
<footer>
<header>
<date/time>
A typical motion control system (with a position feedback loop) consists of the following components:
Application software commands the desired target position.
Motion Controller - which is the brain of the of the system takes that target position and converts it into a voltage reference (+/- 10V)
Amplifier or Drive - that generates the current required to drive the motor - takes the voltage supplied by the motion controller and supplies the required current to the motor.
Motor - that converts electrical energy into mechanical energy - produces the required torque to move to the desired target position.
Mechanical Elements – These are the things that actually do the motion in the system such as a stage or robot.
Feedback device or Position Sensor - senses the position of the motor and reports the result to the controller, thereby closing the loop to the motion controller

## Slide 4: Application Software
App
Software
Motion
Controller
Amp/Drive
Motor
Mechanical
Feedback
Device
Notes: <number>
<footer>
<header>
<date/time>
The First section we will discuss is the application software.

## Slide 5: Software Overview
Configuration
Prototype
Application
Development
Environment
NI-Motion Driver for
LabVIEW,
Measurement Studio,
C/C++ Visual Basic
Motion Assistant
Measurement and Automation Explorer
Notes: <number>
<footer>
<header>
<date/time>
There is a wide range of software that you can use to program your motion control applications. When you initially get started one of the first things you do is configure your system. For this, National Instruments offers Measurement and Automation Explorer, an interactive tool for configuring not only motion control but all other National Instruments hardware as well. For motion control, Measurement and Automation explorer offers, interactive testing and tuning panels that help you verify your systems functionality before doing any programming.
When you have configured your system, you are now ready to start prototyping and developing your application. For prototyping, National Instruments has a tool called Motion Assistant. Motion Assistant, is an interactive tool that enables you to configure moves using a point and click environment and then generate LabVIEW code based on the moves you configure.
After this prototyping phase, the next step is to develop the code. To develop the code, you use National Instruments NI Motion driver software.

## Slide 6: Configuring a Motion Control System
Measurement & Automation Explorer
  Use to configure all National Instruments devices
  Tune servo motors
  Test configuration
  Configure signal routing
  Test NI vision and data acquisition devices
Notes: <number>
<footer>
<header>
<date/time>
You can easily configure National Instruments motion controller, image acquisition boards, and data acquisition boards with Measurement & Automation Explorer, which is shipped with all National Instruments Hardware. This utility is an interactive tool for setting and testing each of your hardware components. With motion control, you can initialize the board, tune servo motors, configure signal routing and test basic moves on the controller. With machine vision, you can capture images from a variety of analog or digital cameras and make adjustments to the images. With data acquisition, you can configure channels and test your device to ensure things are working properly.
© National Instruments Corporation 5 Computer-Based Machine Vision Solutions

## Slide 7: NI-Motion Driver Software
For Windows and LabVIEW Real-Time Systems
  VIs and functions for LabVIEW, Visual Basic, and C
  Measurement and Automation Explorer
    Configuration of motion and other components
    Motor Tuning
For Non-Windows Systems
  Motion Control Hardware DDK
  Linux and VxWorks drivers from Sensing Systems (www.sensingsystems.com)
Notes: The NI Motion Driver software contains functions that enable you to communicate with NI Motion controllers in Windows or LabVIEW Real Time. This driver also contains Measurement and Automation explorer to help you easily configure and tune your motion system.
For non-windows systems you have the option of developing your own driver using the Motion Control Hardware DDK manual that explains how to communicate on a low level with NI motion controllers. For those who do not have the expertise or time to develop their own driver, NI Alliance Member Sensing Systems offers a Linux and VxWorks driver as well as the ability to create other drivers if you need something for another operating system such as Mac OS 10 or RTX.

## Slide 8: NI Motion Assistant Prototyping Software
Configurable
Easy to use
Interactive
No programming required
Programmable
Flexible
Easier integration with other components
Notes: <number>
<footer>
<header>
<date/time>
As mentioned previously, National Instruments has a configurable prototyping environment called Motion Assistant. Configurable environments are often menu driven environments where you can easily configure your system to do what you need it to do without programming. You can think of them as offering pre-written blocks of code that you simply configure to meet your needs. Programmable environments on the other hand, require you to use standard programming languages such as LabVIEW, C, or Visual Basic to accomplish your tasks. Configurable systems offer ease of use, interactive development, and do not require programming ability but may be limited in functionality or in the ability to integrate with other I/O outside of motion. Motion Assistant seeks to bridge the gap by offering all of the features of a configurable system and enabling you to then generate code for LabVIEW that you could then integrate with your system and change as you need.

## Slide 9: Motion Controllers
App
Software
Motion
Controller
Amp/Drive
Motor
Mechanical
Feedback
Device
Notes: <number>
<footer>
<header>
<date/time>
The next portion of the system we will discuss is the motion controller.

## Slide 10: Purpose of the Motion Controller
Calculate the trajectories for each commanded move on the board to prevent host computer interference
Provide the torque commands to the motor drive or amplifier
Monitor limits and emergency stops for supervisory control
Close the PID loop
Notes: The purpose of the motion controller is to calculate the trajectories for each commanded move. This is done on the board itself to prevent host computer interference. For example, you would not want your motion to stop because of some anti-virus software that opens up. The motion controller uses the trajectories to determine the proper torque command to send to the motor amplifier to actually cause motion.
Motion controllers must also monitor the limits and emergency stops for supervisory control as well as close the PID loop. This is also done on the board to ensure high reliability, determinism, and stability of the system.

## Slide 11: Features of a Simple Motion Trajectory
Target velocity
Starting position
Target position
Velocity
Time
Notes: <number>
<footer>
<header>
<date/time>
The motion trajectory describes the profile of the control or command signal output by the motion controller board to the driver / amplifier, resulting in a motor/motion action that follows the profile.
The intelligent motion controller calculates the segments of a motion profile trajectory based on the parameter values programmed you program. The desired target position, maximum target velocity and acceleration values are used by the trajectory algorithm to determine how much time is spent in the three primary segments of a move, acceleration, constant velocity and deceleration.
In the acceleration segment, motion begins from a stopped position or from a previously in-process move, and follows a prescribed acceleration ramp until the speed reaches the target velocity for the move.
Motion continues at the target velocity for a prescribed period until the controller determines that it is time to begin the deceleration segment to slow the motion to a stop exactly at the desired target position. If a move is short enough that the deceleration beginning point occurs before the acceleration has completed, then the profile will appear triangular instead of trapezoidal, and the actual velocity attained may fall short of the desired target velocity.
Enhancements to the basic trapezoidal trajectory include S-curve acceleration/deceleration, where the accel/decel ramp is modified into a non-linear, curved profile. This fine control over the shape of these ramps is very useful for tailoring the performance of a motion trajectory based upon the inertial, frictional forces, motor dynamics and other mechanical limitations in motion systems.

## Slide 12: Typical Motion Profiles Options
Simple single axis point-to-point motion
Requires an axis target position
Notes: <number>
<footer>
<header>
<date/time>
Next, we will discuss some of the various profile options you will typically find on a motion controller. One of the most basic is the simple, single axis point-to-point move. The main thing required for this move is the position it needs to get to. Along with this, the motion controller will also often require the velocity and acceleration you want the motion to move at.

## Slide 13: Typical Motion Profile Options
Y Axis
X Axis
Vector point-to-point motion
Requires X position and Y position
Notes: <number>
<footer>
<header>
<date/time>
The next type of move is the vector point-to-point move. This move involves multiple axes moving in coordination to get from one point to another in 2D or 3D space. The main requirement for a vector move is the final positions on the X, Y, or Z axis. Your motion controller will also require some type of vector velocity and acceleration as well. This type of motion profile is commonly found in XY type applications such as scanning or automated microscopy.

## Slide 14: Typical Motion Profile Options
Original Path
Blended Path
X Axis
Y Axis
Blended motion
Requires two vector moves and a blend factor
Notes: <number>
<footer>
<header>
<date/time>
Another common profile option is blended motion. Blended motion involves two moves that are fused together by a blend as shown in the example here. The main requirement for a blended move is that you have two vector moves and a blend factor which specifies how large the blend will be. Blending is useful for applications where you need continuous motion between two different moves. One of the issues you will run into when using blended motion is that you will not pass through all of the points in your original trajectory. If the specific position along the path is important to you, another option to consider is contouring.

## Slide 15: Typical Motion Profile Options
X Axis
Y Axis
Contouring: spline through a buffer of points
Requires buffer of points
Notes: <number>
<footer>
<header>
<date/time>
Contouring enables you to supply a buffer of those positions and then creates a smooth path or spline through those positions. The advantage of contouring is that you are guaranteed to pass through each position.

## Slide 16: Typical Motion Profile Options
Electronic Gearing: simulating a gear ratio without using physical gears
Requires an axis and a reference such as:
  Another axis
  Encoder feedback
  Analog Feedback
Axis 1
Axis 2
Notes: <number>
<footer>
<header>
<date/time>
Contouring enables you to supply a buffer of those positions and then creates a smooth path or spline through those positions. The advantage of contouring is that you are guaranteed to pass through each position.

## Slide 17: NI Motion Controller Options
Notes: NI offers three main families of motion controllers. The 733x series is a low cost controller for stepper motors that offers most of the basic functions you would need for a wide variety of applications. The 734x series is the mid range series that offers stepper and servo control as well as a few new features such as contouring and electronic gearing. The 735x series is the most advanced series that offers up to 8 axes of stepper and servo control and a host of extra I/O and powerful features including sinusoidal commutation for brushless motors and 4 MHz periodic breakpoints for high speed integration.

## Slide 18: Hardware Integration with NI DAQ and Vision
Single vendor for automated measurement system hardware and software
RTSI for high performance timing and triggering
Similar APIs for fast development
The ability to create integrated, Ethernet-based distributed systems with LabVIEW Real-Time and PXI
Notes: <number>
<footer>
<header>
<date/time>
One of the primary benefits of the National Instruments motion controllers is that they integrate very well with both data acqusition and vision. This enables you to have a single vendor for the control system of your automated measurement applications. This also enables you to high very high performance timing due to the RTSI or Real Time System Integration bus on NI plug-in hardware products. Another advantage of developing integrated systems with NI products is that the similar APIs and various Assistants enable you to develop your applications faster. Finally, the last advantage is that using LabVIEW Real Time, you can create integrated ethernet based systems.

## Slide 19: Embedded Ethernet-Based Systems
Distributed
Reduced downtime
Increased reliability and determinism
Reduced development time with use of existing LabVIEW code
Host Computer
Motion Controller
Data Acquisition
Image Acquisition
PXI LabVIEW
Real-Time controller
Notes: <number>
<footer>
<header>
<date/time>
Real time availability A real-time system is considered deterministic, but this does not mean fast. By nature, vision functions are not deterministic. Image content rather than image size determines the speed of a particular image processing step. An image with more particles in it will be slower than an image with less particles in it. What you can do, however, is determine the longest time a function will take by analyzing the image that has the most content. This technique determines the upper bound, or response time.

## Slide 20: Motion Amplifiers and Drives
App
Software
Motion
Controller
Amp/Drive
Motor
Mechanical
Feedback
Device
Notes: <number>
<footer>
<header>
<date/time>
Next we will discuss amplifiers and power drives.

## Slide 21: Motor Drive Requirements
The motor drive must match the motor technology
  For example, 2-phase stepper motors require 2 phase stepper motor drives, etc…
The motor drive must provide adequate:
  Peak current
  Continuous current
  Voltage
Notes: <number>
<footer>
<header>
<date/time>
The power drive must match the motor technology and also provide the correct peak current, continuous current, and voltage to drive the motor. If your drive supplies too much current, you risk damaging your motor. If your drive supplies too little current, you will not have the full amount of torque your motor is capable of. If you voltage is too low, you will not be able to run your motor at the speed it is capable of. One other thing to consider is how your amplifier will connect to the controller you use.

## Slide 22: NI Motor Drive Products
MID series Stepper and Servo drives
  MID-7604/2 four and two axis 1.4 Amp/phase stepper drive
  MID-7654/2 four and two axis 5 Amp continuous servo drive
Universal Motion Interface (UMI) for easy connectivity to 3rd party drives
See Drive Advisor at ni.com/motion/advisors for info on third party drives
Notes: National Instruments offers a variety of power drive products including the MID series stepper and servo drives. These drives offer easy connectivity to National Instruments controllers and have built in power supplies. For applications that fall outside the range of these drives, NI also has the Universal Motion Interface or UMI option for easy connectivity to third party drives. The Drive advisor found at ni.com/motion contains a list of third party drives for a variety of different motor types.

## Slide 23: Motors and Mechanical Elements
App
Software
Motion
Controller
Amp/Drive
Motor
Position
Voltage
Current
Position Feedback
Mechanical
Feedback
Device
Notes: <number>
<footer>
<header>
<date/time>
The next thing we will discuss is the motor and mechanical part of the system.

## Slide 24: Selecting Components
Analyze the mechanical system
Select motor/stage
Select a power drive
Determine a motion profile
Select a controller
Select a software platform
Notes: <number>
<footer>
<header>
<date/time>
Here are the steps you can follow for designing a motion system. You often start out with analyzing the mechanical system and then choose a motor based on your findings. You then figure out what type of motion profile you will need. Your motor choice will help determine your drive choice and your motion profile choice will help determine your controller choice. Your software platform will help you determine how easy your system will be to put together.

## Slide 25: Mechanical System Analysis
Find torque and inertia at motor shaft
Include all moving parts in calculation
  Load
  Fixture
  Power transmission
Notes: <number>
<footer>
<header>
<date/time>
When you first start out, you should find the torque and inertia at the motor shaft. This will help you determine what size of motor you need to get. To find this out, you need to know things such as the load, the fixture shape and size, and the power transmission.

## Slide 26: Fixture Components
Base plate
Frame
Mechanical links
Bearings & Slides
Fasteners & Brackets
Notes: <number>
<footer>
<header>
<date/time>
Fixture components could consist of a wide variety of things including things such as:
Base plates
Frame for mounting things on
Mechanical links such as those on a robot or couplings between a motor shaft and a power transmission
Bearings and slides
Fasteners and brackets

## Slide 27
Rack & Pinion
Belt and Pulley
Gearbox
Lead Screw
Conveyer
Power Transmissions
Power Transmissions
Notes: <number>
<footer>
<header>
<date/time>
This slide illustrates the power transmission for a motion control system.
A motor is typically connected to a power transmission to get useful linear or rotary motion out of it. Here are some different power transmission types that you could potentially use in your system.

## Slide 28: Calculating Torque & Inertia
r
Inertia of a solid disc:
I = mr2/2
(r = radius m = mass I = inertia)
Rotor inertia should closely match reflected inertia
Choose Iload:Irotor less than 10:1, and ideally 1:1
Rotor with I too small results in instabilities
Rotor with I too large is inefficient
Calculate Tpeak and Trms as seen by the motor
Total torque:
  Friction torque
  Gravity torque
  Acceleration torque (T = Jα)
Verify the torque/speed requirements at each point on the motion profile are within the peak limits on the curve
Diagram from Cleveland Motion Control
Notes: Calculating torque and inertia is important to help you figure out what motor size to get. The above calulations and suggestions should help you identify the range you should go with. After finding this range, you should allow for a factor of safety by over sizing your motor.

## Slide 29: Selecting a Motor
Expensive and complicated drives
Maintenance free, long lifetime, no sparking, high speeds, clean rooms, quiet, run cool
Brushless Motors
Maintenance required, no clean rooms, sparking of brushes causes EMI and danger in explosive environments
Inexpensive, moderate speed, good high end torque, simple drives
Brushed DC
Noisy and resonant, poor high speed torque, not for hot environments, not for variable loads
Inexpensive, can be run open loop, good low-end torque, clean rooms
Stepper
Con
Pro
Robotics
Pick and place
Very high torque appliations
Velocity control
High speed control
Positioning
Micro movement
App
Notes: <number>
<footer>
<header>
<date/time>
Here is a comparison between stepper and servo motors.

## Slide 30: Selecting a Stage
Things to know:
  Resolution
  Length of travel
  Repeatability
  Load capacity
  Motor type
Notes: <number>
<footer>
<header>
<date/time>
Many times it is easier to get a system that already has most of the mechanics done for you such as a stage. Stages come in many varieties and are mechanical devices that are most commonly used to move or position objects from one location or orientation to another.
When choosing a stages, some of the basic specs you should understand are
Resolution – the smallest amount of incremental motion
Length of travel – how far it can go
Repeatability – how close the stage can come to the same position over and over again.
Load capacity – how much mass it can push around
Motor type – which type of motor is used with it to know what type of drive you will need.

## Slide 31: Motor and Stage Advisors
Search 100s of different motors and stages
Compare specifications of different motors and stages
Find connectivity diagrams to show how to connect the stage to the controller
See ni.com/motion/advisors
Notes: National Instruments has a variety of motion advisors for helping you to choose your motor, stage, or drive. See ni.com/motion/advisors for more information.

## Slide 32: Elements of a Motion System
App
Software
Motion
Controller
Amp/Drive
Motor
Mechanical
Feedback
Device
Notes: <number>
<footer>
<header>
<date/time>
Next we will discuss feedback devices.

## Slide 33: Feedback Devices
Encoders
  Incremental encoders
Analog Feedback
  Potentiometer
  Other Sensors (torque, pressure, etc…)
Other Feedback Sources
  IMAQ
  DAQ
Notes: <number>
<footer>
<header>
<date/time>

## Slide 34: Limit Switch and Motion I/O
End of travel limits for preventing damage to system
Home switches for locating reference position
Position breakpoint output for triggering
High-speed position capture input for correlating data with positions
Notes: <number>
<footer>
<header>
<date/time>
Mechanical positioning components typically have end of travel limit switches, as well as a home switch for calibrating the zero position.
These limit switches can be either mechanical, where the switch is physically tripped as a stage moves over it, or electrical (hall effect sensor, phototransistor, etc.).
These limit and home switches provide important feedback to the motion control board for providing safe and accurate operation.
Recall from our discussion that an incremental quadrature encoder can accurately count up or down, depending on the direction of movement. However, it has no idea where the motion actually started.
OPTIONAL: Demo limits and home using the Big-I box and Measurement and Automation Explorer

## Slide 35: Motion System Summary
Motor Drive
Motion Controller
And Software
Motor, Stage, Feedback devices
Third Party
NI or Third Party
NI
Notes: <number>
<footer>
<header>
<date/time>
To review the basics of motion system, they are made up of three main components which include:
Motor or stage: This component is the portion of the system that actually moves. Stages are mechanical platforms that take rotary motion from a motor and transfer it to useful linear motion that you can use to move an object from one location to another. The advantage of using a stage for your motion system is that all of the mechanical design for bearings and drive trains is already done for you. NI has both a Stage Advisor and a Motor Advisor available from ni.com/motion. The Stage Advisor contains a searchable database of over 140 stages that are compatible with NI motion controllers.
Motor drive: This is for taking the low voltage, low current signals from a motion controller and changing them to create enough current and voltage to turn the motors. Each type of motor has a corresponding drive that goes with it. For example stepper motors require stepper drives and DC brushed servo motors require DC brushed servo drives. NI makes a few stepper and servo drives (MID-7604/2, MID-7654/2) and works well with third party drives.
Controller and software: The motion controller acts as the brains of the system and performs vital functions such as calculating motion trajectories and monitoring safety limits. NI offers several different motion controllers including the high performance NI 7344 series for stepper and servo motors as well as the low cost NI 7334 controllers for stepper motors. There is also a variety of software options available for LabVIEW, C/C++, Visual Basic, and Measurement Studio/CVI.

## Slide 36: Motion Advisors
NI Product Advisor
Stage Advisor
Motor Advisor
Drive Advisor
See ni.com/motion/advisors
Notes: National Instruments has a variety of motion advisors for helping you to choose your motor, stage, or drive. See ni.com/motion/advisors for more information.

## Slide 37: NI Motion Product Advisor
Helps you determine:
  The right controller
  Which drives you can use
  The appropriate cables
  Which software packages you need

## Slide 38: Example Project – Cutting a Hole in a Door
Steps:
Configure the system
Define accelerations and velocities
Create a circular motion path
Blend the motion
Download the program to the onboard memory of the motion controller
Notes: In this next section we will cover an example project which will be cutting a hole in a door frame.

## Slide 39: Configuration
One-time process
Control any motor
Virtual Stage
Notes: <number>
<footer>
<header>
<date/time>
To be able to control any motor, nearly every setting you can think of is software configurable: stepper output mode, inhibit polarities, rising/falling edge/level position triggers, PID parameters, etc.
Configuration for your mechanical system is often a one-time process using an easy to use, interactive interface (Measurement and Automation Explorer). There are hundreds of parameters you can optionally configure to optimize your system. Then, within your application, call “Initialize,” and all the parameters you have configured will get set.
In addition, you can run diagnostics and test individual axes of motion using this program. These diagnostics includes a 2-axis virtual stage. This will be useful for our demonstration, because it allows everyone in the audience to see the motion that real world motors move in. It traces the path as well.

## Slide 40: Simple 3 Icon Program for Single Axis Motion
Initialize
  Calls default configuration from MAX
Load Target Position
  Default mode is absolute position Mode
Start Motion
Notes: <number>
<footer>
<header>
<date/time>
Now let’s return to our application. Using the NI Motion software and controller, a basic point to point move involves only three commands.
First, Initialize the board. This will configure all motion parameters to a known state and energize the motors.
Next, load the target position that you wish to move to.
Finally, command the board to Start Motion.
Note that, after you run this program, LabVIEW will complete immediately while the motor is still moving. This is because the motion board has a real time trajectory generator and on-board intelligence to complete the commanded move.
It follows a trapezoidal velocity profile using your default velocity and acceleration parameters, arriving exactly at the commanded target position.

## Slide 41: Set Velocity, Acceleration, and Monitor
Load Velocity
  Counts/Second
  RPM
Load Acceleration
  Counts/Second2
  RPS/sec
Plot position while move not complete
Notes: <number>
<footer>
<header>
<date/time>
For our next step in the simple point-to-point move, we will add a Velocity and Acceleration control. Setting each of these parameters requires one function call.
As shown, velocity and acceleration can be loaded using two different units, depending on your personal preference. Counts/Second and Counts/Sec^2 will allow you to easily specify a low level, precise value. RPM and RPS/sec are higher level real-world units. They also allow you the benefit of moving at speeds below 1 counts/second (since they are floating point parameters).
Once the move begins, we can plot the current position of the moving axis while the move is not complete. This requires two commands, “Check Move Complete” and “Read Position.” We will use a LabVIEW while loop to poll our motion board.
Experiment with different values of velocity and acceleration. Specifically, set a very low acceleration to see and hear the motor ramping up and down in speed. Also notice how quickly you can communicate with the board, thanks to the fast bus speed of our controller. You would not achieve this monitoring performance with a RS-232 controller.

## Slide 42: Add Another Axis
Duplicate all commands (Copy/Paste)
Start Motion twice
Notes: <number>
<footer>
<header>
<date/time>
In only a few minutes, you’ve seen how to make a simple point to point move on one axis. We were able to set the trapezoidal profile values, and monitor the move until it was completed.
Now let’s introduce a second axis by simply copying and pasting the block diagram of one move. Also we will create separate copies of the position, velocity, and acceleration controls in order to set independent values.
If we set velocity and acceleration to be equal on both axes, but with different target positions, you will see that the motion starts on both axes (roughly) at the same time. However, one axis will complete its move before the other one does.
If we were moving a two axis stage or positioner, this is not acceptable to perform vectored moves. We would have to resolve our desired vectored move into component vectors, in terms of velocity and acceleration.
Even then, the move does not truly start and end at the same time, because the LabVIEW code is in a basic race condition and may be off by several milliseconds.

## Slide 43: Coordinate the Axes
Vector Space
Position (x,y,z) =
Velocity = d /dt
Acceleration = d /dt2
V
V
V
Notes: <number>
<footer>
<header>
<date/time>
This graph illustrates the problem of no interpolation vs. linear interpolation, also called using a vector space.
The National Instruments motion interface supports on-board calculations of vectored information, causing motion on two (or three) axes to start and stop at exactly the same time (within microseconds).
To use a vector space, first configure the vector space (X,Y,and Z axes). These can be in any order, and any axis can be disabled for a 2-D VS instead of a 3D VS.
Next, replace the individual “Read Position” functions with a “Read Vector Space Position.”
Load Velocity, Load Acceleration, and Start Motion do not have to be changed, and they will intelligently operate on the vector instead of an individual axis.

## Slide 44: Move in an Arc
Load Circular Arc
  Radius
  Start Angle
  Travel Angle
Notes: <number>
<footer>
<header>
<date/time>
Keeping in mind that our original goal was to move in a circular pattern, we now introduce the circular interpolation mode of the NI Motion controller.
This is similar to linear interpolation in that it operates on a vector space; however instead of loading an (x,y,z) coordinate, you specify three parameters of a circular arc.
In the slide, radius corresponds to label #6, start angle is #4, and travel angle is #2. Using these three parameters you can define any circular arc.
Start angle must be between 0-360°, but the travel angle can be outside of this range for multiple arcs or reverse movement.

## Slide 45: Move in Two Axes
Wait for Move Complete (LabVIEW level)
Load Another Arc
Notes: <number>
<footer>
<header>
<date/time>
Recall that we are using a drilling a circular hole. In order to prevent an uneven cut, we should avoid dropping the drill bit at the edge of the path. This may cause splintering. So, we would like the profile to follow two arcs are shown above.
In the LabVIEW code, just add another “Load Circular Arc” command and another “Start” command. We also have replaced the while loop with a high level function called “Wait for Move Complete.” This is a blocking function that suspends itself until the move is complete.
Now, you can use the 2-axis position plot (virtual stage) to monitor your profile and ensure that the six parameters you have chosen for the two arcs are correct.

## Slide 46: Blending Two Arcs
Blend Motion
Notes: <number>
<footer>
<header>
<date/time>
To further reduce the risk of splintering, it would be nice to move smoothly through the two arcs instead of stopping motion after the first arc and then starting a new motion.
Blending allows you to superimpose two trajectories between two independent moves, so that you can move from point A to B to C without stopping motion at B.
The charts in the slide illustrate a velocity profile with and without blending. In our code, we will replace the “Start Motion” with a “Blend Motion.” Also, we will replace the “Wait for Move Complete” with a “Wait for Blend Complete.”

## Slide 47: Execute the Motion in an Onboard Program
Save to On-Board RAM
  PCI/PXI 7344 On-Board RAM = 64 KB
  6C On-Board RAM = 32 KB
  Each command takes ~10 bytes
  Store up to 32 Programs
  Store up to 120 Variables
Begin/End Program Store
Notes: <number>
<footer>
<header>
<date/time>

## Slide 48: Saving to RAM
RAM
Variables
ROM (Flash)
Program 1
Program 2
Buffer 3
.
.
.
.
.
Program 32
Program 1
Program 2
Buffer 3
.
.
.
.
.
Program 32
Firmware
Motion
Parameters
Program 1
Motion
Parameters
Begin
End
Notes: <number>
<footer>
<header>
<date/time>

## Slide 49: Onboard Program Execution
Trajectory Generator
Host
Computer
Host Communication Handler
Event Handler
Onboard Program (1)
Run Program #
FlexMotion running RTOS
Onboard Program (2)
Onboard Program (3)
Notes: <number>
<footer>
<header>
<date/time>
If a program is saved in volatile or non-volatile memory on the 68331 - then on executing the “Run Program” function causes the Host Communication Thread to spawn a thread - running the onboard program.
The on-board program can execute all the functions that can be executed from the Host Computer. In addition - there are some special functions that allow you to create loops, sleep and manage onboard variables.
Using the “Wait on Condition” function you can cause the onboard program to go to sleep - such that it wakes up only if the condition specified has occurred.. Once the condition occurs the Event Handler thread wakes up the onboard program and it continues executing.

## Slide 50: Wait on Condition
Event Driven
Wait on Condition
  Home Found
  Index Found
  High Speed Capture
  Position Breakpoint
  Velocity Threshold
  Move Complete
  Profile Complete
  Blend Complete
  Motor Off
  Home Input Active
  Limit Input Active
  Software Limit Active
  Program Complete
  IO Port Match
Notes: <number>
<footer>
<header>
<date/time>

## Slide 51: What is MOMO?
Must On / Must Off
Opto-22 definite protocol
Allows tri-state of digital ports (On/Off/don’t care)
Must On=True
Must Off=True
Output=On
Must On=False
Must Off=True
Output=Off
Must On=False
Must Off=False
Output=don’t care
Must On=True
Must Off=False
Output=On
Notes: <number>
<footer>
<header>
<date/time>

## Slide 52: Loop the Program
Insert Program Label
Jump to Label
Notes: <number>
<footer>
<header>
<date/time>

## Slide 53: Insert a Delay After the Trigger
Give the object time to “settle”
Real Time hardware delay
Not affected by Windows
Notes: <number>
<footer>
<header>
<date/time>

## Slide 54: Survive a Power Cycle
Save to ROM
  7344 On-Board ROM = 128 KB
  6C On-Board ROM = 32 KB
  Non-Volatile Memory
Save Default Parameters
  Initialization Parameters
Notes: <number>
<footer>
<header>
<date/time>

## Slide 55: Transfer to ROM
RAM
Variables
ROM (Flash)
Program 1
Program 2
Buffer 3
.
.
.
.
.
Program 32
Program 1
Program 2
Buffer 3
.
.
.
.
.
Program 32
Firmware
Motion
Parameters
Program 1
Program 1
save
save
Program 1
Program 2
Buffer 3
.
.
.
.
.
Program 32
free
save
defaults
Motion
Parameters
Motion
Parameters
save
Notes: <number>
<footer>
<header>
<date/time>

## Slide 56: Independent and Distributed
Enable Auto-Start
Enable Axes
Halt Motion
Notes: <number>
<footer>
<header>
<date/time>

## Slide 57: Auto-Start Onboard
RAM
Variables
ROM (Flash)
Program 1
Program 2
Buffer 3
.
.
.
.
.
Program 32
Program 1
Program 2
Buffer 3
.
.
.
.
.
Program 32
Firmware
Motion
Parameters
Program 1
Motion
Parameters
Auto-Start
Notes: <number>
<footer>
<header>
<date/time>

## Slide 58: Count Number of Jobs Completed
Variables
On-Board Variables
120 Variable Locations
Var 1
Var 2
Var 3
Var 4
Var 120
1
37
38
Notes: <number>
<footer>
<header>
<date/time>

## Slide 59: Vary the Hole Size
Load Constant from Host
Read radius from Variable
  Input Vector
Notes: <number>
<footer>
<header>
<date/time>

## Slide 60: Multi-Thread Onboard Programs
Real-Time operating system
Simultaneously run 10 On-board programs
Notes: <number>
<footer>
<header>
<date/time>

## Slide 61
Types of Motion Applications
Grid Inspection
Pick-And-Place
Velocity Profiling
End of life testing
Microarray handling
Notes: <number>
<footer>
<header>
<date/time>
There are several other types of motion applications that can be performed with the same basic steps that we’ve just outlined.
For example, a grid inspection type of motion is very common. With an overhead camera, actuator, or sensor, a stage moves back and forth in a raster scanning motion to cover all points in a grid. For example, this template may be used for filling or sampling test tubes, inspecting IC labels or legs, or inspecting pixels under a microscope.
A pick-and-place application involves moving from a parts bin to various part targets. At both the bin and the part target, a third axis of motion drops to ‘pick’ or ‘place’ a part.
In a velocity profiling application, a conveyer is driven in velocity mode under a camera or sensor. As an object passes under the camera, the belt decelerates so the inspection can occur with greater detail. After the object has passed, the belt speeds up again to maximize throughput.

## Slide 62: Conclusion of Motion Project
Using NI-Motion is EASY
NI-Motion is POWERFUL
Creating an application with NI-Motion is FAST
Notes: <number>
<footer>
<header>
<date/time>
In a few short steps, we were able to create a motion profile that would take significant hardware effort in a traditional, proprietary system.
In a real machine, we could continue to increase the performance and functionality of this task. For instance, you could download all the code to the controller and have it execute on-board. Then, you could have it wait on a digital trigger. You could also have it stored in non-volatile flash ROM and automatically run after a power cycle. You could also run two of these tasks in parallel on a 4-axis controller, using the on-board real-time multi-threaded operating system.
Hopefully this simple demonstration of a designing a motion project shows that National Instruments motion control is easy, powerful, and fast.

## Slide 63: Global Service and Support
Components
Services
Solutions
Measurement and Automation
Components
Web-
Based
Config
Global
Support
Global
Services
System
Integration
Measurement and Automation
Systems
Driving Down Overall System Cost
Notes: <number>
<footer>
<header>
<date/time>
A successful application requires more that just computer software and hardware technology. When you choose National Instruments software and hardware, you can be assured that we are committed to helping make your computer-based measurement and automation application a success.
National Instruments provides comprehensive support services including technical support, consulting, product training, and more than 500 Alliance members worldwide who can provide you with a wide array of design, development, and system integration services, and also deliver benefits to you that:
  Shorten your application development time
  Keep your software and hardware products up-to-date with the latest features and capabilities
  Provide you with resources to maximize system performance and reliability

## Slide 64: Global Service and Support
Award-Winning Support
  The Association of Support Professionals—Top Ten Web Support Sites
  2,000+ Example programs
  100+ Application notes
  7,000+ Knowledge bases
Field Sales Engineers
  More than 200 engineers worldwide
  Ready to provide on-site assistance
Notes: <number>
<footer>
<header>
<date/time>
A wealth of information exists at ni.com to aid you in the development of your measurement and automation application, including example programs in LabVIEW, Measurement Studio, LabWindows/CVI, and Microsoft Visual Studio. These example programs not only demonstrate some of the more advanced features in the various application development environments, but also demonstrate how to use the hardware and device drivers. Furthermore, if you feel that you have hit a roadblock in your application, you can visit an online community called Developer Exchange, where NI customers from all over the globe talk about their applications and share innovative ways to apply the hardware and software.
Field sales engineers can visit you onsite and consult with you on your measurement and automation applications. These engineers have experience in hundreds of applications that they can immediately apply to your measurement and automation system.

## Slide 65: Global Service and Support
Many training options
  On-site courses for software and hardware
  Technical workshops with content customized for your company/industry
  Online tutorials for NI products and technologies
  Worldwide availability
Notes: <number>
<footer>
<header>
<date/time>
The National Instruments commitment to our customers does not end with a sale. To meet your training needs, National Instruments offers educational tools designed to help you become productive with our products. There are technical seminars, self-paced course kits, videos, interactive computer-based training, hands-on training courses, and a wide variety of online courses that can be completed at your own pace and tailored to your skill level.
NI holds technical seminars in cities throughout the world to inform you about emerging technologies and the latest trends in data acquisition and instrument control.
The hands-on training courses minimize application development time by shortening the initial time needed to become productive. The courses are more than lectures; they give attendees hands-on data acquisition and instrument control applications experience.
Class size is limited to 12 students so that each student can receive personal attention and have opportunities to discuss his or her own applications with the instructor, one-on-one.
Instructors for all National Instruments hands-on training courses are highly qualified National Instruments application engineers, who provide technical support for our products, or Alliance Program members.
During the classes, each student is provided with a computer, plug-in DAQ board, GPIB interface board, a function generator, and a course manual. The course manual serves not only as the classroom manual, containing lecture material and hands-on exercises, but also as a comprehensive reference after the class.

## Slide 66: National Instruments Alliance Program
  More than 500 companies
  System integration
  Products
  Consultants
Talk to NI Sales Engineers for information about Alliance member expertise
Notes: <number>
<footer>
<header>
<date/time>
Throughout our history, National Instruments has worked hard to develop relationships with OEMs, VARs, consultants, system integrators, and developers. These relationships have proven critical to our success. The worldwide National Instruments Alliance Program formalizes these relationships to maximize the benefits for National Instruments, program members, and—most importantly—our mutual customers.
National Instruments products have revolutionized measurement and automation as well as control applications. End-users now have unprecedented power and flexibility to develop their own test and measurement or process monitoring and control systems. However, because of time constraints, lack of experience, or other factors, you may prefer to employ consulting or system integration services. In these cases, you can rely on the expertise available in the vast network of Alliance Program members.
National Instruments is a broad-based supplier of test technologies for your testing needs. Alliance Program members use these test technologies to offer complete turnkey products for specific market needs. In addition, Alliance Program developers offer an array of specialized add-on products that can assist in application development. The Alliance Program offers a valuable portfolio of sales, marketing, and technical benefits designed to give the Alliance Program member tangible results.

## Slide 67: Delivering Customer-Defined Measurement Solutions
Harnessing the power of the PC and the Internet to deliver Measurement and Automation Solutions for the Technical Enterprise.
Request a visit with your local Sales Engineer to assemble your Measurement System today.
Notes: <number>
<footer>
<header>
<date/time>
Harnessing the power of the PC is really what computer-based measurement and automation is all about. The ability to leverage current technologies such as the latest processors, operating system features, networking technologies, and other PC peripherals gives computer-based measurement and automation an edge that other approaches cannot match. The marriage of these PC advances with powerful, modular software and hardware tools that were designed specifically for implementation in a PC, will yield shorter development time and lower overall system costs for your measurement and automation task.
Request a visit with your local sales engineer today to receive a demonstration of what NI software and hardware, combined with your PC, can do for your productivity.