## Slide 1: Integrated Motion, Vision, and Data Acquisition

## Slide 2: Agenda
Virtual Instrumentation
Motion Control
Vision Acquisition and Analysis
Data Acquisition Fundamentals
Imbedded Vision, Motion, and DAQ
Integrated DAQ, Vision and Motion

## Slide 3: What is Virtual Instrumentation?
Customer-Defined
PC-Based Measurement and Automation Solutions
Traditional Vendor-Defined
Instruments
Processor
RAM
ROM
Display
Power
Supply
Hard Disk
Notes: <number>
<footer>
<header>
<date/time>
The virtual instrumentation paradigm has transformed test, measurement, and automation applications from loosely coupled—and often incompatible—stand-alone instruments and devices into tightly integrated, high-performance measurement and automation systems. At the heart of the virtual instrumentation paradigm lies a component that has become increasingly more important—software.
While the hardware advances in the personal computer have driven significant performance improvements and cost reductions compared to traditional stand-alone instruments, it is the highly productive, integrated software that empowers hundreds of thousands of engineers and scientists. A complete set of software tools—from measurement driver architectures and instrument connectivity software, to highly productive application development environments and open connectivity with standard tools across the enterprise—gives engineers and scientists the freedom to create a new level of powerful, customized measurement systems.

## Slide 4: Virtual Instruments for Measurement and Automation
Application Software:
  LabVIEW
  LabWindows/CVI
  Measurement Studio
Hardware and Driver Software
Notes: <number>
<footer>
<header>
<date/time>
Whether acquiring data over GPIB from a traditional boxed instrument or controlling a vision/motion system via a PC, virtual instrumentation applies to measurement and automation tasks across the enterprise.
Several levels exist in a virtual instrumentation system: an I/O layer, a network layer, and a PC layer. However, hardware implemented in a virtual instrumentation scheme must seamlessly interact with other hardware devices. For instance, a device that acquires images from a digital camera must correlate its data to a multitude of other devices, such as a digitizer or an arbitrary waveform generator. A comprehensive, yet flexible timing and triggering software interface glues this virtual instrumentation interaction together.
From the software point of view, examples such as LabVIEW or LabWindows/CVI integrate with the driver software to provide a consistent look and feel to a wide variety of I/O, saving you time and money when programming these devices. The application software environments also provide advanced analysis and presentation capabilities that use the PC’s processor and graphics speed.

## Slide 5: Creating Automated Measurement Systems
Motor Drive
Image Acquisition Board
Motion Controller
Data Acquisition Device
Software
Motor or Stage
Camera or Other Measurement Device
Cables
Notes: <number>
<footer>
<header>
<date/time>
Creating an automated measurement system involving motion control, machine vision, and data acquisition involves several major components. For the motion control system you need a mechanical device to move things with the motion controller. For the machine vision system, you need a camera with image acquisition hardware to get images from the camera into your computer. For the data acquisition system, you need a sensor and a data acquisition device. After selecting the components, you then need to take into consideration what software you will use and how the two systems will work together.

## Slide 6: Configuring An Integrated System
Measurement & Automation Explorer
  Use to configure all National Instruments devices
  Acquire images
  Configure and test motion control hardware
  Configure and test DAQ devices
Notes: <number>
<footer>
<header>
<date/time>
You can easily configure National Instruments motion controller, image acquisition boards, and data acquisition boards with Measurement & Automation Explorer, which is shipped with all National Instruments Hardware. This utility is an interactive tool for setting and testing each of your hardware components. With motion control, you can initialize the board and run basic moves on the controller. With machine vision, you can capture images from a variety of analog or digital cameras and make adjustments to the images. With data acquisition, you can configure channels and test your device to ensure things are working properly.
© National Instruments Corporation 5 Computer-Based Machine Vision Solutions

## Slide 7: Motion Control for Measurement and Automation
Application Software:
  LabVIEW
  LabWindows/CVI
  Measurement Studio
Hardware and Driver Software
Notes: <number>
<footer>
<header>
<date/time>
To begin, we need to first discuss some of the basics of motion control and how it fits in with the rest of the system.

## Slide 8
PC-Based Motion:
Flexibility and Lower Cost
User defined solution
Lower cost and higher performance
Flexibility for setup and reconfiguration
Integrate the entire system solution in the PC
Vendor Defined
User
Defined
Stand-alone or PLC Motion
PC-Based Motion
Low
High
Flexibility
Cost
Notes: <number>
<footer>
<header>
<date/time>
PC based motion control through Virtual instrumentation offers many different benefits. First, you have the ability to completely define your motion system, instead of a remote engineer with little or no understanding of your specific application needs. Second, PC components cost less and perform equivalent or outperform turn-key solutions. If your application needs change, you have the flexibility to modify it, or upgrade specific components to increase performance instead of buying a completely new system. Finally, motion applications are typically integrated into larger systems requiring data acquisition, machine vision, and data analysis. PC-based motion gives you a single environment to perform all of these integrated measurement and automation functions.

## Slide 9: Elements of a Motion System
Application
Software
Motion
Controller
Amplifier
Motor
Feedback
Device
Position
Voltage
Current
Position
Position Feedback
Notes: <number>
<footer>
<header>
<date/time>
A typical motion control system (with a position feedback loop) consists of the following components:
Host - which contains the motion controller - commands the desired target position.
Motion Controller - which is the brain of the of the system takes that target position and converts it into a voltage reference (+/- 10V)
Amplifier - that generates the current required to drive the motor - takes the voltage supplied by the motion controller and supplies the required current to the motor.
Motor - that converts electrical energy into mechanical energy - produces the required torque to move to the desired target position.
Position Sensor - senses the position of the motor and reports the result to the controller, thereby closing the loop to the motion controller

## Slide 10: Selecting Components
Analyze the mechanical system
Select motor/stage
Select a power drive
Determine a motion profile
Select a controller
Select a software platform
Notes: <number>
<footer>
<header>
<date/time>
Here are the steps you can follow for designing a motion system. You often start out with analyzing the mechanical system and then choose a motor based on your findings. You then figure out what type of motion profile you will need. Your motor choice will help determine your drive choice and your motion profile choice will help determine your controller choice. Your software platform will help you determine how easy your system will be to put together.

## Slide 11: Motors and Mechanical Hardware
Application
Software
Motion
Controller
Amplifier
Motor
Feedback
Device
Motor
Notes: <number>
<footer>
<header>
<date/time>
The motor is one of the first things you will choose when designing a system so let’s start there. One of the first

## Slide 12: Selecting a Motor
Expensive and complicated drives
Maintenance free, long lifetime, no sparking, high speeds, clean rooms, quiet, run cool
Brushless Motors
Maintenance required, no clean rooms, sparking of brushes causes EMI and danger in explosive environments
Inexpensive, moderate speed, good high end torque, simple drives
Brushed DC
Noisy and resonant, poor high speed torque, not for hot environments, not for variable loads
Inexpensive, can be run open loop, good low-end torque, clean rooms
Stepper
Con
Pro
Robotics
Pick and place
Very high torque appliations
Velocity control
High speed control
Positioning
Micro movement
App
Notes: <number>
<footer>
<header>
<date/time>
Here is a comparison between stepper and servo motors.

## Slide 13
Rack & Pinion
Belt and Pulley
Gearbox
Lead Screw
Conveyer
Power Transmissions
Power Transmissions
Notes: <number>
<footer>
<header>
<date/time>
This slide illustrates the power transmission for a motion control system.
A motor is typically connected to a power transmission to get useful linear or rotary motion out of it. Here are some different power transmission types that you could potentially use in your system.

## Slide 14: Selecting a Stage
Things to know:
  Resolution
  Length of travel
  Repeatability
  Load capacity
  Motor type
Notes: <number>
<footer>
<header>
<date/time>
Many times it is easier to get a system that already has most of the mechanics done for you such as a stage. Stages come in many varieties and are mechanical devices that are most commonly used to move or position objects from one location or orientation to another.
When choosing a stages, some of the basic specs you should understand are
Resolution – the smallest amount of incremental motion
Length of travel – how far it can go
Repeatability – how close the stage can come to the same position over and over again.
Load capacity – how much mass it can push around
Motor type – which type of motor is used with it to know what type of drive you will need.

## Slide 15: Motor and Stage Advisors
Search 100s of different motors and stages
Compare specifications of different motors and stages
Find connectivity diagrams to show how to connect the stage to the controller
See ni.com/motion/advisors
Notes: National Instruments has a variety of motion advisors for helping you to choose your motor, stage, or drive. See ni.com/motion/advisors for more information.

## Slide 16: Feedback Devices and Limits
Application
Software
Motion
Controller
Amplifier
Motor
Feedback
Device
Notes: <number>
<footer>
<header>
<date/time>
The next part of the motion system we will examine is the feedback device.

## Slide 17: Feedback Devices
Encoders
  Incremental encoders
Analog Feedback
  Potentiometer
  Other Sensors (torque, pressure, etc…)
Other Feedback Sources
  IMAQ
  DAQ
Notes: <number>
<footer>
<header>
<date/time>

## Slide 18: Limit Switch and Motion I/O
End of travel limits for preventing damage to system
Home switches for locating reference position
Position breakpoint output for triggering
High-speed position capture input for correlating data with positions
Notes: <number>
<footer>
<header>
<date/time>
Mechanical positioning components typically have end of travel limit switches, as well as a home switch for calibrating the zero position.
These limit switches can be either mechanical, where the switch is physically tripped as a stage moves over it, or electrical (hall effect sensor, phototransistor, etc.).
These limit and home switches provide important feedback to the motion control board for providing safe and accurate operation.
Recall from our discussion that an incremental quadrature encoder can accurately count up or down, depending on the direction of movement. However, it has no idea where the motion actually started.
OPTIONAL: Demo limits and home using the Big-I box and Measurement and Automation Explorer

## Slide 19: Motor Drive or Amplifier
Application
Software
Motion
Controller
Amplifier
Motor
Position
Sensor
Amplifier
Notes: <number>
<footer>
<header>
<date/time>
The next portion of the system we will examine will be the amplifier.

## Slide 20: Motor Drive Requirements
The motor drive must match the motor technology
  For example, 2-phase stepper motors require 2 phase stepper motor drives, etc…
The motor drive must provide adequate:
  Peak current
  Continuous current
  Voltage
Notes: <number>
<footer>
<header>
<date/time>
The power drive must match the motor technology and also provide the correct peak current, continuous current, and voltage to drive the motor. If your drive supplies too much current, you risk damaging your motor. If your drive supplies too little current, you will not have the full amount of torque your motor is capable of. If you voltage is too low, you will not be able to run your motor at the speed it is capable of.

## Slide 21: NI Motor Drive Products
MID series Stepper and Servo drives
Universal Motion Interface (UMI) for easy connectivity to 3rd party drives
See Drive Advisor at ni.com/motion/advisors for info on third party drives
Notes: NI has a variety of power drive products including the MID series stepper and servo drives. For applications that fall outside the range of these drives, NI also has the Universal Motion Interface or UMI option for easy connectivity to third party drives. The Drive advisor contains a list of third party drives for a variety of different motor types.
The amplifier used in the demo is integrated with the motor and connected through using a special NI developed interface.

## Slide 22: Motion Controllers
Application
Software
Motion
Controller
Amplifier
Motor
Position
Sensor
Motion
Controller
Notes: <number>
<footer>
<header>
<date/time>
The next thing we will discuss is the motion controller.

## Slide 23: Purpose of Motion Controller
Calculate the trajectories for each commanded move on the board to prevent Windows interference
Provide the torque commands to the motor drive or amplifier
Monitor limits and emergency stops for supervisory control
Close the PID loop

## Slide 24: Types of Profiles Available for Motion Control
Simple point-to-point move
Vector point-to-point move
Blended motion
Contouring/Arbitrary paths
Target Position, Velocity, Acceleration
Target Position (X,Y,Z), Vector Velocity, Vector Acceleration
Target Position A, Target Position B, blend factor
[Buffer of points]
Notes: <number>
<footer>
<header>
<date/time>
Here are several types of common profiles.

## Slide 25: Features of a Simple Motion Trajectory
A motion trajectory begins at the Starting Position, Accelerates using the Acceleration value and runs at the Target Velocity for a predetermined period and, then decelerates to the Target Position.
Time
Notes: <number>
<footer>
<header>
<date/time>
The motion trajectory describes the profile of the control or command signal output by the motion controller board to the driver / amplifier, resulting in a motor/motion action that follows the profile.
The intelligent motion controller calculates the segments of a motion profile trajectory based on the parameter values programmed by the user for the move selected. The desired target position, maximum target velocity and acceleration values are used by the trajectory algorithm to determine how much time is spent in the three primary segments of a move, acceleration, constant velocity and deceleration.
In the acceleration segment, motion begins from a stopped position or from a previously in-process move, and follows a prescribed acceleration ramp until the speed reaches the target velocity for the move.
Motion continues at the target velocity for a prescribed period until the controller determines that it is time to begin the deceleration segment to slow the motion to a stop exactly at the desired target position. If a move is short enough that the deceleration beginning point occurs before the acceleration has completed, then the profile will appear triangular instead of trapezoidal, and the actual velocity attained may fall short of the desired target velocity.
Enhancements to the basic trapezoidal trajectory include S-curve acceleration/deceleration, where the accel/decel ramp is modified into a non-linear, curved profile. This fine control over the shape of these ramps is very useful for tailoring the performance of a motion trajectory based upon the inertial, frictional forces, motor dynamics and other mechanical limitations in motion systems.

## Slide 26: NI Motion Controller Comparison

## Slide 27: Motion System Hardware
Motor Drive
Motion Controller
and Software
Motor, Stage,
Feedback device
Third Party
NI or Third Party
NI
Notes: <number>
<footer>
<header>
<date/time>
Motion systems are made up of three main components:
Motor or stage: This component is the portion of the system that actually moves. Stages are mechanical platforms that take rotary motion from a motor and transfer it to useful linear motion that you can use to move an object from one location to another. The advantage of using a stage for your motion system is that all of the mechanical design for bearings and drive trains is already done for you. NI has both a Stage Advisor and a Motor Advisor available from ni.com/motion. The Stage Advisor contains a searchable database of over 140 stages that are compatible with NI motion controllers.
Motor drive: This is for taking the low voltage, low current signals from a motion controller and changing them to create enough current and voltage to turn the motors. Each type of motor has a corresponding drive that goes with it. For example stepper motors require stepper drives and DC brushed servo motors require DC brushed servo drives. NI makes a few stepper and servo drives (MID-7604/2, MID-7654/2) and works well with third party drives.
Controller and software: The motion controller acts as the brains of the system and performs vital functions such as calculating motion trajectories and monitoring safety limits. NI offers several different motion controllers including the high performance NI 7344 series for stepper and servo motors as well as the low cost NI 7334 controllers for stepper motors. There is also a variety of software options available for LabVIEW, C/C++, Visual Basic, and Measurement Studio/CVI.

## Slide 28: NI Motion Product Advisor
Helps you determine:
  The right controller
  Which drives you can use
  The appropriate cables
  Which software packages you need

## Slide 29: Application Software
Application
Software
Motion
Controller
Amplifier
Motor
Position
Sensor
Notes: <number>
<footer>
<header>
<date/time>
The last portion we will examine will be the Application software.

## Slide 30: The Big Picture for Software
Specification
Configuration
Prototype
Application Development
Environment
Motion Advisors
LabVIEW
Measurement Studio
C/C++
Visual Basic
Motion Assistant
Measurement and Automation Explorer
Notes: <number>
<footer>
<header>
<date/time>

## Slide 31: Configurable vs. Programmable
Configurable
Easy to use
Interactive
No programming required
Programmable
Flexible
Easier integration with other components
Notes: <number>
<footer>
<header>
<date/time>
Configurable environments are often menu driven environments where you can easily go through and configure your system to do what you need it to do. You can think of them as offering pre-written blocks of code that you simply configure to meet your needs. Programmable environments on the other hand, require you to use standard programming languages such as LabVIEW, C, or Visual Basic to accomplish your tasks. Configurable systems offer ease of use, interactive development, and do not require programming ability. However, these types of systems often limit the flexibility and integration with other components in the system. Motion Assistant seeks to bridge the gap by offering all of the features of a configurable system and enabling you to then generate code for the more flexible programmable environments.

## Slide 32
Types of Motion Applications
Grid Inspection
Pick-And-Place
Velocity Profiling
End of life testing
Microarray handling
Notes: <number>
<footer>
<header>
<date/time>
There are several other types of motion applications that can be performed with the same basic steps that we’ve just outlined.
For example, a grid inspection type of motion is very common. With an overhead camera, actuator, or sensor, a stage moves back and forth in a raster scanning motion to cover all points in a grid. For example, this template may be used for filling or sampling test tubes, inspecting IC labels or legs, or inspecting pixels under a microscope.
A pick-and-place application involves moving from a parts bin to various part targets. At both the bin and the part target, a third axis of motion drops to ‘pick’ or ‘place’ a part.
In a velocity profiling application, a conveyer is driven in velocity mode under a camera or sensor. As an object passes under the camera, the belt decelerates so the inspection can occur with greater detail. After the object has passed, the belt speeds up again to maximize throughput.

## Slide 33
Application Software:
  LabVIEW
  LabWindows/CVI
  Measurement Studio
Data Acquisition
Integrating Motion, Vision, and DAQ Together
Notes: <number>
<footer>
<header>
<date/time>

## Slide 34: Integration: What does it mean?
First level: components residing without conflict in the same system but using different software
Second level: Single piece of application level software speaking to different components in the same system
Third level: Synchronized hardware and software components communicating together interdependently

## Slide 35: Synchronization
Coordinating measurements or actions in your system to occur simultaneously or in such as way that they work together
Synchronization is needed to
  Acquire measurements from multiple devices at the same time
  Coordinate actions from different hardware
  Accurately control timing events between devices
Notes: The main objective of synchronization of multiple measurement devices is correlated measurements and/or precise control of process execution, or when the timing of measurements are taken. In most cases, you are interested in correlation in terms of time, but correlation can occasionally be in different terms, such as position. For temporal correlation, you must synchronize measurements to correlate with the sample clock of your measurement device. In other words, it is pointless to examine measurements synchronized to within nanoseconds if your sampling clocks are 1 MHz. The objective is a system with synchronized devices that are synchronized to sub-microsecond accuracy. Precise timing of measurements is a prerequisite of the measurement device. In many applications, it is crucial to precisely know the timing of when a measurement is taken relative to some event like a trigger. It may also be important to take multiple measurements all at the same time, so they are synchronized. In many cases, these measurements may vary from motor positions, to analog voltages, to digital patterns, to images, and having the ability to synchronize the acquisition of all these different measurements can be very powerful and provide valuable data for one instant in time.

## Slide 36: Options for Synchronization
Host Communication
Externally cabling for routing signals
Internally routing through RTSI cable on PCI boards
Internally routing through PXI bus or Star trigger on PXI boards
Direct Communication through RTSI/PXI trigger bus
Notes: <number>
<footer>
<header>
<date/time>
RTSI functionality varies depending on the board type. For example, on 7344 Series motion controller boards, you can directly read and write to the RTSI pins. You can also configure them as high-speed capture inputs or breakpoint outputs. High-speed capture inputs are used as a trigger to capture and store position or initiate motion events. Breakpoint outputs are used to trigger other devices by asserting at preset positions. On E Series DAQ boards, 15 timing signals are available to RTSI, including timebase, acquisition clock, and general-purpose counter signals. On National Instruments image acquisition devices, a variety of trigger and video synchronization signals are available.

## Slide 37
PXI Trigger Bus
System
Controller
Star Trigger
Controller
Peripheral
10 MHz
CLK
132 Mb/s, 33 MHz, 32-bit Computer Bus
Star Trigger
Windows Real-Time OS
Motion
Controller
Peripheral
Local
Bus
PXI Signal Integration
-Timing and triggering improves performance
Notes: <number>
<footer>
<header>
<date/time>
Electrically, PXI adds a trigger bus (eight lines), a star trigger (13 slot-specific signals), a 10 MHz reference clock (equally distributed), and local buses (13 lines wide). The star trigger control functionality is separated from the main system controller to enable the use of standard CompactPCI controllers and to require users to pay for the star trigger feature only if they need it.
PXI Trigger Bus: Eight bused trigger lines link all PXI slots in a bus segment so that multiple boards can interact and control each other’s events through hardware.
System Reference Clock: A highly accurate 10 MHz clock is independently distributed to each PXI peripheral slot through equal-length traces. Multiple cards can use this common time base for the synchronization of events.
Star Trigger: A special star trigger slot is defined, which provides an independent dedicated line for each, up to 13 peripheral slots on a single backplane. When a star trigger controller plugs in to this slot, you control, monitor, or route triggers among peripheral slots with very low skew (within 1 nanosecond).
Local Bus: A right and left local bus composed of 13 lines is available to each peripheral slot for private communication between adjacent slots. Pairs of peripherals can pass analog or digital signals back and forth using the local bus.

## Slide 38: Examples of Integration and Synchronization
Motion Control and Machine Vision
Motion Control and Data Acquisition
Machine Vision and Data Acquisition
Notes: Here are some examples of when these different types of synchronization may be used:
Acquire measurements from multiple devices at the same time
If you had multiple analog input devices and you wanted to acquire measurements from both boards at the same time, you could use synchronization to trigger each board to acquire data simultaneously.
Coordinate actions from different hardware
If you needed to acquire an image at certain positions of the motor, you could have the motion control card output pulses when it reaches the predefined locations that will trigger the image acquisition card to acquire an image.
Accurately control timing events between devices
If you were controlling a laser with an digital signal, and need to take an accurate reading with a DMM exactly 1 microsecond after deasserting the digital signal, you could have a delayed pulse go to the DMM to control when the reading is taken relative to when the laser is shut off.

## Slide 39: Motion Control and Machine Vision
Correlate position and image data
Capture images at specific positions
Vision-guided motion control

## Slide 40: Motion Control And Data Acquisition
Correlate position and measurement data
Trigger measurements at specific positions
DAQ as feedback to a motion system

## Slide 41: Machine Vision and Data Acquisition
Capture visual and measurement data simultaneously
Trigger images on reaching analog trigger

## Slide 42: Embedded Vision, Motion, and DAQ
LabVIEW Real-Time support for vision and motion gives you:
  The ability to create embedded vision, motion, and DAQ applications
  A high level of reliability
  A distributed solution for integrated applications
Notes: <number>
<footer>
<header>
<date/time>
After developing your programs, you can send them to LabVIEW to run on the host machine. There may be times, however, when you want to create embedded applications to increase reliability or to work with embedded data acquisition systems. To enable you to accomplish this, both NI IMAQ Vision and NI Motion programs can be run using LabVIEW Real-Time. Creating programs and running them in LabVIEW Real-Time offers several distinct advantages including:
The ability to create real-time integrated applications
A higher level of reliability than Windows offers
A distributed solution: no other system offers distributed motion, vision, and data acquisition from a single location.

## Slide 43: Real-Time Systems
Reduce downtime
Increase reliability and determinism
Use existing LabVIEW code and target LabVIEW Real Time controller
Host Computer
Motion Controller
Data Acquisition
Image Acquisition
PXI LabVIEW
Real-Time controller
Notes: <number>
<footer>
<header>
<date/time>
With the lower cost of vision systems, more manufacturing systems are beginning to use them. In a high-throughput manufacturing environment, reliability becomes very important for keeping both production and safety levels high. Non-reliable systems can cost manufacturers millions of dollars when they go down and can put workers at risk. Now, you can use NI IMAQ Vision 6.1 development module to create a PC-based vision system that takes advantage of the extra reliability offered by LabVIEW Real-Time PXI.
A real-time system is considered deterministic, but this does not mean fast. By nature, vision functions are not deterministic. Image content rather than image size determines the speed of a particular image processing step. An image with more particles in it will be slower than an image with less particles in it. What you can do, however, is determine the longest time a function will take by analyzing the image that has the most content. This technique determines the upper bound, or response time.
To create an embedded vision system using LabVIEW RT, you can use existing code and the code you develop from Vision Builder. You simply download the code to the target PXI controller running LabVIEW RT. The applications where this type of technology is often found are critical applications such as those found in manufacturing plants, nuclear power plants, and aerospace systems.

## Slide 44: Global Service and Support
Components
Services
Solutions
Measurement and Automation
Components
Web-
Based
Config
Global
Support
Global
Services
System
Integration
Measurement and Automation
Systems
Driving Down Overall System Cost
Notes: <number>
<footer>
<header>
<date/time>
A successful application requires more that just computer software and hardware technology. When you choose National Instruments software and hardware, you can be assured that we are committed to helping make your computer-based measurement and automation application a success.
National Instruments provides comprehensive support services including technical support, consulting, product training, and more than 500 Alliance members worldwide who can provide you with a wide array of design, development, and system integration services, and also deliver benefits to you that:
  Shorten your application development time
  Keep your software and hardware products up-to-date with the latest features and capabilities
  Provide you with resources to maximize system performance and reliability

## Slide 45: Global Service and Support
Award-Winning Support
  The Association of Support Professionals—Top Ten Web Support Sites
  2,000+ Example programs
  100+ Application notes
  7,000+ Knowledge bases
Field Sales Engineers
  More than 200 engineers worldwide
  Ready to provide on-site assistance
Notes: <number>
<footer>
<header>
<date/time>
A wealth of information exists at ni.com to aid you in the development of your measurement and automation application, including example programs in LabVIEW, Measurement Studio, LabWindows/CVI, and Microsoft Visual Studio. These example programs not only demonstrate some of the more advanced features in the various application development environments, but also demonstrate how to use the hardware and device drivers. Furthermore, if you feel that you have hit a roadblock in your application, you can visit an online community called Developer Exchange, where NI customers from all over the globe talk about their applications and share innovative ways to apply the hardware and software.
Field sales engineers can visit you onsite and consult with you on your measurement and automation applications. These engineers have experience in hundreds of applications that they can immediately apply to your measurement and automation system.

## Slide 46: Global Service and Support
Many training options
  On-site courses for software and hardware
  Technical workshops with content customized for your company/industry
  Online tutorials for NI products and technologies
  Worldwide availability
Notes: <number>
<footer>
<header>
<date/time>
The National Instruments commitment to our customers does not end with a sale. To meet your training needs, National Instruments offers educational tools designed to help you become productive with our products. There are technical seminars, self-paced course kits, videos, interactive computer-based training, hands-on training courses, and a wide variety of online courses that can be completed at your own pace and tailored to your skill level.
NI holds technical seminars in cities throughout the world to inform you about emerging technologies and the latest trends in data acquisition and instrument control.
The hands-on training courses minimize application development time by shortening the initial time needed to become productive. The courses are more than lectures; they give attendees hands-on data acquisition and instrument control applications experience.
Class size is limited to 12 students so that each student can receive personal attention and have opportunities to discuss his or her own applications with the instructor, one-on-one.
Instructors for all National Instruments hands-on training courses are highly qualified National Instruments application engineers, who provide technical support for our products, or Alliance Program members.
During the classes, each student is provided with a computer, plug-in DAQ board, GPIB interface board, a function generator, and a course manual. The course manual serves not only as the classroom manual, containing lecture material and hands-on exercises, but also as a comprehensive reference after the class.

## Slide 47: National Instruments Alliance Program
  More than 500 companies
  System integration
  Products
  Consultants
Talk to NI Sales Engineers for information about Alliance member expertise
Notes: <number>
<footer>
<header>
<date/time>
Throughout our history, National Instruments has worked hard to develop relationships with OEMs, VARs, consultants, system integrators, and developers. These relationships have proven critical to our success. The worldwide National Instruments Alliance Program formalizes these relationships to maximize the benefits for National Instruments, program members, and—most importantly—our mutual customers.
National Instruments products have revolutionized measurement and automation as well as control applications. End-users now have unprecedented power and flexibility to develop their own test and measurement or process monitoring and control systems. However, because of time constraints, lack of experience, or other factors, you may prefer to employ consulting or system integration services. In these cases, you can rely on the expertise available in the vast network of Alliance Program members.
National Instruments is a broad-based supplier of test technologies for your testing needs. Alliance Program members use these test technologies to offer complete turnkey products for specific market needs. In addition, Alliance Program developers offer an array of specialized add-on products that can assist in application development. The Alliance Program offers a valuable portfolio of sales, marketing, and technical benefits designed to give the Alliance Program member tangible results.

## Slide 48: Delivering Customer-Defined Measurement Solutions
Harnessing the power of the PC and the Internet to deliver Measurement and Automation Solutions for the Technical Enterprise.
Request a visit with your local Sales Engineer to assemble your Measurement System today.
Notes: <number>
<footer>
<header>
<date/time>
Harnessing the power of the PC is really what computer-based measurement and automation is all about. The ability to leverage current technologies such as the latest processors, operating system features, networking technologies, and other PC peripherals gives computer-based measurement and automation an edge that other approaches cannot match. The marriage of these PC advances with powerful, modular software and hardware tools that were designed specifically for implementation in a PC, will yield shorter development time and lower overall system costs for your measurement and automation task.
Request a visit with your local sales engineer today to receive a demonstration of what NI software and hardware, combined with your PC, can do for your productivity.