## Slide 1: Intelligent Networks with LabVIEW™ Real-Time and the FieldPoint™ 2000 Family
Web Event
September 18th, 2001
Notes: Welcome to the FieldPoint 2000 Web event. My name is Shawn Liu and I am an engineer at National Instruments. I am accompanied today by Todd Walter and Raecine Meza.
Today this Web event will be hosted by the Webex technology. First let me explain some of the details on how to use this live interactive online seminar tool. During the presentation you can switch between the window you see now and a full screen view of the presentation with the button on the bottom tool bar with a window inside a window. On the right hand side of your current window you will see the online chatting location. Feel free to enter comments during the presentation. From time to time we will switch from the presentation to another application. You will be able to view what is happening with that application with a separate window. Lastly, with so many participants logged on there may be a slight delay in the video feed.
Today, National Instruments is excited to present this Web event on the FieldPoint 2000 Family of intelligent network modules. This module combines the power and ease-of-use of current computer technology with a networked, compact system to create more flexible and productive applications for industrial environments.

## Slide 2: Industrial Application Requirements
Easy-to-use software tools
Open platforms
Reliable performance
Long-term solution with easy maintenance
Notes: The power and flexibility of PC-based measurement technologies are now migrating from the laboratory setting to more industrial settings such as machine control on a manufacturing floor to embedded data logging in a vehicle. While some of these technologies have been adopted with success such as Ethernet connectivity and PC-based software programming tools, engineers are still hesitant to use these tools for various reasons.
Traditionally, engineers have been limited to proprietary systems to solve their industrial applications. Rarely do these proprietary systems meet all the required features and specifications of any given application. However, developing a custom application for an industrial environment requires in-depth knowledge of low-level real-time operating system kernels and presents problems with hardware maintenance as well. These engineers needed a software tool that was easy-to-use, but still powerful enough to define the exact behavior of an industrial system.
Another driving factor in solving industrial applications was a need to integrate these systems into existing enterprise operations. To increase productivity, it has become vital for companies to perform this integration. This requires more than simple Ethernet connectivity; it requires intelligent software that efficiently and seamlessly connects with other nodes on the network.
While these first two requirements are important, they must not be achieved while sacrificing reliability. Most industrial applications operate for extended periods of time while performing critical tasks. In these situations, reliability is still a key requirement.
In addition, since these systems are long-term solutions, they must be easy to maintain. With proprietary systems, this often required the help of consultants, etc. On the other hand, engineers that develop their own applications with custom hardware run into problems maintaining this hardware. This maintenance takes engineering time and becomes even more of an issue if the original engineer transfers to a separate group or leaves the company.

## Slide 3: Introducing….
FieldPoint 2000 Family—LabVIEW running embedded on an Ethernet-based compact FieldPoint module
FieldPoint 2000 Node
LabVIEW Application
Notes: National Instruments, a pioneer in PC-based measurement and automation, now introduces the FieldPoint 2000 Family of intelligent network modules. The FieldPoint 2000 Family combines the flexibility of a PC-based technology with the reliability of a stand-alone industrial solution. With the FieldPoint 2000 Family, engineers create applications with the easy-to use graphical development environment of LabVIEW Real-Time on a Windows desktop, then download this application through Ethernet to the dedicated processor embedded on the FieldPoint 2000 system.
The FieldPoint 2000 Family allows engineers to create systems that perform with the flexibility and power of a PC but in packaging that is much more appropriate for industrial environments. The FieldPoint 2000 Family consists of two models, the FP-2000 and the FP-2010. While they are almost identical in features, the FP-2010 has extra non-volatile memory for larger datalogging applications.

## Slide 4: LabVIEW Real-Time Development
Intuitive development
Notes: The LabVIEW Real-Time development system is an intuitive environment for engineers and scientists. Applications are created graphically with functions represented by blocks on the diagram and data between these functions represented by wires. Since these applications are analogous to flow chart designs, they are easier to create and analyze. With the graphical programming paradigm, engineers no longer have to concern themselves with syntax, miss-spelled variables and other text-based programming issues. With the block diagram representing the application and graphical debugging utilities, it is also easier to isolate problems in the application.

## Slide 5: LabVIEW Real-Time Development
Flexible environment
Intuitive development
Notes: While the intuitive LabVIEW development environment reduces development time, it is still flexible enough to create a custom application. With almost unlimited built-in libraries, engineers can pick and choose function blocks ranging from simple Boolean arithmetic to complex PID control algorithms. The built-in libraries make it easy to integrate any number of functions from the data acquisition, data logging, analysis, signal processing, network connectivity libraries to create a unique solution.

## Slide 6: LabVIEW Real-Time Development
Flexible environment
Intuitive development
Rapid deployment
Notes: In addition, LabVIEW Real-Time downloads applications to the embedded device with a simple pull-down menu for rapid deployment of systems. The intelligent software downloads the application using a high-speed Ethernet connection and is even able to maintain a user interface for debugging during development. Therefore, the development of an application for the FP-20xx appears identical to developing a standard desktop application, removing the need of having any in-depth knowledge of the real-time kernel.

## Slide 7: Distributed FieldPoint Systems
I/O Modules
Terminal Bases
Network Modules
Notes: <number>
<footer>
<header>
<date/time>
FieldPoint is an easy-to-use modular hardware platform for distributed I/O. These systems are small and compact making it an ideal measurement and control solution in remote or industrial locations. Each FieldPoint system consist of a network module, terminal bases and I/O modules.
The network modules act as the main controller for FieldPoint systems and support a variety of network protocols ranging from RS-232 to Ethernet. For instance, the FieldPoint 2000 Family of network modules are based on Ethernet. With the modular architecture, engineers can upgrade a serial based FieldPoint to a stand-alone intelligent Ethernet based system by replacing the network module.
Terminal bases are connected to the network module to create a high-speed local bus for the FieldPoint system. All FieldPoint I/O modules can be plugged into these terminal bases that have both spring locked connections and screw terminal connections. These components connect to industry-standard DIN rails and serve as the backplane for field wiring and I/O modules.
The wide selection of I/O modules include 8-16 channels of NIST-traceable analog input and output, discrete input and output, quadrature encoders input, pulse generation output, thermocouple inputs, and RTD inputs. The Hot Plug-and-Play system architecture allows engineers to replace one I/O module with a similar I/O module without disrupting the behavior of the rest of the system. With one network module, you can control up to 9 I/O modules.
With the FieldPoint Explorer configuration utility engineers can configure an entire bank of FieldPoint modules. Users have the ability to configure the range of input values, safety shutdown states, and timeout parameters.

## Slide 8: Compact, Industrial Module
  Small dimensions:
    4.3 X 4.3 X 3.6 in
    10.9 X 10.9 X 9.1 cm
  Din-rail mountable
  Wide Temperature range:
    -25 to +55 °C
Notes: The FieldPoint I/O modules are compact modules ideal for usage in industrial environments, where space is limited, or where placing a standard desktop computer is not an option. A FieldPoint 2000 module is approximately ½ the size of a brick. The systems can be din-rail mounted to increase space on the factory floor and be placed in locations with stringent temperature demands. A FieldPoint 2000 based system can operate efficiently in environments from –25 to 55 degrees Celsius.

## Slide 9: Development Steps
Step 1. Develop
Windows PC
Notes: The LabVIEW Real-Time development environment is a superset of the LabVIEW development environment making it possible to create real-time and Windows-based measurement and automation solutions with one development system. With this software architecture, developing a LabVIEW Real-Time measurement and automation application is almost identical to developing a standard LabVIEW for Windows measurement and automation application.
First, develop your LabVIEW application on the Windows desktop with all the built-in libraries and tools.

## Slide 10: Development Steps
Step 1. Develop
Step 2. Download
FieldPoint 2000 System
Windows PC
Notes: Step 2. With a simple pull-down menu from the development environment, you can download and run the application. This is a single step process that removes all the traditional complexity involved with creating real-time or embedded solutions. This requires no knowledge of the real-time operating system, yet delivers real-time performance.

## Slide 11: Development Steps
Step 1. Develop
Step 2. Download
FieldPoint 2000 System
Windows PC
Step 3. Debug
Notes: Step 3. Debug the LabVIEW Real-Time application while it is running on the embedded target from the development system with all the debugging features such as breakpoints, single stepping, and probes are available in LabVIEW. The intuitive nature of these debugging tools help isolate problems faster.

## Slide 12: Development Steps
Step 1. Develop
Step 2. Download
FieldPoint 2000 System
Windows PC
Step 3. Debug
Step 4. Deploy
Notes: Step 4. Deploy the application. With the professional development system, you can download the application to the static (Flash) memory on the FP-20xx. After deploying the application, you have the choice of disconnecting it to behave as a stand-alone unit or network it as part of a larger measurement and automation system.

## Slide 13: Demonstration
Creating and Deploying a LabVIEW Real-Time Application
Notes: [Demo a simple FP-2000 application being downloaded onto the FieldPoint system:
Step 1. Show LabVIEW functionality with front panel and block diagram.
Step 2. Open existing application with program included.
Step 3. Show that this is exactly the same tools.
Step 4. Download and run the program. Use debug tools to verify the solution is working correctly.
Step 5. Show that the application can disconnect and reconnect seamlessly. (Optional)]

## Slide 14
Reliable Stand-alone Performance
Dedicated processor
Notes: The FP-20xx has many features that enable it to act as a stand-alone device. Since most stand-alone device reside in remote or inaccessible locations, it is important for these system to be reliable to eliminate the need for constant maintenance. The dedicated processor in the FP-20xx runs a real-time operating system which executes the LabVIEW Real-Time application deterministically. The reliability of the real-time operating system also reduces the chances of system malfunction. (and DRAM)

## Slide 15
Reliable Stand-alone Performance
Dedicated processor
Watchdog timer
Notes: The FP-20xx includes a Watchdog timer that monitors the overall operation of the FieldPoint system. When the watchdog senses that the system has a malfunction, it can run a separate maintenance routine or even reboot the FieldPoint system. The operation of the watchdog is completely user-defined through a simple and intuitive protocol.

## Slide 16
Reliable Stand-alone Performance
Dedicated processor
Watchdog timer
User-defined dip switches and LEDs
Notes: The FP-20xx also includes 5 dip switches and 3 tri-color LEDs and 1 bi-color LED that can be used for user interaction as a stand-alone system. For instance, the LEDs can be used to signify certain states of operation while the dip switches can be configured to specify the startup state of the FieldPoint system.

## Slide 17
Reliable Stand-alone Performance
Dedicated processor
Watchdog timer
On-board static memory
User-defined dip switches and LEDs
Notes: There are two options for the onboard static memory consisting of 3 MB or 11 MB of CompactFlash memory. The Flash memory acts as a hard drive for the system and can be used to store startup applications or data. For instance, you can configure the FP-2000 to monitor the temperature inside an environmental chamber while logging that data to the Flash memory. The FP-2010 is ideal for large data-logging applications with the larger 11 MB of Flash memory.

## Slide 18
Reliable Stand-alone Performance
Dedicated processor
Watchdog timer
On-board static memory
Connector for redundant power supply
User-defined dip switches and LEDs
Notes: The FP-20xx includes a second set of screw terminals to connect a backup power supply. The system will automatically switch to this second power supply, when it senses a problem with the first power supply.

## Slide 19
Reliable Stand-alone Performance
Dedicated processor
Watchdog timer
Serial port
On-board static memory
Connector for redundant power supply
User-defined dip switches and LEDs
Notes: The RS-232 serial power allows the FP-20xx to connect to existing systems. In addition, it can be used to connect other serial devices such as a serial LED which can be used to display information for the operator, serial based flow meters, and other serial FieldPoint systems.

## Slide 20: Create a Stand-alone System
Data-logging applications
  In-line data analysis
Control applications
  Device level intelligence
Download Application
Notes: With LabVIEW Real-Time downloading the code into the FP-20xx, you can create a stand-alone system. For instance, you can create a custom data-logging application that acquires the data from the FieldPoint I/O module and logs the data to the local Flash memory. With over 100 analysis routines such as digital filters, spectrums analysis, signal processing, and curve fitting in LabVIEW, you can include custom in-line data analysis on the FP-20xx node. The in-line analysis can convert the raw data into more effective information by averaging a set of temperatures or even linearizing data for non-linear sensors. (Open Data Format)
You can also create a stand-alone control application that continually monitors and responds to a set of stimuli. For instance, this system can be used to monitor and control the pressure in an environmental chamber. With built-in PID, fuzzy logic and other control algorithms, you can build a custom control routine for the system. With this custom control routine running in the stand-alone control node, the FP-20xx has device level intelligence where it doesn’t rely on a main supervisory control station to make decisions for it. In addition to being more reliable, this improves the performance of the system with a real-time system responding deterministically to stimuli.

## Slide 21: Deploy a Stand-alone System
Example: In-vehicle system
FP-2000 Network Module
FP-2010
FP-TC-120
FP-QUAD-510
FP-AI-110
Thermocouple module connected to brake pad and engine
Quadrature encoder module connected to axle to monitor rotation
Analog input module connected to torque and strain
Din-rail mounting
Notes: Let us look at an example of the stand-alone data logging system such as an in-vehicle data acquisition system. These systems are often used to monitor the condition of the vehicle during trial runs around a test track. With the rigorous environment and limited space it is often difficult to use standard desktop computers to monitor these conditions while proprietary stand-alone measurement devices are too rigid and expensive. With a FP-2000 based system, you could connect to a thermocouple module to measure temperature around the vehicle, as well as a quadrature encoder module to measure the speed of the main axle, and an analog input module with strain gauges to measure the flexibility of struts.
With LabVIEW Real-Time, you can download the data logging application to the FP-2000, then reconnect to it at a later time to retrieve the information for any further post processing.

## Slide 22: Demonstration
In-Vehicle Data Logging
Notes: [Demo a simple data logging example downloaded to the FP-2000
Step 1. Explain gauges and other front panels objects.
Step 2. Show the simple protocol used to log data.
Step 3. Create the executable and download to Flash.
Step 4. Open up a post processing example that reads a prerecorded data logging file.]

## Slide 23
Open Network Connectivity
Connect to local area resources
  Existing performance databases
  Operator stations
  Supervisory stations
  Peer-to-peer communication
Extend to the World Wide Web
  Embedded Web server
Notes: While the FP-20xx can operate as a powerful stand-alone system, its networking features enable it to be integrated into a larger network of real-time systems. With the growth and acceptance of Ethernet, companies are beginning to realize the benefits of networking their entire enterprise with this fast data highway. For instance, systems in the manufacturing line that once operated independently are now being connected to the local network to share information such as manufacturing yields and component test results.
But simply adding an RJ-45 Ethernet connector to a device does not make it fully connected to the rest of the enterprise. With enterprise resources supporting various protocols, the device must be flexible and intelligent enough to communicate with all these resources at the same time. With LabVIEW Real-Time running on the FP-20xx, you can develop application to speak to various local area resources such as statistical performance databases that manufacturing engineers can access, operator stations on the manufacturing floor, supervisory stations located in the main control room or you can even share information with other FP-20xx nodes to operate more efficiently.
With the networking features built-in to the LabVIEW development library, you can even extend past the resources of the enterprise to easily publish information through a web browser or through other tools such as the LabVIEW player. This allows your system to be monitored from different geographic locations and by a larger audience as well.

## Slide 24: Create a Networked System
Engineering Workbench
Performance Database
Device
Testing
Pressure and Temperature Monitoring
Machine Control and Monitoring
Manufacturing Systems
Ethernet Data Highway
Enterprise Systems
Operator Station
World Wide Web
Notes: While the FP-20xx is flexible enough to operate in many different types of networked setups. It can be part of small dedicated network of 5-10 intelligent nodes or it can be connected to the local are network on a manufacturing floor which has a gateway to the rest of the World Wide Web.
In this diagram, we have an example of a prototypical manufacturing system that could be used to create electronic components. In this system there may be test chambers that must be monitored to guarantee the integrity of the tests. The devices are loaded and unloaded into the test chamber with a machine that must be constantly maintained for high throughput. In this example, FP-20xx systems monitor the pressure, temperature of the test chamber. A second system could perform the tests inside the chamber such as measuring analog voltage levels. A third system can be used to control the machine as it loads and unloads the test chamber while simultaneously monitoring the machine to predict failures before they occur.
Operators on the manufacturing floor must have the ability to check on all the systems when necessary. With the integrated networking features of the FP-20xx, this can be done from one operator station that is connected to the same local area network. If the local area network of the manufacturing system is connected to the rest of the enterprise, engineers can then view the results of manufacturing verification of the electronic components from their desks. The data gathered from the device testing node can be sent to a performance database then retrieved later or directly to the desktop of the engineer.
The system can be expanded further to broadcast information over the world wide web as well. For instance, an engineer could then monitor the testing of the electronic components from their office or from their home computer.

## Slide 25: Integrated Control and Monitoring
FP-2000
FP-AI-110
FP-AO-200
FP-TC-120
Analog output module to adjust valve output
Thermocouple module to measure the temperature of valves
Analog input module to measure pressure
Example: Vacuum pump
FP-2000 Network Module
Notes: The flexibility of the FP-20xx system also enables the user to design integrated control and monitoring systems. For instance, vacuum pumps are commonly used in manufacturing to create a simulated atmospheric pressure. Often one system is used to control the pressure while a second system is required to routinely check the vacuum pump for maintenance issues. With the FP-20xx system you can create one system that controls the pressure of the valve by measuring the pressure and adjusting the valve from the vacuum pump while another module could be monitoring sensitive areas which heat up during the operation such as the variable output valve or the engine in the pump.

## Slide 26: Demonstration
Vacuum Pump Monitoring and Control
Notes: [Demo a simple data logging example downloaded to the FP-2000
Step 1. Explain gauges and other front panels objects.
Step 2. Show the simple protocol used to log data.
Step 3. Create the executable and download to Flash.
Step 4. Open up a post processing example that reads a prerecorded data logging file.]

## Slide 27: Other Typical Application
Embedded datalogging
Machine monitoring and control
Distributed control
Process control
Distributed monitoring
Predictive maintenance
Notes: There are other typical applications that can use the FP-2000 such as distributed control, process control, distributed monitoring and predictive maintenance. While these systems have been services by proprietary stand-alone systems, their requirements have exceeded the capabilities of those systems and now require standard off-the-shelve tools.

## Slide 28
Reduce development time
  Graphical development environment
  Off-the-shelf modular hardware
Easy maintenance
Flexible system with reliability
  User-defined solutions
  Dedicated performance
FieldPoint 2000 Family
Notes: Engineers can use LabVIEW Real-Time and FieldPoint to reduce development time. With the graphical development environment of LabVIEW, engineers will be able to develop their application in less time. The modular FieldPoint hardware is ready-to-run so that engineers don’t have to concern themselves with proprietary hardware.
With LabVIEW, engineers have a productive tool they can use to modify the application or grow it according the changing system specifications. The modular hardware can be added to an existing system for more I/O and is even hot-swappable making it easy to maintain in the case of hardware failures.
The flexibility of the PC through the LabVIEW development environment enables engineers to define their own solutions entirely. They can develop a single stand-alone system or an entire network of intelligent distributed nodes. The dedicated processor on the FP-2000 ensures that while the intelligent node is more flexible, it has the same reliable characteristics of traditional proprietary systems.

## Slide 29: Polling questions
What industry do you work in?
Does your factory or laboratory have Ethernet connectivity?
Who thinks they need Flash memory?
Are moving parts a concern in your application?
Is temperature a concern in your application?
What is the coolest feature in the FP-2000?
Are you performing control?
What kind of systems do you currently use?
Are you familiar with LabVIEW?