## Slide 1
<date/time>
<footer>
Notes: <number>
<footer>
<header>
<date/time>

## Slide 2: Distributed I/O and Data Acquisition
N
N
N
N
Industrial Network
N
N
N
N
N
N
N
N

## Slide 3: FieldPoint – Distributed I/O
Modular
Networked
Easy-to-Use
Industrial

## Slide 4: Modularity
I/O Modules
Terminal Bases
Network Modules

## Slide 5: FieldPoint – I/O Modules
8 to 16 channels/module
Isolated to 3,000 Vrms
Hot-swappable, plug-and-play
Variety of I/O types
  thermocouples, RTDs
  mV, V (up to 36 V), 20 mA
  discrete I/O, relays
  counters, PWM outputs

## Slide 6: FieldPoint – I/O Options
I/O Modules
I/O Modules
Terminal Bases

## Slide 7: Network Interface Options
Serial
  RS-485 and RS-232
  Optomux, 115 kbaud
Ethernet TCP/IP
  10 Mbps and 100 Mbps
FOUNDATION Fieldbus, H1
  Embedded function blocks
    AI, AO, DI, DO, PID

## Slide 8: FieldPoint with RS-232/RS-485
RS-232 or
RS-485
FP-1000 RS-232 Network Interface
  Connects directly to PC COM port
  Second RS-485 connector to additional FP-1001 modules
FP-1001 RS-485 Network Interface
RS-485
Up to 25 banks (1,200 m)

## Slide 9: Ethernet Connectivity
FP-1600 Network Interface
  TCP/IP Compatibility
  10 Mbps and 100 Mbps
  Event-driven communications
  Instant data connectivity to network, intranet, internet
10Base-T or 100Base-TX

## Slide 10: Distributed Control with Fieldbus
FP-3000 Network Interface/Controller Module
  FOUNDATION Fieldbus H1
  Link Active Scheduler
Embedded Function Blocks
  PID function block for standalone, distributed control
  AI, AO, DI, DO, CDO blocks
    alarming, trending, filtering, scaling, interlocks
PID
FP-3000
AI
AO

## Slide 11: FieldPoint Technology
HotPnP Plug and Play
  Hot-pluggable modules
  Auto-configuration
  Electronic data sheets on modules
  Replacement modules inherit configuration of replaced module
Robustness and Reliability
  Isolation on each module
  Wide operating temp. range
    -40°C to + 70°C (-40°F to +160°F)

## Slide 12: FieldPoint Technology (continued)
High-Quality I/O
Programmable power-up states
Programmable watchdog states
  For communication loss
Diagnostics
  Field wiring
  Hardware errors
  Modules return error conditions

## Slide 13: Key Technologies Converge
Data Acquisition (DAQ)
Industrial Comm.
Software
I/O technology
Precision measurements
Sensor interfacing
PC interfaces
Networking technology
Hardware drivers/servers
Windows technology
HMI/SCADA
PC-Based Networked I/O

## Slide 14: FieldPoint Software
FieldPoint Explorer
FieldPoint Server
  BridgeVIEW
  LabVIEW VIs
  LW/CVI
Lookout Driver
OPC Server
FieldPoint
Server (DLL)
BridgeVIEW
LabVIEW,
LW/CVI
Lookout
Driver
N
N
N
N

## Slide 15: Configuration Software
Quick Configuration
  Network and communications
    baud rate, addessing, IP, etc.
  FieldPoint hardware
    ranges, filters, power-up states, etc.
  Servers
    named tages, scan rate, etc.
Troubleshooting, monitoring
Windows NT/98/95

## Slide 16: FieldPoint OPC Server
Wide connectivity to software systems
Easy integration into HMI/SCADA software packages
Seamlessly access server (and I/O) over the PC network (using DCOM)

## Slide 17: FieldPoint – Summary
Modular
Easy
  To install, configure, use, and maintain
  Software Integration
Networked
  Serial, Ethernet, and Fieldbus
Industrial
  Isolated, robust, wide temperature range