## Slide 1: Managing High-Density Switch Systems with NI Switch Executive How to Avoid the 7 Most Common Problems in Switch Programming
Ron Harrison
Automated Test Software
Product Marketing
Notes: This presentation addresses the importance of switching in today’s automated test systems by illustrating the challenges that test engineers commonly face when implementing switching and demonstrating a typical high-density switch system for test. NI Switch Executive will be presented as well to highlight how many switching challenges can be solved by a commercial-off-the-shelf switch management software. By leveraging NI Switch Executive, you can save on development time and system maintenance and it enables you to easily reuse existing switch hardware as well as the software Powerful PXI based modular switch hardware will also be discussed to inform you of the latest in compact, rugged, high-performance and switching options.

## Slide 2: Switching Overview
Sample 2-wire matrix setup with 2 matrices
Notes: This is a sample matrix setup between 2 matrix modules configured in a 2-wire 4x8 topology. Each bend in the route requires 2 relays to actuate. Therefore each route has 4 relays to be controlled and the entire system requires 4x4 = 16 relay calls. This would require at least 20 function calls and VIs. The demonstration here is connecting all of these routes to perform a Frequency Response Test on UUT2 (FreqRespTest2).

## Slide 3: Challenges in Building ATE Systems
Switching takes a high proportion of automated test development time
  Configuring switch layouts (types of signals, routing,
  switch module interconnections)
  Automating switching through programming
Switch configuration and programming overhead reduces test throughput
Extensive switch system maintenance
Switching usually represents 30 – 50% of ATE System Costs
Notes: <number>
<footer>
<header>
<date/time>
The concept of switching is relatively simple one. However, in designing and building an ATE system, switching is often an after-thought. This leads to rushed development and an ill-planned switching architecture which prevents reusability of test code and makes maintenance a nightmare. Essentially, once you begin combining and integrating multiple switches and switch configurations to meet the measurement needs of your test system, switching can become very complex and tedious if you do not carefully choose your switching software and hardware tools. Some of the challenges associated with integrating switching into an ATE test system include:
Signal types
Routing
Hardwire connections
Programming
Maintenance
costs
While switching always reduces the overall test system cost (otherwise you wouldn’t use it in the first place) it still accounts for nearly 30 – 50% of the overall automated test system cost. This is often due to the choice of test specific hardware and the lack of software reuse and having to redevelop test code. Thus, it is very important to select modular switching hardware and software that is designed to deliver reduced instrumentation costs but also increased performance while lowering potential development and maintenance costs.
The following presentation will outline the 7 hurdles in switch system development and discuss the alternatives to solving these challenges.

## Slide 4: 1) Big Channel Count = Big Headache
Large switching systems are difficult to program and maintain
Previous methods of switch configuration:
  Rough in-house utility (hard-coded)
  Spreadsheet based
  *.txt or *.ini based
Notes: Perhaps the most obvious challenge in developing high-density switching systems is the programming. Mathematically, increasing your switch channel count by one increases the possible signal routes or endpoint-pairs exponentially. To illustrate this concept, a 4 channel system can have 6 possible endpoint-pairs while 5 channels can have 24 and 6 can have 120. (3x2x1 vs. 4x3x2x1 vs. 5x4x3x2x1).
[Example with endpoints A, B, C, D. Possible pairs are:AB, AC, AD, BC, BD, CD.]
Now, there is a 1-to-1 relationship between number of channels and switch programming, therefore, the larger the channel count system, exponentially more complex the programming. Switch programming is further hindered by organizing or defining your signal mapping or routing. Typically, engineers will use a spreadsheet to organize their signals and routing. In the diagram above, we see a table that correlates instrument or device under test endpoint to switch pin, to switch position and also to relay number. Once this mapping is complete, programming begins and it is usually hard-coded and tied to specific tests or instrument code. Just programming the system becomes complex let alone trying to reuse instrument code and maintain the system.

## Slide 5: 1) Recommendations:
Use a data management tool (database software)
Use channel aliases instead of hard-coded channels
DEMO: Alias Names & Routes and Route Groups
Notes: The recommendation to alleviate this particular challenge is to develop a utility or use a data management tool such as a database to create the relationships between instrument and DUT I/O and switch endpoint. Also, if you can further abstract your programming by using aliases, it becomes simper to reconfigure your switching without having to rewrite your test program. This is because you can simply change the signal name that an alias refers to in your database or utility without having to change your programming since it makes reference to a switch endpoint using the alias.
Now signal routing is typically more challenging than signal mapping. Either hard-coded routes must be employed in your database for every endpoint pair or a routing utility must be developed to coordinate between the endpoints selected and the corresponding switch relays to close to create the path.
NI Switch Executive builds on this concept of channel aliasing (naming) and signal routing. NI Switch Executive creates a virtual device that contains all the switch configuration and routing while providing a simple application programming interface (API) to access the endpoints and signal routes. This allows you to abstract the low-level configuration of your switch system while keeping your switch programming simple. Let’s take a look at NI Switch Executive.

## Slide 6: 2) “These registers are making me crazy!?”
Register-level or byte instructions become tedious
Mistakes and shorts are common
Difficult to tie back to signal names
Code is hard to document…
…And very hard to debug
110101010010101011010100110101010
1010101101010101001101001010101001100111
Notes: In switch system development, it is common for engineers to develop their own switch hardware and use a controller or digital I/O module to control switching. The challenge with this is that you either have to use register-level programming to automate your controller or digital I/O module, or in the case that your digital I/O module comes with a driver, you will be limited to simple digital functions. Each relay on your switch has to be individually controlled by commands and for high-density switch systems, the probability of programming error increases dramatically. Common errors include incomplete routes where one of the relays in the path hasn’t been switched (an open) or shorts where paths are accidentally connected together, potentially damaging equipment or your device. This not only makes debugging difficult since it deals with the hardware but the programming doesn’t tie back to signal names or aliases. Other problems begin to surface as well such as documenting and maintaining this code.
Aghhh!

## Slide 7: 2) Recommendation:
Avoid register-level/digital I/O programming
Use IVI-compliant switches
  HW and SW from NI included
IVI-driver benefits:
  Simulation
  Performance
  Easy-to-use
  Interchangeability
NI Switch Executive
Switch Hardware Driver
NI Switch Hardware
(PXI and SCXI)
Cytec CY128
(VXI)
Notes: <number>
<footer>
<header>
<date/time>
One of the easiest ways to resolve this challenge is to use commercially available switch hardware such as National Instruments PXI and SCXI switch modules. Most commercially available switch modules come with drivers that implement common switching functions such as individual relay control or more complex routing such as routing a channel to the common on a multiplexer switch. Now IVI or Interchangeable Virtual Instruments driver (IVISwtch standard) is an common interface for switch modules including all NI switches and many 3rd-party switches. It defines a common switch interface that allows compatible IVI switches to be swapped out without disrupting programming. This means I can replace my current switch (for whatever reason: damaged, to small, slow etc.) for any other IVI compatible switch without having to modify any programming whatsoever; it could even swap a GPIB based IVI switch for a PXI-based switch.
What makes IVI-compatible switches even more attractive is that switch management software, such as NI Switch Executive, is built on top of the IVI switch class driver and works with any IVI-compliant switch driver.
What all of this means is that you can use a programming interface designed for switches, making it easier to program switches.

## Slide 8: Some Multi-Vendor IVI Switch Drivers
NATIONAL INSTRUMENTS
  PXI-2501/2503 48x1 MUX/Matrix
  PXI-2529 128 Crosspoint Matrix
  PXI-2530 128 ch MUX/Matrix
  PXI-2565 16 ch SPST Relay
  PXI-2566 16 ch SPDT Relay
  PXI-2567 64 ch Relay Driver
  PXI-2568 31 ch SPST Relay
  PXI-2569 100 ch SPST Relay
  PXI-2570 40 ch SPDT Relay
  PXI-2590 4x1 RF MUX
  PXI-2591 4x1 RF MUX
  PXI-2593 16 ch MUX/Matrix
  SCXI-1127/1128 64x1 MUX/Matrix
  SCXI-1129 4x64 Matrix
  SCXI-1130 256 ch MUX/Matrix
  SCXI-1160 16 SPDT Relay
  SCXI-1161 8 SPDT Relay
  SCXI-1191 Quad 4x1 RF MUX
  And many more…
Agilent/HP
  GPIB -HP3499A, 3499B, 3488A Switch/Control System
  Over 30 plug-in modules (Relay, MUX, Matrix)
ASCOR
  PXI-70xx Series (Relay, MUX, & Matrix)
RACAL
  VXI-1260-30A (MUX)
  VXI-1260-30B (MUX)
  VXI-1260-30C (MUX)
  VXI-1260-30D (MUX)
  VXI-1260-40A (Matrix)
  VXI-1260-40B (Matrix)
  VXI-1260-40C (Matrix)
Pickering
  PXI-40-1xx-xx (Relays)
  PXI-40-5xx-xx (Matrices)
  PXI-40-6xx-xx (MUX)
  PXI-40-7xx-xx (RF)
C&H Technologies
  VXI-412C (Relay)
  VXI-414C (Relay)
  VXI-415C (MUX)
  VXI-416C (Relay)
Notes: <number>
<footer>
<header>
<date/time>
This slide outlines a partial list of commercially available switch hardware built on the IVI-class switch driver in a variety of form factors. National Instruments for instance has over 75 switch topologies to choose from ranging from multiplexer to matrix as well as RF and general-purpose, supporting signals from DC to RF and from low to high-power.

## Slide 9: 3) “When can I get my hands on hardware?”
Lack of validation/hardware simulation
Software cannot be tested until hardware is built
Result: “Surprise!!!”
NO Simulation
With Simulation
Notes: Switch programming is inherently a hands-on situation where most of your switch programming occurs once you’ve installed and configured the hardware. In part because it is quicker to debug, but mostly because managing all the inter-dependencies between signal endpoints and routes requires prototyping and verification. Another problem is that without the hardware, you don’t have the ability to compile your program and validate the rest of your system including instrument programming, database logging or report generation unless you create highly modular components and a framework not requiring the hardware. This is a challenge mainly because the hardware itself takes time to setup and configure as opposed to instruments, such as digitizers, which are ready to run right-away.
The slide above depicts a common high-density switch project timeline. It takes roughly an equivalent amount of time to define the connections and implement the wiring as it does to program. Because software is so heavily tied to the hardware configuration being complete, the project timeline can be double the time necessary. Notice with hardware simulation, the hardware setup and configuration can be done concurrently with the software design.

## Slide 10: 3) Recommendation:
Simulate IVI devices - no hardware is needed for:
  NI switches/drivers
  and 3rd-party IVI switches
Validate configuration using NI Switch Executive validation tool
Develop a software framework that leverages a configurations
  “Save, Export, or Revert” your switch configurations
Notes: The key to concurrent software development and hardware setup and configuration is software simulation of the hardware. If you develop functions that simulate the hardware behavior you can easily develop your system in parallel; when the hardware is complete, you can replace simulated function calls with the hardware specific functions. This is further simplified by creating a switch software framework that allows you to use pre-built switch configurations to test with.
Since NI Switch Executive leverages the IVI switch-class driver, it can easily simulate a switch configuration thus if you are using an IVI-compliant switch device, the driver can be installed and run in simulation mode with NI Switch Executive without requiring hardware. NI Switch Executive also supports saving, reverting and exporting a switch configuration to use on another computer or station, allowing for quicker development and configuration reuse.

## Slide 11: Validate NI Switch Executive Configuration
Validation performed in both hardware and simulation
Notes: NI Switch Executive includes a switch system validation feature that will verify if your IVI switch configuration and driver are correct, make sure your routes are switching the correct relays and that the endpoints specified can be connected as well as verifying all the routes in a route group to determine if they are all compatible (no shorts). This validation can be run using hardware, which will actually test each route and route group by actuating each of the relays, or in simulation mode which leverages the simulation provided by the IVI switch-class driver.
Either way, this gives you a great advantage in making sure your switch system is doing what you want it to do.

## Slide 12: 4) “How do I make 1 matrix out of 10 modules?”
Connected modules or external wires are not recognized
Managing multiple modules leads to messy software
Multi-module configuration require system intelligence
c0
c5
c1
c2
c3
c6
c4
c7
r0
r3
r2
r1
UUT2_In
UUT2_Out2
UUT2_OUT
UUT2_Vcc
c0
c5
c1
c2
c3
c6
c4
c7
UUT_In
UUT_Out2
UUT_OUT
UUT_Vcc
DCPower
Scope
Source
DMM
Notes: Perhaps one of the biggest challenges in high-density switch system design is integrating multiple switch modules. Whether you are routing through these modules to increase system density or if you are incorporating multiple modules to duplicate tests, programming easily becomes difficult. At least when using a single switch device, routing by connecting and actuating relays is easier to visualize; once a second module is added, visualizing and synchronizing the modules becomes very challenging. You have to understand in software how your modules are connected together and then you have to find a path across that hardwire. Typically this requires system intelligence or a lot of patience.
The diagram on the slide demonstrates expanding the number of columns of a switch matrix by connecting the 4 rows together. Effectively, we are combining 2 4x8 2-wire switch modules to create a 4x16 matrix. So developing a software routing must take 3 pieces of information. The first is which endpoints (or columns) to route, the second is knowing which relays to close to get to a given row and the third is knowing which rows are connected together. Based on this it is easy to see how a 200 x 200 matrix involving 75 switch modules becomes a problem.

## Slide 13: 4) Recommendation:
Build intelligence on your database architecture
Demo: Hardwires/buses & routing through multiple switches
Notes: A solution to this difficult challenge is to build the intelligence into your switch routing software to handle the 3 unknowns of multimodule routing.
A – Which endpoints need to be connected together
B – Which relays in the switch modules route those endpoints
C – How are the 2 modules containing the 2 endpoints connected together.
NI Switch Executive switch management hardware automatically handles multimodule routing by answering the three questions above. In your virtual device, besides specifying which signals are connected to which switch channels, you would also configure how the switch modules are connected together. By identifying this, Switch Executive can map out all the possible routes from the one switch to the other. This means it can automatically route your signal to a “virtual” endpoint which is your system hardwire on one switch and do the same on the other switch module making sure the 2 hardwires have been configured to be connected.
This will be much more apparent when we demonstrate multimodule-routing in NI Switch Executive.

## Slide 14: 5) Unwanted Connections
Multiple signal levels and sources in the same system
  High and low frequency RF
  High and low voltages
  High and low currents
Operational safety problems
  Exposed pins, weak grounds
  Unexpected shorts
  Damaged equipment
Notes: Unwanted connections is a big problem in switch system design because the ramifications could be extreme. For example, if you have a mixed-signal switching system with a sensitive RF instrument taking measurements and you accidentally connect it to a high-voltage power supply, you would certainly damage the RF instrument. This problem is further compounded when implementing high-density switching systems because of the greater number of possible connections and function calls required.
Typical pitfalls resulting in this scenario include simple configuration errors to difficult to manage program logic.
Incorrect configuration of the hardwires connecting multiple modules
Incorrect configuration of the channels names associated with switch endpoints
Incorrect configuration of the relays mapping endpoints to other endpoints in a switch
4)Programming errors such as forgetting to disconnect a channel route before activating a new route that shorts with the original one
5)Copy/Paste syndrome where you copy switch code to implement a different route and miss editing one of the function parameters or values
6)Simply referencing the wrong switch/channel/column/row/relay etc.

## Slide 15: 5) Recommendation:
Simulate first – avoid surprises
Make sure unwanted connections are never made
Notes: If you don’t have a switch management program to oversee all of your routes and route groups the key to avoiding this problem is to simulate your switch program WITHOUT instruments or power. In this case, you could step through every switch case in your program and use a DMM or ohm-meter to measure the short between the referenced channels and double check the logic before integrating the hardware. However this becomes painstakingly long and can also be prone to errors without discipline.
The easiest way to avert unwanted/unknown connections is to use a switch management program such as NI Switch Executive. Since NI Switch Executive employs a virtual device to manage all of your switch configurations and routes, it is quite easy to implement channel exclusions to identify routes and connections that should never be made. Once this is done, the validation process in NI Switch Executive checks all routes and route groups for combinations that expose a potential exclusion.
NI Switch Executive has 2 different channel exclusion mechanisms that you can use. The first is mutual exclusion set in which all channels or endpoints configured in a mutual exclusion set can not be connected together. The second type of exclusion is set exclusions. In set exclusions, you define sets or groups of channels that can be connected together within a given group but not across groups. By using these two combinations of exclusions, almost any channel exclusion mechanism can be defined.
Another advantage of channel exclusions is to route around a given relay. For example if a given relay is beyond its defined life (1 billion cycles is typical) you might not want to route through that relay in the chance that it fails. Therefore, you can create a mutual exclusion for the column and row that intersect that relay and that path relay will never be activated.

## Slide 16: 6) “NOW, I have to DOCUMENT it???”
Lack of code documentation
Difficult test system update
  Attrition, staff changes
  Memory (after a few months)
Limited code re-use
Significantly lower efficiency
Notes: The most undervalued task in switch system development also happens to be the most appreciated when maintaining or reusing switch code; and this is documentation. Most engineers avoid it during programming and most hate having to do it after they’ve completed programming. However, documentation is the most important part of a switch system. Since you are often times programming at the relay level, making connections and disconnections at various points in the code, it is critical to identify the reason that code is being called. Otherwise what could be a completely obvious switch application can be extremely difficult to decipher. Some of the benefits that documentation brings include simpler system maintenance, better code reuse and greater efficiency as more engineers are involved in development or maintenance.

## Slide 17: 6) Recommendation:
Use channel aliases in program (more intuitive)
One click documentation – built with your database
Demo: Simplified switch programming and reporting
Notes: An obvious solution to this problem is to simply document your code. There are however techniques to make it easier to document. If you get in the habit of using aliases, for your switch endpoints, hardwire connections and switch modules it is much easier to interpret the code. This, of course, is in addition to abstracting the actual switch relay or endpoint you are referring to thus allowing you to alter your endpoint without having to modify every point in the code that it is being called.
NI Switch Executive also includes one-click documentation for the entire switch system defined by a virtual device. Since NI Switch Executive abstracts all the low-level switch configuration in a virtual device and gives the user a system-level programming interface for switch programming, it is simple for NI Switch Executive to quickly document the entire system. NI Switch Executive creates an HTML report that identifies which switches are part of the system, which channels (switch endpoints), what the channel aliases are, the hardwire connections between switch modules, the channel exclusions defined as well as your routes and route group configurations. All of it is documented in a single report.
Another big advantage to the one-click documentation that NI Switch Executive offers is the ability create your entire switch system using simulation drivers and then use the documentation to quickly setup and configure your hardware.

## Slide 18: 7) “Reusing and Maintaining Switch Code?!”
Hard coded, intertwined switching and test functions
Test modules tied to specific switching system
Notes: At this point, most of the discussion has centered around implementation details of specific switching challenges. However, at a higher level, how do you reuse and maintain your test code. With hare-coded switching and test functions, the test code is specific to the test you are performing. If you wanted to leverage this development for another project, you would have to scrap all of the switching code in all of the test modules and restart. This is almost as long as rewriting the new test module to begin with since the switching code and test code is so intertwined.
Another challenge at this level is maintaining the switch code. For example, what happens if you have to move the DMM to another endpoint. In every instance of your test code where you referred to the DMM, you would have change to reference the new value. Maintenance easily becomes more troublesome as the system scales or takes on new functionality.

## Slide 19: 7) Recommendation:
Separate test code from switching code
Abstract low-level switch configuration from test programming
Use modular test management framework such as NI TestStand
Notes: The most important part of test code reuse is modularity. If you could create individual test modules or tests that require switching before or after, it is much easier to reuse those individual modules. There is no switching included. This basically describes separating test code from switching code. In the screenshot depicted here, we see that we can implement all our test module code as a subVI and include it within the sequence structure. This means, the correct switching will occur for that specific module but it is not included with the module. I can still reuse that module later on.
The key to maintaining and reusing switching code is the abstraction of the low-level switching details. In the screenshot above, we see the system-level programming interface for NI Switch Executive. It has a VI to refer to the specific virtual device called (SwitchSystem1) and it has a VI used to make the switch connections for Test_DUT1. What this implies is that I can completely update or modify my switching code at a virtual device level by changing the switch configuration but I can keep my system-level programming the same. For example, if Test_DUT1 was a route that connected c0 of matrix1 to c9 of matrix3, I can reconfigure the route to go fro c0 of matrix1 to c5 of matrix8. This is all down behind the scenes and the programming remains constant. Also, maintenance becomes much easier since the reconfiguration is done behind the scenes.

## Slide 20: 7) Recommendation Continued
NI TestStand
  Modular test software framework
  Enables pre- and post-test switching
Notes: <number>
<footer>
<header>
<date/time>
Designed to integrate with new and existing test systems, NI Switch Executive not only offers the new software features mentioned previously for reducing the amount of time required to configure a switching system, it also provides seamless integration with NI TestStand for controlling your switching needs within your test sequences instead of your test programs. This is paramount in reusable, modular test system design since NI TestStand is a test management software that promotes the design of simple, reusable modular test components. Now you can simply add switching to any of the test components in a TestStand sequence without having to add any code. This delivers the ultimate modular test architecture and reduces the typical test application example presented earlier in this presentation to a very simple and manageable piece of test code that is focused solely on acquiring the necessary measurements.

## Slide 21: Use Case: Diode Testing
…
Notes: In this case we will examine a typical high-density switching application consisting of characterizing 63 diodes. The system consists of an NI DAQ multifunction I/O device which is providing an analog voltage to each of the diodes. As current flows through the diode and through each resistor, a high-precision DMM is measuring the voltage across the resistor. Knowing the exact resistance of each resistor, by stepping the analog voltage we can determine the corresponding current.
We will use the ultrahigh-density PXI-2532 512-crosspoint matrix switch to switch between the DMM and each of the 63 resistor endpoints. This demo consists of 3 parts:
Looking at the NI Switch Executive virtual device for the diode test and stepping through the configuration of the system.
Viewing the NI Switch Executive application programming interface in LabVIEW and running the diode test.
Seeing how NI Switch Executive is integrated into NI TestStand for to create a modular, reusable test architecture using switching.

## Slide 22: Summary
Significantly reduces development time and costs by:
Providing fast assisted end-to-end routing and configuration
Requiring little or no programming; saves development time and easier to maintain test code
Increasing system throughput and switch lifetime
Simplifying multi-module switch integration
NI Switch Executive Switch Management Software
Notes: <number>
<footer>
<header>
<date/time>
NI Switch Executive is an intelligent switch management and routing application. With NI Switch Executive, you gain increased development productivity by interactively configuring and naming switch modules, external connections, and signal routes. You also increase test code reuse and system performance with switch programming in conjunction with National Instruments TestStand, LabVIEW, and Measurement Studio. Ultimately, NI Switch Executive and modular NI switch hardware simplifies switch system configuration and increases test performance, lowering your cost to test.

## Slide 23: Online Resources
ni.com/switchexecutive
ni.com/switches
Switch Product Selection Guide
“Next Generation Switching: Density, Price, and SPECS”
“How to Choose the Right Relay”
High-Density Switch Solutions Overview