## Slide 1: Internet Technologies, Data Publishing, Remote Measurements, and Distributed Execution
by
Jeff Laney Measurement Studio Product Manager National Instruments

## Slide 2: Virtual Instrumentation
Acquire
Analyze
Present
Notes: As we look at the history of measurements, scientists and engineers took some of the first measurements using electrical devices, such as analog meters, which were crude by today’s standards. Over time, these devices evolved into increasingly sophisticated and complex stand-alone instruments, such as spectrum analyzers and vector network analyzers. While delivering a marked increase in measurement capability and flexibility, these instruments had and still have a number of limitations; they generally do not permit the user to modify the set of functions or operations they can perform. This is because the data acquisition, analysis, and presentation properties of the instrument are determined by the vendor and are not subject to alteration. In addition, traditional instruments have generally lagged behind computers in processing power and data storage capacity. The whole concept of virtual instrumentation is to create measurement systems by combining measurement hardware and software components with mainstream computer technologies, such as desktop PCs or workstations. By incorporating industry-standard computers into your system architecture, you effectively capture superior processing power, performance, and data storage in your measurement system. PCs and workstations especially deliver significant gains over traditional instruments in the realm of data analysis and presentation. Because computers are so versatile, your measurement systems automatically inherit another advantage over traditional instruments. That is, your system can evolve and change over time according to your needs by simply modifying the various software and hardware components instead of buying completely new stand-alone instruments, which can be very costly.
Hopefully, the benefits of using computer-based measurement systems are apparent to you. Many measurement systems today only contain a single computer. What would happen if we were to expand such a system to include more than one computer or even span an entire network? By doing this, you can capture all of the advantages networks provide for your measurement application.

## Slide 3: Distributed Virtual Instruments
Acquire
Anywhere
Analyze
Anywhere
Present
Anywhere
Notes: Because computers are linked together in a network, you can naturally transfer data from one computer to another in a variety of forms. Perhaps you want to take data in one location and then send it to another site. Or you might even want to send multiple copies of the same data to other parts of your enterprise. Still, you may need to log measurements periodically to a remote database. All of these scenarios are possible and even practical with network measurement systems.
If a network consists of a number of computers, couldn’t you distribute the various tasks you want to perform in your measurement application among several different machines? Of course you can. Probably not all of the computers in your network are identical. Some may have larger disk drives or have more physical memory. Some may have better processors and some may not have expansion slots available for measurement hardware. Because you have a whole variety of different computing machines in a network, you have the power to optimize the performance of your system by picking and choosing which measurement tasks should be performed on which machines. Why not perform the most computationally intensive tasks, such as image processing, on the machines with the best processors and leave less critical tasks to slower computers? You can also preserve the computer infrastructure within your network by distributing execution. If your measurement system requires a substantial amount of processing power, you can just divide your measurement system among several machines instead of purchasing new computer equipment.
Networks have changed the face of measurements by unleashing the potential of your measurement system. No longer is it a matter of acquiring, analyzing, and presenting data at a single location. Now with Internet and network technologies, you can acquire anywhere, analyze anywhere, and present anywhere literally.

## Slide 4: Types of Measurement Networks
Remote Measurements
Data
Publishing
Distributed Execution
Measurement and Automation System
Notes: Even though there are an endless number of distinct measurement and automation systems you can create, there are three widespread tasks common to most architectures. All the remainder of this presentation is dedicated to discussing these tasks and a number of specific technologies ideally suited for each one. These three commonly-encountered types of networks are publishing data, taking remote measurements, and distributing execution. Each has unique characteristics that define when to use each.

## Slide 5: Data Publishing
Remote Measurements
Data
Publishing
Distributed Execution
Measurement and Automation System
Notes: The demand for data publishing certainly shows no signs of decline. All in fact, the Internet and data transfer protocols such as HTTP and FTP, coupled with tools such as e-mail, have probably served to only increase the amount of data that is shared on a daily basis, whether it be internal to a corporation or on a more global scale.

## Slide 6: Data Publishing Present Anywhere
Publish data to multiple clients
Acquire and Analyze
Present
Present
Present
Notes: Typically, data publishing is best represented by a single-source to multiple client transmission model. All this means that generally a single measurement device is responsible for broadcasting data to any number of receiving machines. In some cases, it may not be known at the data source the exact number of clients that will request the data, which may present a challenge when writing the software applications for the system.
This slide shows a pictorial representation of a simple data publishing system. Note the single computer which distributes data to multiple client machines.

## Slide 7: Data Publishing HTML
Methodologies
  Pull
  Push
  Clint/server
Notes: The most popular form of publishing today is the World Wide Web. All there are three main technologies used to publish information over the web. The first method used is called “pulling” the data. This is the first technology that was available over the web, and this is how most web pages are delivered to your browser. You request a page, pull, and the web server delivers/updates the information.
Another popular method is the “push” method of publishing data. This has become very popular among internet information companies such as Yahoo and PointCast. Here you subscribe to different types or interests of information and when the server has something new of that type it pushes it out to your Web page or application.
Finally, the full client/server model can be used through the Web with the use of ActiveX and Java. With full client server support, there is both a push and a pull, and these are usually optimized for the least network traffic. With client/server technologies, you can subscribe and change information while it is automatically updated when new data becomes available.
National Instruments software has support for the Pull method using the built in Web server, and the full client/server method using DataSocket™.

## Slide 8: Data Publishing Web Server (Pull)
Publish HTML documents
Cross-platform
Large number of clients
Security features
Standard in LabVIEW™, Lookout™, part of Measurement Studio™ - CVI™ Internet toolkit
Notes: One tool that is particularly useful in reporting results is a Web server. All a Web server’s purpose is to publish HTML documents on the Web. There are a myriad of applications available for populating HTML documents with your data to create professional reports; and with some programming languages, you can programmatically generate Web content. Once you have compiled your report in HTML format, then simply use a Web server to post data to clients across the Internet.
There are a number of advantages to using a Web server to distribute reports. First, Web servers publish data in a format that is recognized on a large majority of the available computing platforms. This means that you can publish your reports on a Web server that is running on Linux, for example, and a client machine running Macintosh OS has the ability to display the report. Web-based reports offer significant flexibility when it comes to computing platforms. It is very easy to embed pictures, graphics, and even sound into a Web page. Plus, you can present simple to complex data using the hierarchical nature of hyper-text, and Web servers easily manages a large number of clients.
Many of National Instruments software development environments have built-in Web servers as well. In this case, little or no programming is required to publish application data on the Web. Generally, Web servers also provide security features to selectively block or give access to various clients. Let’s take a look, then, at one such application that has a built-in Web server.

## Slide 9: Data Publishing DataSocket (Client/Server)
Live data transfer
Multiple clients
One high-level API for all data source types
URL to specify connection
Notes: Most client/server architectures are proprietary and used only by one application. The technology is usually built on top of TCP/IP and is programmed from ground up by the person creating the application. National Instruments has created an API and server architecture called DataSocket that makes creating full client/server applications easier.
DataSocket is an API that is in all National Instruments development environments. You can communicate with different servers, such as HTTP, FTP, OPC, and the DataSocket server using this API. This is a two way communication, so you can send information to the server, such as changing a test parameter, and receive information from the server, such as viewing the data currently being acquired. DataSocket supports multiple clients and is optimized to reduce network traffic. Now, with the databinding ActiveX control, you can create interactive Web pages that can control your whole measurement application from anywhere in the world.

## Slide 10: Data Publishing Example: Live Weather Station
Acquisition
LabVIEW
Remote SCXI™
Distribution
LabVIEW
DataSocket server outside firewall
Web Clients
DataSocket client
Web browser weather monitors
Notes: To collect the weather information, a remote SCXI chassis, with various signal conditioning modules, interfaces to the various weather instruments for measuring the current weather conditions. This SCXI chassis and signal conditioning modules are controlled using LabVIEW.
Not only is LabVIEW used to actually acquire the weather measurements, it also distributes the data. It does this by posting data updates to the DataSocket Server, which is located outside our Internet firewall. This isolates the publishing of the acquisition data from National Instruments internal network. Thus, anyone can run our weather applications and get weather updates from Austin. The DataSocket server publishes all the data from the weather station to any Web clients that connect to the weather monitoring applications. This is a streaming data publishing technology, and all data collected by the weather system is sent to the client Web browser as quickly as its collected.

## Slide 11: Remote Measurements
Remote Measurements
Data
Publishing
Distributed Execution
Measurement and Automation System
Notes: Instead of data publishing, we will now focus on the gathering of data over a network. This can obviously be done locally on a single machine connected directly to the device, but it is often desirable or even required that measurements be taken at a remote site. Using Ethernet based measurement devices, you can overcome any distance limitations your past setup encountered.

## Slide 12
Acquire
Acquire
Acquire
Analyze and Present
Measurement node physically separated from PC with Measurement and automation application
  Harsh environment, space, cost
  Distributed signals
Remote Measurements
Acquire Anywhere
Notes: This is a simple diagram portraying a system designed to take a remote measurement. One characteristic of such a system is that the measurement device is remote, meaning that it is physically distant from the client computer requesting the measurement data. The link between the client computer and the remote measurement device is made through the network, most commonly using Ethernet.
One main difference between a system that publishes data and one that takes remote measurements is found in the number of clients receiving the data. Whereas a publishing system typically distributes data to more than one client, a system designed for remote measurements is generally point-to-point. This means that such a system generally consists of a single measurement device collecting data and sending it back to a single computer. Additionally, a remote measurement system is very device-centric. In many instances, the measurements are collected with a device or transducer and not by a computer. However, when publishing measurements as discussed in a data publishing system, the data publisher is generally a computer rather than a discrete device.
Even if you have a device that does not support a direct connection to the network, you can still connect that device to a local computer and use the computer to reflect the measurements onto the network, thus making it appear as a networked measurement device.

## Slide 13: Remote Measurements Acquire Anywhere
Serial (RS-232/485)
  Cheap
  Slow
Wireless
  Needed for cases where wires are impossible
  Costly
Ethernet
  Widely available
  Cheap and Fast
Notes: Remote measurements aren’t always necessary over Ethernet. A multitude of other networks exist, such as serial and Firewire. Serial network connections are the most popular, and they exist in RS-232 and RS-485 versions. With the RS-232 you get a single point-to-point connection over a short distance, while RS-485 adds multidrop capability and longer distances. Wireless radio modems extend the serial connection 20 miles or longer using radio modems. And of course Ethernet connects all of the devices and computers plugged into either LAN or Internet around the world.
Table of Remote Measurement Options:
1 Serial systems can be extender beyond 4,000 m user repeaters, long-haul modems, dial-up modems, etc.
2 Ethernet 10BaseT and 100BaseTx segments are limited to 100 m each. Repeaters and transceivers extend the segment length using fiber optics and coax, and Ethernet systems using TCP/IP have virtually unilimited coverage due to availability of Internet connection.

## Slide 14: Remote Measurements Acquire Anywhere
USB
  Cheap (free)
  Short distance/slow
IEEE 1394 (Extended)
  Fast
  Expensive
MXI™-3
  Very high speed
  Most complete solution
Notes: Here are some of the other networks used for remote measurements that are perhaps less known. USB, the universal serial bus, has become quite popular in the computer world with the transfer of up to 12 Mbytes/s from distances of up to 5 meters. This can be extended to 30 meters with additional hubs.With IEEE 1394, also known as Firewire, transfers of 100 to 400 Mbs are possible. Normally the distance is only a couple of feet, but a pair of 1394 extenders now available from NEC can further the distance up to 500 m over fiber optic cable. Of course, MXI-3 offers unmatched advantages of extending the PXI/Compact PCI bus between computers.
Contact Information for Complimentary Remote Measurement Products:
NEC MX Series 1394 Adapter
Sanshin Electronics Corporation
Attn : Kaz Mizutani
Tel : 949-727-4435, ext 14
email: MXsanshin@msn.com
MiniDAQ Wireless Data Acquisition Transceiver (uses DAQCard)
ViaSat, Inc.
www.viasat.com/minidat
e-mail: minidat@viasat.com

## Slide 15: Distributed Execution
Remote Measurements
Data
Publishing
Distributed Execution
Measurement and Automation System
Notes: Up to this point, we have focused mostly on how you can use various new technologies to improve your measurement or automation systems. Now we will discuss how you can improve the performance of your system, increase its flexibility, and use many of the computers in a network to make a coordinated measurement system.

## Slide 16: Distributed Execution Analyze Anywhere
Acquire
Analyze
Present
Notes: With distributed execution, you execute various tasks in your measurement system across several different computers so that no one machine becomes stressed under a heavy load of the required operations. Additionally, you can coordinate measurement operations across many computers into a single system. All you can acquire and reduce data at the computer taking the measurement. Reducing your data before sending it helps reduce network congestion.
You can use distributed execution to control a system remotely. You can split execution so that the measurement system can reside on a remote machine, and the controlling portion resides on a computer in a more comfortable location.
Distributing execution provides some definite advantages. You can selectively choose which portions of your cumulative measurement tasks run on which machines, often in parallel, resulting in improved system performance. Moreover, because you can distribute your application in such a way that no single computer becomes a bottleneck in your measurement system, these systems will not be as taxed. Distributing execution means you can protect your computer capital investment.
A typical measurement solution consists of an acquisition element, an analysis component, and some type of presentation capability. With distributed execution, you can break up these tasks and run them on different computers. No longer is it acquire, analyze, and present - it’s acquire anywhere, analyze anywhere, and present anywhere.

## Slide 17: Distributed Execution
Technologies
  COM/DCOM
    TestStand™ — remote sequence call
  C – Remote procedure call (RPC)
  Java – Remote method invocation (RMI)
  LabVIEW – VI server
Notes: There are many technologies available to distribute the execution of an application across many machines. For the Windows platforms, there is Distributed Component Object Mode) DCOM you can invoke any COM object from another machine on the network. A COM object can be a DLL or EXE that has the COM interface integrated into it. One such application is TestStand which can be used to do a remote sequence call on another machine.
The popular programming languages such as C/C++ and JAVA both have ways to call or execute code on another machine. LabWindows™/CVI, a full ANSI C compiler, can invoke an RPC. Java has remote method invocation, which does much of the same thing that C’s RPC can do. LabVIEW has taken remote execution a step further and made remote execution easier with the VI Server.

## Slide 18: TestStand Remote Sequence Call
TestStand Sequence
LAN
Init
Generate
Report
Unit Under Test
Seq A
Seq C
Seq B
Notes: TestStand is a test management program that can sequence tests written in National Instruments LabVIEWand LabWindows/CVI and Microsoft Visual Basic and Visual C++, and other test languages. It delivers intelligent sequencing (branching, looping, etc.), report-generation, and database connectivity.
With TestStand distributed architecture, you run tests painlessly on remote machines. Using this client-server model, you can have a single computer sequencing through a series of tests and archiving results, while each test is run on a different networked machine. With distributed architecture, you decrease test time, and improve efficiency of your production line by creating tests that pass information to each other over a network. This process is often called parallel testing and can greatly improve your production test throughput.

## Slide 19: LabVIEW Remote VI Call
LabVIEW VIs easily distributed across a network
Ideal for distributed analysis, or adding control/data reduction at measurement node
Works across platforms
Notes: LabVIEW is a graphical programming language that greatly simplifies creating measurement and automation applications. As a programming language, LabVIEW can execute code on another machine. With the use of VI Server in LabVIEW, you call and run other applications on machines on your LAN, so you can distribute any part of your application to multiple machines. You can have multiple machines doing analysis on information collected from an Ethernet device and published to thousands of users on the Web. The possibilities are amazing.

## Slide 20: Demo — TestStand Remote Sequence Call