## Slide 1
Multisystem Extension Interface
for PXI and CompactPCI

## Slide 2: Virtual Instrumentation via PC Control
HS488 - 8 MB/s
GPIB
>1 MB/s
MXI-3
~100 MB/s
MXI, MXI-2
>10 MB/s
Notes: At the heart of virtual instrumentation is the link between standard PCs and instrumentation equipment. GPIB (IEEE 488) was the first link between PCs and instruments that ushered in the virtual instrumentation age in the early 1980s. GPIB is still very widely used today, however, it's typical bandwidth of 1 Mbyte/s drove the development of faster links. High Speed 488 (HS488) built on the standard GPIB architecture to offer a dramatic improvement to 8 Mbytes/s for connections to box instruments.
The VXI architecture introduced in 1988 defined a modular instrumentation architecture where multiple instrument modules fit into a single standardized mainframe or chassis. With VXI came the introduction of a new technology called MXI (Multisystem Extension Interface) that linked PCs to modular instrumentation at rates more than 10 times faster than the original GPIB link. Like GPIB, MXI also evolved to a second generation, MXI-2, where the link to VXI was further increased to over 30 Mbytes/s.
In 1997, the introduction of PXI dramatically lowered the cost and reduced the size of modular instrumentation. However, the only choice for controlling PXI was with an embedded controller. Therefore, MXI-3 was developed as the link between the PC and PXI. By using the latest technology available MXI-3 delivers a 10X performance increase over the original MXI bus and a 100X increase over the original GPIB bus. Best of all, MXI-3 delivers this exceptional performance with complete software transparency.

## Slide 3: So What’s the Problem?
PCs are low on slots
Embedded computers cost more than PCs
7 CompactPCI slots aren’t enough
MXI-2 can’t extend PXI
Notes: One of the primary problems facing system designers today is the falling number of available slots in today's PCs. Measurement and automation system developers want to use PC technology because it offers very high performance with wide software support and flexibility for minimal cost. However, application requirements often demand more than the three or four PCI slots available in most PCs today. This points to one of the benefits of the PXI/CompactPCI architecture where a single bus segment has 8 slots -- one for an embedded controller and seven for peripherals. In many applications the rugged features of a PXI system with multiple slots and a compact embedded controller are attractive. However, in other applications, developers prefer to use a standard desktop PC instead of a more expensive embedded controller. Using an off-the-shelf PC is the least expensive control option and also allows designers to benefit from the very latest in PC technology. Until MXI-3, users had few options other than to run their PXI/CompactPCI systems with an embedded controller. MXI-2 is not an effective control technology for PXI systems because of bandwidth limitations and the lack of software transparency. MXI-3 now gives PC developers more slots to work with. The technology can also be used together with embedded controllers to extend PXI systems beyond the limitation of only seven peripheral slots. This brings an unprecedented level of scalability to the PXI/CompactPCI architecture.

## Slide 4: Standard PCI Expansion PCI-to-PCI Bridging
DRAM
CPU
Cache
ISA
…
PCI Bus #0
Chip Set
PCI Bus #1
Slot N
Slot 1
Slot 2
Slot 1
Slot 2
Slot 3
Slot 4
Primary
Secondary
PCI-to-PCI Bridge
Slot 1
Slot 2
Slot 3
Slot 4
Software Transparent!
Notes: MXI-3 extension technology is built upon a core standard architecture defined in the PCI-PCI Bridging specifications. A PCI-PCI bridge is simply a device that allows transparent expansion of one PCI bus to another. PCI-PCI bridging is widely used to provide more PCI slots in industrial computers, servers, and other monolithic PCI-based systems. The benefits of this standard architecture include complete software transparency, high bandwidth, flexible configurations, and most importantly PCI-PCI bridging is supported by the standard PC architecture. This includes standard BIOS support and compatibility with configuration utilities such as Windows Plug and Play.

## Slide 5: Standard PCI-PCI Bridge
PCI 0
PCI 1
Notes: The primary limitation of PCI-PCI bridging is the fact that it is designed for monolithic (single box) systems and is implemented as a single chip mounted on a PC motherboard. Therefore standard PCI-PCI bridges do not provide a ready link to external systems.

## Slide 6: MXI-3 Implementation of PCI-PCI Bridge
PRIMARY
SECONDARY
PCI 0
PCI 1
Notes: MXI-3 innovates on the standard PCI-PCI bridge architecture by splitting the bridge in two and connecting the two halves through a 1.5 Gigabit/s serial link. The system interfaces with the MXI-3 link exactly as it would with a standard PCI-PCI bridge. Transfers between the two PCI buses occur according to the windowing rules provided in the PCI to PCI Bridge Architecture Specification. MXI-3 benefits fully from all the benefits of PCI-PCI bridging because it complies with all the detailed requirements defined in the bridging specification.

## Slide 7: MXI-3 Architecture
MXI-3
Serial I/F
MXI-3
High Speed Serial Link
1.5 GHz
Primary
Secondary
PCI-to-PCI Bridge
Still Software Transparent!
Serial I/F
PCI
CompactPCI
PCI 1
PCI 0
Notes: The circuitry required for each half of the PCI-PCI bridge is contained within the MXI-3 ASIC developed by National Instruments. The high-speed serial link is implemented with standard driver components, connectors, and cables.
Every MXI-3 link consists of a primary and a secondary MXI-3 card and a copper or fiber optic cable connecting the two cards. A primary MXI-3 card corresponds to the primary PCI interface of a monolithic PCI-PCI bridge. It acts as a PCI initiator and target, but does not provide any additional PCI functions. A secondary MXI-3 card provides clock distribution and arbitration for its PCI bus segment.

## Slide 8: Configurations for MXI-3
PCI to PXI/CompactPCI
PXI/CPCI to PXI/CPCI
Notes: By plugging a PCI MXI-3 card into a desktop PC and a PXI MXI-3 card into slot 1 of a CompactPCI/PXI chassis and connecting the two cards with a cable, you can transparently link the CompactPCI/PXI chassis to the PC. The application and driver software will run unmodified on that PC as if the PC were embedded in slot 1 of the CompactPCI/PXI chassis. By plugging a PXI MXI-3 card into any of slots 2-8 of a CompactPCI/PXI chassis and a PXI MXI-3 card into slot 1 of an additional CompactPCI/PXI chassis and connecting the cards with a cable, one CompactPCI/PXI chassis can be expanded to two. The PXI MXI-3 cards detect the slot they reside in and automatically configure themselves as primary or secondary.
Since MXI-3 complies with the standard PCI-PCI bridging architecture, it can take advantage of a variety of other extension configurations. MXI-3 can be used to daisy-chain multiple systems in row, all under the control of the primary system -- in this case a PC. Star configurations are also possible using multiple MXI-3 cards in the primary system.

## Slide 9: Media Types and Distance
Copper
  small flexible, shielded cable
  up to 10 m distance
Fiber Optic
  two Fiber Optic Cables
  up to 200 m distance!
What’s This?
Notes: Both copper and fiber optic interconnects are available for MXI-3. Copper links are the least expensive interconnect and can span up to 10 meters between systems. Fiber optic links offer connections between systems separated by up to 200 meters without repeaters.

## Slide 10: MXI-3 Extension Kits and Boards
PXI-PCI8330 Kit: Copper PC-to-PXI/CompactPCI Kit
  Includes PCI-8330, PXI-8330, and 2 m Copper cable
PXI-PCI8335 Kit: Fiber optic PC-to-PXI/CompactPCI Kit
  Includes PCI-8335, PXI-8335, and 30 m fiber cable
For other configurations, use board and cable-only kits:
  PCI-8330: Copper Extension Board
  PCI-8335: Fiber Optic Extension Board
  PXI-8330: Copper Extension Module
  PXI-8335: Fiber Optic Extension Module
  2, 5, and 10 m Copper cables available separately
  30 m Fiber Optic cable available separately
    Other Fiber Optic lengths available from Molex, Inc.
Notes: Several configurations of MXI-3 products are available.

## Slide 11: MXI-3 Benefits Summary
More slots
Transparent
High speed
Short and L O N G distances
Notes: MXI-3 expands the range of possible applications for PCs and PXI/CompactPCI by giving the end-user more I/O slots to work with. With both copper and fiber optic interfaces, the distance between systems can be as great as 200 meters. By providing a very high-speed, software transparent link MXI-3 gives users an easy way to expand their test, measurement, data acquisition, and industrial automation systems.