## Slide 1: New Developments for PXI and CompactPCI
Carsten Puls
PXI/CompactPCI
Product Marketing Manager
NI CONFIDENTIAL

## Slide 2: Overview
Review of CompactPCI and PXI Technology
New PXI Products
New MXI-3 Technology
Application Examples
MXI-3 Demo

## Slide 3
PCI electrical specification
Eurocard mechanical specifications
Latest connector technologies
PCI
Eurocard packaging
IEC connectors
CompactPCI
PXI Starts with CompactPCI

## Slide 4
PXI Combines Standard Technologies
CompactPCI
PCI

## Slide 5: PXI is a System-level Specification
Electrical
Mechanical
Software
Instrumentation Extensions
CompactPCI
PCIbus
EuroCard
High Performance Connectors
Components
Systems

## Slide 6: Mechanical Extensions
PXI adds: - Environmental specs. - Cooling
All 3U cards work in 6U systems
64-bit PCI and
PXI Features
3U
PXI/CPCI
J1
J2
32-bit PCI
6U
PXI/CPCI
J5
J4
J3
J2
J1
64-bit PCI and
PXI Features
32-bit PCI
PXI Reserved
PXI Reserved
PXI Reserved

## Slide 7
Controllers MUST Support a standard software framework: - Windows NT - Windows 95/98
Peripherals MUST be supplied with a WIN32 Device Driver.
Software Extensions

## Slide 8
Trigger Bus
System
Controller
Star Trigger
Controller
Peripheral
Peripheral
Peripheral
10 MHz
CLK
132 Mb/s, 33 MHz, 32-bit Computer Bus
Star Trigger
Local
Bus
Electrical Features

## Slide 9: The PXI Specification Body
Charter of this multivendor group is to: - Promote PXI/CompactPCI - Ensure Interoperability - Control the PXI Specification
Focus on end-user success
>50 multinational company members
www.pxisa.org
Systems Alliance

## Slide 10: PXI Systems Alliance Members
GenRad
Gespac
Goepel Electronic
GDE Systems (Marconi)
GTE-ERS
Innovative Integration
KineticSystems
LeCroy
MAC Panel
MEN Mikro Elektronik
Talon Instruments
Acqiris
Advanced Power Designs
Advanced Test Methods
Alphi Technology
AMP
Analogic
ASCOR
ARVOO Engineering
ATEME
A&T Engineering Tech. Ctr.
B&B Technologies
BittWare Research Systems
Bode Enterprises
BRIME
C&H Technologies
CHROMA ATE
Data Patterns
Dateppli
Datum
Dolch Computer Systems
National Instruments
Pickering Interfaces
PX Instrument Tech.
Racal Instruments
Quantum Controls
SBS GreenSpring
Shaanxi HiTech
Spincraft Engineering
SRC
TestWare
Tracewell Systems
TTI Testron
Vero Electronics (APW)
Virginia Panel Corp.
ZYNX
Schroff
Marek Micro
ERNI
Ballard Technology

## Slide 11
Extend
CompactPCI
Price
Performance
Desktop PC
VXI
Modular Instrumentation
for Mainstream Users
PXI Fills a Gap between PCs and VXI

## Slide 12: New Products and Technology
Instrument Chassis
Arbitrary Waveform Generators
Real-time acquisition/control modules
Online PXI Configurator
Remote PC control of PXI with MXI-3

## Slide 13: NI PXI/CompactPCI Products
PXI Controller
PXI-8150B Series
INTERFACES:
GPIB
SCSI+Enet
PCMCIA
CAN + DeviceNET
RS-232
RS-485
50+ PXI Modules
DATA ACQ. & CONTROL:
RT Series
Multifunction I/O
Digital I/O
Analog Output
Image Acquisition
Motion Control
Counter/Timers
INSTRUMENTS:
Oscilloscopes
Digital Multimeters
Arbitrary Waveform Generator
Temperature Meter
Switch Multiplexers
Serial Data Analyzers
MXI-2 Kits for VXI/VME
PXI and PXI/SCXI Chassis

## Slide 14
MXI
GPIB
VXI orVME
Stand-alone
Instrument
PXI System
Modules
Modules
CompactPCI
PXI Works with Other Standards

## Slide 15: PXI Configurator -- Online!
POINT:
  www.natinst.com/pxiconfig
CLICK:
  choose chassis
  choose controller
  choose modules
CONFIGURE:
  place modules in slots
  select accessories
  review the online price quote
  order complete systems online!
www.natinst.com/pxiconfig

## Slide 16: Multisystem Extension Interface for PXI/CompactPCI

## Slide 17: Virtual Instrumentation via PC Control
HS488 - 8 MB/s
GPIB
>1 MB/s
MXI-3
~100 MB/s
MXI, MXI-2
>10 MB/s

## Slide 18: So What’s the Problem?
PCs are low on slots
Embedded computers cost more than PCs
7 CompactPCI slots aren’t enough
MXI-2 can’t extend PXI

## Slide 19: Standard PCI Expansion PCI-to-PCI Bridging
DRAM
CPU
Cache
ISA
…
PCI Bus #0
Chip Set
PCI Bus #1
Slot N
Slot 1
Slot 2
Slot 1
Slot 2
Slot 3
Slot 4
Primary
Secondary
PCI-to-PCI Bridge
Slot 1
Slot 2
Slot 3
Slot 4
Software Transparent!

## Slide 20: Standard PCI-PCI Bridge
PCI 0
PCI 1

## Slide 21: MXI-3 Implementation of PCI-PCI Bridge
PRIMARY
SECONDARY
PCI 0
PCI 1

## Slide 22: MXI-3 Architecture
MXI-3
Serial I/F
MXI-3
High Speed Serial Link
1.5 GHz
Primary
Secondary
PCI-to-PCI Bridge
Still Software Transparent!
Serial I/F
PCI
CompactPCI
PCI 1
PCI 0

## Slide 23: Initial Applications for MXI-3
PCI to PXI/CompactPCI
PXI/CPCI to PXI/CPCI

## Slide 24: Media Types and Distance
Copper
  small flexible cable, 2 twisted pairs
  up to 10M distance
Fiber Optic
  two Fiber Optic Cables
  up to 200 M distance!
What’s This?

## Slide 25: MXI-3 Benefits Summary
More slots for PCs and PXI/CompactPCI
Software transparent
Very high speed
Short and L O N G distances
Lower cost control

## Slide 26: Application Examples
MXI-3:
  Low-cost Functional Test Systems
  Engine development systems
Other PXI applications:
  High-security surveillance - Los Alamos
  Remote drill-site monitoring - Data Science Automation
  Robotic actuator testing - UT Robotics Research
  Digital Receiver End-of-Line Test - NDS Ltd.
Refer to www.natinst.com and click on Customer Solutions