## Slide 1: CANbus Solutions and National Instruments

## Slide 2: Agenda
Automotive test systems
Introduction to CAN
CAN basics
Overview of National Instruments CAN solution
Typical automotive test applications
Synchronization capabilities with CAN and DAQ
Real- time capabilities with CAN and DAQ
Notes: The purpose of this presentation is to:
1. Introduce NI-CAN as a platform for CAN based automotive test system.
2. Offer a real time hardware based synchronization solution between the traditional sensor based DAQ test system and the CAN based test system

## Slide 3: Traditional Test Systems
PC
DAQ
Signal
Conditioning
Thick cable harness
Point to Point wiring
Sensor-Based Vehicle
Notes: In the past few decades, the need for improvements in automotive technology has led to increased usage of electronic control systems for functions such as engine timing, anti-lock brake systems, and distributorless ignition.
With conventional wiring, data is exchanged in these systems using dedicated signal lines. As the complexity and number of devices has increased, usage of dedicated signal lines has become increasingly difficult and expensive.
With traditional sensors, transducers and wiring, current automotive test systems require a high speed DAQ board and a signal conditioning chassis (SCXI™).
As automotive manufacturers are moving to in-vehicle networks (the advantages of which are discussed later), CAN based test systems are gaining importance along with the existence of DAQ based systems.
DAQ based tests systems remain in existence to verify the integrity of the newly developed CAN based systems.
Since data is acquired on the CAN and DAQ test systems simultaneously, it is essential to provide timing and triggering signal between the CAN and DAQ test system. This capability allows easy simultaneous charting, logging and correlation of the data acquired by each individual system.
As we will learn later, a hardware based synchronization solution is more effective and accurate than using a software based solution

## Slide 4: CAN-based Test Systems
PC
CAN
Need:
Validate vehicle CAN systems
Single CAN cable
DAQ
Requirement:
Synchronization with DAQ
Notes: With CAN data is transmitted using a single pair of wires, resulting in lower wiring cost for testing.
To validate the CAN sensors (devices), a DAQ measurement system is necessary in addition to the CAN system.
If the data collected from the two systems is not synchronized with common timing and triggering signals, it becomes extremely difficult to chart and analyze the data.

## Slide 5: Introduction to CAN
So, what is CAN?

## Slide 6: CAN – Open Industry Standard
Invented by Bosch in mid-80s
High-speed CAN – ISO 11898
Low-speed CAN – ISO 11519 (fault tolerant CAN)
Heavily used in automotive
Physical layer for DeviceNet, CANOpen, SDS
Notes: To overcome the limitations of conventional automotive wiring, Bosch developed the Controller Area Network (CAN) in the mid-1980s.
As CAN implementations increased in the automotive industry, CAN (high speed) was standardized internationally as ISO 11898, CAN (low speed, for car body electronics) was standardized as ISO 11519. CAN chips were created by major semiconductor manufacturers such as Intel, Motorola, and Philips.
High-speed CAN is commonly used to control “control” devices within an automobile, such as engine, transmission, ABS, etc... High-speed handles baud rates up to 1Mbaud. Low-speed CAN is commonly used to control “comfort” devices in an automobile, such as seat adjustment, mirror adjustment, and door locking. It differs from High-speed CAN in that the maximum baud rate is 125K and it utilizes CAN transceivers that offer fault-tolerant capability. This enables the CAN bus to keep operating even if one of the wires is cut or short-circuited because it operates on relative changes in voltage. The fault tolerance feature means that communications capability is maintained even if any of the ISO11519 wiring failures occur. The transceiver solves many common and frequent wiring problems such as poor connectors, and also overcomes short circuits of either transmission wire to ground or battery voltage, or the other transmission wire. The transceiver resolves the fault situation without involvement of external hardware or software. On the detection of a fault, the transceiver switches to a one wire transmission mode and automatically switches back to differential mode if the fault is removed.
With these developments, many manufacturers of industrial automation equipment began to consider CAN for usage in industrial applications.
By the mid-1990s, CAN was specified as the basis of many industrial device networking protocols, including DeviceNet, CANOpen, and Smart Distributed System (SDS).

## Slide 7: Huge Market in Automotive
Well established in German/European automotive
High growth in U.S./Japanese automotive

## Slide 8: CAN – Automotive Applications
Transmission
Lights
ABS
Power Windows
Power Steering
Instrument Panel
Notes: Examples of CAN devices include Engine controller, transmission, ABS, Lights, Power Window, instrument panel, etc…

## Slide 9: Other CAN Markets
Military Systems
Farm Machinery
Avionics
Public Transportation
CAN
Notes: Comparison of the requirements for automotive and industrial device networks showed many similarities, including the transition away from dedicated signal lines, low cost, resistance to harsh environments, and real-time capabilities.
Because of these similarities, CAN became widely used in industrial applications such as textile machinery, packaging machines, and production line equipment such as photoelectric sensors and motion.
With its growing popularity in automotive and industrial applications, CAN has been increasingly used in a wide variety of diverse applications. Usage in systems such as agricultural equipment, nautical machinery, medical apparatus, semiconductor manufacturing equipment, avionics and machine tools testify to the incredible versatility of CAN.

## Slide 10: CAN Basics

## Slide 11: Types of CAN
High speed CAN (ISO 11898)
  Up to 1 M bits/sec transmission rate
Low speed CAN (ISO 11519)
  Up to 125 K bits/sec transmission rate
  Fault tolerant

## Slide 12: Benefits of CAN
Lower cost from reduced wiring – Multidrop cable
  Compared to two wire point-to-point wiring
Highly robust protocol
  Built-in determinism
  Fault tolerant (low-speed CAN)
Reliable – proven in field
  Track history of 10+ years in the automotive industry

## Slide 13: CAN Physical Layer Specifications
CAN data (up to 8 data bytes in a frame)
Maximum 1 Mbit/sec
40 Meters at 1 Mbit/sec
6 Km at 10 kbit/sec
Maximum 2032 nodes per bus (theoretical)
  Approximately 100 node practical due to transceiver
  About 3-10 nodes are used in practice
Notes: Using CAN, devices (controllers, sensors, and actuators) are connected on a common serial bus. This network of devices can be thought of as a scaled down, real-time, low cost version of networks used to connect personal computers. Any device on a CAN network can communicate with any other device using a common pair of wires.

## Slide 14: CAN Frame Types
Data frames - Arbitration ID (11 bit or 29 bit)
  Indicates message priority
Remote frame
Error frame
Overload frame
Notes: In a CAN network, the messages transferred across the network are called frames.
The Data Frame
The CAN protocol supports two Data frame formats as defined in the Bosch version 2.0 specifications, the essential difference being in the length of the arbitration ID. In the standard frame format (also known as 2.0A), the length of the ID is 11 bits. In the extended frame format (also known as 2.0B), the length of the ID is 29 bits.
The Remote Frame
The Remote Frame is just like the Data Frame, with two important differences: 1) it is explicitly marked as a Remote Frame (the RTR bit in the Arbitration Field is recessive) and 2) there is no Data Field.
The intended purpose of the Remote Frame is to request the transmission of the corresponding Data Frame.
The Error Frame
The Error Frame is a special packet that violates the framing rules of a CAN message. It is transmitted when a node detects a fault and will cause all other nodes to detect a fault - so they will send Error Frames, too. The transmitter will then automatically try to retransmit the message.
The Overload Frame
It is very similar to the Error Frame with regard to the format and it is transmitted by a node that becomes too busy. The Overload Frame is not used very often.

## Slide 15: CAN Arbitration
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
Device A transmits
ID = 110 0100 0111 (647 hex)
Device B transmits
ID = 110 1100 0111 (6C7 hex)
Device B loses, and goes idle until end of frame
Device A wins, and proceeds
When two devices attempt to transmit simultaneously, CAN uses non-destructive bitwise arbitration to resolve the collision.

## Slide 16: CAN Data Frame – Example
0x5
….
Temperature
Pressure
Torque
….
ID
4 bytes
2 bytes
2 bytes
Data – 8 bytes
Gearbox CAN Data Frame
0x10
….
Temperature
Torque
….
ID
4 bytes
2 bytes
ABS CAN Data Frame
Data – 8 byte ( 2 bytes not used)
Notes: CAN data frames can be up to 8 bytes in length. Data frames often comprise of multiple signals or values within the frame. In the above example the CAN frame identified by arbitration ID ”0x10” contains a temperature value that is 4 bytes in length and a Torque value that is 2 bytes in length. Another example is ID “0x5” which contains a temperature, pressure, and torque value and utilizes all 8 bytes of the CAN data frame.

## Slide 17: National Instruments CAN Solution

## Slide 18: National Instruments CAN Hardware
High speed CAN (ISO 11898)
  PCI, PXI/CompactPCI, PCMCIA, ISA
  1 and 2 ports
  Max. Baud rate 1mb/s
Low speed CAN (ISO 11519)
  PCI, PXI/CompactPCI, PCMCIA
  1 and 2 ports
  Max. Baud rate of 125kb/s
Dual speed CAN (ISO 11898 & ISO 11519)
  PCI, PXI/CompactPCI, PCMCIA
  2 ports (1 high speed and 1 low speed)

## Slide 19: National Instruments CAN Software
LabVIEW VI library
LabWindows/CVI language interface
C/C++ language interface
Bus Monitor utility – for easy monitoring and logging
Special CAN bus features
  Support for synchronization with NI-DAQ
  Support for LabVIEW Real-Time under PXI
Notes: LabVIEW VI library
  Several examples are shipped with NI-CAN and NI-DAQ to teach end users about the API
VB language interface (beta)
  Currently this interface is a .bas library
  The correct way to do this is to use ActiveX
  Only available from the NI FTP site
The Bus Monitor is a utility that can be used to simply monitor and log CAN bus traffic. This utility is supplied with the driver, NI-CAN.

## Slide 20: NI-CAN access to the CAN bus
Object oriented architecture
CAN Network Interface Object - CAN port
  Low level access to CAN bus
  When writing or reading you must specify the ID, data length, etc... of interest
CAN Object - encapsulates a specific arbitration ID along with its data
  High level access
  At configuration time, you specify ID, data length, etc.. of interest
Notes: NI-CAN uses object-oriented terminology and concepts.
In object-oriented terminology, the term class describes a classification of an object, and the term instance refers to a specific instance of that object. The term object is generally used as a synonym for instance.
For example, NI-CAN defines a class called the CAN Network Interface Object, which encapsulates any network interface port on a National Instruments CAN hardware product. Specific instances of the CAN Network Interface Object are referenced with names like CAN0 and CAN1. Each instance of a particular class has attributes that define its externally visible qualities, as well as methods that are used to perform actions. For example, each instance of the CAN Network Interface Object has an attribute for the baud rate (bits per second) used for communication, as well as a method used to transmit CAN frames onto the network.
The CAN Object encapsulates a specific arbitration ID, along with its data. In addition to providing the ability to transmit and receive frames for a specific arbitration ID, CAN Objects also provide various forms of background access.

## Slide 21: NI-CAN – Network Interface Object
ID1
ID2
ID3
Notes: The CAN Network Interface Object encapsulates the entire CAN network interface. Its attributes are used to configure settings that apply to the network interface as a whole. For example, the CAN Network Interface Object contains an attribute you can use to set the baud rate that the network interface hardware uses for communication. The CAN Network Interface Object is used to communicate generically on the CAN device network. For example, you can use the write function to transmit a CAN remote frame to a pushbutton device, then use the read function to retrieve the resulting CAN data frame. Because the CAN Network Interface Object provides direct access to the network interface, the write and read functions require all information about the CAN frame to be specified, including arbitration ID, whether the frame is a CAN data frame or a CAN remote frame, the number of data bytes, and the frame data (assuming a CAN data frame).
The Network Interface can be configured to do a buffered acquisition in which its Read Queue is allocated to buffer high speed incoming data. Comparators masks can be used to retrieve Arbitration IDs of interest, otherwise all the data from the network is placed in the read queue. This feature is valuable in analyzer applications in which it necessary to know which devices are active on the network.

## Slide 22: NI-CAN – CAN Objects
ID1
ID2
ID3
ID1
ID3
ID2
Receive data periodically using remote frame
Transmit data periodically
Transmit periodic waveform
Notes: The CAN Object encapsulates a specific arbitration ID, along with its data. In addition to providing the ability to transmit and receive frames for a specific arbitration ID, CAN Objects also provide various forms of background access. For example, you can configure a CAN Object for arbitration ID 13 to automatically transmit a CAN remote frame every 500 ms, and to store the data of the resulting CAN data frame for later retrieval. After the CAN Object is configured in this manner, you can use the read function to obtain a single data byte that holds the most recent state of the pushbutton.

## Slide 23: NI-CAN Architecture (Windows)
Shared Memory
CAN Stack
CAN Network
RTSI
PC
Your Application
NI-CAN Driver
Notes: A 32-bit, multitasking aware device driver is used to interface with NI-CAN hardware. Under Windows 9x, this is a dynamically loadable, Plug and Play aware virtual device driver (VxD). Under Windows NT/2000, this is a native kernel driver.
A Win32 dynamic link library, nican.dll, acts as the interface between all CAN applications and the NI-CAN device driver.
NI-CAN hardware products also have an on-board microprocessor. This microprocessor is used so that all time-critical aspects of the NI-CAN software can be executed separately from your Windows application. The firmware image (CAN stack) which runs on the on-board microprocessor, is loaded and executed automatically when your NI-CAN application starts up.

## Slide 24: Automotive Test Applications

## Slide 25: Typical CAN Applications
CAN device durability testing
CAN device validation testing
Examples:
  Torture testing of a gear box
  Testing instrument clusters
  Testing an ABS system

## Slide 26: Example – Gearbox Test
Temp
Pressure
Torque
….
…..
CAN Frames
DAQ-controlling the test stand -”Soft”
CAN bus
PC
CAN
DAQ
Temp
T
T
P
DAQ Synchronized with CAN - “Hard”
Notes: The above test has the following features:
• 32 A/D channels with 500 Hz scan clock
• Displaying and logging of data in 1h files
• Synchronous sampling of CAN frames
• Triggering of A/D channels with CAN data
  • Gear shifts are signalled by a CAN frame
  • Every shift is a trigger event
  • Display 500 ms pre trigger and post trigger of A/D and CAN data for every shift

## Slide 27: Synchronization with CAN & DAQ

## Slide 28: Software Synchronization
Loop/global variable controlled
Pros
  Easy to implement
Cons
  Non-deterministic due to software latency
  Measurement data not time-correlated with CAN data
    Requires manual correlation for charting or analysis
Notes: As noted in slide 4, the physical quantity being measured by DAQ and CAN devices must be done as close together (synchronized in time) to correlate the data. This synchronization can be done in software, but the latency of the software (operating system) introduces delays that may not be acceptable for some automotive test applications.

## Slide 29: Hardware Synchronization
Hardware controlled
Pros
  Very deterministic because no software timing
  Measurements time-correlated with CAN data
    Simplifies charting and analysis
Cons
  Requires support from hardware vendor
Notes: National Instruments CAN, DAQ boards are equipped with a Real Time System Integration (RTSI) bus that allows routing of timing/trigger signals between them.
In a system that is coupled using the RTSI bus, a CAN or DAQ board can be the Master, driving the timing/trigger signals while other DAQ or CAN boards are Slaves to this timing signal and base their actions on this signal. Since the RTSI timing signals are handled in hardware, the host software running on the PC, does not interact in the acquisition or transmission (other than retrieving the data when it has being acquired or writing new data).

## Slide 30: RTSI™ – Real Time System Integration
Timing and Trigger bus used by National Instruments
  PXI: implemented on PXI trigger bus
  PCI: requires RTSI cable
CAN board configurable as RTSI master or slave
Synchronize to one or more CAN or DAQ interfaces
Synchronize to one or more CAN frames
Notes: Before beginning to use RTSI between CAN and DAQ, a decision has to be made as to which board should be used as the Master. NI-CAN software allows easy configuration of the Network Interface or CAN Objects as a Master or the Slave.
The software attribute that configures the object as a Master or Slave is the RTSI Mode. The following RTSI Modes are available in NI-CAN:
1. Disable RTSI
2. On RTSI Input - Transmit CAN Frame
3. On RTSI Input - Timestamp RTSI event
4. RTSI Output on Receiving CAN Frame
5. RTSI Output on Transmitting CAN Frame
6. RTSI Output on ncAction call
Modes 2 & 3 configure the object (Network Interface or CAN Object) as a Slave that takes an action on the RTSI signal.
Modes 4-6 configure the object (Network Interface or CAN Object) as a Master.

## Slide 31: DAQ as RTSI Master
Transmit CAN frame on RTSI input from DAQ
  Synchronize to DAQ update clock for transmitting single frame or waveform
Timestamp RTSI trigger on RTSI input from DAQ
  Synchronize to DAQ scan clock for data correlation
  CAN read queue collects asynchronous CAN data as well as DAQ triggers
Notes: With DAQ (or IMAQ) board as the driver of the RTSI signal, it is possible to :
1. Time stamp the RTSI event and log it to the Read Queue
2. Transmit a CAN frame on the RTSI event
If a DAQ board is used, it could be configured to do an AI or AO operation for each of the above modes. Hence the DAQ board could route the Scan or the Update clock to RTSI and the CAN board could either log this event to the Read Queue or transmit a frame.
This functionality is available for the Network Interface as well as CAN Objects. Some background modes are supported with RTSI. For example, a DAQ board could be loaded with a buffer of data values that constitute a sine wave. In a similar way, the Write Queue could be loaded with an identical waveform to be transmitted via the CAN device. Once the CAN object is configured to transmit waveform on RTSI, it will transmit whenever the update clock signal arrives on the configured RTSI line. Note that the application software interaction would be load another set of waveform data if necessary, otherwise the timing and transmission are all handled in hardware (real time)

## Slide 32: DAQ Masters Synchronization Event
RTSI
CAN card
DAQ card
node
node
node
Transmit CAN when DAQ sends RTSI
AI/AO
AI Scan Clock or
AO Clock Update
LabVIEW Memory
DAQ 1
DAQ 2
DAQ 3
CAN1
CAN2
CAN3
…..
…..
}
node
node
node
RTSI
CAN card
DAQ card
AI Scan Clock or
AO Clock Update
Log Time stamp when DAQ sends RTSI
AI/AO

## Slide 33: CAN as RTSI Master
Output RTSI trigger on receiving a
CAN frame
  DAQ uses RTSI signal as acquisition clock
Output RTSI trigger on transmission of
CAN frame
  similar to analog output from DAQ
Output RTSI trigger on demand
  manual control via pushbutton
Notes: With CAN as a driver of the RTSI signal, it is possible to:
1. Output a RTSI signal on receiving a CAN frame
2. Output a RTSI trigger on (sucessful) transmission of CAN frame
3. Output a RTSI trigger on demand
A DAQ and/or IMAQ board could use this trigger to either perform an acquisition or an output.

## Slide 34: CAN Masters Synchronization Event
CAN card
DAQ card
node
node
node
Ack
AI/AO
AI/AO
Output RTSI on CAN frame received
RTSI
Output RTSI on CAN frame transmit
CAN card
DAQ card
node
node
node
RTSI

## Slide 35: Real- time capabilities with CAN

## Slide 36: NI-CAN and LabVIEW Real-Time
Applications: ECU testing, simulation, & validation
Develop on a PC with LabVIEW
Deploy on a PXI controller with LabVIEW Real-Time
No modification to your code
Supports synchronization of CAN and DAQ
Deterministic timing

## Slide 37: LabVIEW™ Real-Time CAN Architecture
CAN Network
LabVIEW Front Panel
Download (Ethernet)
PC
PXI Chassis
Controller
Running
LabVIEW-RT
NI-CAN driver
RTSI (Trigger) Bus on back plane
DAQ
Board
CAN Interface
Shared Memory
CAN Stack
LabVIEW Application
Notes: In the case of a LabVIEW-RT based test system, the LabVIEW NI-CAN application – that was developed on a Windows based PC can be downloaded to a PXI controller running LabVIEW-RT and having PXI CAN boards in the chassis. The LabVIEW environment allows a quick selection of the target (host PC or PXI controller).

## Slide 38: Summary
Open standard used in:
  Automotive
  Public Transportation
  Avionics
  Military
CAN & DAQ synchronization – a must for validation
CAN + LabVIEW Real-Time = deterministic timing

## Slide 39: Useful Information
LabVIEW Starter Kits on NI’s Developer Zone
  Go to “Development Library” then “Industrial Networks”
  Or click here: CAN Starter Kits
Starter Kit examples:
  CAN-DAQ Synchronization
  CANdb for LabVIEW
  SAE J1939