## Slide 1: Overview of PCI Express

## Slide 2: Agenda
History of PCI
Introduction to PCI Express
Benefits of PCI Express
PCI Express Architecture
Virtual Instrumentation and PCI Express
Notes: In this session we will discuss the challenges facing the current PC architecture, and review the various levels of the PCI Express interface. We will also look at the evolutionary form factors for PCI Express.

## Slide 3: History of PCI Express

## Slide 4: History of PCI
PCI Overview
PC Architecture with PCI
Challenges Facing PCI
Notes: In this session we will discuss the challenges facing the current PC architecture, and review the various levels of the PCI Express interface. We will also look at the evolutionary form factors for PCI Express.

## Slide 5: PCI Bus History and Overview
Speeds of 33MHz – 66MHz
Unifying effect on PC
Processor Independence
Buffered Isolation
Bus Mastering
Plug-and-Play Operation
Notes: The PCI bus brought a number of advantages over previous bus implementations. Among the most important were processor independence, buffered isolation, bus mastering, and true plug-and-play operation. Buffered isolation essentially isolates, both electrically and by clock domains, the CPU local bus from the PCI bus. This feature brings two main benefits to system performance. The first is the ability to run concurrent cycles on the PCI bus and CPU bus; the second allows an increase in the CPU local bus frequency, independent of the PCI bus speed and loading. With bus mastering, PCI devices can gain access to the PCI bus through an arbitration process and master the bus transaction directly, as opposed to waiting for the host CPU to service the device, which results in a reduction of overall latency on servicing I/O transactions. Finally, plug-and-play operation, which permits devices to be automatically detected and configured, eliminated the manual setting of switches and jumpers for base address and DMA interrupts that frustrated users of ISA-based boards.

## Slide 6: PC Architecture with PCI
Notes: The PC architecture of 2003 consists of a number of diverging requirements for each of the interconnects, for instance graphics cards are interfaced via the Advanced Graphics Port (APG), and the memory bridge is connected to the I/O bridge via a number of interfaces including Hublink® as illustrated above.

## Slide 7: PCI Challenges
Limited Bandwidth
Bandwidth shared between all devices
Limited host pin-count
Lack of support for real time data transfer
Stringent routing rules
Lack of scaling with frequency and voltage
Absence of power management
Notes: As PCI clock frequencies have become inadequate in certain applications, the PCI derivates such as PCI-X and Advanced Graphics Port (AGP) have sought to provide bandwidth relief by increasing bus frequencies. A side effect of increasing frequencies is a commensurate reduction in the distance the bus can be routed and the number of connectors the bus transceivers can drive, which leads to the concept of dividing the PCI bus into multiple segments. Each of these segments requires a full PCI-X bus to be routed from the host driving silicon to each active slot. For example, the 64-bit PCI-X requires 150 pins for each segment. Clearly this is costly to implement and places strain on routing, board layer count and chip package pin-outs. This extra cost is justified only where the bandwidth is crucial, such as in servers.
Applications such as data acquisition, waveform generation, and multimedia applications including streaming audio and video require guaranteed bandwidth and deterministic latency, without which the user experiences glitches. The original PCI specification did not address these issues because the applications were not prevalent at the time the specification was developed. Today’s isochronous data transfers, such as high-definition uncompressed video and audio, demonstrate the need for the I/O system to include isochronous transfers. A side effect of isochronous transfers is that the local PCI Express devices need a lot less memory for buffering purposes than typical PCI devices use for minimizing variable bandwidth issues.
Finally next-generation I/O requirements such as quality of service measurements and
power management will improve data integrity and permit selective powering-down of system devices – an important consideration as the amount of power required by modern PCs continues to grow. Virtual Channels permit data to be routed via virtual routes; data transfers to take place even if other channels are blocked by outstanding transactions.
Although the PCI bus is showing signs of age in some areas, the transition to PCI Express will be a long one, and the PCI bus will remain a strong contender for I/O expansion for many years to come. Modern PCs introduced in 2004 and later will have a combination of PCI and PCI Express slots, with the ratio changing more towards PCI Express as the technology is adopted.

## Slide 8: Introduction to PCI Express

## Slide 9: Introduction to PCI Express
Evolution of PC Buses
PCI Express in Desktops
ExpressCard: PCI Express for Laptops
Notes: As PCI clock frequencies have become inadequate in certain applications, the PCI derivates such as PCI-X and Advanced Graphics Port (AGP) have sought to provide bandwidth relief by increasing bus frequencies. A side effect of increasing frequencies is a commensurate reduction in the distance the bus can be routed and the number of connectors the bus transceivers can drive, which leads to the concept of dividing the PCI bus into multiple segments. Each of these segments requires a full PCI-X bus to be routed from the host driving silicon to each active slot. For example, the 64-bit PCI-X requires 150 pins for each segment. Clearly this is costly to implement and places strain on routing, board layer count and chip package pin-outs. This extra cost is justified only where the bandwidth is crucial, such as in servers.
Applications such as data acquisition, waveform generation, and multimedia applications including streaming audio and video require guaranteed bandwidth and deterministic latency, without which the user experiences glitches. The original PCI specification did not address these issues because the applications were not prevalent at the time the specification was developed. Today’s isochronous data transfers, such as high-definition uncompressed video and audio, demonstrate the need for the I/O system to include isochronous transfers. A side effect of isochronous transfers is that the local PCI Express devices need a lot less memory for buffering purposes than typical PCI devices use for minimizing variable bandwidth issues.
Finally next-generation I/O requirements such as quality of service measurements and
power management will improve data integrity and permit selective powering-down of system devices – an important consideration as the amount of power required by modern PCs continues to grow. Virtual Channels permit data to be routed via virtual routes; data transfers to take place even if other channels are blocked by outstanding transactions.
Although the PCI bus is showing signs of age in some areas, the transition to PCI Express will be a long one, and the PCI bus will remain a strong contender for I/O expansion for many years to come. Modern PCs introduced in 2004 and later will have a combination of PCI and PCI Express slots, with the ratio changing more towards PCI Express as the technology is adopted.

## Slide 10: Evolution of PC Buses
80s
90s
00s
ISA Bus
PCI Bus
8.33 MHz
66 MHz
1 GHz
5 GHz
10 GHz
15 GHz
AGPx
VESA
VL
EISA
MCA
HL
PCIx
>12 GHz Copper Signalling Limit
1 GHz Parallel Bus Limit
20 GHz+
Notes: When the PCI Bus was first introduced in the early 1990’s, it had a unifying effect on the plethora of I/O busses that were available on a PC at that time, such as VESA Local bus, EISA, ISA and Micro channel as shown above. It was first implemented as a chip-to-chip interconnect and a replacement for the fragmented ISA Bus. During these early years, the 33Mhz PCI bus was a good match for I/O bandwidth requirements of mainstream peripherals available at the time. Today, however, the story is quite different. Processor and memory frequencies have increased frequently, with processor speeds increasing at the most aggressive rate. Over the intervening period, the PCI bus has increased in frequency from 33Mhz to 66MHz while processor speeds have increased from 33MHz to 3 GHz. Emerging I/O technologies such as Gigabit Ethernet and 1394B can monopolize nearly all of the available PCI bus bandwidth as a single device on the bus.

## Slide 11: Evolution of Industry Standard Bus Throughput
40X
Notes: <number>
<footer>
<header>
<date/time>
Gigabit Ethernet : 1000 MBit/s
PCI Express x16 : 2.5 GBit/s times 16 lines.
PCI Express is 8B/10B encoded. Ethernet is 4B/5B encoded, so

## Slide 12: Industry Bus Performance

## Slide 13: PCI Express: Evolutionary Model of PCI
Serial interconnect @ 2.5Gb/S
  PCI transactions are packetized and then serialized
  LVDS Signalling, point-to-point, 8B/10B encoded
  Bandwidth is available PER slot, and in BOTH directions
  X1 gives real-world performance of 200MByts/S/direction
  X16 gives real-world performance of 3.2GBytes/S per direction

## Slide 14: PCI Express in Desktops
Intel 925XE Express Chipset
x16 PCIe
Replaced AGP
Four
x1 PCIe
Six
PCI

## Slide 15: ExpressCard : PCI Express for Laptops
34mm and 54 mm form-factors
Both USB 2.0
And PCIe signaling
on host
Notes: <number>
<footer>
<header>
<date/time>
Host has both
Card can be one or other

## Slide 16: Benefits of PCI Express

## Slide 17: Benefits of PCI Express
Bandwidth Improvements
Software Backward Compatibility
Layered Architecture
Next Generation I/O
I/O Simplification

## Slide 18: Improved Bandwidth
Up to 30X bandwidth increase over PCI
Scalable bandwidth by increasing lane width

## Slide 19: Dedicated Bandwidth
PCI Express dedicates bandwidth per device

## Slide 20: Software Backward Compatibility
PCI and PCI Express use same software model
New hardware layers deliver 30X performance of PCI
PCI PnP Model (init, enum, config)
PCI Software/Driver Model
Packet-based Protocol
Data Integrity
Point-to-point, serial, differential…
Physical
Data Link
Transaction
S/W
OS Config
No OS Impact
Future speeds and
encoding technologies
only impact physical layer

## Slide 21: Benefits of PCI Express
Layered Architecture
  Adapts to new technologies, while preserving software investment.
  Future increased signaling rates
  Software compatibility
Next-Generation I/O
  Isochronous (guaranteed) bandwidth
  Key for next generation high performance data acquisition and multimedia applications

## Slide 22: Up-plugging
Installing boards in higher lane slots
  Allowed by PCI Express
  Example: plugging a x4 PCI Express module in a x8 slot
  Caveat: Motherboard vendors only required to support a x1 data rate in this configuration
    Full bandwidth support will be vendor specific

## Slide 23: Down-plugging
Installing boards in lower lane slot
  Physically prevented by the design of the slots and connectors for Desktop (PCI) form-factor
  Will be allowed in CompactPCI Express and PXI Express

## Slide 24: Card Interoperability
The specification only guarantees a x1 connection when down plugging (i.e. a x4 card in a x16 slot may only negotiate to a x1)

## Slide 25: PCI Express Architecture

## Slide 26: PCI Express Architecture
PCI Express Layers
8B/10B Encoding
Scalable Lane Widths
Isochronous Transfer
PCI Express Flow Control

## Slide 27: PCI Express Layers
PCI PnP Model (init, enum, config)
PCI Software/Driver Model
Packet-based Protocol
Data Integrity
Point-to-point, serial, differential…
Physical
Data Link
Transaction
S/W
OS Config
No OS Impact
Future speeds and
encoding technologies
only impact physical layer
Notes: The PCI Express Architecture is specified in layers, as shown in above. Compatibility with the PCI addressing model (a load-store architecture with a flat address space) is maintained to ensure that all existing applications and drivers operate unchanged. The PCI Express configuration uses standard mechanisms defined in the PCI plug-and-play specification. The software layers will generate read and write requests that are transported by the transaction layer to the I/O devices using a packet-based, split-transaction protocol. The link layer adds sequence numbers and CRC to these packets to create a highly reliable data transfer mechanism. The basic physical layer consists of a dual simplex channel that is implemented as a transmit pair and a receive pair. The initial speed of 2.5Gb/S in each direction provides a 200 Mbytes/s communications channel in each direction, which is close to four times the classic PCI data rate.

## Slide 28: PCI Express Physical Layer
Point to point differential interconnect with 2 endpoints
Two unidirectional links, No Sideband Signals
Bit rate: > 2.5Gb/s/pin/dir and beyond
Clocking: Embedded clock signaling using 8b/10b encoding
Interface Width: Per direction: x1, x2, x4, x8, x12, x16, x32
Gen-2 (5GB/s) speed increase in mid ‘06
Device A
Frame
Frame
Sequence
Number
Packet
Request
CRC
Frame
CRC
Packet
Request
Sequence
Number
Frame
Data
Data
Data
Data
Clock
Clock
Device B
X1 Lane
Notes: The fundamental PCI Express link consists of two low-voltage AC-coupled differential pairs of signals (a transmit pair and a receive pair) as shown in above. The physical link signal uses a de-emphasis scheme to reduce intersymbol interference, thus improving data integrity. A data clock is embedded using the 8b/10b encoding scheme to achieve very high data rates. The initial signaling frequency is 2.5 Gb/s/direction (Generation 1 signalling) and this is expected to increase in line with advances in silicon technology to 10 Gb/s/direction (the practical maximum for signals in copper). The physical layer transports packets between the link layers of two PCI Express agents.

## Slide 29: 8B/10B Encoding
Consumes 20% of available bandwidth
  Incorporated into 250 Mbytes/s bandwidth numbers already
Guarantees minimum transition density
Allows for clock recovery on each transition
Routing Flexibility
  No need to address clock/data skew

## Slide 30: PCI Express Lane Width
Byte Stream
{conceptual}
Byte 0
Byte 1
Byte 2
Byte 3
Byte 4
Byte 5
. . .
Byte 4
Byte 0
Byte 5
Byte 1
Byte 6
Byte 2
Byte 7
Byte 3
Lane 0
8b/10b
P > S
Lane 1
8b/10b
P > S
Lane 2
8b/10b
P > S
Lane 3
8b/10b
P > S
Lane 0
8b/10b
P > S
Byte 2
Byte 3
Byte 1
Byte 0
Byte 0
Byte 1
Byte 2
Byte 3
Byte 4
Byte 5
. . .
Bandwidth is selectable using multiple lanes
Notes: PCI Express introduces the concept of multiple lanes to increase system bandwidth. In the example on the left, a x1 lane sequentially transfers bytes in the order they are received, which are encoded using the 8b/10b scheme and then converted from parallel to serial. In the example on the right, multiple lanes are used to split up the incoming byte stream among the 4 lanes, quadrupling the effective bandwidth.

## Slide 31: Isochronous Support
PCI Express employs a traffic class (TC) / virtual channel (VC) scheme
Traffic Class determines priority.
Device drivers or application software assign the traffic class
Virtual channels are hardware buffers on PCIe devices
Flexible (and complicated) mapping of TC’s to specific VC buffers inside devices
Internal arbitration and prioritization takes place in order to determine which packets are forwarded first.

## Slide 32: Flow Control in PCI Express
Credit-based flow control
  Can only transmit if receiver has buffer space
  No dropped packets
  No retries (Doesn’t send if packet cannot be received)
  Congestion spreads “up the chain”
Split transaction
  Request packets requiring a response are split
Handled entirely within the data link layer
Frees up bandwidth

## Slide 33: Single-Point Transfers
Reduces Bus Contention for Deterministic Communication
  PCI
    PCI Jitter from competing bus mastering sources (e.g., Ethernet and DAQ devices)
  PCIe
    Independent links to process Ethernet and DAQ device data
    Parallel Tx/Rx transfers per link
    Virtual Channels / Traffic classes
      Needed to support isochronous transfers
      Allows separate, prioritized traffic paths for single point data
      Does not require advanced switching
    When implemented on AS, allows transparent use of multiple processors
Notes: <number>
<footer>
<header>
<date/time>

## Slide 34: Virtual Instrumentation and PCI Express

## Slide 35: PCI Express M Series Data Acquisition
Up to 32 channels, 16-bit, 1.25 MS/s analog inputs
High-speed analog, digital, and counter I/O on a single device
x1 PCI Express connector
Backward software compatibility
NI PCIe-6251 Ÿ NI PCIe-6259
Notes: <number>
<footer>
<header>
<date/time>
In August 2005, National Instruments introduced the industry’s first PC-based multifunction data acquisition devices for latest PC bus – PCI Express. The release came with an introduction of two new high-speed M Series devices. The NI PCIe-6251 and NI PCIe-6259 have the same specifications as the high-speed PCI M Series devices including 16-bit, 1.25 MS/s, up to 32 analog input channels; up to 4 analog outputs at max update rate of 2.8 MS/s; up to 32 high-speed digital I/O lines clocked at 10 MHz; two, 32-bit 80 MHz counter/timers with direct support for z-indexing and quadrature encoder measurements; and many other device features including 6 DMA channels, 2 year calibration interval, and a 3 year device warranty. The difference, however, the new devices deliver the performance on a x1 (“by-1”) PCI Express connector to allow for the advantages of PCI Express. The unmatched bandwidth available with PCI Express also comes with backward compatibility for software written for an equivalent PCI device. For instance, an application created for the PCI-6251 will work with the PCIe-6251 without any changes to the code. For more information on National Instruments M Series DAQ, visit ni.com/daq.

## Slide 36: Industry’s First PCI Express Frame Grabber
NI PCIe-1429
  Supports any Camera Link camera
  x4 PCI Express connector
    680 MB/second throughput (Camera Link maximum)
  PCI Express Vision in Action!

## Slide 37: NI PCIe-GPIB
x1 PCI Express interface
High-performance GPIB
  1.5 Mbytes/s (standard)
  7.9 Mbytes/s (HS488)
Ships with NI-488.2 for Windows 2000/XP
For applications with available PCI Express slot(s)
Notes: Here is a picture of several different PCIe card types.

## Slide 38: PCI Express Control of PXI with MXI-Express
Two MXI-Express kits
  NI PXI-PCIe8361 has one x1 cabled PCI Express link
  NI PXI-PCIe8362 has two x1 cabled PCI Express links
Control of two PXI chassis from a single PCI Express board with the NI PCIe-8362
Over 40% increase in the throughput of PCI control of PXI with MXI-4
Sustained throughput
  160 MB/s (two chassis)
  110 MB/s (one chassis)
Notes: <number>
<footer>
<header>
<date/time>
With the National Instruments MXI-Express kits, you control PXI and CompactPCI systems from your desktop, server, or workstation PC through a fully transparent, high-bandwidth cabled PCI Express link. The MXI-Express link consists of a PCI Express board in a PC, connected via a MXI-Express cable to a PXI module in slot 1 of a PXI chassis. The PCI Express board is available in two configurations. The National Instruments PXI-PCIe8361 kit includes a PCI Express board with one x1 (“by one”) PCI Express link that provides up to 110 MB/s of sustained throughput when cabled to a PXI chassis. The National Instruments PXI-PCIe8362 kit provides two x1 PCI Express links, each of which you can cable to individual PXI chassis to provide up to a total of 160 MB/s of sustained throughput. The National Instruments PXI-8360 module, used in both kits, implements a PCI Express-to-PCI bridge. With MXI-Express, you can use PXI modules as if they are PCI boards directly installed in your PC. To learn more about MXI-Express, visit ni.com/pxi.

## Slide 39: PCI Express Overview
PCI Express is the next evolution in PC bus technology
  Up to 30X bandwidth improvement over PCI
  Dedicated bandwidth per device
  Backward software compatibility
PCI and PCI Express will be offered side-by-side in Desktop PCs during adoption stages
PCI Express fuels new applications for control, test, and design with Virtual Instrumentation