## Slide 1: Parallel Testing and TestStand™ 2.0
James Grey
TestStand Software Architect

## Slide 2: Agenda
Parallel testing
  Background information
  Parallel Process models
  Synchronization
Notes: I'm going to start by discussing general issues involved in parallel test systems and then I will talk about the new parallel process models and the new synchronization tools in TestStand 2.0.

## Slide 3: Benefits of Parallel Test
Increase throughput
Improve hardware utilization
Notes: Why would you want to implement parallelism in your testers? From NI’s perspective, the answer is “because our customers have overwhelming requested the ability to build parallel testers. “
Some of the reasons they cite are:
Increase Throughput - test more units per hour
Improve Hardware Utilization - reduce idle time on expensive hardware

## Slide 4: Benefits of Parallel Test (Cont..)
Allows for a natural representation of concurrent operations
  Multi-UUT
    Batch
    Parallel production lines
  Simultaneous control of heterogeneous devices
      Stimulus and Measurement
      Transmit and Receive
      Environmental control during testing
Notes: Another reason to use parallel tasks is that it can be the cleanest way to implement a system that performs concurrent operations. There are different ways to implement concurrent testing including Batch and Parallel testing that I will discuss in more detail later.

## Slide 5: Parallelism for Speed
Non-parallel test software is typically I/O bound
  Serial Port, Ethernet, GPIB
  Hard disk, database
  Measurement devices
  UUT, fixture control, assembly line handlers
  CPU cycles are wasted while waiting for operations to complete
Notes: If you need more speed, just buy a faster computer. Right?
This works great up to the point where you have the fastest computer available. However, even an infinitely fast computer will speed your test system up only a limited amount. This is because testing a product is never a pure computational task. A test system spends much of its time waiting for various types of I/O.
If your system has multiple threads, you increase the chance that CPU cycles that would otherwise be wasted waiting for I/O can be put to good use.
Also, you can get more CPU cycles with a multiprocessor computer but unless your system is multithreaded, you won't be able to utilize the additional CPU power.

## Slide 6: Techniques for Parallel Test
How
  Multiple computers or operating system processes
    Useful when parallel tasks do not interact
      Minimal interaction allows for simpler implementation
    Can be inefficient or difficult to share resources
  Multiple threads
    Easier to share resources
    Highest performance on a single computer
Notes: How can you add parallelism to your test system? Three fundamental ways are with: Multiple Computers, Multiple Processes, or Multiple Threads.
The first two are the simplest. For example, it might not require any additional software development to duplicate an entire test system and run it independently in parallel.
However, duplication can be expensive. In many systems, there are instruments, computers, and devices that you could share between test heads.
Also, even if you duplicate your test system, there are likely to be additional opportunities for parallelism within each system.
Note that if test heads interact to share resources, or for other reasons, multiple computers and multiple processes can be difficult to implement and inefficient. In this case, you should consider a multithreaded system.

## Slide 7: Multiple Processes
Program1.exe
Main Thread
Driver
Instances
Data
Program2.exe
Main Thread
Driver
Instances
Data
Notes: It is easy to understand that there are issues involved when multiple computers must interact over a network. However, this diagram shows that there are also issues even when you run multiple processes on a single machine.
The OS isolates the memory of each process. This prevents a buggy program from crashing the whole system. However, this also makes sharing data and driver instances difficult and often inefficient. To communicate between processes, you must use mechanisms like shared memory, pipes, and out-of-process ActiveX servers. For software components that do not come with source code, you might not even have these options.

## Slide 8: Multiple Threads
Program1.exe
Thread 1
Driver
Instances
Data
Thread 2
Notes: Fortunately, you can have multiple threads of execution in a single process. There is no overhead or barrier to sharing resources between threads in the same process.
You can use TestStand to build multi-machine,multi-process, or multithreaded test systems. However, because it often the most efficient choice, I am going to focus on multi-threaded systems.

## Slide 9: Parallel Test Challenges
Test Executive must support parallelism
O/S services can require low level coding
Coordinating access to shared resources requires synchronization
Perils of synchronization
  Deadlock
  Increased complexity!
Notes: Why hasn't everyone built multithreaded test systems?
First, it is hard to get started if your Test Executive does not support multithreading.
Also, some people find low-level operating system multithreading functions such as InitializeCriticalSection, PulseEvent, and AfxBeginThread to be intimidating.
Finally, in a parallel system you must synchronize your tasks so that they don’t conflict when they share a resource. When you synchronize to prevent race conditions, you add complexity and you risk deadlock.
Later in the presentation I’ll discuss race conditions and deadlock in more detail.

## Slide 10: Parallel Test With TestStand 2.0
Features
  Asynchronous sequence calls (Easier than in TS 1.0.x)
  Synchronization steps
    Lock, Queue, Notification, Wait, Batch, Thread Priority, Rendezvous, Semaphore
  Synchronization properties
    Lock, Batch
  Batch and Parallel process models
Benefits
  Easy to configure, no low-level coding
  Flexible and integrated
Notes: How does TestStand help you to build parallel test systems?
TestStand has always supported parallel execution. TestStand 2.0 just makes it a whole lot easier.
TestStand makes launching threads as easy as calling a subsequence. TestStand also provides high-level configurable synchronization objects to help your coordinate your threads.
In addition, TestStand now includes two new process models for testing UUTs in parallel out of the box
I will first go more in to detail about process models and then I’ll discuss synchronization.

## Slide 11: Types of Parallel Testing
Batch
  All test sockets operate on a group of UUTs
    Oven test
Independent
  Each test socket operates independently
    End-of-line functional test
Other
  Stimulus and Response, etc.
  <your situation here>
Notes: To help introduce the parallel process models in TestStand 2.0, it is worth noting that there are many types of parallel test systems.
At one extreme, you can have a system operate on a batch of UUTs at a time. The UUTs enter and exit the tester as a group but are tested in parallel.
Another type of tester could test UUTs relatively independently. An example is a dual well tester where you can test one UUT while reloading the second fixture with a new UUT.
However, these common situations are certainly not the only ones in which you might employ parallel test.

## Slide 12: Process Models for Parallel Testing
What is a process model?
  Coordinates tests, UUT handling, reporting, logging, …
Two new process models
  Batch
  Parallel
Both similar to existing sequential model
  Callbacks: PreUUT, PostUUT, etc.
  Configuration options
Notes: Now that we've identified some common types of parallel test, I'll describe how the new TestStand 2.0 process models function.
First, I should review what a process model is. How many people know what a TestStand process model is?
In TestStand, a process model is simply another sequence file that defines the common set of actions that surround the running of your test sequence files. These actions include identifying the UUT, generating test reports, and logging results to a database.
The new Process models are the Batch and Parallel models and they provide out of the box implementations of the Batch and independent parallel testing scenarios that the previous slide describes.
They are similar to the non-parallel default process model in that they have configuration options, generate reports, and have callbacks you can override such as PreUUT.

## Slide 13: Parallel vs. Batch Models
Parallel
Test
Fixture
Test
Fixture
Test
Fixture
UUT
UUT
UUT
UUT
UUT
Batch
Test Fixture
UUT
UUT
UUT
UUT
UUT
UUT
Common Carrier
Common Carrier
Notes: This diagram illustrates the differences between the parallel and batch models.
In the parallel model, each test socket tests UUTs independently. Each test socket has its own thread of execution.
In the batch model, each test socket also has its own thread. However, all test sockets begin and end testing together for a given set of UUTs. Typically the UUTs in a batch must be tested together because they reside in a common carrier or because they must share a multi-uut test resource such as a temperature chamber.

## Slide 14: A Batch Starts and Ends as a Unit
Test
Test
Test
Test
Test
Test
Socket 1
Socket 2
Socket 0
Start testing all units in the batch
Wait until all units complete
Notes: A batch test starts on all test sockets at the same time. The batch test is not complete until all test sockets complete testing.

## Slide 15: Synchronized Sections in a Batch
Test
Test
Test
Test
Test
Test
Socket 1
Socket 2
Socket 0
Wait for all units
Wait for all units
Synchronized
Section
Notes: A batch test automatically synchronizes the start and end of testing on all test sockets. In addition, you can add a special area of synchronization in your test sequences called a synchronized section.
A synchronized section is similar to the entire batch test in that all test sockets enter and leave the section at the same time. Synchronized sections only take effect when your sequence runs under a batch process model.

## Slide 16: Synchronized Sections (Cont.)
Three Types
  Parallel
  Serial
  One-Thread-Only
Notes: When you create a synchronized section, you specify one of three section types: Parallel, Serial, or One Thread Only.

## Slide 17: Parallel Sections
Test
Test
Test
Test
Test
Test
Socket 1
Socket 2
Socket 0
Wait for all units
Wait for all units
No synchronization within parallel section
Test
Test
Test
Notes: A parallel section is the simplest type of section. It does not perform any action beyond synchronizing all test sockets at the beginning and end of the section.

## Slide 18: Serial Sections
Shared resource
Socket 1
Socket 2
Socket 0
Wait for all units
Wait for all units
Test
Test
Test
Test
Test
Test
Test
Test
Test
Shared resource
Wait for all units
Each test socket executes in series
Notes: A serial section restricts execution so that only one test socket executes the steps in the section at a time. Each test socket runs in ascending test socket order.
You can use a serial section to give each socket exclusive access to a resource that all test sockets share.

## Slide 19: One-Thread-Only Sections
Socket 1
Socket 2
Socket 0
Wait for all units
Wait for all units
Test
Test
Test
Only one test socket executes the actions in the section
Action
Action
Action
Action
Action
Action
Notes: Only the first test socket executes the steps in a one-thread-only section. The remaining test sockets skip the step in the section.
You can use a one-thread-only section to ensure that an action that applies to all test sockets executes only once. An example would be changing the temperature in a test chamber.

## Slide 20: Batch Testing Demo
(show model file)
Configurable number of UUTS
  A separate thread tests each UUT
(run demo)
Batch reports
Notes: This is a demo that comes with TestStand 2.0.
<load TestStand\Examples\MultiUUT\BatchUUT.Seq>
Note that when I loaded the file, the current process model became the Batch Model (The current model is shown in the lower right corner of the sequence editor status bar.). That is because this sequence file specifies that it runs under the Batch model.
<Show sequence file properties dialog box>
You can specify that a sequence file use a particular model or you can change the default model for your entire test station.
Notice that if I switch to another sequence file window, the current model is again the default model. With the default model, there are no Model Options to configure. This is why the Model Options menu item is dim.
When the Batch model is active, I can configure additional model options.
< Select Configure>>Model Options >
I will specify how many test sockets that my test station has. For this demo, I'll select 8. This tells the batch model to run my test sequence simultaneously on 8 separate test sockets.
<Show synchronization property and steps>
< Run TestUUTs entry point>
When I start the sequence in TestUUTs mode, the batch model displays a dialog that allows me to specify the serial numbers of each UUT in the batch and a serial number for the batch itself.
This demo demonstrates the different types of batch synchronization. First, it simulates changing the temperature in a chamber that contains all the UUTS in the batch. In this case, the test step runs only once no matter how many test sockets are in the system.
Next, the sequence demonstrates sharing access to an instrument. The sequence uses a serial section to ensure that each test socket waits its turn to use the pulse generator.
Finally, the sequence allows a test to run in parallel on all test sockets. This is where the sequence gains a performance advantage over testing each UUT one at a time.
Notice that the Batch model generates a summary report for all of the UUTs in the batch. It has links to the individual reports for each UUT.
The Batch model also provides number of additional report configuration options.
For example, I could store the summary reports and the UUT reports in the same file. I could store the reports in separate files for each test socket, or I could store each report in a separate files.

## Slide 21: Parallel Demo
Notes: <Demo Prep: Save ParallelComputer.seq in TestStand20\examples\demo\c\>
This demo is a variation of the usual computer motherboard-testing demo. The only changes I’ve made have been to make each test take ¾ seconds longer, and to specify that the sequence runs under the parallel model.
<Load TestStand20\examples\demo\c\ParallelComputer.seq \>
Note that when I load this file, the current process model becomes the Parallel Model because the file properties are set to select that model.
For this parallel demo, I'll change the number of test sockets to two <select Configure>>Model Opptions> to demonstrate a dual well system.
<Run TestUUTs entry point. Move the UUT dialog slightly to the right to expose a portion of the underlying execution windows>
Notice that not only can I specify the serial number for each UUT, but I can also start testing on any test socket at anytime. First, I'll start testing on socket 1 <Select the components to simulate pass/fail>. As the first test runs, you could imagine that I'm manually loading the second UUT into socket 2.
<Short pause>
Now I start socket 2 <Select the components to simulate pass/fail>. Notice that when socket 1 finishes, socket 2 is still testing. I can load a new UUT into socket 1 when I'm still testing on socket 2.
Thus, my test system doesn't have to stop testing just because I need to load and unload UUTs.
Note that other than selecting the parallel process model, this file has no modifications for parallel execution.

## Slide 22: How do You Identify the Test Socket?
New properties in TestStand 2.0
  RunState.TestSockets.MyIndex
  RunState.TestSockets.Count
Batch and Parallel process models update these properties
Notes: How does your test sequence know which test socket to test when you run it under the Batch or Parallel process models?
Your test sequence can examine two RunState properties to determine the number of test sockets in the system and the zero-based index of the test socket on which it is testing.
To enable a real test sequence file to run under the parallel and batch models you must ensure that each test operates on its designated test socket. If your test sockets do not share resources, this might be the only modification you need.

## Slide 23: Asynchronous Sequence Calls
Start your own thread or execution, no process model required
Optional setting on Sequence Call Dialog Box
Notes: You don't have to use a process model to launch multiple threads in your test system. You can specify that any sequence call runs in its own thread or execution. I'll show a demo of this later. You can still launch new executions using the TestStand API, but it can be easier to use a sequence call.
For example, the multi UUT process models use the sequence call step to launch the executions for each test socket.
You can use the sequence call step to create new thread or execution anytime you need it by just selecting the option from the Multithreading ring.

## Slide 24: Executions vs. Threads
An execution is a group of threads
  Begins with a single thread
  Asynchronous sequence calls create additional threads
  All threads in execution suspend or terminate when the execution suspends or terminates
  An execution completes when all of its threads complete
Notes: The sequence call step enables you to launch threads or executions. What’s the difference?
The difference is than execution is a container of threads. It must contain at least one thread, but it can contain more.
All the threads in an execution suspend or terminate as a unit.

## Slide 25: Executions vs. Threads (Cont.)
Additional Execution Traits
  Can run under a process model
  Report
  Separate Window (in NI GUIs)
Batch and Parallel models create an execution for each test socket
  Separate report for each test socket
  Enables test sockets to independently terminate or suspend
Notes: Executions can also have an associated process model and report.
The Batch and Parallel models create an execution for each test socket so that each socket has its own report and window, and so that each socket can terminate independently.

## Slide 26: Synchronization and Resource Sharing
Old Way - Synchronize in code modules
  LabVIEW Mutex, etc.
  Win32 Critical Section, etc.
New Way – Synchronize in TestStand
  Synchronization Steps
  Synchronization Properties
Notes: Once you have multiple threads running, you will probably need to synchronize between them. In the past this meant low level coding. Now you have the option of synchronizing at a higher level.
TestStand 2.0 provides a rich set of step types you can use for synchronization and it also provides certain synchronization properties as an integral part of every step.

## Slide 27: Synchronization Step Types
Step Types
  Lock, Rendezvous, Queue, Notification, Wait, Batch Synchronization, …
Common Features
  Names and references
  Timeouts
  Suspension/termination friendly
  Shareable among processes and machines
  Configurable object and operation lifetimes
    Example: Acquire lock for duration of sequence
Notes: There are several different types of synchronization steps.
The synchronization steps share several common features. In general, each creates a synchronization object you can refer to with a name. For example, you can create a Lock named "DMM1".
You can also specify that a step times out if it cannot synchronize in a specified amount of time.
Synchronization steps recognize when you terminate or suspend execution. In contrast, a thread that blocks on a Windows critical section in a code module cannot be safely terminated by any means.
You can use synchronization step to synchronize between processes on a single machine and between multiple machines on a network.
Another common feature is that you can specify the lifetime of the synchronization object a step creates or the lifetime of an operation a synchronization step performs. For example, you could specify that a step holds a synchronization lock until the end of the current sequence.

## Slide 28: Locks
Socket 1
Socket 2
Socket 0
Shared Resource
Lock
Test
Test
Test
Test
Test
Notes: The most important and commonly used type of synchronization is a lock. You use a lock to guarantee exclusive access to a resource.

## Slide 29: Locks - Race Conditions
Operation 1
X = X + 1
  Move X  Register*
  Increment Register
  Move Register  X
Operation 2
X = X + 1
  Move X  Register*
  Increment Register
  Move Register  X
X starts at 0
X increments twice
X is now 1, not 2! The value of X is “corrupt”
Problem 1: Your program does not do what you specify
*Registers are thread specific
Notes: You need exclusive access to a shared resource to avoid race conditions.
A race condition occurs when the results of two or more tasks can vary depending on the order in which the computer executes the instructions in the tasks.
The first problem you can have is corrupted information. In this example, two tasks increment the same number. However, if instructions in the tasks happen to execute in the order show by the arrows, the number is not correctly incremented.

## Slide 30: Locks - Race Conditions (Cont.)
Measure A
  Apply switch route A
  Read voltage
Measure B
  Apply switch route B
  Read voltage
Both measurements use route B!
Multithread safe instrument drivers don’t protect you!
Problem 2: Your program does not do what you intend
Notes: Even if you can protect individual actions such as incrementing a variable or calling a driver function, the same problem arises for higher-level operations you create by combining multiple actions.
In this example, you get an incorrect reading even if each switch and measurement function you call is individually “thread-safe”.

## Slide 31: Locks provide Thread Safety
Test Stimulus/Response
Lock DMM 1
Test DMM 1
Unlock DMM 1
Lock Fgen + Scope
Unlock Fgen + Scope
Test Stimulus/Response
Lock DMM 2
Test DMM 2
Unlock DMM 2
Lock Fgen + Scope
Unlock Fgen + Scope
FGen
Scope
DMM1
DMM2
Scope
FGen
Scope
FGen
FGen
Scope
FGen
Scope
FGen
Scope
FGen
Scope
FGen
Scope
DMM1
DMM2
DMM1
DMM2
Notes: To avoid race conditions, you use a lock to prevent another thread from accessing a shared resource while you use it.
In this example, the two threads first acquire locks for different DMMs. Because the locks are not the same, both threads proceed in parallel.
Next, both threads try to acquire the same lock for a shared function generator and scope. In this case, one thread acquires the lock and the other thread blocks until the first thread releases the lock.
As long as all threads acquire the appropriate lock before accessing a shared resource, a thread is guaranteed exclusive use of the resource while it holds the lock.

## Slide 32: Nested Locks
Nested locks in same thread always succeed
  Threads “own” locks
Balance nested locks with unlocks
Notes: Locks have thread affinity. Only one thread can acquire a given lock at a particular time. Once a thread owns the lock, it can acquire the lock any number of additional times without the possibility of waiting.
A thread must release a lock the same number of times it acquires it to free the lock for use by another thread.

## Slide 33: Locks and Deadlock
Lock DMM
Lock Scope
Test
Lock Scope
Lock DMM
Test
Deadlock occurs when two threads each wait forever to acquire a resource held by the other thread.
Acquiring multiple locks one at a time can lead to deadlock
Notes: Locks prevent race conditions. However, locks introduce a new danger: Deadlock!
Deadlock occurs when two threads each wait forever trying to acquire locks that the other thread holds.
The more locks you have, the easier it is to unintentionally create deadlock.

## Slide 34: Locks and Deadlocks (Cont.)
Deadlock prevention
  Always acquire locks in same order
    or
  Acquire all locks in one operation
    Specify an array of locks
Deadlock detection
  Automatic
  TestStand identifies the threads and locks that cause the deadlock
Notes: What can you do to prevent deadlock?
First, you can make sure you always acquire your locks in the same order. However, this is error prone, especially if you acquire different groups of locks that have only a few locks in common.
Instead, you can use a TestStand feature that allows you to acquire a group of locks in a single operation. TestStand ensures that no lock in the group is acquired until you can acquire all the locks in the group.
However, sometimes you can’t acquire all the locks you need in the same place. If you aren’t careful about which locks you acquire and in the order you acquire them, you will get deadlock. What happens in TestStand when deadlock occurs?
Instead of hanging indefinitely, TestStand immediately reports a deadlock runtime error and identifies the threads and locks that cause the deadlock to help you diagnose the problem.

## Slide 35: Lock Step Configuration Dialog
Notes: How do you create a lock in TestStand?
One way is to insert a Lock step in your sequence. This is the configuration dialog for a lock step. The configuration dialogs for other synchronization steps are similar.
First, you select the operation the step performs. You can choose to create a lock to use later, but the Lock operation has a convenient option that creates the lock when you acquire it if the lock did not already exist.
Next you specify the name of the Lock. It is a good practice to create lock names that reflect resource the lock protects. For example, you might name a lock “DMM1”.
You do not have to name synchronization objects. For example, when you create a lock you can store the lock object in an ActiveX reference variable. You then specify the variable in place of a lock name when you acquire the lock.
For the Lock operation, you can also specify when to release the lock you acquire, and whether to timeout if you cannot acquire the lock.

## Slide 36: Step Synchronization Properties
Convenient method for placing a Lock or Batch Synchronized Section around an individual step
Notes: If you just want to lock the execution of a single step or apply batch synchronization to a single step, you do not need to surround the step with synchronization steps.
Instead, it can be easier to use the built-in step synchronization properties. For example, to place a lock around the execution of a step, you need only checkmark a single option.

## Slide 37: Batch Synchronization Step
All test socket threads rendezvous at the beginning and end of the section
Section Types:
  Parallel
  Serial
  One-Thread-Only
Notes: You use a Batch Synchronization step to create a synchronized section around a group of step you run under the batch model.
You can configure whether the step marks the beginning or the end of a synchronized section. If the step begins a section, you also specify the type of synchronized section.

## Slide 38: Rendezvous Step
Waits until a specific number of threads reach designated locations
Notes: Another type of synchronization that TestStand provides is the Rendezvous. You can use a rendezvous to wait until several threads reach designated locations before letting any of these threads proceed further.

## Slide 39: Rendezvous Cont.
Create Rendezvous
Test Sequence
Wait
Thread 1
Thread 2
Tx Test 1
Tx Test 2
Rx Test
Rendezvous
Tx Test 1
Tx Test 2
Rx Test
Rendezvous
Notes: Here is an example of a sequence that launches two subsequences in separate threads. The subsequences use a rendezvous to ensure all transmit tests complete before the receive tests start. In this example, we rendezvous before the receive tests in order to configure and start an RF generator that both tests share.

## Slide 40: Queue Step
Stores any type of data
Can send data from one thread to another
  Queue commands for worker thread to execute
  Queue results or measurements for worker thread to process or store
Notes: TestStand provides queues in which you can store any type of data. Queues are good way to send commands to or receive results from worker threads you create.

## Slide 41: Queue Step Cont.
Create Queue
Acquire Data
Enqueue
Loop
Dequeue
Analyze
Store
Loop
Thread 1
Thread 2
Notes: In this illustration, one thread acquires measurements and enqueues them for another thread to analyze.
You can specify that the consuming thread blocks when there is no data to process. You can also specify that the producing thread blocks if the queue exceeds a certain size.

## Slide 42: Wait Step
Wait for
  Thread or Execution completion
    The Wait step reports the results, status and error state of the thread or execution
  Time interval
    Delay without wasting CPU cycles
  Next multiple of a time interval
    Useful to control the speed of a loop
Notes: You can use a wait step to wait until a thread or execution completes or to wait until a time interval expires. When you call a subsequence in new thread or execution, the subsequence call returns only whether the subsequence launches successfully. To obtain the Pass/Fail status of an asynchronous subsequence, you use a Wait step to wait for the subsequence to complete. The wait step then returns the status and results of the subsequence.

## Slide 43: Notification Step
For sending and receiving events
  An event can contain data of any type
To receive an event, Wait on a Notification
To send an event, Set or Pulse a Notification. You can send events to:
  All threads
  Only the first thread to wait on the Notification
  Only threads currently waiting on the Notification
  Only the first thread currently waiting on the Notification
Notes: Use a Notification Step to send events to or receives events from other threads. To receive an event, you wait for it to occur. Each event can contain a single data item of any data type.

## Slide 44: Advanced Synchronization
Thread Priority
  Specifies operating system thread priority
Semaphore
  Similar to Lock
  Restricts access to a resource to a specific number of simultaneous users
  Nested locks can block
Batch Specification
  Use in batch process models
Notes: TestStand also provides advanced types of synchronization for specialized situations.
You can use the thread priority step to control the operating system priority of a TestStand thread.
You can use a semaphore to limit the number of simultaneous users of a resource. For example, you might limit a communication channel to 4 simultaneous users to help ensure adequate bandwidth for each user.
You use a batch specification step to specify the threads in a batch. Typically you would not use this step unless you are writing a batch process model.

## Slide 45: Synchronization Demo
Locks and asynchronous sequence calls
Notes: Now I will demonstrate how you can create threads and synchronize them in TestStand.
<Open syncdialogs.seq>
I have a simple sequence that calls a subsequence. The sequence call step is configured to call the subsequence four times in a loop. The subsequence displays two message boxes named Message 1 and Message 2 <show subsequence>. After the last loop of the subsequence completes, the main sequence displays one more message box named Final Message.
<Run main sequence directly >
Note that message one and message two display the loop index of the step that calls the subsequence.
Since the main sequence calls the subsequence four times, the two dialogs appear four different times. The two dialogs appear lower down the screen each loop iteration.
So far, we haven’t used any threads or synchronization. To change that, I will now specify that each subsequence call runs in its own thread. You do this by selecting Specify Module from the context menu of the Sequence Call step. In the Edit Sequence Call dialog box that appears, you select Run Sequence in New Thread from the Multithreading and Remote Execution ring control.
<Set subsequence call to run in new thread>
Now when I run, each subsequence call returns immediately after launching a subsequence thread. Thus, all four loop iterations run at the same time. You can see that since we did not wait for the subsequence threads to complete, we reach the Final Dialog right away.
If I click the first message dialog from the third loop, the third thread advances to its second dialog. If you breakpoint, you can see where each thread is.
<Select break and show each thread>.
Notice that only the third thread has reached its second message box.
I will now resume execution.
<Select resume>
I can dismiss the dialogs in any thread in any order. Each thread progresses independently. The execution completes when the last thread completes
--
Now, lets pretend that Message Box 2 is a shared instrument that only one thread can use at a time. How can we enforce this? With a lock!
I’ll put a lock around the Message Box 2 step by using the step synchronization properties tab. Notice that all I need to do is checkmark the lock control for the step!
<Checkmark the lock checkbox in the step>.
Notice that the flow control field of the step now denotes that it runs under a lock.
Can you guess what will happen when I run this time?
<Run>
Just as before all the threads display message box 1. Now however, only one thread can display message box 2 at a time.
<Click second message box 1>
Now the second thread owns the lock.
<Click the first and third message box 1’s>
The first and third threads are done with message box 1 but can’t get the lock to use message box 2. If we break, you can see that they are waiting to run that step.
<Break, show threads, resume, dismiss second threads message box 2>
When the second thread releases the lock, another thread can acquire it.
<Keep clicking to let all threads progress until done>
Any questions about this demo?

## Slide 46: Summary
Parallelism can improve performance and hardware utilization
Multithreading enables parallel operations to interact efficiently
TestStand 2.0 makes it easy to launch and synchronize threads
The Parallel and Batch models provide implementations for common parallel test scenarios
Notes: To summarize, parallelism can increase speed. Also, when your system performs concurrent logical actions, placing each action in its own thread can actually simplify your test system.
TestStand makes it easy to launch and synchronize threads
The Parallel and Batch models make it easier to test multiple UUTs in parallel.

## Slide 47: Resources
TestStand 2.0 User Manual
  Chapter 11, Synchronization Step Types
  Chapter 13 – 40, Module Adapters – Sequence Adapter
  Chapter 14, Process Models
<TestStand20>\Components\NI\Models\TestStandModels\TestStandProcessModels.PDF
Developer Exchange
  www.ni.com/exchange
Notes: Here are some sources of additional information. The user manual documents the relevant features but if you have a specific scenario or question, I would recommend posting a question to the developer exchange website.