## Slide 1: Understanding USB 2.0

## Slide 2: Agenda
USB communication
  3 layers
USB protocol
  Packet types
  Transfer types
USB 2.0
  Changes
  Compatibility with 1.1
USB for measurement & automation

## Slide 3: USB Technology Overview
Host & client
Communication is done via packets
Application Software Layer
Protocol Engine Layer
Physical Layer
Host
Device
Client software
USB System
Software
USB Bus
Interface
USB Bus
Interface
USB Logical
Device
Device Function
HC
SIE
SIE
Notes: <number>
<footer>
<header>
<date/time>
Host – Only 1 host exists on the bus. It controls all media access.
Device – A device cannot access the bus without approval from host.

## Slide 4: Physical Layer
Max # of devices per host = 127
Max distance between any device (or hub) = 5 m
Signaling
  LSB first
  Special signals
    Reset
    Suspend
    Resume
    EOP
Encoding/Decoding (SIE)
  Bit-stuffed NRZI
Protocol Engine Layer
Application Software Layer
Physical Layer
Host
Device
Client
software
USB System
Software
USB Bus
Interface
USB Bus
Interface
USB Logical
Device
Device
Function
HC
SIE
SIE
+5 V | -Data | +Data | GND
Notes: <number>
<footer>
<header>
<date/time>
The Physical Layer
The physical layer forms the base of USB communication and is comprised of the hardware and cables that transmit the digital “1” and “0” signals. USB connectors have four pins:
D+ : The positive lead of the differential pair of signaling wires
D- : The negative lead of the differential pair of signaling wires
Vbus : 5 V bus power supply
GND : -5 V
Host:
HC (host controller) is only a part of the host’s physical layer, initiates transactions and controls access to the USB. It partitions the time into 1 millisecond “frames” and issues a start-of-frame (SOF) packet at each 1 ms interval. In addition, it processes requests for data to and from the host and handles errors.
SIE (serial interface engine) serializes and de-serializes the USB transmissions, performs the encoding and decoding of the signals, generates or verifies CRC (which will be discussed in more detail later), and detects the packet’s ID (PID) as well as special signals such as start-of-packet (SOP), end-of-packet (EOP), and RESET signals.
Device:
Also has SIE, same function as in host
Special signaling:
Reset – Host resets the device by sending 0 for 2.5 usec
Suspend – In the absence of bus traffic from any powered state for more than 3 ms, all devices that are supplied power via the Universal Serial Bus (USB) must enter Suspend mode. Bus-powered devices draw current from the USB. These devices must reduce their power consumption to meet USB specifications. A device in Suspend mode can resume operation when any non-idle signal is received on its upstream port. It can also resume operation from the application via an external interrupt.
Resume – Suspended device will resume operation when it receives a K signal for at least 20 mSec (0 for low speed, 1 for full speed). Device can wake itself up or receive signal from host.
EOP - End of packet. Signaled by a Single Ended Zero (SE0) for approximately 2 bit times followed by a J (0 for low speed, 1 for full speed) for 1 bit time.
NRZI – non return to zero inverted
Bit stuffing – adding zero after six successive 1’s.

## Slide 5: Protocol Engine Layer
Host: USB system software
  Bus bandwidth & power
  2 driver software pieces
Device: USB logical device
  1 or more endpoints
Protocol Engine Layer
Application Software Layer
Physical Layer
Host
Device
Client
software
USB System
Software
USB Bus
Interface
USB Bus
Interface
USB Logical
Device
Device
Function
HC
SIE
SIE
Notes: <number>
<footer>
<header>
<date/time>
The Protocol Engine Layer
This middle layer is referred to as the “USB system software” layer on the host and as the “USB logical device” layer on the device because it performs different functions on each. The USB system software allocates bus bandwidth and manages bus power so that devices can access the bus. The USB system software also contains two driver software pieces, one of which provides the interface to the host controller, and another that identifies and enumerates devices on the bus and services their data requests.
The USB logical device is composed of one or more endpoints that transfer data. These endpoints are uni-directional in communication (IN supports only transfers from the device, while OUT supports only transfers from the host). Each endpoint has a certain transfer type, which will be discussed later.

## Slide 6: Application Software Layer
Host:
  Software user interacts with
  Device driver software
Device:
  Functions of device
Protocol Engine Layer
Application Software Layer
Physical Layer
Host
Device
Client
software
USB System
Software
USB Bus
Interface
USB Bus
Interface
USB Logical
Device
Device
Function
HC
SIE
SIE
Notes: <number>
<footer>
<header>
<date/time>
The Application Layer
This layer is the client software that the user interacts with on the host and the functions that the device performs.

## Slide 7: Transaction Example
Host
Device
Communication through series of packets
OUT
IN
OUT Token
Data
Handshake
IN Token
Data
Handshake
Notes: <number>
<footer>
<header>
<date/time>
This is an example of interrupt transfers

## Slide 8: Packet Types
Token
  PID defines the type of token (OUT, IN, SOF, SETUP)
  Sent by the host to initiate transaction
  OUT - “I am sending device ADDR, endpoint ENDP data”
  IN - “Device ADDR, endpoint ENDP, send data”
PID
ADDR
ENDP
CRC
Notes: <number>
<footer>
<header>
<date/time>
SOF – start of frame
Setup – for configuration of device
Packet Types
If the host wishes to send or receive data from a device, it issues it a token addressed to that device. This token is a special packet with the composition shown in Figure 3. The ADDR (device address – 7 bits) and ENDP (endpoint – 4 bits) fields uniquely defines which endpoint on which device is about to receive or send data. The CRC (cyclic redundancy check – 3 bits) field is used to protect the packet and detect errors. PID is 8 bits. Token packets are a total of 22 bits.

## Slide 9: Packet Types
Data
  Data field 0-1023 bits
Handshake
  Only PID
  ACK, NAK
  STALL
PID
Data
CRC16
PID
Notes: <number>
<footer>
<header>
<date/time>
Once a token has been sent to a device, data packets containing the actual data to be transmitted are sent to the device (for OUT transactions) or data packets are received from the device by the host (for IN transactions).
Handshake packets are optional and are simply indicate the success or failure of the transaction. Its 8-bit PID indicates this in the following ways:
ACK – Packet transmission was successful
NAK – Device is unable to send or receive data due to an error
STALL – The specific endpoint is halted or the specific SETUP command is not supported.

## Slide 10: Transfer Types
Transfer Type | Guaranteed | 
 | Accuracy | Bandwidth
Control | Yes | Yes
Bulk | Yes | No
Isochronous | No | Yes
Interrupt (polled) | Yes | Yes
Notes: <number>
<footer>
<header>
<date/time>
Transfer Types
Control – used to configure the device, either at enumeration or at any state in the communication process.
Bulk – typically used by devices such as printers and scanners, vary in allocated bandwidth but focus more on accuracy of the data.
Isochronous - guarantee bandwidth but are less concerned about the accuracy of the data. Therefore, no handshake phase occurs in isochronous transfers. Audio and video devices often use this type of transfer because slight errors are often not detectable by human senses.
Interrupt - Keyboards, mouse, and other types of input devices that regularly need to report small chunks of data use interrupt transfers. A USB device that uses these types of transfers defines in its initial configuration the time interval it wants to send or receive information, and then the host must poll that device at the specifies interval.

## Slide 11: USB 2.0
New high-speed devices
  Max speed 480 Mbits/s
Split frames
  1.1 frame = 1 ms
  2.0 microframe = 125 μs
PING & NYET (not yet) packets
Split transactions – data transmission & ACK can be separate
Backward & forward compatible with 1.1
  1.1 devices are low or full-speed in 2.0
  2.0 high-speed devices are full-speed in 1.1
Notes: <number>
<footer>
<header>
<date/time>
USB 2.0
The release of USB 2.0 established a new category of high-speed devices that can reach a maximum transfer rate of 480 Mb/s, 40 times faster than the previous USB specification’s maximum transfer rate of 12 Mb/s. This created a total of three classes of USB devices: low-speed (1.5 Mb/s), full-speed (12 Mb/s), and high -speed (480 Mb/s). Because the physical connections have not changed, USB 2.0 is both forwards and backwards compatible with USB 1.1. This means that USB 1.1 devices can function with a USB 2.0 host, and USB 2.0 devices can function with a USB 1.1 host (however, they will function as a full-speed device).
In addition to speed changes, the new high-speed protocol includes some other differences. It splits the existing 1 ms frame into eight 125 s microframes. It also increases the number of data bytes transferred per microframe (512 bytes/microframe from 64 bytes/frame). Full-speed devices can transfer up to 19 transfers/frame and high-speed device can transfer up to 13 transfers/microframe, or 104 transfers/frame. Since large data packets can consume large amounts of bandwidth, a new PING command and a NYET (not yet) packet were introduced. The PING command is used to ask a device whether it can accept a full packet if one is sent. If it receives a NYET handshake, the host shall resume PINGing the device until it is ready for another packet.
Another change in 2.0 is the notion of a split transaction. Since full-speed devices are much slower than the high-speed devices, if the transmitting of data and the receipt of the acknowledgement handshake were still one atomic operation (as they are in USB 1.1), communication on the entire bus would be slowed down. Therefore, the two stages of communication are “split” when the host is communicating with downstream hubs. This allows the host to communicate with high-speed devices and not wait idle until the full-speed device returns the handshake.

## Slide 12: USB for Measurement & Automation
Benefits
  Single cable
  Easily embeddable
  Plug & play setup/configuration
  Portable
  Computer agnostic – works on laptops and desktops
  USB 2.0 offers faster transfer rates, enabling higher speed acquisitions

## Slide 13: NI USB DAQ Devices – Over Two Dozen Choices
High performance
from $595
USB DAQ for Sensors & High Voltages
from $395
Low cost DAQ
from $145
Notes: High performance multifunction DAQ
  DAQPad-6015 – 16-channel, 200 kS/s, 16-bit multifunction DAQ
  DAQPad-6016 – 16-channel, 200 kS/s, 16-bit multifunction DAQ with extended DIO
  SCXI-1600 – 16-bit 200 kS/s digitizer for SCXI
DAQ with signal conditioning – starting at $395
  USB-9211 – 4 channel, 12 S/s, 24-bit thermocouple measurement device – 250 Vrms isolation
  USB-9215 – 4 channel, 20 kS/s, 16-bit simultaneous sampling analog input device – 250 Vrms isolation
Low cost DAQ – starting at $145
  USB-6008 – 8 channel, 10 kS/s, 12-bit multifunction DAQ
  USB-6009 – 8 channel, 50 kS/s, 14-bit multifunction DAQ