## Slide 2: Advanced LabVIEW FPGA Programming Optimizing for Speed and Size
Joseph DiGiovanni
LabVIEW FPGA Module Product Support Engineer
NIWEEK 2005
Notes: When programming National Instruments reconfigurable I/O FPGA devices with the LabVIEW FPGA Module, you need to understand certain constraints to create efficient FPGA applications. Some of these constraints include limited size and speed. This presentation will cover ways to recognize FPGA application inefficiencies and guidelines to follow when writing or reviewing applications. Also discuss parallel operation creation, code pipelining, and appropriate RAM use.

## Slide 3: Topics
Benchmarking VIs
How LabVIEW is transformed for FPGA
Optimizing for Speed
Optimizing for Size
Notes: Over the next hour we will discuss how LabVIEW is transformed for the FPGA and good programming practices. We will examine inefficiencies and recognize how we can improve code for speed and size.

## Slide 4: Benchmark Your VIs Loop Rate
1 Tick = 1 Clock cycle
Clock cycle depends on compile rate (Default 40MHz)
32-bit counter increments on rising edge of the clock
Tick Count function returns the counter value
Notes: What is a tick?

## Slide 5: Benchmark Your VIs Loop Rate
Timestamp each iteration
Calculate the difference
Measurements done in parallel*
Code can be removed later
*take advantage of parallel execution of FPGA
Notes: The Tick Count VI can be used to benchmark you application as well as create custom timing VIs. Here we see an example of how the tick count is used to benchmark the execution period of a looping structure.

## Slide 6: Benchmark Your VIs Execution Time
Get initial time
Execute code
Get final time
Calculate the difference
Measurements done in parallel*
Code can be removed later
*take advantage of parallel execution of FPGA
Notes: Here the Tick Count is used to benchmark a frame of code.

## Slide 7: Benchmarking Your VIs Size
Speed
  Theoretical maximum compile rate shown in parenthesis
Size
  IOBs – Input/Output Blocks
  MULT18X18s - multipliers
  SLICEs – Combination of LookUp Tables (LUTs) and Flip Flops (FFs)
  BUFGMUXs – portal to the clock net, which is used to clock FFs
Notes: After compiling, a report is generated which provides information on speed and size of the compiled VI. The Device Utilization summary provides information on the number of SLICEs used. This metric is the most important measure of your programs size in hardware. The design process should be an iterative process. During the process you will notice the SLICEs used will most likely increase as your program gets larger. You must be aware of what operations you have added if you notice a significant increase in SLICEs used.

## Slide 8: Too Big, Too Slow?
Modify code for improving speed or size, or both
  Helps to understand how LabVIEW is transformed for FPGA

## Slide 9: How LabVIEW is Transformed for FPGA
Three components necessary to maintain data flow
  The corresponding logic function
  Synchronization
  The enable chain
Notes: LabVIEW executes code in a dataflow manner. Nodes execute when data is present on all of the nodes inputs. When the node finishes execution the outputs of the node pass data to the next node downstream. LabVIEW FPGA uses 3 components to maintain this dataflow paradigm. First the node has logic corresponding to its function. In this figure we see the boolean not function and its associated logic. The next component needed for dataflow is synchronization. This component registers the outputs of the function in order to isolate the logic from timing uncertainties. Finally additional logic referred to as the “enable chain” is used to coordinate the dataflow by validating the inputs and outputs.
What is a register (FF)? Passes data from input to output on rising edge of clock. Synchronous because everything runs off of same clock.

## Slide 10: Enforcing Dataflow in FPGA
Now that we see how LabVIEW is transformed for FPGA lets examine how to optimize
FFs
FFs
FFs
Notes: This is a simple VI that has a boolean control and not function and a digital output function. Let’s step through the functions to see how this would be transformed for the FPGA.
The boolean control has some logic associated with the data register to retrieve data from a host application. There is also a FF used as a link the enable chain. The not function has the logic associated with the function itself, a synchronization FF, and a enable chain FF. The digital output has a synchronization FF and an enable chain FF as well.
Let’s examine how stringing this logic together would execute. When the program is run the enable line goes high. This enables the synchronization FF associated with the boolean control. Meanwhile a rising edge of the clock pushes the data from the register through the FF. Downstream the previous values are held on the outputs of the FFs. During the next rising edge of the clock the synchronization FF associated with the not function passes the new value through. Downstream the dio is still held at the initial value because the enable in on its FF is still low. On the third rising edge of the clock the enable in of the digital output is high and the new value is pushed through the FF to the I/O pins.
Lets abstract all the logic that is actually implemented and just call them FFs. Lets see where these FFs get placed.
This data is synchronized using a FF that pushes the data through the FF on the first rising edge of the clock.

## Slide 11: Optimizing for Speed
Parallel Loops
Pipelining
Single Cycle Timed Loops
Example

## Slide 12: Parallel Execution
Graphical programming promotes parallel code architectures
LabVIEW Windows and Real-Time serializes execution
LabVIEW FPGA implements truly parallel execution
Notes: Using the parallel nature of graphical programming and the truly parallel implementation on the FPGA you can separate your code into different code segments which can run in parallel and achieve a faster loop rate than when everything is in one process. As you develop your code start thinking about logical pieces to break the code into different segments.

## Slide 13: Parallel Execution Example
Loop rates limited by longest path
AI takes 170 ticks, DI takes 1 tick
Separate functions to allow DI to run independent of AI
173 Ticks ~ 4.3uSec
4 Ticks ~ .1 uSec
Notes: This example has AI and DIO in one loop. The loop takes 173 ticks to execute. The AI takes 170 of this ticks. Therefore we are sampling the AI and DI at about 230KHz or about every 4.3uSec. What if we have a digital pulse that only lasts 4 uSec. We could entirely miss the digital signal. We need a way to read the DI faster. Separate the DI from AI in parallel loops. The DI loop can now sample at about

## Slide 14: Pipelining
Within a loop you can split up your code into different loop iterations to reduce the length of each iteration
  Handle different parts of the process flow in parallel within one loop iteration
  Pass data to the next using shift registers
A
B
A
B
Notes: Pipelining is the process of breaking up code within a loop and dividing it up into different iterations of the same loop. Therefore the length of the data flow process within one loop iteration is reduced and the loop can run faster while executing the same code in parallel.
The diagram illustrates how a process consisting of A and B can be broken up and run in parallel to reduce the length of each loop iteration.

## Slide 15: Pipelining Example
720 clock cycles (18 μs)
365 clock cycles (9.13 μs)
Notes: Example showing how pipelining the analog input and output operations drastically reduces the loop period, increasing the sample rate or control loop rate. Since the analog input and analog output operations both take a long time to run on the FPGA it is very efficient to put them in parallel on the FPGA and have them run at the same time.

## Slide 16: Single-Cycle Timed Loop (SCTL)
Loop contents execute in a single clock period
Minimizes synchronization and enable chain overhead
However, there are restrictions
  Some VIs and functions can’t be used in the loop at all
    Analog input, analog output
    Nested loops
    Any that require more than a single clock cycle to execute
    Shared resources
Loop timer
Wait
Notes: The Single Cycle Timed Loop (SCTL) is a special form of the While loop available on the FPGA. It uses the same representation as the timed loop on the Windows or RT target, but has little in common with that structure. Conceptually it is a While loop that runs in one clock cycle of the FPGA for each iteration of the SCTL. Thus the loop rate of the SCTL is the same as the clock frequency of the FPGA. This of course offers us great benefits with regards to the performance of our VIs, executing code extremely fast.
In addition the code generated by the compiler from the SCTL is more optimized and takes up less space on the FPGA compared to the same code inside of a regular while loop.
So why wouldn’t you always use the SCTL? There are some significant limitations to the use of the SCTL I your application.
To use the SCTL all operations inside the SCTL must fit within one cycle of the FPGA clock. This is determined by the code generator before starting the compiler. The code generator will give an error message if the SCTL can not generate the proper code for the compiler.
You can use the pipelining technique to reduce the length of each run through the SCTL by breaking up the code among multiple iterations of the SCTL. In addition to pipelining, you can use a State machine within the SCTL to better organize your code and run through a sequence of steps. The basic component of the state Machine is a Case structure with each containing one state and using a shift register to determine the next state after each iteration of the loop. Of course each state must be able ti run in one clock cycle.
Using shift registers and a counter value you can implement the functionality of a For loop or add a specific number of Wait states to your program execution.

## Slide 17: SCTL Example
Saved 5 Ticks by placing this code in a SCTL
1 Tick
6 Ticks
Notes: Example of the SCTL to perform some data processing within one clock cycle. The same operation in a While loop would require about 6 clock cycles including the overhead of the While loop. The SCTL also removes the enable chain overhead and therefore uses less FPGA slices. As shown the SCTL uses 5% less slices than the code outside the SCTL.

## Slide 18: Improving Loop Performance
What to do if your diagram executes too slowly?
12 clock cycles
1
2
3
4
5
6
7
8
9
10
FFs
FFs
FFs
FFs
FFs
FFs
FFs
FFs
FFs
FFs
FFs
FFs
FFs
FFs
11
12
Notes: The longest path is from the DIO to the position indicator. Very little is done in parallel.

## Slide 19: Reduce the Depth of the Data Flow
Shorten the longest path
9 clock cycles
1
2
3
4
5
6
7
FFs
FFs
FFs
FFs
FFs
FFs
FFs
FFs
FFs
FFs
FFs
FFs
8
9
Notes: We just took advantage of parallelism. What about pipelining?

## Slide 20: Pipeline the Diagram
Watch out for pipeline effects
6 clock cycles
1
2
3
4
FFs
FFs
FFs
FFs
FFs
FFs
FFs
FFs
FFs
FFs
FFs
FFs
5
6
Notes: Further reduced by pipelining. Need to remember that the position indicator is from the previous iteration of the loop.

## Slide 21: Use the Single-Cycle Timed Loop
Eliminates synchronization and enable chain in the loop
1 clock cycle
1
FFs
FFs
FFs
FFs
FFs
Notes: The single cycle loop has removed the synchronization and enable chain. The operations inside the loop can all take place within 1 clock cycle. We will see that the SCTL can also be used for size improvements because of the removal of the enable chain logic.

## Slide 22: Optimizing for Size
SubVIs
Front Panel Objects
Datatypes
Functions Using Lots of Space
Single Cycle Timed Loops
Example
Notes: <number>
Another major constraint of the FPGA is the limited number of gates on the device. The techniques in the list will be investigated to help reduce the size of a FPGA program.

## Slide 23: Sharing SubVIs
Non-Reentrant subVI is a shared resource
  Slower execution
  Less space (generally)
Reentrant subVI recreate logic for each instance
  Faster execution
  More space (generally)
Reentrant Non-Reentrant
Number of MULT18X18s 18 out of 40 45% 3 out of 40 7%
Number of SLICEs 2116 out of 5120 41% 2028 out of 5120 39%
Notes: Example of maintaining state information in the main VI and passing it into a subVI.

## Slide 24: Limit Front Panel Objects (FPO)
Have additional logic to control data transfers to/from host
Front Panel Arrays are very expensive
  Reduce array sizes
  Store data in user memory instead
Notes: When optimizing your code for the amount of space it uses on the FPGA, you should consider the front panel controls and indicators you are using. Each front panel object and the data it represents takes up a significant portion of the FPGA space. By reducing the number of these objects and reducing the size of any arrays used on the front panel you can significantly reduce the FPGA space required by the VI.
Instead of creating large arrays to store data and transfer it to the host application, store the data in user memory from you FPGA VI and transfer it in smaller blocks to the host application.

## Slide 25: Misuse of Front Panel Arrays for Data Transfer
This diagram uses a front panel array to pass data to host
Tutorial Using Clusters and Arrays in LabVIEW FPGA
Notes: When optimizing your code for the amount of space it uses on the FPGA, you should consider the front panel controls and indicators you are using. Each front panel object and the data it represents takes up a significant portion of the FPGA space. By reducing the number of these objects and reducing the size of any arrays used on the front panel you can significantly reduce the FPGA space required by the VI.
Instead of creating large arrays to store data and transfer it to the host application, store the data in user memory from you FPGA VI and transfer it in smaller blocks to the host application.

## Slide 26: Better Data Transfer Method
Use scalars to pass data between FPGA memory and host
Tutorial Using Clusters and Arrays in LabVIEW FPGA
Notes: When optimizing your code for the amount of space it uses on the FPGA, you should consider the front panel controls and indicators you are using. Each front panel object and the data it represents takes up a significant portion of the FPGA space. By reducing the number of these objects and reducing the size of any arrays used on the front panel you can significantly reduce the FPGA space required by the VI.
Instead of creating large arrays to store data and transfer it to the host application, store the data in user memory from you FPGA VI and transfer it in smaller blocks to the host application.

## Slide 27: Use Minimum Datatype Necessary
BAD

## Slide 28: Datatype Bitpacking
Combine small datatypes into a 32 bit numeric
  Reduces front panel objects
  Faster data transfers to/from host
BAD
Split Number

## Slide 29: Functions Using Lots of Space
Quotient Remainder
Scale By Power of 2 (should use constant for power)
Array Functions (should use constants where possible)

## Slide 30: Single Cycle Timed Loop
FFs
FFs
FFs
FFs
FFs
FFs
FFs
FFs
FFs
FFs
FFs
FFs
FFs
Removes Enable Chain Overhead
FFs

## Slide 31: Optimize for Size
This VI is Too large to compile, Why?
Notes: <number>
This VI uses an array to store sinewave data. The array is indexed to get a value. In addition, four previous points are stored in shift registers. The previous four values are averaged. This VI is too large to compile. What can be done to help optimize this code?

## Slide 32: Optimize for Size
This VI takes 21% of the 1M gate FPGA. Can we do better?
Notes: <number>
We have replaced the array with a lookup table. This change alone has allowed us to compile the program and use only 18% of a 1 million gate FPGA. Can we further optimize the program? Hint: what primitives use a large amount of FPGA space?
Number of SLICEs 1090 out of 5120 21%

## Slide 33: Optimize for Size
This VI takes 9% of the FPGA, can we do better?
Notes: <number>
We have removed both Quotient Remainder (QR) functions. One of the QR functions was being used to index through the lookup table. This was replaced by a shift register counter operation. This shift register counter operation is a very common technique in FPGA. The other QR function was replace by a scale by 2 to the power of n. Because the scale by 2 has a constant input it uses very little FPGA space. Note: Scale by 2^ -2 is equal to dividing by 4.
Can we do better?
Number of SLICEs 511 out of 5120 9%

## Slide 34: Optimize for Size
This VI uses 8% of the FPGA
Notes: <number>
The design was modified to use a SCTL. We added a shift register counter to replace the function of the loop timer. This new counter in combination with the case structures make only certain code execute at a specified rate. Every 5000 iterations the index register will increment and new values will be pushed into the averaging shift registers.

## Slide 35: Summary
Use Timing VIs to benchmark your code
FPGA uses an “enable chain” to maintain dataflow
Improve speed performance by
  reducing depth of dataflow path
  using parallel loops and pipelining
  using Single Cycle Timed Loops
Improve size usage by
  Sharing common code in subVIs
  Minimizing arrays and Front Panel Objects
  Use appropriate datatypes
  Be aware of large functions
  using Single Cycle Timed Loops
Notes: <number>