## Slide 1: Dynamic Signal Measurement Basics Sensors
Tachometers
Notes: Typical sensors used for dynamic signal measurements are accelerometers, microphones, and tachometers. Other common sensors include displacement probes, velocity probes, and hammers.
Even before doing any actual measurements, it is important to select your sensors carefully and to make sure that they will be well suited for the analysis you plan to perform.
We will briefly introduce you to tachometers, their principle of operation, and their typical characteristics.

## Slide 2: Tachometers
Measure
  Angular position
  Angular speed (rpm)
Used for
  Order analysis
  Order tracking
  Angular averaging
Notes: When dealing with rotating machines, it is important to be able to relate any measurement from an accelerometer or a microphone to the actual rotational speed of the machine under test. A tachometer will basically track the angular position of a shaft versus time and so lead to the measurement of the angular speed (commonly expressed in rpm, revolutions per minute).
More than providing this angular speed information, the signal from the tachometer is needed to perform advanced analysis such as order tracking, order analysis, and angular averaging.

## Slide 3: How a Tachometer Works
Uses a wheel with N teeth (N pulses/rev)
Detects the presence of the teeth via an optical sensor (reflection) or a magnetic sensor (proximity)
time
V
rpm
Notes: To measure the angular position, a wheel with N teeth is commonly mounted on the shaft. The tachometer then detects the presence of the teeth via either an optical sensor (transition from a reflective surface to a nonreflective one) or a magnetic sensor (proximity of the tooth). In some cases, a small stripe of reflective tape is simply attached to the shaft, generating one pulse per revolution.
The output signal of the tachometer is a pulse train, the time between two consecutive pulses being directly related to the angular speed of the shaft.
If the absolute angular position is needed, a special wheel with a “missing” tooth can be used. A typical example would be a wheel with 59 teeth uniformly placed every 6° (360°/60), the missing (60th) tooth being related to a known position of the shaft (such as the top dead center for the crankshaft in an engine).