## Slide 1: Dynamic Signal Measurement Basics Signal Processing
Swept Sine
Notes: Swept Sine is a signal processing technique use to obtain the frequency response of a system, such as a loud speaker, by applying a swept in frequency of tones and analyzing the response for each applying excitation signal or tone. Some basic principles of this technique are briefly described here.

## Slide 2: Swept Sine Analysis
Step through sequence of frequencies
    Start Frequency, Stop Frequency, Number of Points
    Frequencies can be linearly or logarithmically spaced
Measure the magnitude and phase at each frequency
    Spectrum of
    Chan A and Chan B
    Frequency Response
    B(f)/A(f)
Notes: A swept sine measurement is a sine sweep that steps through a specified sequence of frequency points. At each frequency, the source tone is maintained and the inputs to the analyzer are measured only at that source frequency. Both the magnitude and phase of each component is measured so that the frequency response of input/output systems can be characterized.
After each measurement, the source frequency is then adjusted to the next frequency in the sweep sequence, and a new measurement is taken at this new frequency.

## Slide 3: Swept Sine - Optimizing Sweep Time
Sweep time can be optimized
  More time at lower frequencies, less time at higher
  Skip regions of little change, fine tune frequencies with narrow response functions.
Notes: To optimize total measurement time when sweeping a large frequency range, the bandwidth at each frequency line can be configured to be inversely proportional to the frequency. This has the effect that more time is used for lower frequency measurements and less time for higher frequency measurements.
You can also optimize sweep time for narrow response functions by configuring the swept sine analyzer to skip frequencies where the response remains fairly constant, and to increase frequency resolution where the response is changing rapidly.

## Slide 4: Swept Sine - Dynamic Range
Dynamic range can be optimized at each frequency
  Adjust source amplitude
  Adjust input range
  Both improve dynamic range at particular frequencies
Notes: Comparing the swept sine measurement technique to the FFT measurement, the swept sine measures only one line at a time and is therefore much slower to the FFT which measures a group of frequencies simultaneously.
On the other hand, swept sine analyzers can optimize their measurements at each frequency by adjusting the source output power and input voltage range to increase the S/N ratio. Adapting to the system under measurement in this fashion can extend the effective dynamic range of the DSA to beyond 140 dB.