## Slide 1: Dynamic Signal Measurement Basics Signal Processing
Order Analysis
Notes: One of the signal processing techniques used to perform vibration analysis in rotating machinery is Order Analysis. Some of the basic concepts on this technique are briefly overviewed here.

## Slide 2: Order Analysis
Technique dedicated to the analysis of rotating machines operated over a wide range of speeds.
Express the frequency content as a function of orders, i.e. harmonics of the rotational speed.
  at 3,000 rpm order 1 = 50 Hz, order 2 = 100 Hz, …
  at 6,000 rpm order 1 = 100 Hz, order 2 = 200 Hz, …
Notes: Order analysis is the ideal technique to analyze complex noise and vibration problems directly related to the rotational speed of the machine under test.
Typical applications include the analysis of gear mesh and bearing defects that exhibit complex array of components at different frequencies as well as sideband frequencies.
Imbalance and misalignment are lower order components present in most, if not all, of rotational machines.
Order analysis is also the perfect tool to study resonance phenomena and understand the contribution from the source (constant order excitation) and the response of the structure (constant frequency). The worst resonance problems appear at particular rotational speeds where a high, order-related, excitation emphasizes the weakness of a structural resonance.
Other common applications cover the analysis of speed reducer, timing chain, valve noise, etc.

## Slide 3: Order Analysis
Various noise and vibration problems are directly related to the rotational speed:
  gear mesh
  bearing defects
  mass imbalance
  misalignment
  resonance
  valve noise
Notes: Order analysis is a technique dedicated to the analysis of rotating machines operated over a wide range of speeds.
The purpose of order analysis is to express the frequency content at any rotational speed as a function of orders. Orders are basically harmonics of the rotational speed. But due to the various complex phenomena involved and, sometimes, multiple rotational speed of different parts, orders can be noninteger multiples of the fundamental frequency (first order).
A typical example could be a four-cylinder engine during a run-up test. The major source of noise and vibration from this engine is related to the combustion process, which happens twice per revolution, thus leading to a strong contribution of the second order. At 3,000 rpm, the second order corresponds to 100 Hz, but at 6,000 rpm it will show up at 200 Hz.

## Slide 4: Order Analysis
Lock the sampling times to constant shaft positions
FFT transforms the angular domain into the order domain
Constant delta time
Constant delta angle
Notes: The basic concept of order analysis is to lock the sampling times to constant shaft positions. So, when the rotational speed is changed, the original signal is no longer sampled at constant time intervals but, instead, at constant angle intervals.
To obtain this signal sampled at constant shaft position, two different techniques can be used. The first one, external sampling, relies on the hardware to lock the sampling times to constant shaft positions. The second one, digital resampling, is based on the use of an interpolation algorithm to interpolate the original data acquired at constant sampling frequency and generate a resampled signal at constant shaft positions.
Applying an FFT on this signal then transforms the angular domain into the order domain (in the same way as an FFT transforms the time domain into the frequency domain). The resulting spectral lines represent constant orders (instead of constant frequencies).

## Slide 5: Order Analysis
Higher order which can be analyzed
Order resolution
Os : angular sampling frequency
R : total number of revolutions
N : FFT block size
Notes: The use of the FFT to transform the angular domain into the order domain leads to some important relationships.
The highest order (Om) which can be analyzed is directly related to the angular sampling frequency Os (number of samples per revolution):
The order resolution is given by:
These relationships are similar to the ones obtained for the frequency domain:
and

## Slide 6: Order Analysis
Two different techniques can be used to obtain a signal sampled at constant shaft positions:
  external sampling
  digital resampling
Notes: In order to obtain this signal sampled at constant shaft positions, two different techniques can be used.
The first one, external sampling, relies on the hardware to lock the sampling times to constant shaft positions.
The second one, digital resampling, is based on the use of a reconstruction algorithm to interpolate the original data acquired at constant sampling frequency and generate a resampled signal at constant shaft positions.
In both cases, the FFT then transforms the angular domain into the order domain. Results are displayed as waterfall, color map or order tracks.

## Slide 7: Order Analysis
External sampling:
  sampling pulses are generated by a shaft encoder or a ratio synthesizer
  anti-aliasing is ensured by an analog tracking filter
Serious limitations for rapidly changing shaft speed and higher orders
Additional specific hardware is required
Notes: In order to generate the sampling pulses at uniform angular intervals, the “ideal” technique would be based on the use of a shaft encoder. But in most cases shaft encoders are not practical to install and one has to look for another approach.
A simple tachometer is then used to generate one pulse per revolution and a ratio synthesizer (phase-locked loop) generates higher number of pulses per revolution. But this technique introduces serious limitations for rapidly changing shaft speed due to the time delay of the phase-locked loop and also for higher orders due to the phase noise of the ratio synthesizer (“smearing” of the higher order spectral lines).
In both cases anti-aliasing has to be provided by an analog low pass tracking filter, adding to the need of additional hardware.

## Slide 8: Order Analysis
Digital resampling:
  new sampling times calculated from tachometer pulses
  reconstruction function resamples the original signal at new sampling times
  anti-aliasing ensured by analog filter and digital low pass filtering during reconstruction
More accurate order analysis with less hardware requirements
Notes: When digital resampling is used, the original signal is acquired at a constant sampling frequency. The new sampling times are calculated based on the tachometer pulses and a model for the evolution of the shaft speed. A reconstruction function is then used to resample the original signal at these new sampling times, hence closely approaching the ideal sampling times that would be generated by a shaft encoder.
Anti-aliasing is ensured by the classical use of an analog low pass filter during the acquisition at constant frequency, in conjunction with digital low pass filtering during reconstruction, so eliminating the need (and the limitations) of low pass tracking filters for this purpose.
This technique results in more accurate order tracking and less hardware requirements. It can be used for both post processing and real-time analysis.