## Slide 1: Advanced Real Time Programming Techniques
Joe Hays
LabVIEW™ RT Product Support Engineer
Thurs Aug 17
12:00-1:15 p.m, 3:30-4:45 p.m.
Hickory (9C)
Notes: Welcome to the advanced track presentation on real time programming techniques with LabVIEW RT.

## Slide 2: Presentation Overview
Embedded versus real time needs
Real time (RT) case study
RT optimization “rules of thumb”
Notes: This presentation focuses on programming techniques to increase your real time performance in LabVIEW RT applications. This will mainly be done through a case study that walks us through various methods of approaching a problem. Through a number of iterations we will converge on a robust high performance real time solution.
I would like to point out the companion presentations to this session. Hopefully you were able to attend Greg Morrow’s “Introduction to Real-Time Control” (PR1A), yesterday. Likewise, there is one more short course offered by John Limroth today entitled “Real Time Programming with LabVIEW RT” in the Exhibit Hall (3G) from 1:45-4:45. This short course will give you the chance to actually get your hands on the product.

## Slide 3: Embedded Vs. Real Time
Do you need deterministic or embedded characteristics?
What is your real time need?
What level of determinism do you need?
Note: This presentation focuses on maximizing determinism in LabVIEW RT applications.
Notes: One of the first questions an engineer needs to ask when implementing a system with LabVIEW RT is “Do I have real time constraints?” In other words, are you using LabVIEW RT just for its embedded qualities: reliability, off-load processing, headless black box features, etc.? Or, does your application need determinism? Does it need “hard real time” characteristics?
If your application only needs the embedded characteristics, no special considerations are necessary when programming. It’s just LabVIEW programming. On the other hand, if your application has real time needs, certain general “rules of thumb” need to be followed. Higher levels of determinism require more careful programming. The focus of this presentation is to address these applications that have real time constraints and what the programming techniques are that help achieve the appropriate level of determinism.

## Slide 4: RT Case Study
System – simple PID controller (PXI-8156B, 333MHz)
Objective:
  Achieve nanosecond determinism
Notes: To facilitate the investigation of good real time programming techniques we will use a case study. For the purposes of our investigation we’ll iterate through a number of different control loop methodologies in exploration of a control system with nanosecond determinism.

## Slide 5: Execution & Preemption
Preemption vs. round robin scheduling
Determinism and thread priorities (“time-critical”)
Sleep mode
Notes: Before we take a look at our first approach for a solution I’d like to review some principles related to LabVIEW RT.
Scheduling:
The real time operating system (RTOS) that LabVIEW RT runs on (PharLap), implements a preemptive thread scheduling algorithm. Any thread scheduled on the processor will be preempted (or kicked off) if a higher priority thread requests to be run by scheduler (or wakes up). Threads that have the same priority will be scheduled in a round robin fashion in increments of 10 [mS]. This is not the case for time critical priority (highest) threads. They must cooperatively relinquish control of the processor for any other thread to gain access to it.
Thread Priorities:
LabVIEW RT, like its parent LabVIEW, is a multithreaded environment. Users can design their applications to take advantage of the multithreading capabilities of LabVIEW RT to increase the performance of their applications. Multithreading must be used for “hard real time” applications. The preemptive scheduling of the RTOS is imperative for user’s code to be executed deterministically. Having said that… the time critical priority (highest) setting in a VI’s setup dialog is the only priority that can provide “hard real time” determinism. All other priorites (including high priority) will not have a guarantee in preempting all other threads in the system. (The LabVIEW execution system has a number of “worker threads” behind the scenes in any application. Many of these threads have high priority settings and will thus preempt or round robin with all of the user’s code except that which is set to time critical priority. Some of these threads implement LabVIEW’s own scheduling mechanism within a single thread.)
Note: If you are unfamiliar with the multithreading capabilities of LabVIEW, consider a thread as a set of operations executed as a group. Different threads gain access to the processor to be run through the operating system’s scheduling mechanism. This group of executions is collected and organized by LabVIEW’s execution system before it is handed off to the operating system to be scheduled on the processor.

## Slide 6: Execution & Preemption
Notes: Sleep Mode:
Sleep mode can be thought of as the amount of time a thread, or VI, proactively takes itself off of the LabVIEW and operating system scheduling mechanisms. Users can provide a sleep mode in a VI by using the functions Wait Until Next ms Multiple, or Wait (ms).
If a time critical priority thread provides no sleep mode all other threads on the system will be starved out. They will never execute! This is the bittersweet characteristic of an RTOS (and the mechanism that allows for true hard/precise determinism). Also, LabVIEW RT’s time critical priority threads have another unique characteristic that is different from normal LabVIEW scheduling. If any VI on a time critical thread goes to sleep the entire thread goes to sleep. Even other VIs on the same thread that did not request to go to sleep will sleep. This is only the case for the time critical priority. Conversely, if two VIs (or two loops for that matter), that are executing on the same thread other than time critical priority and one of them goes to sleep, the other VIs on the same thread will continue to execute. In other words, LabVIEW RT’s execution system will not schedule operations from parallel VIs, or loops, when any one of them sleeps in a time critical priority thread. All other priority threads in LabVIEW RT, and all threads in normal LabVIEW, will continue to schedule operations from parallel loops, and/or VIs, in similar threads.
NOTE: when controlling the rate of a software loop by using the Wait Until Next ms Multiple function users can only achieve rates in multiples 1 [mS] multiples. This means, you can either run your loop at full speed providing no sleep at all… or, you can achieve loop rates of 1000, 500, 333.33, 250, 200, etc… [Hz]. We will discuss a method of implementing loop rates with a finer sleep mode resolution than 1 [mS] multiples.

## Slide 7: Software Timed Loop
First attempt – software timing
Notes: Now let’s first look at our control loop and how to achieve nanosecond determinism. To begin, we could use an existing example that ships with NI-DAQ. In many soft real time applications this example would provide an adequate solution. We’ll quickly see that for our tightly constrained real time system this method is unacceptable. The example’s name is “PID Control Loop.vi” and can be found at the following path:
~\LabVIEW\Examples\DAQ\Solution\Control.llb\PID Control Loop.vi
This example implements an entirely software-timed control loop. All analog acquisitions and analog outputs are initiated through software. As a result we are limited to the deterministic capabilities of software. Fortunately, with LabVIEW RT, software determinism is frequently adequate. For our system, though, we’re shooting for robust nanosecond determinism.
Let’s take a look at the results…

## Slide 8: Software Timed Loop (Results)
Software timing:
  Rate – ~1600 (Hz)
  Jitter – software dependent (1.6 mS)
  Determinism robustness – low
We can do better than this!
Notes: The control method implemented by “PID Control Loop.vi” has the following results:
Its rate, or performance, when run on the PXI-8156B/333 [MHz] controller was around 1600 [Hz]. This was achieved by:
    Setting the Loop Delay equal to zero (which lets the VI run at full speed). This provides no sleep mode!
    Setting the VI Priority to Time critical priority (highest).
The maximum jitter or indeterminism, experienced over tens of thousands of iterations was around 25 [uS] with a standard deviation of around 1.45 [uS]. Not bad at all for a first attempt!
NOTE: Jitter is a measure of indeterminism in a control system. It can be defined as the change in time relative to a nominal value. For example, if this control loop had a nominal rate of 1000 [Hz], or 1 [mS] between iterations, the maximum jitter experienced by the system would the largest difference between the nominal 1 [mS] and actual executed rate.
Parallel Memory Management:
As part of the investigation for a robust control system these benchmarks were performed with parallel executing memory operations. These memory operations, when performed in parallel, can be a very common source of jitter. If the time critical control loop, or thread, tries to perform any memory management while another thread has locked the memory manager out (through a mutex), the time critical loop must wait. This is known as a priority inversion and induces indeterminism in time critical threads. For our studies, memory operations were performed in a normal priority thread in parallel to the time critical priority real time control loop thread to investigate the robustness of our algorithm.

## Slide 9: Software Timed Loop (Results)
Notes: This VI ranked low for determinism robustness. This is more evident when the sleep mode, or Loop Delay, is set to a non-zero value. When the Loop Delay had a value of zero no time was ever given to the thread performing the memory operations. As a result, no priority inversions where experienced and fairly acceptable jitter values of 25 [uS] were experienced. With a non-zero sleep mode in the VI, time is given to the thread executing the parallel memory operations. This test revealed that our controller VI has memory operations inside its loop. (Memory operations inside the loop are something we must always avoid when minimizing jitter!) As a result large unbounded spikes in jitter were experienced (my tests saw spikes on the order of 1.6 [mS]). Yet, this example is highly robust if implemented with no sleep mode.
Note: the size of the jitter spikes is a function of the size of the memory blocks being manipulated at a time in the parallel loop. Larger memory operations hold onto the blocking memory manager mutex longer and induce longer priority inversions on the time critical thread trying to execute the control loop. My test was manipulating blocks of memory on the order of 216 bytes.

## Slide 10: Software Timed Loop (Results)
Notes: Summary of Results:
Rate Region Max. Jitter Std. Dev. Sleep (?) Robustness
*******************************************************************
<= 1000 1.6 [mS] ~300 [uS] Yes Low
1600 25 [uS] ~1.45 [uS] No High
As a result, this method for implementing a real time control system (with determinism on the order of 25 [uS]), is reliable if no parallel operations are being executed. This is frequently the case when using the RT Series 7030/xxxx plug-in DAQ devices.

## Slide 11: Hardware vs. Software Jitter
LabVIEW RT leverages the power of hardware (HW) determinism:
Or, Te + Tj = Twc  T
(t)
(HW clock events, T)
(Code execution time, Te)
(Worst case jitter, Tj)
(Worst case loop time, Twc)
Notes: Our first look at a solution to this control system was an entirely software driven controller. National Instruments is in a unique position to integrate its hardware and software in such a way to allow users to harness the “hard real time” determinism of the data acquisition hardware. Hardware has determinism on the order of nanoseconds.
We will shortly see that jitter in our software will no longer be an issue for the system under control. The system under control will experience the determinism provided by the hardware. The jitter experienced by the software will only be a limiting factor to increasing the performance of the overall system.
This slide shows the effects of anchoring your software to the data acquisition hardware. At very accurately spaced hardware clock cycles both analog inputs and outputs are acquired/updated simultaneously. The benefit to the user is that the system under control will not experience the jitter the software has. In essence, as long as the nominal “Code Execution Time”, Te, plus the “Worst Case Jitter” spike, Tj, is less than the “HW clock event” loop rate, T, your system will always experience hardware determinism! This is on the order of nanoseconds!
As I said before, by leveraging the determinism of the hardware, software jitter only becomes a limiting factor of the overall performance of the control loop (i.e. it limits the maximum control loop rate). Therefore, it is still imperative to continue our study in minimizing software jitter…

## Slide 12: Pseudo Hardware Timed
Second attempt
Notes: The next VI is also a shipping example with NI-DAQ, “Analog IO Control Loop (hw timed).vi”. It can be found at:
~\LabVIEW\Examples\DAQ\Analog_IO\Analog_IO.llb\Analog IO Control Loop (hw timed).vi
I have nicknamed this the “pseudo hardware timed control loop.vi”. It’s pseudo hardware timed because on inspecting the block diagram you’ll see the analog output is not synchronized with the analog input. In fact, it’s not being driven by a clock at all! This example is an interesting step in the evolution of our controller as it shows a solution that is anchored in time through a hardware clock, but does not fully hide the software jitter from the system under control.
  AI Single Scan.vi Sleep Mode:
  The AI Single Scan.vi is a synchronous call. It puts the VI to sleep until the hardware acquires a point. The sequence of events are:
      Hardware clock comes in
      ADC acquires point
      Interrupts PXI-8156B
      Interrupt service routine wakes up user’s time critical priority control loop VI, Analog IO Control Loop (hw timed).vi in this case.
      User’s code executes, loops around, and goes back to sleep until the next hardware clock cycle comes in.

## Slide 13: Pseudo Hardware Timed
Notes:   NOTE: while the loop is asleep in the AI Single Scan.vi node other threads can execute! This feature of AI Single Scan.vi putting a thread to sleep until a scan is acquired by the hardware is a new feature of NI-DAQ 6.7.0 and is only implemented if your NI-RT.INI file on the PXI-8156B has the following key:
  [NI-DAQ]
  UseSleepingTimedNonBuffered=TRUE
  Otherwise, the synchronous AI Single Scan.vi node completely blocks out any processing on the RT platform. All threads will be starved until this node wakes up and the loop explicitly provides a sleep using one of the methods previously mentioned. Another large advantage of this sleeping capability is the ability to resolve sleep modes at a finer granularity than 1 [mS] achievable with the LabVIEW built-in functions.
The AI Single Scan.vi sub-VI provides an anchor in the software execution to a very deterministic hardware clock. Even though the analog output is software generated and is susceptible to the effects of software jitter (and passes that jitter along to the system under control), it is anchored in time to a deterministic hardware event. One progressive step in the evolution of our robust nanosecond deterministic controller.

## Slide 14: Pseudo Hardware Timed (Results)
Pseudo hardware timing
  Rate – 5200 (Hz)
  Jitter – software dependent outputs, but anchored hardware inputs (550 µS)
  Determinism robustness – medium
We can do better than this!
Notes: Let’s look at the results…
Rate: we immediately see this example implements more efficient code. We achieved a maximum control loop rate of around 5200 (Hz). This is 3.25 times faster than our previous example!
Jitter: the system under control is still experiencing the software jitter through the analog output code. I measured a maximum software jitter of around 16 [uS] if I ran at full speed (i.e. no sleep mode). When the control loop was running at less than 2300 [Hz] I measured a maximum jitter of 550 [uS].
  (Recall, at rates less than 2300 [Hz] the AI Single Scan node provides a sleep mode that allows our parallel memory operations to execute. These parallel memory operations are the source of the 550 [uS] jitter. You’ll immediately notice that this is around ½ the magnitude of the maximum jitter spike experienced by the first solution with that same amount of sleep mode.)
  So, we’ve already made some progress in the robustness of the controller algorithm, but we’re still not there yet. The presence of the 550 [uS] jitter limits the maximum rate achievable (i.e. 5200 [Hz]).

## Slide 15: Pseudo Hardware Timed (Results)
Notes: Windows of Real Time Execution
Recall our equation that allows us to harness the power of hardware determinism:
Te + Tj = Twc  T
The time for our code to execute (Te), and the maximum jitter (Tj), when sleep mode is present, are essentially fixed values. As we try to increase the rate of our controller (i.e. decreasing T), we observe a window of real time execution---regions of execution rates where we can maintain hardware determinism. These windows exist because of the different maximum jitters experienced between rates that provide a sleep mode and those that do not. The differences in jitter are a result of memory operations being performed within the control loop. A highly robust controller – which is what we’re shooting for – has no memory allocations in the control loop and, hence, has small uniform maximum jitter no matter the control loop rate. Since this example has memory management in the control loop, the parallel memory management occurring in the normal priority thread causes larger jitter spikes. As a result there is a region of loop rates where the T has decreased below the sum of the code execution time (Te), and the maximum jitter (Tj).
Due to the results observed when sleep mode is provided this VI ranks medium for determinism robustness. Jitter spikes are less in magnitude due to the parallel memory operations when compared to the previous solution but, this solution is still not very robust. So, I give it a rating of medium robustness. When no sleep mode is provided this example provides a better performing robust solution than the complete software solution.

## Slide 16: Pseudo Hardware Timed (Results)
Notes: Summary of Results:
Rate Region Max. Jitter Std. Dev. Sleep (?) Robustness
**************************************************************
0 – 2300 550 [uS] ~290 [uS] Yes Medium
5000 – 5400 16 [uS] ~1.5 [uS] No
High
As a result, this method for implementing a real time control system (with determinism on the order of 16 [uS]), is reliable if no parallel operations are being executed. This can be achieved by looping at rates greater than or equal to 5000 [Hz], or by making the following modification in your NI-RT.INI file to turn off the default sleeping effect in the AI Single Scan.vi.
  [NI-DAQ]
  UseSleepingTimedNonBuffered=FALSE
We can still do better than this though! Let’s look at another example…

## Slide 17: Hardware Timed Loop
Third attempt – hardware timing
Notes: The next VI is also a shipping example with NI-DAQ, “Real-Time PID Control.vi” It can be found at:
~\LabVIEW\Examples\DAQ\Solution\Control.llb\Real-Time PID Control.vi
This is our first fully simultaneous analog input/output hardware clocked example. It provides the sleeping benefits of AI Single Scan.vi that were previously mentioned. We benefit from that in that we can resolve a finer resolution of control loop speeds and still allow other lower priority parallel operations to execute. The largest benefit of this example, though, is that it completely masks the software jitter from the system under control as long as our execution equation:
Te + Tj = Twc  T
is satisfied. This means the system under control feels the determinism of the hardware timing engine. This is on the order of nanoseconds!
Let’s take a look at the results…

## Slide 18: Hardware Timed Loop (Results)
Hardware timing
  Rate – 6400 (Hz)
  Jitter – hardware dependent (nS)
  Robustness to memory allocations – medium
We can do better than this!
Notes: Let’s look at the results…
Rate: Once again, we see a performance improvement. This example now implements more efficient analog output code compared to our previous solution. This change allowed us to achieved a maximum control loop rate of around 6400 (Hz). This is a 400% performance increase compared to our initial solution and 23% improvement over the last.
Jitter: As previously stated, with this new implementation the system under control will not experience any of the software jitter as long as the code execution (Te), plus the maximum jitter spikes (Tj), never add up to be more time than the loop delay time (T). Having said that, the software jitter is still very important to observe for performance and robustness considerations. This example experienced a software jitter of around 13 (uS), with a standard deviation of 3.6 (uS), when running at maximum speed of 6400 [Hz] – remember, this means no sleep mode and hence no parallel memory operations! – and 580 (uS), with a standard deviation of 279 (uS) when the nominal loop rate was at 1000 [Hz].
The presence of sizable jitter spikes when sleep mode is introduced is a result of some memory allocations occurring in the NI-DAQ subVIs. This will become evident during our next design iteration. Also, with a difference between the non-sleep mode and sleep mode jitter results this example experiences windows of real time execution (as in our previous example).

## Slide 19: Hardware Timed Loop (Results)
Notes: Due to the results observed when sleep mode is provided this VI ranks medium for determinism robustness. When no sleep mode is provided this example provides a better performing robust solution than the complete software solution.
Rate Region Max. Jitter Std. Dev. Sleep (?) Robustness
**********************************************************
0 – 2400 580 [uS] ~279 [uS] Yes Medium
5900 – 6400 13 [uS] ~3.6 [uS] No High
As a result, this method for implementing a real time control system (with determinism on the order of 13 [uS]), is reliable if no parallel operations are being executed. This can be achieved by following the same previously prescribed steps: looping at rates greater than or equal to 5900 [Hz], or by modifying your NI-RT.INI file to turn off the default sleeping effect in the AI Single Scan.vi.
Remember, though, now your system is getting nanosecond determinism!
We can still do better than this! Now, we need to increase the robustness!

## Slide 20: RT Optimizations
Avoid all memory management!
  Remove build array (pre-allocate)
  Pre-allocate memory buffers for DAQ operations
Minimize global and local variables in loop
Turn off debugging/enable logging/auto handling of menus
Read newest data/read oldest data
Notes: Here is a list of modifications you can make to increase both your robustness and performance rates.
Memory management inside the control loop is unquestionably the largest offending element. We must remove – or minimize it if it can’t be removed – all memory management within the real time control loop!
  This can be done by avoiding any function that perform a memory allocation. The classic example is the Build Array function. This can be avoided by pre-allocating arrays outside the loop and using the Replace Array Element function.
  The present NI-DAQ subVIs are causing small memory allocations. National Instruments is already working on removing all of these small allocations in future releases of the driver software. In the mean time, users can make minor modifications to the VI.LIB VIs to allow pre-allocation of LabVIEW buffer sizes used to receive data from the driver.
Global and local variables are protected resources in the LabVIEW engine. As such, access to these resources are more expensive. None of the examples we’ve looked at today use globals, nor locals, but it is valuable to comment on the importance of minimizing their use. Mutexes, especially with global variables used in parallel operations, can induce jitter into the real time application.
When users build applications into separate run-time applications certain optimizations are made in the compiled code. We can approach that optimized compiled state in the development environment by removing the following options in the real time VI’s Setup:
    Window Options: Allow Debugging (Compile in debugging code)
    Window Options: Enable Log/Print at Completion
    Window Options: Auto handling of menus at launch

## Slide 21: RT Optimizations
Notes:   This is valuable when investigating the performance of your code before you build it into an executable.
To monitor true real time execution – from a software point of view – we can use the Data Remaining parameter returned from the AI Single Scan.vi. This parameter tells us whether or not the software has fallen behind relative to the hardware clock driving the operations. This feedback is performed by reading the number of points in the hardware FIFO buffer at the time of the AI Single Scan node execution. If more than one point is in the buffer we know that the software did not keep real time. Larger lags in control loop code execution are experienced the first few iterations after all the configuration code has been executed due to processor caching effects. This is only experienced at the very beginning of execution. Therefore, modifying the code to return newest data for the first few iterations, and then switch back to return oldest data for the remainder of operation will provide the accurate feedback and still bypass the caching effect at the beginning.
Note: return newest data reads all the data in the FIFO before looking for data remaining. This gives inaccurate feedback as to the real time performance of the control loop.

## Slide 22: Optimized Loop
Fourth attempt – optimized hardware timing
Notes: If we take the previous example and take advantage of the following optimizations:
  Avoid all memory management!
    Remove build array (pre-allocate)
    Pre-allocate memory buffers for DAQ operations
  Turn off debugging / enable logging / auto handling of menus
  Read newest data / read oldest data
…we can achieve a very robust real time controller with hardware accurate jitter!

## Slide 23: Optimized Loop (Results)
Optimized hardware timing
  Rate – 10200 (Hz)
  Jitter – hardware dependent (nS)
  Robustness to memory allocations – high
Notes: Let’s look at the results…
Rate: Once again, we see a performance improvement. By applying the mentioned optimizations this example now runs at 10200 [Hz]. This is 6.375 times faster than our original software controlled solution, 1.96 times faster than the pseudo hardware timed solution, and 1.59 times faster than the fully hardware driven solution!
Jitter: The comments about hardware jitter apply here as well. As long as the code keeps real time the system under test doesn’t see the software jitter. Looping at full speed, 10200 [Hz], no sleep mode and no parallel memory operations, this optimized example now experiences a maximum jitter of 12 (uS), with a standard deviation of 2.07 (uS). With a nominal loop rate of 1000 [Hz], this example experienced a maximum jitter spike of 86 (uS), with a standard deviation of 26.74 (uS).
The large advantage of this example is that with the minimized memory operations in the control loop the robustness of the solution is very high. No windows of real time execution apply to this solution. This solution will provide nanosecond determinism for loop rates from 0 – 10200 [Hz]! When sleep mode is present there is a slight increase of jitter but it is not significant enough to remove the real time performance for any loop rate in its spectrum. Therefore, this solution has a high robustness rating.
In conclusion, by taking an existing example of NI-DAQ 6.7.0 we were able to provide a few minor modifications and achieve a real time controller with nanosecond jitter determinism to the system under control! The modifications to the NI-DAQ VIs needed to achieve this level of performance are presently being worked on so users in the future will not need to make the custom modifications.

## Slide 24: Present LabVIEW RT Constraints
ALL NI-DAQ calls MUST be done within the RT loop!
Single RT loop in the entire application
Notes: There are a few constraints with the present LabVIEW RT and NI-DAQ driver software implementations that users need to be aware of:
Presently, the NI-DAQ software is not a multithreading driver. In other words, only one operation can have access to the NI-DAQ driver at a time. As a result of this constraint, every NI-DAQ VI in an application must be called in the real time loop. If NI-DAQ VIs are called outside the real time loop, jitter will be introduced as the time critical priority thread can experience a priority inversion.
To guarantee real time execution, users should only implement a single real time VI, with a single loop, throughout the entire application.

## Slide 25: Summary of Results
Use hardware timed loops
Use the time critical priority for your real time control VI
Sleep mode
  NI-DAQ sleep mode
  Windows of real time execution
Remove all memory allocations within the real time loop
Notes: We can achieve a very deterministic controller by harnessing the accuracy of the data acquisition hardware timing. This requires the real time controller VI to have the time critical priority setting. If parallel operations are required, the inherent sleeping mode of the NI-DAQ AI Single Scan.vi provides the ability to resolve loop resolutions finer than 1 mS and still allow other operations to execute in parallel. With the optimizations mentioned a very robust controller that spans the entire frequency range of the system is achieved. One major optimization required by the end user is to remove all memory allocations within the loop. Future NI-DAQ versions will not have the present small memory allocations. For now, users can make small modifications to these VIs to increase robustness and performance.