## Slide 1: Advanced Software Techniques for Instrument Control
Dan Mondrik
Senior Software Engineer
Thurs Aug 17
12:00-1:15 p.m., 3:30-4:45 p.m.
Ash (10A)

## Slide 2: Presentation Outline
General overview of VISA
What's new in NI-VISA™ 2.5
  New I/O functionality for Ethernet, GPIB, VXI
  Better performance
Better integration
  LabVIEW™ 6i
  Measurement & Automation Explorer (MAX)
  Measurement Studio™
VISA, IVI, and instrument drivers

## Slide 3: General Overview of VISA
Virtual Instrument Software Architecture
Supports multiple hardware interface types
  GPIB, VXI, VME, Serial, PXI, and more
Most instrument drivers use VISA for I/O
Supported in all NI application development environments
  Same driver, different flavors tailored to each ADE
Notes: VISA provides an application programming interface (API) for many development environments such as Measurement Studio and LabVIEW. VISA presents a common foundation for the development, delivery, and interoperability of high-level multi-vendor system software components, such as instrument drivers and application software. VISA is a published standard that is used by VXIplug&play and IVI instrument drivers.
NI-VISA, the National Instruments implementation of the VISA I/O standard, is a comprehensive package for configuring, programming and troubleshooting instrumentation systems. NI-VISA includes libraries, interactive utilities such as NI Spy™ and the VISA Interactive Control, and configuration programs such as Measurement and Automation Explorer (MAX). See the NI-VISA Web page at ni.com/visa
NI-VISA 2.5 is supported on Windows 2000/NT/98/95, MacOS 8/9, Linux x86, Solaris 2.6/7, and HPUX 10.20.

## Slide 4: New! Ethernet Support
NI-VISA control of Ethernet instruments
TCP-IP instrument protocol
  Currently used mostly by Agilent instruments
  Good 488.2 protocol for new Ethernet instruments
Raw TCP-IP sockets
  Similar to LabVIEW and LabWindows™/CVI libraries
  Adds control of “no-delay” and “keep-alive” options
Notes: The Ethernet implementation in NI-VISA 2.5 provides client support only, which allows a user to connect to a device at a given IP address. It does not implement servant support such as listening for and accepting connections.
For low-level socket communication, the VISA resource name includes the port number, such as “TCPIP::<hostname>::<port>::SOCKET”. If an Ethernet device supports the TCP-IP Instrument Protocol, which is a recommended communication mechanism, the VISA resource name is “TCPIP::<hostname>::INSTR”.
Both VISA Ethernet protocols support Write, Read, AssertTrigger, ReadSTB, and Clear. A VXI-11 device also adds SRQ event capability.
If you are an instrument vendor and you plan to support the Ethernet interface, contact National Instruments for information on the TCP-IP Instrument Protocol, also known as VXI-11. Implementing this protocol makes it easier for VISA users to integrate your product into their systems.
In NI-VISA 2.5, Ethernet is currently supported on only Win32.

## Slide 5: Extended GPIB Support
Better async performance in LabVIEW 6i
  Same speed as traditional GPIB calls
New board-level control
  Supported features
    Assert or query bus lines such as IFC or SRQ
    Send miscellaneous GPIB commands
    Perform non-controller I/O (pass control, set status byte)
  VISA resource name is “GPIB::INTFC”
  LabVIEW VISA class is “GPIB BoardInterface”
Notes: NI-VISA 2.5 adds support for many customer-requested GPIB features, so you can use VISA for all your GPIB requirements. NI-488 is not going away, but now NI-VISA is on par with NI-488 in terms of supported GPIB features. If you need to control instruments on multiple interface types, such as GPIB and VXI, we recommend that you use VISA.
A GPIB BoardInterface (INTFC) resource lets a controller interact with any devices connected to the board associated with the given resource. Advanced GPIB users who need to control multiple devices simultaneously or need to have multiple controllers in a single system typically use the INTFC resource. In addition to providing basic I/O services such as Write, Read, and AssertTrigger, the controller can directly manipulate several lines on the bus (ATN, IFC, REN, SRQ) and pass control to other devices with controller capability. Although this resource can also monitor some of the bus lines, the GPIB Analyzer is preferable because it monitors the bus continuously and does not depend on your application making driver calls. If you do not need such advanced functions, use device-level calls with the INSTR resource.
NI-VISA will by default attempt to detect a GPIB-VXI at primary address 1. If you have a device at that address that does not recognize “*IDN?\n”, you should turn this feature off in MAX.

## Slide 6: Extended VXI Support
New mainframe/extender control
  Supported features
    Assert or query bus lines such as Sysreset or Sysfail
    Assert VXI/VME interrupts
    Map trigger lines together (TTL, ECL, Front Panel)
  VISA resource name is “VXI::BACKPLANE”
  LabVIEW VISA class is “VXI/GPIB-VXI Backplane”
Use NI-VISA rather than NI-VXI™ for new VXI applications
Notes: NI-VISA 2.5 adds support for many customer-requested VXI features, so National Instruments recommends that you use VISA for all your VXI requirements.
A VXI Mainframe/Backplane resource encapsulates the operations and properties of each mainframe (or chassis) in a VXIbus system. This resource type lets a controller query and manipulate specific lines on a specific mainframe in a given VXI system. Backplane services allow the user to map, unmap, assert, and receive hardware triggers, and also to assert and receive various utility and interrupt signals. This includes advanced functionality that might not be available in all implementations or on all controllers.

## Slide 7: Extended Serial Support
Better async performance in LabVIEW 6i
  More efficient CPU usage on read operations
New supported features
  Custom baud rates, not limited to 256 K
    Any value allowed by hardware is now valid in NI-VISA
  Handles up to 256 ports, not limited to 32
Use NI-VISA rather than the traditional serial icons for new serial applications in LabVIEW
Notes: NI-VISA serial support has been extended to support higher baud rates. On the Macintosh, it now supports 115 Kb and 230 Kb. On Windows, some RS-485 interface boards transfer data at 460 Kb and beyond.
If you use Serial instruments and you do not use VISA, you should still use MAX for configuring your system.

## Slide 8: PXI Support
NI-VISA handles third party PCI and PXI cards
Supported features
  Register-level access with efficient peek/poke
  Block moves, including FIFO access
  Interrupt notification at the user level using either queues or callbacks
Register a device with PXI Driver Wizard
  Specifies NI-VISA as the Windows driver
Notes: The Windows operating system can associate only one kernel driver with a given PCI or PXI card. Therefore, NI-VISA cannot be used to control a system device that has another driver installed, such as a video card. To allow NI-VISA to access your plug-in card, run the PXI Driver Development Wizard, install the output file, and reboot Windows.
To write C or C++ source code that uses NI-VISA for the PXI interface, you must define NIVISA_PXI before including visa.h. The NI-VISA 2.5 Programmer Reference Manual documents valid parameters for accessing PXI instruments. PCI and PXI cards are indistinguishable to Windows, so all documentation references to PXI also apply to PCI. To open a device, use the resource string "PXI::<DeviceNumber>::INSTR".
If you are an instrument vendor and you plan to provide instruments in the PXI form factor, contact National Instruments for information on the PXI Systems Alliance. Also see the PXI alliance Web site at pxisa.org
In NI-VISA 2.5, PXI is supported on only Win32.

## Slide 9: New! Mixed Systems Support
NI and Agilent controllers plugged into same PC work seamlessly together with NI-VISA
Configure third party controllers with third party software environment
  MAX does not display VISA resources attached to third party controllers
  Use VISA Interactive Control (VISAIC) to interact with these resources
Notes: NI-VISA now supports an open model for plug-in modules called Passports. If you are a controller vendor and you want to integrate with NI-VISA, contact National Instruments for information on the Passport model.
With this release, NI-VISA supports more hardware controller combinations than any other VISA. If you are using Agilent controller hardware and want to use NI-VISA, see the readme.txt in the NIvisa directory for configuration details. LabVIEW and NI-DAQ work best with NI-VISA.

## Slide 10: Integration with LabVIEW 6i
Automatically create VISA I/O controls
  Drag a VISA resource or alias from MAX and drop it in LabVIEW 6i
  This combines the functionality of the VISA refnum and the resource name controls from LabVIEW 5
VISA session management
  VISA Open is no longer required
    LabVIEW will open a session to a resource when it is used as an input
  VISA Close is optional but recommended
Notes: The VISA I/O control (also known as the VISA Resource Name control) is new to LabVIEW 6i. It replaces the old VISA refnum and makes it a more useful front panel control because it visually displays the VISA resource name or alias. The same control also allows users to select from a drop-down box listing all available VISA resources, thus making initialization easier for both novice and advanced users. The VISA I/O control is similar to the IVI Logical Name and DAQ Channel Name controls.
While wiring the session control from one VI to another makes for a cleaner diagram, it is no longer required. LabVIEW now recognizes the VISA Resource Name embedded in the control and reuses an existing session to that resource when such a session already exists. If this is the first use of a given resource, LabVIEW automatically opens a session and stores it for future use in other VIs. This does not preclude the use of VISA Open, nor does it preclude advanced practices such as opening multiple sessions to a given resource.
Finally, it is still a good idea to call VISA Close because it is better to explicitly release resources when you are done with them. However, if you omit this step, LabVIEW will call VISA Close for you automatically when LabVIEW exits.

## Slide 11: Sample G Source Comparison
LabVIEW 5
LabVIEW 6i
Notes: This sample code performs a simple query to a device at a given address.
Each diagram displays the minimal valid working diagram for this task for the respective version of LabVIEW.
Because VISA Open and VISA Close are no longer required steps, the Easy VISA VIs no longer exist in LabVIEW 6i.

## Slide 12: Integration with LabVIEW 6i (cont.)
Serial palette now displays VISA icons
  Same functionality as traditional serial palette
  Old “serpdrv” is still supported for backward compatibility
Notes: The traditional serial VIs are still handled in LabVIEW 6i, and they can be found in the I/O Compatibility palette. However, we recommend that you use the VISA icons instead, which are now displayed on the main Serial palette. Advanced functions that were available in some of the undocumented traditional serial VIs (such as querying or manipulating modem lines) can be accessed with the VISA property node.
If you encounter problems when converting your G code from the traditional serial VIs to VISA, please contact National Instruments.

## Slide 13: Integration with MAX
In Windows, MAX is the new NI-VISA configuration environment
  T&M Explorer is no longer shipped or needed
Property pages exist for all VISA resources
Create or modify VISA aliases in MAX
Notes: Measurement & Automation Explorer (MAX) is the unified National Instruments configuration tool.
NI-VISA 2.5 is configured through MAX. Viewing and configuring GPIB, PXI, Serial, Ethernet, or VXI controllers and instruments is easy. If you need help, enable the task list in the rightmost pane for assistance with common tasks.

## Slide 14: Integration with MAX (cont.)
VXI, VME, GPIB-VXI
  One address map view for A16, A24, A32
  Mainframe connection views for MXI-2
  NI controller configuration
Serial
  Synchronizes VISA port settings with OS
    Applets such as HyperTerminal use same settings
  MAX automatically adds aliases if not already set
    You can now use “COM1” for “ASRL1::INSTR”
Notes: For VXI and VME systems, the functionality of T&M Explorer has been brought into MAX, and in many cases made easier. The address map view has been simplified and brought up to the top level for a VXI system. If you click on a VXI system on the left side, device addresses and a complete memory map view will be displayed on the right side. If you expand a VXI system tree on the left side, you will see how all chasses in the system are connected. Finally, local controller details are now configured similarly for all VXI controllers, including the GPIB-VXI.
For Serial systems, click on “Ports (Serial & Parallel)” on the left side. All port names will be displayed on the right side, along with their system bindings and port settings.

## Slide 15: Integration with Measurement Studio
LabWindows/CVI
  Function panels for all VISA operations
Tools for Visual Basic
  VISA ActiveX controls
  Formerly known as ComponentWorks™
Tools for Visual C++
  VISA C++ classes
  Formerly known as ComponentWorks++
Notes: Measurement Studio was introduced in February 2000. It comprises tools for ANSI C, Visual Basic, and Visual C++ developers.
Each of these products has a VISA interface for instrument control. While this part of this presentation focuses on the C++ API for VISA, National Instruments is committed to further developing the VISA interface for all Measurement Studio users.

## Slide 16: New! C++ API for VISA
Simplifies I/O programming for C++ users
  Intuitive extension of VISA object model
  Handles VISA Resource Manager sessions automatically
Includes support for VISA 2.0 functions
NI-VISA 2.5 features will be added later
  Can access them now using the C API
Notes: If you prefer writing your instrument control code in C++, you should use the VISA C++ classes in Measurement Studio. Anything you can do in NI-VISA with the C API, you should be able to do easier with the C++ API.
The next four slides compare two common tasks that take half the variables and half the code to accomplish in C++.

## Slide 17: Find Resources in CVI
ViSession drm, findlist;
ViUInt32 count;
ViChar desc[VI_FIND_BUFLEN];
viOpenDefaultRM (&drm);
viFindRsrc (drm, “?*INSTR”, &findlist, &count, desc);
while (count--) {
printf (“Found: %s\n”, desc);
viFindNext (findlist, desc);
}
viClose (drm);

## Slide 18: Find Resources in C++
CNiVisaResourceList findlist (“?*INSTR”);
ViUInt32 count = findlist.GetCount();
while (count--)
cout << “Found:” << findlist[count] << endl;
Notes: By passing the search expression to the CNiVisaResourceList constructor, you don't need to worry about the VISA resource manager session. Iteration over the results is done on the object, not by making repeated driver calls to viFindNext(). And the object is closed automatically when it goes out of scope, such as at the end of the function.
(Of course, LabVIEW users know they can do this with one icon and one indicator…)

## Slide 19: VISA I/O in CVI
ViSession drm, io;
ViUInt32 count;
ViChar buf[1024];
viOpenDefaultRM (&drm);
viOpen (drm, “GPIB::14::INSTR”, 0, 0, &io);
viWrite (io, “*IDN?\n”, 6, &count);
viRead (io, buf, 1024, &count);
printf (“Identity: %*s\n”, count, buf);
viClose (drm);

## Slide 20: VISA I/O in C++
CNiVisaSession io (“GPIB::14::INSTR”);
CString buf;
io.Write (“*IDN?\n”);
io.Read (buf, 1024);
cout << “Identity:” << buf << endl;
Notes: By passing the VISA resource name to the CNiVisaSession constructor, you don't need to worry about the VISA resource manager session. I/O is simpler because the C++ types carry the size information with them. Again, the object is closed automatically when it goes out of scope at the end of the function.

## Slide 21: Demonstration

## Slide 22: VISA, IVI, and Instrument Drivers
Modern instrument drivers are built with VISA
IVI drivers add power
  Builds on the VISA model
  Provides state caching for higher performance
  Adds simulation capabilities
  Increases multi-thread protection
When is each appropriate?
  Instrument vendors should provide IVI drivers
  Customers should use drivers if they exist
  Use VISA directly if no driver exists
Notes: Any instrument driver is better than none. If you receive an instrument driver along with an instrument, you're almost always better off using the driver, regardless of how it was developed. Some drivers are written in LabVIEW, most are done in LabWindows/CVI, and a few are created in other environments – but LabVIEW can access them all.
Most instrument drivers for GPIB, VXI, and Serial have been written with VISA over the last five years. Most IVI drivers being developed today use VISA for all of these interfaces. IVI drivers are more powerful than many traditional instrument drivers, but they all perform some of the same basic I/O functionality.
If you are an instrument vendor and you do not currently provide instrument drivers, contact National Instruments for information on the IVI foundation. Also see the IVI Web site at ivifoundation.org
You can download drivers from the Instrument Driver Library on the National Instruments Developer Zone at http://zone.ni.com

## Slide 23: Conclusions
NI-VISA 2.5 is available now!
  ftp://ftp.ni.com/support/visa/drivers
  Ships with LabVIEW 6i
  NI-VISA 2.5 is faster, more powerful, and supports more interfaces
VISA is the way to program instruments over GPIB, VXI, Serial, PXI, or Ethernet
Notes:   If you control instruments with LabVIEW, MAX, instrument drivers, or Measurement Studio, then you should download NI-VISA 2.5.
  The NI-VISA 2.5 runtime installer is available free.