## Slide 1
<date/time>
Tackling High Channel Count Applications in LabVIEW
Stefano Zanetti
Automation Software Product Manager
Thurs Aug 17
12:00-1:15 p.m, 3:30-4:45 p.m.
Mulberry (10B)

## Slide 2: Agenda
What is high channel count?
Data and networked system management tools
The next generation of BridgeVIEW 
Conclusion
Notes: During this presentation we will first define what a high channel count system is, then talk about the tools you need to efficiently manage such a system. During the demonstration, we will show you the next generation of BridgeVIEW and how you can use built-in tools to perform high channel count datalogging and supervisory control of a large system.

## Slide 3: Definition of High Channel Count
Not a straight answer
Key words:
  Multiple I/Os sources
  Datalogging
  Supervisory control
  Distributed system
Notes: We do not have a straight answer in terms of the number of channels to define what a high channel count system is: 40, 50, 100, 1000 channels – it depends on the complexity of the system. A complexity you can define not only in terms of the number of channels, but also size of the system (distributed and networked). A distributed system with only a few dozen channels per machine may require easy-to-use tools to manage a networked system, or a single machine with hundreds of mixed I/O channels may require database, alarm, and events capabilities. In both cases, data and networked system management tools are required to efficiently control such a system.

## Slide 4: High Channel Count Application
Machine automation/control
Machine monitoring
Production test
Process control
Instruments I/Os
Distributed I/Os
PLCs
Plug-in boards
Signal Conditioning
Notes: Look at the following scenario with a single machine high channel count system.
Company XYZ needs to come up with a more efficient way to produce a chemical substance. They need to create a pilot plant. One computer is connected to a couple of PLCs that control the reactor, FieldPoint™ gets the temperature of the system in various places, and a few scales controlled via GPIB are sitting next to the system to make sure that the right quantity of the primary substances are used. You need data management tools to collect all the data, store it in a database, manage the alarms if the temperature goes above a certain level, and provide real-time and historical trending.
Key words: high channel count, and mixed I/O sources (GPIB, FieldPoint, PLCs)

## Slide 5: High Channel Count Application (cont.)
PCI
GPIB
Serial
USB
1394
PXI Real-Time
Ethernet IP Nodes
Manufacturing
Laboratory
GPIB Enet
Serial Enet
Internet
Web Browser
Distributed I/Os
PLCs
Notes: For this example, assume in a very simplified manner that we are assembling a cell phone. We have different PCs networked together along the production line. At the beginning of the line some PLCs/LabVIEW RT are performing discrete control (cover assembly) – in the middle of the line FieldPoint counts the cell phone units on the conveyer belt, at the end of the production line a machine is performing quality control tests of the LCD display with LabVIEW and IMAQ™. A main computer collects all the data from the different machines. It logs the data into a database, manages the alarms, provides real-time and historical trending, implements security for the different users (operator, engineer, administrator), and provides connectivity to other machines in the manufacturing floor.
Key words: high channel count, distributed and networked system, and mixed I/O sources (DAQ, PLC, FieldPoint, GPIB, IMAQ)

## Slide 6: Increase Your Productivity
Data management tools
Networked system management tools
Event-driven architecture
Easy connectivity
Notes: You can easily develop an application with a small number of channels by programming the data acquisition on a channel-by-channel basis. But what about having an application with a large number of channels to manage? Data and networked system management tools, such as channel configuration, datalogging, real-time and historical trending, and alarm handling, easy networking can dramatically increase productivity and help efficiently manage high channel count and distributed systems. An event-driven architecture stops the system from continuously polling I/Os and slowing down the overall system performance. Ease of connectivity help integrate a high channel count system I/Os from different sources.

## Slide 7: Solution
Today:
  BridgeVIEW
Tomorrow:
  LabVIEW tools
    High channel count datalogging
    Supervisory control of distributed systems
Notes: Today the solution is BridgeVIEW. Very soon you can leverage BridgeVIEW technology in LabVIEW that provides you with improved tools for high channel count datalogging and supervisory control of a distributed system.

## Slide 8: New Functions
Built-in tools
  Alarm and event management
  Distributed logging
  Trending
  Easy networking
  Security
Event-driven architecture
OPC connectivity
Notes: AT2F-<number>
Tackling High Channel Count Applications in LabVIEW
<header>
<date/time>
With LabVIEW datalogging and supervisory control technology – the next generation of BridgeView™ - users can leverage unparalleled features and flexible tools for developing applications that require high channel count datalogging and supervisory control of distributed systems.
LabVIEW provides built-in tools to manage applications with a large channel count. These tools include a configuration utility for creating, editing and logging I/Os, and setting alarms, and real-time and historical trending to get a quick snapshot of your data at any time.
Also LabVIEW adds a number of powerful features and tools specifically targeted for the manufacturing floor, such as networked system management tools for distributed applications, including networked database for distributed logging, full alarm and event management, easy networking, built-in security, OPC connectivity to connect to industrial devices (such as PLCs), event-driven architecture to handle high channel count applications
The module will also build some of your program for you. This is similar to the Wizards in LabVIEW – open a window, specify what you want to do, and the module will pre-build much of your system. In short, this LabVIEW module adds functions to LabVIEW that you need to develop high channel count and distributed systems effectively.

## Slide 9: Architecture
OPC
DDE
VIs
Servers
Engine
Event-driven I/O processing
Alarm and event management
Real-Time and historical trending
Networking
Logging
Scaling
Notes: AT2F-<number>
Tackling High Channel Count Applications in LabVIEW
<header>
<date/time>
The module has a tag-based architecture. You communicate with various hardware devices such as National Instruments DAQ boards, distributed I/O or PLCs. You communicate with a multitude of control devices, industrial networks, and special I/O such as vision and motion control cards.
The module architecture consists of one main piece – The Engine.
Engine – The engine is the heart of this LabVIEW datalogging and supervisory control technology. It maintains a real-time database, which is an in-memory snapshot of all tags in the system. The engine also processes information associated with the tags and provides services such as engineering unit scaling, logging to a historical database called Citadel, calculating alarm conditions, and logging and printing alarms and events. The engine runs as a separate process. The LabVIEW process and the engine communicate data and events through a high-performance DLL interface.
With LabVIEW, you build the graphic user interface to control and monitor your application to advanced data analysis, visualization, and real-time applications controlling chemical processes or machinery in a factory.
The device servers manage all of the I/O communication with the devices in the system. They are specific to the device interface (PLCs, NI-DAQ hardware, distributed I/O, and so on) and communication protocol you are using. Device servers run as separate threads within the engine process. They are one of three types: OLE for Process Control (OPC), VI-based (G), or Dynamic Data Exchange (DDE).

## Slide 10: Let’s Build an Application…
Distributed I/Os
Notes: AT2F-<number>
Tackling High Channel Count Applications in LabVIEW
<header>
<date/time>
With this example, you see the ease of development and management of a high channel count and distributed system with LabVIEW.

## Slide 11: Tag Configuration Editor
Tag management
Alarms & events handling
Historical logging
Scaling
Import/export spreadsheet
Notes: AT2F-<number>
Tackling High Channel Count Applications in LabVIEW
<header>
<date/time>
Tag Configuration Editor helps manage tags. Tags are real-world I/O points or memory tags. A memory tag does not directly connect to an I/O point, it represents an internal or calculated variable. LabVIEW supports four tag data types – analog, discrete, bit array, and string. You can perform a variety of processing on the tags depending on the data type, such as logging the tag values to disk, keeping track of alarms and events, and performing scaling. However, in a system with large channel or item counts, it can be tedious to configure tags on channel-by-channel basis. You can use two methods for easier implementation of tag configuration for large channel counts – import/export spreadsheet functionality and the configuration wizard. Configuring tags in a spreadsheet application, such as Excel, easily imports, exports, and store information of large numbers of tags in a tab-delimited text file. This format is compatible with most spreadsheet applications.
LabVIEW supports online reconfiguration from the Tag Configuration Editor for most tag attributes. This means that you can change tag configuration, either manually through the Tag Configuration Editor or programmatically using graphical programming, and apply these changes to the engine without restarting.

## Slide 12: Alarm Summary and Event History
HMI Wizard
Alarm acknowledgment
Grouping and filtering
Event logging and printing
15 alarm priority levels
Alarms and events VIs
Notes: AT2F-<number>
Tackling High Channel Count Applications in LabVIEW
<header>
<date/time>
For most applications, you monitor abnormal conditions in process. These conditions associate either with the tags themselves or with the LabVIEW system.
You monitor these conditions (alarms) and assign priority levels to indicate severity of an alarm state for tags in the Tag Configuration Editor. You can group several tags into a single tag group for easier access. You also can filter alarms to display alarms corresponding to a user specified range of priorities.
You easily can implement alarm summary, alarm acknowledgment, and event history with the HMI G Wizard, which automatically generates the diagram with the appropriate alarm and event VIs. There also are alarms and events VIs for custom alarm and event handling.

## Slide 13: Trending
Historical trending
  Historical trend viewer
Real-time trending
  Tag monitor
Trend VIs
SQL
Notes: AT2F-<number>
Tackling High Channel Count Applications in LabVIEW
<header>
<date/time>
For viewing historical data, you create a front panel to display the logged data or access the logged data using the Historical Trend Viewer (HTV) utility. Here, you view up to eight plots at a time. You display analog or digital values, because the data can be autoscaled depending on the range. With the HTV, not only can you view the data as traces, but you can track specific data points and timestamps using cursors. You posess the flexibility to specify the timespan of the viewed data and reflect any change in value. You can access historical data through the HTV without having your application running. It is basically a stand-alone utility. If the application is running, the HTV updates the trend with the data acquired, combining the historical and real-time data in a single trend.
For viewing real-time data with respect to time, LabVIEW is a simple interface namely, the Real-Time Trend. You use scaling features, panning, scrolling and zooming functionality. You may customize the trend to meet your system needs.
You can then use the HMI G Wizard to associate the trend with the tags to be monitored. There are no limits on how many trends you can display. The HMI G Wizard creates the code using the Trend Tags VI.

## Slide 14: Networking and Datalogging
Networked database
Alarm and event logging
Easy networking
OPC client/server
Web clients
Internet
Web Browser
1
n
……
Notes: AT2F-<number>
Tackling High Channel Count Applications in LabVIEW
<header>
<date/time>
LabVIEW includes a networked database for distributed logging with simultaneous reading and writing capabilities from different clients. The database stores not only raw data, but also information such as timestamp, alarms, and event management for a better historical record of your system.
The built-in OPC client interface provides standardized connectivity to plant floor devices, making integration significantly easier in a multivendor environment and providing more choices in selecting hardware and software vendors for your automation system. The OPC server capabilities allow data to be distributed in a standard format to clients, including low-end HMI products and higher-level business systems.

## Slide 15: Security
Operator interface security
Access control for utilities
Password-based user accounts
Import/export user account information
Access levels
Notes: AT2F-<number>
Tackling High Channel Count Applications in LabVIEW
<header>
<date/time>
High channel count and distributed applications often require security to control operator access to the system. LabVIEW includes seven default access levels that define user privileges. You can define up to 10 levels. The privileges represent functionality that you can access or modify. To implement security, you create password-based user accounts that are assigned an access level. For example, the access level determines whether a person can launch data management utilities such as the Tag Configuration Editor and the Historical Trend Viewer.
In addition to the LabVIEW environment security, you may want to control operator access to specific front panel objects. LabVIEW provides a mechanism to implement object security, where you can control whether the user can see or operate the object. For example, a specific operator may be able to view process variables but not change setpoints.
With the built-in Security VIs, you can programmatically control the operability and visibility of the operator interface. There are also functions (VIs) available to determine security status and log in programmatically. This way, you can develop your own security measures for your HMI application. You can also import or export user account information when you have to distribute your application.

## Slide 16: Conclusion
It’s the IDEAL tool for –
  High channel count datalogging
  Supervisory control of distributed systems
LabVIEW tools for the manufacturing floor
Notes: LabVIEW has a collection of tools ideal for developing and managing a high channel count system.
Also, LabVIEW adds powerful tools for your manufacturing applications, such as –
Networked database for distributed logging
Full alarm and event management
Easy networking
Built-in security
OPC connectivity to connect to industrial devices, such as PLCs
Event-driven architecture to handle high channel count applications