## Slide 1: What’s New in VXI?
Scott Kovner
Group Manager – PXI™/VXI Software
Fri Aug 18
12:00-1:15 p.m., 3:30-4:45 p.m.
Ash (10A)

## Slide 2: Agenda
Current VXI hardware offering
Current VXI controller software
New software – NI-VXI™ 3.0
New hardware

## Slide 3: Hardware Overview
Embedded controllers
Remote controllers
VXIpc™
MXI™-2, GPIB, or IEEE 1394
Notes: VXI controllers are either embedded controllers or remote controllers. Embedded controller products are PCs designed to fit directly into a VXI chassis. With remote controllers, you can control a VXI chassis over a connection bus.

## Slide 4: Embedded Controllers
VXIpc-870 Series – dual slot, very high performance
VXIpc-740 Series – single slot, economical
VXI/VMEpc™-650 Series – B size controllers

## Slide 5: VXIpc-870 Embedded Controller
Desktop PC in a 2 slot VXI chassis
Pentium III, 450 MHz
PCI expansion slot or internal CD-ROM
Complete peripheral set
  GPIB, parallel port, 2 serial ports, 2 USB ports, 10/100BaseT Ethernet, Ultra Wide SCSI-3, keyboard & mouse ports, PC card, floppy
3 SMB connections for trigger and external clock routing
VXI MITE™ ASIC

## Slide 6: The VXI MITE Chip
Core technology for MXI, VXI, and PCI
DMA controller
  Fast block moves
  FIFO access
  Synchronous MXI protocol
Shared VXI memory (SIMM or system RAM)
Multiple address windows to VXI
VME64
And more…
Notes: AT3E-<number>
What’s New in VXI?
<header>
<date/time>
The MITE is a high-speed bus interface ASIC with built-in support for VXI, MXI, PCI, and general-purpose asynchronous and I/O buses. It has DMA controllers for moving data quickly between the ports.
The MITE can also use new, faster protocols for accessing blocks of data.

## Slide 7: VXIpc-740 and VXIpc-745
Single slot, economical choice for VXI embedded control
100 MHz 486 processor
Both have keyboard port, serial port, floppy, PC card slots
VXIpc-745 also has GPIB, Ethernet
VXI MITE ASIC

## Slide 8: VXI/VMEpc-650 series
Embedded controllers for B size VXI or VME
  2 slot, 6U height
233 or 166 MHz Pentium
Peripherals
  10/100BaseT Ethernet, Ultra Wide SCSI, GPIB, two USB ports, two serial ports, parallel port, floppy, mouse and keyboard ports
VXI MITE ASIC

## Slide 9: Remote VXI Controllers
PCI-MXI-2 – highest overall performance of any remote control solution for VXI
VXI-1394, VXI-1394/G – convenient, economical control of VXI (and GPIB)
GPIB-VXI – add VXI frames to GPIB systems, affordably

## Slide 10: PCI-MXI-2
PCI-MXI-2
VXI-MXI-2
(32-bit)
(64/32-bit)
(32-bit)
DMA
DMA
PCI
MXI-2
VXI
Notes: AT3E-<number>
What’s New in VXI?
<header>
<date/time>
18
MXI-2 is National Instruments “bus-on-a-cable” technology for controlling a VXI system. Because of the direct mapping of register accesses from the PC to the VXI bus, MXI-2 provides the fastest accesses times for individual register accesses. MXI-2 also has a fast protocol for bursting blocks of data, called the Synchronous MXI protocol. This protocol can sustain 22 MB/s on the MXI-2 bus, although the end-to-end performance depends on many system integration factors (bridge chip, types of instruments, and so on).

## Slide 11: VXI-1394
VXI
PCI
PC Memory
IEEE 1394 Host Adapter
VXI-1394
VXI Memory
(32-bit)
(32-bit)
IEEE 1394
serial
header
data
data
header
data
data
Create packet
Decode packet
Notes: AT3E-<number>
What’s New in VXI?
<header>
<date/time>
The VXI-1394 uses the convenient IEEE 1394 bus to control a VXI chassis. IEEE 1394 is a serial bus with fairly good burst data rates. Because of the levels of translation required for IEEE 1394 packets, this bus is not suited for applications that require fast register access times. However, the VXI-1394 can be an effective solution for applications that need to move blocks of data using a simple cabling solution.
In order to provide better performance for the register intensive Word Serial protocol, the VXI-1394 has an onboard microcontroller that translates between IEEE 1394 data streams and instrument messages.

## Slide 12: GPIB-VXI
PCI-GPIB
GPIB-VXI/C
(32-bit)
(8-bit)
(32-bit)
“*IDN?”
PCI
GPIB
VXI
Notes: AT3E-<number>
What’s New in VXI?
<header>
<date/time>
14
Many of the early VXI systems used GPIB-VXI interface cards as the system controller. GPIB-VXI controllers make your VXI instruments appear as stand-alone GPIB instruments. To write application software for these systems, you can use the same NI-488™-based software you use to program monolithic GPIB instruments. Although there are attractive programming benefits to using GPIB-VXI interface cards for VXI system control, data throughput rates realized using this approach are much slower than embedded VXI controllers or MXI. The GPIB-VXI is appropriate for systems with mostly message-based devices.

## Slide 13: Current Software
NI-VISA™
NI-VXI
Supported operating systems

## Slide 14: NI-VISA
VISA is the industry-standard API for VXI, GPIB, serial, PXI, and Ethernet systems
VXIplug&play alliance promotes interoperability between VISA vendors and instrument vendors
Current shipping version is NI-VISA 2.5

## Slide 15: NI-VISA 2.5
What’s new in NI-VISA 2.5
  New I/O functionality for Ethernet, GPIB, VXI
  Better performance
Better integration
  LabVIEW™ 6i
  Measurement & Automation Explorer (MAX)
  Measurement Studio™
More information at NIWeek presentation
  Advanced Software Techniques – VISA for Instrument Control

## Slide 16: NI-VXI 2.x
Instrument control software for VXI controller products
Includes NI-VXI development tools
  T&M Explorer
  VXI interactive control (VIC)
  VISA tools (NI-Spy, VISAIC)
NI-VXI API

## Slide 17: NI-VXI 2.x tools
T&M Explorer can configure NI controllers and instruments on VXI
Open VISA sessions to instruments
Get Help on setting up your instruments

## Slide 18: NI-VXI is available on…
Windows 2000/NT/ME/9X – all controllers
Linux – PCI-MXI-2, PXI-MXI-2, VXIpc-870
Solaris 2.x – PCI-MXI-2, PXI-MXI-2
Mac OS 9 – PCI-MXI-2
VxWorks – VXIpc
HP-UX 10.20 – PCI-MXI-2
Notes: NI-VXI works on many platforms, although not every controller works on every operating system. For example, Windows 95 does not handle IEEE 1394, so the VXI-1394 is not supported under Windows 95. Please check for driver availability for your platform of choice.