## Slide 1: Measuring with Vision
Dinesh Nair
Software Engineer
Fri Aug 18
12:00-1:15 p.m., 3:30-4:45 p.m.
Mulberry (10B)

## Slide 2: Agenda
Introduction
Dimensional measurements
Thermal measurements
Strain measurements
Flow measurements
Summary

## Slide 3: Introduction
Machine vision has matured into a precise and reliable measurement tool in many industries and applications
New technologies in software and imaging sensors make vision a low-cost measurement tool

## Slide 4: Dimensional Measurements
Obtaining quantifiable measurements from an image:
  Distances
  Angles
  Center of mass
  Area
  Circular fit
Also known as gauging
Notes: Gauging – measures lengths, diameters, angles, and other critical dimensions of objects in an image.
A gauging application locates the component(s) you need to inspect for dimensional attributes. After locating the component, the application makes measurements on the component or measures distances between the component and other landmarks in the image. If the measurements fall outside set tolerance levels, the component is rejected.
You can use gauging online during the manufacturing process or offline. For offline gauging, you need only a sample of components to determine the quality of an entire batch of components.

## Slide 5: Components
Fundamental imaging parameters
Image quality
  Signal conditioning
Calibration
  Pixel to real-world units
Measurement tools
  Identifying landmarks
  Calculating measurements
  Sub-pixel analysis
Notes: When you set up an imaging system for gauging applications, carefully consider the different components of the system.
Set up your system so that acquired images contain the information necessary for the imaging software to make measurements. The way you setup your system depends on the type of measurements you need to make and the type of measurement tools that you plan to use.
To make precise measurements, give equal consideration to calibrating your imaging system accurately. Calibration allows you to make measurements in real-world units and compare the measurements to defined standards.

## Slide 6: Fundamental Imaging Parameters
field of view
Field of view
working distance
Working distance
resolution
Resolution
sensor size
Sensor size
depth of field
Depth of field
Notes: Field of view (FOV) – area of the object under inspection that the camera sees. This area becomes the image
Working distance – distance from the front of the lens to the object under inspection
Resolution – smallest feature size that the imaging system can distinguish
Depth of field – maximum depth of the object that remains in focus
Sensor size – size of the camera sensor’s active area, which is typically specified by the sensor’s horizontal dimension
Edmund Scientific is a very good resource for information imaging systems.
edmundscientific.com

## Slide 7: Image Quality
Measurements are only as good as the information you can extract from the image.
resolution
perspective
depth of field
contrast
distortion
image quality
resolution
distortion
Notes: Image quality determines the type of information extracted from the image. The quality of an image depends on many factors, such as resolution, contrast, depth of field, perspective, and distortion. You must have sufficient image quality to extract information necessary to make measurements for an application. The desired quality varies from application to application.

## Slide 8: Resolution/Contrast
Resolution — The amount of object detail reproduced by the imaging system.
Contrast — The difference between object and background grayscale values reproduced by the imaging system.
Camera, lens, and lighting are important in determining resolution and contrast.
Notes: Resolution – measure of the imaging system’s ability to reproduce object detail. A low resolution image usually blurs object details.
Contrast – difference between the intensity values associated with the object and the intensity values of the background. Just as resolution is important in defining object details, contrast is important in separating objects from the background.
Although you can define resolution and contrast separately, they are closely related. In most imaging applications you should consider resolution and contrast together. Spatial resolution is often defined as the resolution of an image at a fixed contrast.

## Slide 9: Resolution — Camera Sensor Size
Minimum pixel resolution required by an imaging system:
axis length = 60mm
smallest feature size = 0.2 mm (fine lines)
minimum resolution
(60 / 0.2) x 2 = 600
length of object’s longest axis
smallest feature’s size
x 2

## Slide 10: Resolution — Lens Focal Length
Field of view (FOV) = Length of the object’s longest axis
Working distance (WD) = Distance from object to the lens
Sensor size (S) = Horizontal dimension of the camera’s sensor in mm
focal length = S x (WD / FOV)

## Slide 11: Resolution — Lens Focal Length
lens
sensor
scene
S
FOV
WD
focal length
sensor size (S) x working distance (WD)
field of view (FOV)
focal length =

## Slide 12: Focal Length Example
6mm lens at 0.3 m
12.5mm lens
at 0.3 m
25mm lens
at 0.3 m
sensor size = 6.4mm

## Slide 13: Distortion
Geometric aberration due to optical errors in the lens
Misplaces information about the object in the image plane
original
distortion
Notes: Because of optical errors, the lens magnifies different points of the object under inspection by different amounts. The optical error manifests itself as a distorted image. Objects are misplaced in the image relative to the center of the field of view.
Notice that no information about the object is lost to distortion. Distortion simply misplaces image information.

## Slide 14: Distortion (cont.)
You can measure and factor distortion into the calculation of measurements
distortion error
Notes: Because distortion is a geometric remapping of the scene, you can compute the amount of distortion by comparing information in the distorted (actual) image to the same information in the object.
For example, a grid of dots on an object (shown by the red dots in the figure above) appears distorted in the image of the object (shown by the black dots). Because you know that the image is of a distorted grid and you have information about the true location of the dots, you can compute the amount of distortion in the image. With this distortion information, you can use software to correct the image.

## Slide 15: Calibration
Process of relating pixel measurements to real-world measurements
Essential when you need to make accurate measurements in real-world units
Notes: When you want to make accurate measurements in real-world units, you must calibrate your imaging setup. Calibration computes pixel to real-world transformations while taking into account many errors that may be inherent to the imaging setup.

## Slide 16: Uses of Calibration
Account for (and remove) errors due to
Transform image coordinates to real-world coordinates and back again
known orientation offset
lens distortion
perspective
Notes: Use calibration to rectify measurement errors that the imaging setup can cause. Errors that may show up in an imaging system include:
  distortion from optical error in the lens
  perspective errors from the camera imaging the object from an angle
Also, you can use calibration to specify your own coordinate system in the image by setting a new origin and orientation of the axes.
The calibration process takes into account imaging system errors and the user-defined coordinate system to compute the information needed to accurately transform pixel measurements to real-world measurements and back.

## Slide 17: Calibrating an Imaging Setup
Image a grid of dots with known real-world distances between the dots
Learn calibration (mapping) information
original grid
image of the grid
Notes: To calibrate an imaging setup, follow these steps:
1. Create a grid of dots on the object under inspection.
2. Measure the distance between these dots in real-world units.
3. Acquire an image of this grid using the current imaging setup.
4. Input the acquired image and the distances between the dots to the calibration software. The calibration software computes the information required to convert measurement values from pixels to real-world units.
5. Apply the calibration information to the measurements in one of the following ways:
  Directly apply calibration information to convert measurement values from pixel units to real-world units
  Apply calibration information to correct errors due to the imaging setup, such as lens distortion, and then perform the measurements
6. Save the calibration information for future use (optional).

## Slide 18: Calibration Example
Correcting an image to account for camera perspective
calibration
information
original image
corrected image
Notes: In this example, the camera is looking at the objects from an angle. Thus, the objects appear skewed in the image. The calibration process determines the position and angle of the camera with respect to the objects. You can use this information to correct the image so that the objects appear in their true shapes.

## Slide 19: Measurement Tools
Blob analysis
  Finds locations of binary objects
Edge detection
  Detects points of sharp changes in intensity
  Effective method to determine spatial extent of grayscale objects
Pattern matching
  Finds location and extent of patterns in an image
Notes: Blob analysis, edge detection, and pattern matching are software tools for making measurements. To make measurements, you first need image landmarks to guide you.
If you need to make measurements on objects that do not have a well-defined shape, use blob analysis. If you need to find a few points on the boundaries of an object in a grayscale image and processing time is important, use edge detection. If you need to locate detailed components or objects in grayscale images, use pattern matching.
Image quality depends on the software tool that you use. Blob analysis requires good contrast between the background and all regions of an object, which makes the thresholding process simple. On the other hand, edge detection requires a high contrast at the object’s boundaries. Pattern matching works on images with varying qualities.

## Slide 20: Measurement Tools (cont.)
Geometry
  Distance
  Angle
  Areas
  Line detection algorithms
  Center of mass
  Circular fit determination
  And many more ...
Notes: Once you identify the landmarks of the image, you can make a number of different measurements using the properties of these features.

## Slide 21: Blob Analysis
Thresholding creates a binary image, separating particles from the background.
Blob analysis returns properties of binary objects that you can use to calculate measurements:
  Size in pixels
  Center of mass
  Longest segment
  and more ...
Notes: You can use blob analysis (particle analysis) functions to find dozens of blob features, such as the orientation, area, perimeter, center of mass, and coordinates of each blob. You can use these unique parameters to perform many tasks, such as identifying parts in a sorting application or ensuring that a part meets quality standards.

## Slide 22: Edge Detection
Finds points of significant intensity changes in an image
Works on line profiles
Detect boundaries of objects quickly
line profile
edge points
Notes: Edge detection is an important image processing function. Edge detection clearly determines the boundaries or edges of an object, which appear as intensity discontinuities in an image. Once the software finds the edges in the image, you can use the location of the edges to compute the distances between them.
Edge detection works on a one-dimensional profile. The software analyzes the pixel values along the profile to detect significant intensity changes. You can specify characteristics of the intensity changes to determine what changes constitute an edge.
Because edge detection works only on one-dimensional data, it is a very quick way to find object boundaries or other areas of significant intensity changes.

## Slide 23: Edge Detection
Contrast – Minimum difference between the average pixel intensity before and after the edge
Width – Number of pixels that are averaged to find the contrast on either side of the edge
Steepness – Minimum number of pixels that correspond to the transition area of the edge
steepness
width
width
contrast
edge located
pixels
Notes: An edge is defined as the magnitude of the intensity change at a location in the image. The contrast parameter defines this magnitude. If you specify a large contrast, only edges with very high intensity changes are found.
To compute the contrast at any point along the pixel profile, the software averages pixels before and after the point. You define the number of pixels averaged on each side by setting the width parameter. After computing the average, the software computes the difference between these averages to determine the contrast. Filtering reduces the effects of noise along the profile. If you expect the image to contain a lot of noise, use a large filter width.
The steepness parameter defines the slope of the edge. Specify a large steepness value to indicate that the edges along the profile have a gradual slope or transition region.

## Slide 24: Pattern Matching
Finds reference patterns (templates) in an image and reports the following:
  Location(s) in the image
  Angle of rotation
  Scale
Works under conditions of
  Varying light
  Noise, blur, and partial occlusion
Notes: Pattern matching is a technique that quickly locates known reference patterns in an image. With pattern matching, you create a template that represents the object for which you are searching. Then, you search for occurrences of the object in each acquired image of your machine vision application. The software calculates a score for each object occurrence that indicates how closely the occurrence matches the template.
Pattern matching is the key element to many machine vision applications. Pattern matching can provide information about the presence or absence, number, and location of an object within an image. In gauging applications, pattern matching locates key components before the software performs measurements on the components, such as lengths, diameters, angles, and distances between components.

## Slide 25: Sub-Pixel Accuracy
Returns edge detection or pattern matching information in fractions of a pixel
Uses interpolation and fitting techniques to estimate sub-pixel accuracy
Accuracy of one-fourth of a pixel is possible under good imaging conditions
Notes: If image resolution is high enough, most measurement applications can make accurate measurements using only pixel accuracy. However, obtaining the minimum image resolution needed by a gauging application is sometimes difficult. In these cases, you need to find edge positions or template locations with sub-pixel accuracy.
Sub-pixel analysis is a software method that estimates the pixel values provided by a higher resolution imaging system. With the imaging system components and software tools available today, you can reliably estimate one-fourth sub-pixel accuracy. However, the results of the estimation depend heavily on the imaging setup, such as lighting conditions and the camera lens. Before resorting to sub-pixel information, try to improve the image resolution.

## Slide 26: Sub-Pixel and Edge Detection
Interpolation between pixels
Quadratic or cubic fitting
pixels
edge located
line profile
interpolates edge location between pixels
Notes: To compute the location of an edge with sub-pixel precision, the edge detection software first fits a higher-order interpolating function (such as a quadratic or cubic function) to the pixel intensity data.
The interpolating function provides the edge detection algorithm with pixel intensity values between the original pixel values. The software then uses the intensity information to find the location of the edge with sub-pixel accuracy.

## Slide 27: Gauging Demonstration

## Slide 28: Thermal Measurements
Infrared Machine Vision (IRMV) uses IR (thermal) imaging in a process, process control, or instrumentation system
Applications include the following:
    Heat detection
    Temperature measurement
    Thermal analysis
    Seeing through obscurants
    Process monitoring and control
    76,000+ thermocouples
flir.com

## Slide 29: Infrared Imaging
infrared spectrum
visible spectrum
flir.com
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>

## Slide 30: ThermoVision IRMVTM320 Series
Family: ThermoVision IRMV™
Series/Version: 320/160
Model: (V) Vision
(M) Monitor
(C) Control
flir.com

## Slide 31: Performance
Fast: (60 Hz acquisition and display)
Accurate: (2% or 2°C)
High sensitivity: (.1 °C)
High resolution: (320 x 240)
Longwave IR imaging
flir.com
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>

## Slide 32: IRMV Applications
flir.com

## Slide 33: Automotive
Die casting, aluminium
Anti-rust filling of doors
Injection moulding
Back-lit defroster
Glass bending
Deep drawing
Stamping
Welding
Painting
Forging
Gluing
Cylinder heads
flir.com

## Slide 34: Foam-Fill Seat Application
ThermoVision in an automated inspection of foaming molds
flir.com

## Slide 35: Seam Welding Applications
IR Camera added to robot-controlled welding process for real-time inspection of the heat-affected zone
Online assurance of the quality of minimum safety standard welded components
flir.com

## Slide 36: Die Casting Application
parts presence
mold/part uniformity
flir.com

## Slide 37: Casting Applications
inner portion of wheel
outer portion of wheel
www.flir.com

## Slide 38: Battery Level Inspection
flir.com

## Slide 39: Glass Applications
Glass bending stress evaluation
Quench and anneal control
Defroster/antenna quality control
Safety glass delaminations
Glass bottle fabrication
Sterilization quality control
flir.com

## Slide 40
thermal uniformity
of glass
defroster continuity
flir.com

## Slide 41: Ford Wixom
flir.com

## Slide 42: Glass Bending
ThermoVision image of automobile windshield after exiting LEHR at a glass bending facility
flir.com

## Slide 43
parts position
spot placement
data readout
www.flir.com

## Slide 44: ThermoSoniX ™
Combines IR imaging with ultrasonic induced localized heating to find flaws, cracks, and defects in parts
Co-developed with Indigo Systems Corp.
t=0
t=100 ms.
t=400 ms.
disc brake arm (cast part) application
Solutions for science and industry
Image Therm Engineering, Inc.

## Slide 45: Strain Measurements
Method for measuring strain in highly deformable materials
Developed by Stress Engineering Services Inc.
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>
SES is a full-service engineering consulting firm that has been in business since 1972. SES specializes in high-end analysis and design with experience in finite element analysis in conjunction with traditional empirical measurement techniques. SES is a National Instruments Alliance member with offices in Colorado, Texas, and Ohio.
, Inc.

## Slide 46: Challenges of Straining Soft Material
Accurate strain measurements require large samples and expensive sensors
Most instrument techniques for strain measurement permanently damage the specimen
Test time is lengthy
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>
When designing products with a newly developed material, you need to fully characterize that material. Using previous technologies, fully characterizing a material cost a great deal of time and money. SES has developed a new characterizing technique that allows for a simple test with real-time results.

## Slide 47: Strain Measurement Solution
Apply 2D grid of “dots”
Blob analysis calculates x,y coordinates of each dot
Calculate strains and Poisson’s ratio for each dot location
Verify test with known materials
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>
Using the Optical Strain Measurement System, you can test a material with a single run and obtain real-time results. Because a transducer is not mounted on the specimen, you do not need to correct for transducer effects or to perform a hysteresis analysis typical in most transducers. The test does not damage the specimen, so you can use the material in subsequent tests. The Optical Strain Measurement System has been tested against known standards and proven highly accurate.

## Slide 48: Elastomer Application
Measure transverse strain
Measure axial strain
Benefits
  More precise – incompressibility assumption is inaccurate
  Multiple strain tests do not damage material
  Less expensive
  Fast test
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>
The following is a real-world case history: SES received a new material to characterize for use in a design. Using the Optical Strain Measurement System, SES obtained the necessary results in a single test. The test revealed that the material is incompressible, disproving a common assumption that the material could be compressed. With the Optical Strain Measurement System, SES can generate product designs with the confidence that the designs are based on sound experimental data.

## Slide 50
Elastomer Application
testing an elastomer sample
monitoring blow molding process

## Slide 51: Velocity and Acceleration Measurements
Define the pattern to locate
Use pattern matching to locate matches in subsequent images
Assume closest object is best match
Need acquisition rate, distance, and orientation to make measurements
Draw vectors to show direction and speed
1
2
3

## Slide 52: Velocity and Acceleration (cont.)
Template size and orientation search angle affect calculation speed
Applications
  Spray characterization
  Fluid research
  Fuel injector research
  Defense

## Slide 53: Spray Measurements
Fluid dynamic characterization of an aerosol spray
Measurements include the following:
  Divergence angle of spray
  Cross-sectional ellipticity and uniformity of spray
  Time evolution of the developing spray
Solutions for science and industry

## Slide 54: SprayVIEW ™
High-speed, optical characterization of sprays
  Pharmaceutical, aerospace, and automotive applications in both R&D and QA
  Up to 1,000 frames/second acquisition rates
  Patented hardware and software tools
  Measures plume geometry and particle dispersion
Double click to play image sequence
Solutions for science and industry
Image Therm Engineering, Inc.

## Slide 55: Summary
Vision is a mature, low-cost, reliable measurement tool
Vision makes precise dimensional, thermal, and velocity measurements in addition to many other types of measurements
Choose all pieces of your imaging system carefully to create an environment suitable for making reliable measurements