## Slide 1: Connecting Multiple Platforms in a Hybrid Test System

## Slide 2: Outline
Hybrid Systems Overview
Bus Technology Considerations
Why Multiple Platforms?
System Topologies
Connectivity between Platforms
Extensibility
Advantages of a Multiplatform System
Summary

## Slide 3: Hybrid ATE Systems Overview
A hybrid system combines components from multiple ATE platforms
  Streamlines system transition and maintenance
  Protects investment in existing software and hardware
  Allows easy integration of advances in ATE system development
Layered architecture is important
Multiple hybrid topologies
Notes: Hybrid ATE systems provide developers with a long-term ATE system that can evolve with short commercial technology lifecycles. Hybrid ATE systems take advantage of a 5 layer architecture to increase reusability, connectivity, extensibility, and module replacement.
By following the layered architecture, you create a test framework that allows you to replace and/or add components without having to re-architect the system. By clearly defining the system, you can take advantage of multiple buses using a variety of hybrid topologies. This allows you to meet multiple needs – protect the investment in existing hardware and software while being able to integrate the latest technologies.

## Slide 4: Issues For System Developers
Creating best system for specific UUT measurement needs
Longevity
  Preserve investment in test hardware and software
  Test platforms versus test system life cycles forces mid-life upgrades
  Streamlining system maintenance and upgrade
Integration with latest technologies
Notes: System developers want to design the best test system for their UUT measurement needs. A large part of creating the best test system is designing one with longevity - with the ability to preserve their investment in hardware and software as well as streamline the processes for maintenance and upgrades. In addition, a good test system provides the developer with the ability to build on top of their test system by integrating the latest technologies.

## Slide 5: Five Layer ATE Architecture
- TestStand, DIAdem
System Management
- LabVIEW, LabWindows/CVI, C++
Application
- VISA, LV PnP, IVI, MAX, DAQmx
Measurement and Control Services
- PXI, VXI, Desktop PC, GPIB
Computing
- Instruments, Data Acquisition, Vision, Motion
Device I/O
Notes: Moving from the bottom up, we’ll start with the actual hardware devices that you use to perform testing and automation. This layer includes the various instruments and data acquisition used in your system. Developers want to choose the devices that meet measurement needs and also scale with changing system needs. Oftentimes, the devices used will require multiple instrumentation buses. The computing layer above refers to the instrumentation buses used and the method and topologies that connect these buses. Users should choose a topology that meets timing and synchronization needs, allows them to protect investment in hardware, and add new components to benefit from advancing technologies. The measurement and control services is the layer that integrate the hardware with the software. It provides configuration utilities, soft front panels, and drivers with APIs to ease programming. With tight integration with the application layer, these APIs should appear as a seamless part of the application development environment. The application layer refers to the software used to create the test programs. For instance, developers might create a program to take a measurement with a DMM and another program to generate a signal. The system management layer allows users to call these programs, manage various user levels, log and manage data, and generate reports.

## Slide 6: Evolution of Automated Test Platforms
“Big Iron” ATE
Traditional GPIB-Based ATE
User-Defined ATE
Instrument on
a Card
Proprietary Tester
Stand Alone
VXI
PC/PXI
Notes: <number>
<footer>
<date/time>
The introduction of new platforms for test and measurement has been steady for in recent history. Many of these platforms remain popular today; some cater to particular applications while others are utilized for many applications. The availability of various platforms, both new and old, can force test engineers to utilize existing test equipment with newer equipment that may be offered on different platforms. Test equipment manufacturers offer various solutions to combine multiple platforms into hybrid automated test systems.

## Slide 7: Bus Technology Considerations
Variety of buses available
  PXI, VXI, GPIB, etc…
Key bus factors that affect instrument performance
  Latency
  Bandwidth
Other considerations
  Timing and synchronization
  Distributed networks and remote monitoring
  Standard software frameworks
Notes: <number>
<footer>
<date/time>
When considering the instruments for a system, people often evaluate buses based on the instruments that are available—looking for their measurement needs to be met. Does the bus provide instruments with the sampling rate, bandwidth, and so on, that is needed for the test system. When addressing these concerns, however, it is important to factor in the capabilities of the instrumentation bus itself as this affects the performance of the instruments you choose and their ability to work together to give you useful measurements. Factors like latency and bandwidth of the bus will affect the performance of the instrument.
Timing and synchronization vary by bus and should be evaluated as well since it affects the ability to communicate between instruments and tightly correlate signals.
In addition, as you consider buses, you should also compare other factors
Distributed networks and remote monitoring: Some systems require either remote control of systems or distributed networks. Sometimes software can help in the deployment of these remote systems; however, some buses also simplify distribution.
Standard software frameworks: does the bus specification implement a software framework? Software frameworks ensure that a user has a complete, multivendor system solution from the start and prevents market fragmentation due to competing standards from multiple vendors. This helps to ensure software interoperability.

## Slide 8: Latency and Bandwidth
Latency measures the delay of transmission of data across a bus
Bandwidth measures the rate at which data is sent across the bus (typically MBytes/s)
Notes: <number>
<footer>
<date/time>
First we will address these key bus characteristics that affect instrument performance. Both latency and bandwidth impact the ability to support instrument performance, high-speed systems, and high-channel-count systems.
Using a highway analogy, you can think of a bus as the highway. The latency measures the delay of transmission of data, so you can think of it as corresponding to the number of stoplights in the road. The bandwidth measures the rate at which data is sent across the bus, and thus corresponds to the width of the road and speed of travel.

## Slide 9: Impact on Application
Latency
Important for applications that include
  Digital multimeter (DMM) measurements
  Switching
  Instrument configuration
Serial buses tend to have higher or worse latency
Bandwidth
Important for applications that send large sets of data or require data streaming
  RF applications
  Waveform acquisition or generation
High-speed or high-channel systems often require 10 to 100 MBytes/s or more
Notes: <number>
<footer>
<date/time>
Why do latency and bandwidth matter? They help determine whether you can actually perform the measurements needed. Since latency is the delay of transmission of data, it is important to use a bus with lower latency in applications like DMM measurements, switching, or instrument configuration. Typically you will find that serial buses have a higher latency. (Exception to this is PCI Express which is serial, but packetizes data and has an extremely fast data link at 2.5 Gbps so that the typical latency is very low).
For applications that transfer large sets of data or require data streaming common to applications like RF and waveform acquisition and generation, you will need a bus with higher bandwidth. In addition, high-speed and/or high-channel systems require 10 to 100 Mbytes/s or greater bandwidth.

## Slide 10: Industry Bus Performance
Notes: <number>
<footer>
<date/time>
This chart provides a reference for comparing the buses in terms of latency and bandwidth. Notice that PCI Express is highlighted because it is an emerging technology, which we will be discussing later. A few points to note with the chart, decreasing or improving latency moves to the right and note that both scales are logarithmic. From the chart, you can see the tradeoffs between latency and bandwidth for the various buses. As noted earlier, you can see that the serial buses tend to have higher latency (with the exception of PCI Express). You will notice that PCI/PXI provides both the best latency and bandwidth for measurements making it ideal for many applications.

## Slide 11: Timing and Synchronization
Used for handling synchronous events
  For example, Starting signal generator and digitizer at same time
Used for performing asynchronous events
  For example, Handshaking with switch and DMM, Arb, and so on
Backplane buses provide most direct and accurate method of synchronization (PXI and VXI)
IEEE 1588 protocol provides external synchronization (LAN)
Input and output triggers available for GPIB, USB, and 1394
Notes: <number>
<footer>
<date/time>
Timing and synchronization is an important factor to consider and will be discussed more in depth in another session. It enables the communication between the instruments in your system which is very important for correlating all of the data taken for one device under test. Timing and synchronization impacts your ability to handle both synchronous and asynchronous events. The various buses provides different levels of synchronization. Backplane buses provide the easiest and most direct connection between instruments as well as the most accurate synchronization. 1588 protocol provides a method for synchronizing over large areas using LAN. GPIB, USB, and 1394 provide the most basic level of synchronization with input and output triggers.

## Slide 12
Software is Key
With proper software tools you can:
  Abstract system complexity
  Use instruments of various buses
  Integrate instruments into one system
Notes: <number>
<footer>
<date/time>
We have discussed many of the important bus factors to consider, but an important thing to remember is that software is key no matter which bus you choose. With the growing complexity of devices, you face growing complexity in the test system. There is inherent test system complexity and artificial complexity, introduced by the tools used. The right software allows you to reduce the artificial system complexity by providing tools to simplify taking measurements, performing analysis, and presenting data. With the right software tools, you can work with any mixture of bus technologies. This allows you to take instruments or various buses and integrate them into one system.
The screenshots show how easy it is to do this – the first screenshot shows Measurement & Automation Explorer (MAX), a configuration manager provided with NI drivers. It allows you to see all of your instruments and integrates the buses into one environment. Here you can see there are PXI, VXI, and FieldPoint instruments. MAX allows you to configure the instruments, ensure they are working properly, and create aliases and tasks for your system. LabVIEW, in the second screenshot, integrates the configurations made in MAX to simplify programming. In addition, LabVIEW simplifies user interface development and provides built-in analysis functions.

## Slide 13: Software Standard Frameworks
Impacts development and integration of the system:
  Ease system integration tasks
  Driver software eases programming
    VISA
    Plug and Play drivers
PXI and VXI specify a standard driver framework
Virtual Instrumentation Software Architecture (VISA) available for PXI,VXI, LAN, GPIB, USB, and 1394
Notes: <number>
<footer>
<date/time>
Software is important no matter what bus you use, but some buses outline a standard software framework for its instruments to help system integration and to ease programming. This typically includes things like specifying a driver should be provided, providing help documents, and using a standard like VISA. VISA provides the same application programming interface (API) to talk to instruments of a variety of bus types. Thus you can talk to PXI, GPIB, VXI, LAN, etc. instruments all with the same driver standard.
To help ensure that a user has a complete, multivendor system solution, PXI specifies that both system controller modules and PXI peripheral modules have to meet certain requirements for operating system and tool support. PXI requires that peripheral modules provide software for installing, configuring, and controlling the modules under Windows and recommends that instrumentation class PXI modules provide a user-level interface that is supported under the common development environments. PXI requires that system controller modules supply a VISA implementation that supports the PXI bus and also recommends that instrumentation class PXI peripheral modules should provide instrument drivers and soft front panels that are consistent with VXIplug&play instrument driver specifications.
For buses like LAN, GPIB, USB, and 1394 that do not specify a standard framework, you can still take advantage of the VISA open standard.

## Slide 14: Bus Comparison
Best
Better
Good
1
1
1
Notes: <number>
<footer>
<date/time>
We’ve discussed many factors for evaluating bus technologies. This chart provides a reference that you can come back to in the future. It summarizes the points discussed today and some of the main factors you should consider when evaluating bus technologies. To highlight a few points, PXI provides a best solution for latency, throughput, and timing and synchronization. As a result, it is a very good bus option for high channel count and data streaming applications.

## Slide 15: Why Multiple Platforms?
UUT drives Measurement Requirements
Measurement Requirements drive Instrument Selection
Instrument Selection drives ATE bus choices
Optimize Price/Performance
Instrument
ATE bus
Price/
Performance
Measurement
Requirements
UUT
Multiple platforms supports instrument selection
Protect investment in hardware and software
Allows integration of latest technologies
Notes: When designing a system, the first consideration is looking for instruments that meet the measurement functionality required for the system. The device under test (UUT) will drive the measurement requirements which will then drive the instruments available. When selecting instruments, developers should not constrain themselves to one bus, but rather should let the instrument selection drive the ATE buses used in the test system. From there, the developer can optimize price and performance options and iterate on the process until determining the best instruments for the system.
During the instrument selection process, the developer should also factor in maximizing investments by using existing hardware along with newer technologies.

## Slide 16: Computing
Instrument selection should drive the buses used
Multiplatform systems allow you to:
  Use the best instruments for your system
  Integrate custom or legacy hardware thereby protecting your investments
  Integrate latest technology to take advantage of newer performance and cost options
Interconnectivity provided by controllers
  Interfaces and peripheral connections
  Ability to share triggers, clocks, and other signals
Notes: Your measurement needs should drive the bus you use. With the many ATE bus options available, you don’t want to limit yourself to the instruments available to just one bus. Many connectivity options are available so that you can design a system with a topology to meet your specific system needs.
If any instruments need to be added or replaced, a multi-platform system is easily extensible and allows you to mix and match ATE buses . Multi-platform systems also meet the need for longevity by providing a system that protects your investment in hardware and software and integrate the latest technologies.

## Slide 17: ATE Connectivity Options
Control Interface | Bus Type
Embedded Control | PXI, VXI
PCI-to-PXI | MXI-4
PCI/PXI-to-VXI | MXI-2, USB
VXI-to-PXI | MXI-41
Ethernet-to-PXI | Ethernet
PC to Stand-Alone Instrument | GPIB,USB, Ethernet , Serial
Many connectivity options
Try to stay simple and modular
1Requires VXIpc with built-in PCI expansion slot
Notes: There are many methods of control available for VXI and PXI. VXI and PXI both have embedded and remote control options available. Some of the more popular tools available to connect platforms include Ethernet, GPIB, MXI-4, and MXI-2 solutions.
Keeping PC and PXI in the center gives developers the most connectivity and interface options. With the most standard interface options available, the developer can easily connect to other instrumentation buses.
In addition, developers can synchronize across VXI and PXI chassis by taking advantage of the clock and triggering capabilities available with each bus.

## Slide 18: NI VXI Products – CLK and Trigger Capabilities
Summary of VXI External Timing and Triggering Connectors |  |  | 
Product Type | Model Name | Trigger | CLK 10
VXI MXI-2 Controller | NI VXI-801x | 2 in/out (SMB) | 1 in/out (SMB)
USB-VXI Controller | NI VXI-USB | 2 in/out (SMB) | 1 in/out (SMB)
VXI MXI-3 Controller | NI VXI-834x | 2 in/out (SMB) | 1 in/out (SMB)
GPIB-VXI Controller | NI GPIB-VXI/C | 2 in/out (BNC) | 1 in/out (BNC)
Embedded Controller | NI VXIpc-870B Series NI VXIpc-770 Series | 2 in/out (SMB) | 1 in/out (SMB)
Note: Many other VXI I/O modules or chassis have the ability to route triggers from the VXI backplane to a gront panel connector. This is module-specific, so please check the I/O module functionality in your system. |  |  | 
Notes: All of the NI VXI controllers provide timing and triggering connectors to synchronize multiple chassis. This chart lists the standard interfaces available with NI VXI controllers. In addition, these connectors can be used to synchronize with PXI chassis.

## Slide 19: NI PXI Products – CLK and Trigger Capabilities
Notes: PXI also provides many controllers with timing and triggering capabilities to synchronize multiple PXI chassis. These connectors can also be used to synchronize with a VXI chassis.

## Slide 20: Example Multi-platform System: VXI Control of PXI and GPIB
VXI
MXI-4 or ENET
For MXI-4, use VXIpc embedded controller with built-in PCI slot (ex. 872B)
PXI
VXI Slot 0 Controller Options:
VXIpc Embedded Controller
PXI System Controller Options:
PXI-MXI-4 or PXI Embedded
Stand Alone
GPIB
Notes: A developer could extend an existing VXI system and add PXI chassis for general purpose instrumentation. This allows to continue using existing instrumentation but also introduce newer technologies into the system.

## Slide 21: VXI to PXI and GPIB Example
VXIpc-872B with PCI MXI-4
PXI MXI-4
MXI-4 link
GPIB
instrument
GPIB Connection
PXI 6652
Shared Trigger
VXI
Instruments
PXI
Instruments
Notes: From the previous example, the VXIpc-872B and the PXI 6652 slot 2 timing module can share triggers.

## Slide 22: VXI to Multiple PXI Chassis and GPIB Example
VXIpc-872B with PCI MXI-4
PXI MXI-4
MXI-4 link
GPIB
instrument
GPIB Connection
PXI 6652
Shared Trigger
VXI
Instruments
PXI
Instruments
PXI MXI-4
PXI MXI-4
PXI 6652
PXI
Instruments
MXI-4 link
Splitter
Notes: To share triggers across multiple PXI chassis, split the trigger cable (with an actual splitter) before driving it to the 6652's, instead of going in and out of the first 6652. Try to keep the cable lengths equal from the splitter to each PXI chassis:

## Slide 23: VXI to Multiple PXI Chassis and GPIB Example
VXIpc-872B with PCI MXI-4
PXI MXI-4
MXI-4 link
GPIB
instrument
GPIB Connection
PXI 6652
Shared Trigger
VXI
Instruments
PXI
Instruments
PXI MXI-4
PXI MXI-4
PXI 6652
PXI
Instruments
MXI-4 link
Shared Trigger
Notes: Or if the PXI chassis is the trigger source, use the first PXI-6652 as the source of the trigger, split it twice, routing one to each of the other chassis (VXI and PXI), and the last connection back to the original PXI-6652, all with equal cable length. That's what we do in our NI-Sync examples to minimize skew between the chassis. The VXI chassis probably still won't be as synchronized as the two PXI chassis because the electrical characteristics are different:

## Slide 24: VXI Control of PXI and GPIB Use Cases
Adding a PXI chassis to an existing VXI embedded controller-based system
Minimizing large-system cost
  Use VXI chassis for existing, custom, unique, or high-performance VXI modules
  Use PXI chassis for general-purpose instrumentation
Notes: The primary use cases for VXI-based hybrid systems is adding a PXI chassis or GPIB instrument to an existing VXI embedded controller-based system and minimizing large-system cost. A developer can minimize cost by using the VXI chassis or GPIB for existing, custom, unique, or high-performance VXI modules and PXI chassis for modular instrumentation and multifunction hardware integration.
For MXI-4 link, use a VXIpc Embedded Controller that contains a built-in PCI slot for PCI MXI-4, such as the NI VXIpc-872B.

## Slide 25: Example Multiplatform System: PC Control of PXI, VXI, and GPIB
PXI
VXI
Desktop or
Rack-Mount PC
MXI-4 (copper or fiber-optic) or
Ethernet Link to PXI System Controller
MXI-2, USB, GPIB, or Ethernet
Link to VXI Slot 0 Controller
VXI Slot 0 Controller Options:
VXI-MXI-2, VXI-USB, GPIB, or VXIpc
Embedded Controller (for Ethernet)
PXI System Controller Options:
PXI-MXI-4 or PXI Embedded Controller (for Ethernet)
Stand Alone
GPIB
Notes: A developer could also control multiple buses from a PC. In this example, a developer could use the VXI-USB to control a VXI chassis and a MXI-4 to control the PXI chassis.

## Slide 26: PCI to PXI, VXI, and GPIB Example
NI-8350 Rack-Mount Controller
GPIB Instrument
PXI Instruments
PXI MXI-4
VXI-USB
VXI Instruments
MXI-4
USB
GPIB
Shared
Trigger
Notes: To share triggers between the PXI and VXI chassis, the developer could use the timing and triggering connectors available on both remote controllers.

## Slide 27: PC Control of PXI, VXI, and GPIB Use Cases
Adding a new PXI or VXI chassis to an existing system already based on PC control
Desiring the combination of high processor performance and low-cost of the latest PCs on the market
Minimizing large-system cost
  Use VXI chassis for existing, custom, unique, or specialized VXI modules
  Use PXI chassis for high-performance and general-purpose instrumentation
Notes: The primary use case for PC control of PXI, VXI, and GPIB is adding a new PXI or VXI chassis to an existing system based on PC control or wanting to the low-cost, high processor performance available with the latest PCs on the market.
This allows users to minimize system cost by using the VXI chassis for existing equipment and the PXI chassis for high-performance and general-purpose instrumentations.

## Slide 28: Example Multi-platform System: PXI Control of VXI and GPIB
VXI
VXI Slot 0 Controller Options:
VXI-MXI-2, GPIB or VXIpc Embedded Controller
PXI
MXI-2, USB 2.0, GPIB, or ENET Link
PXI System Controller:
PXI Embedded Controller
Install MXI-2, USB 2.0, GPIB, or
ENET Peripherals in PXI chassis
Stand Alone
GPIB or
ENET Link
Notes: A developer could also use embedded control of PXI and then use a remote controller like PXI-MXI-2 to control a VXI chassis.

## Slide 29: PXI to VXI, and GPIB Example
GPIB Instrument
PXI Instruments
PXI 8186
VXI-PXI-8015
VXI Instruments
MXI-2
GPIB
Shared Trigger, Clock
PXI 8320
Notes: Using the PXI-MXI-2 interface, users can share clocks and triggers across the VXI and PXI chassis.

## Slide 30: PXI Controlling VXI Via Remote VISA
Notes: Another method of controlling VXI from PXI is through Remote VISA. By using the TCP/IP address, the user could remotely connect with a VXI chassis. This access is easily done through Remote VISA so that the VXI chassis looks like it is local to the system. In this screen shot, the user can just specify the address of the VXI chassis and interact with it as though it were directly connected.

## Slide 31: PXI Control of VXI and GPIB Use Cases
Adding a VXI chassis to an existing PXI system
Expansion or phased transition of system to high performance and lower-cost PXI technology
Benefits of PXI as a system core:
  Leverages PC based technology on a rugged platform that can support manufacturing long life
  Continues to offer new products, allowing for easy system expansion
  Multiple options for connectivity to other platforms
Notes: The primary use cases for PXI-based hybrid systems are adding a VXI chassis or GPIB instrument to an existing PXI system to meet unique requirements or expansion or phased transition of VXI or GPIB-based system to PXI technology
The benefits of PXI as a system core:
Leverages PC based technology on a rugged platform that can support manufacturing long life
Continues to offer new products, allowing for easy system expansion
Multiple options for connectivity to other platforms

## Slide 32: Ideal Hybrid System: PXI in the “Center”
Low latency PXI access to measurement devices
  PXI includes timing and synchronization capabilities
PXI offers a high Windows native slot count
  Add other buses (CAN, SCSI, 1394) or more serial ports
  Access them directly from the PC, not through special driver
PXI offers connectivity to other ATE buses
  GPIB, Ethernet, Serial, USB built into the controller
  VXI, Gb Ethernet easily available
  Other buses can use Remote VISA for messaging
Notes: An ideal hybrid system uses PXI in the center because it provides low latency PXI access to measurement devices, a high Windows native slot count, and plenty of connectivity to other ATE buses.
PXI has tight timing and synchronization capabilities along with very low latency to enable many complex measurements. In addition, with high native slot count available, users can add buses and access them from the PC, not through a special driver. PXI offers plenty of connectivity options like GPIB, Ethernet, Serial, and USB which provides a way to connect to other ATE buses.

## Slide 33: Distributed Control of Hybrid VXI/PXI Systems
Ethernet
Use embedded controllers in all systems
Transfer data between systems using software
  ie Datasocket (LabVIEW, CVI, C/C++, Visual Basic, etc)
Notes: A developer could also create a distributed system to control multiple VXI and PXI chassis. By using embedded controllers, a ser could interconnect VXI and PXI through Ethernet and transfer data between systems using software like Datasocket, LabVIEW, CVI, etc.

## Slide 34: Distributed Control of Hybrid VXI/PXI Systems
Primary Use Cases:
  Distributed system with multiple measurement units
  Adding a new PXI or VXI chassis to an existing system
Minimize large-system cost
  Use VXI chassis for existing, custom, unique, or specialized VXI modules
  Use PXI chassis for high-performance and general-purpose instrumentation
Notes: The primary use case for this type of system is for a test system that requires distributed control like antenna range testing. This allows users to add PXI or VXI instrumentation to the system as needed and still meet distributed needs. By using software like Datasocket and ADEs like LabVIEW, CVI, and Measurement Studio that provide tools for connectivity, developers can meet distribution needs with this type of system topology. This also minimizes system cost by using the VXI chassis for existing equipment and the PXI chassis for high-performance and general-purpose instrumentations.

## Slide 35: Summary of Hybrid VXI/PXI System Control Options
Many options for the following topologies
  VXI as the hybrid system controller
  PXI as the hybrid system controller
  PC as the hybrid system controller
  Distributed control (ie multiple independent PXI and VXI controllers with inter-communication)
Combinations and permutations (ie multiple chassis systems, etc) are nearly endless.
Mix or match to your needs.
Notes: Many hybrid topologies are available to customers when designing a hybrid test system. Developers should determine which topology will best meet system needs.

## Slide 36: Extensibility
Accommodating new application needs does not require redesigning the system
  Clearly architected system modularizes the system so that components can be added as needed
  Add components without rewriting software
Ability to integrate new technologies to improve performance or lower cost of system
Notes: Through the hybrid topology, developers do not need to redesign a test system to accommodate new application needs. The hybrid test system allows users to easily grow a system no that components can be added as needed. It also does not require an rewriting of existing software to add new components. This provides developers with a way to integrate new technologies to improve the cost or performance of the system.

## Slide 37: Advantages of a Multiplatform System
Full utilization of hardware instrumentation available
Meets needs for longevity
  Protect investment in hardware
  Streamlines the upgrades and maintenance
Adding new components is simplified
  Allows you to add new ‘modules’ without redesign
  Allows you to incorporate the latest technology
Notes: Hybrid multiplatform systems allow users to fully utilize hardware instrumentation as opposed to limiting an application to just one instrumentation bus. This allows users to accommodate for longevity needs by maximizing investments in existing hardware and streamlining maintenance and upgrades. The process of adding new components is simplified because the user has a modular test system in which components can be easily introduced.

## Slide 38: Demo: Wireless Communications Test System
3D Power Spectrum, Occupied Bandwidth, Auto Find (LabVIEW)
TestStand
MAX, VXI ResMan, VISA, IVI and PnP Drivers
PCI (NI-8350), PXI MXI-4, VXI-USB, GPIB
2.7 GHz PXI RF Signal Analyzer, 8.5 GHz VXI RF Signal Analyzer, PXI DMM, PXI Switch, GPIB Power Supply
Notes: For a wireless communications system, you can see how the layers work together to integrate the buses for this test application. Through the architecture the user can integrate VXI and GPIB instruments with some newer PXI instruments. This allows the user to take advantage of existing hardware and software and still incorporate newer technologies for the price/performance benefits.

## Slide 39: Demo: Wireless Communications Test System
Test Head
Test Receiver
(UUT)
2.4 GHz
900 MHz
NI-8350 (PCI)
GPIB Power Supply
PXI 4060
PXI MXI-4
VXI-USB
VXI RF Signal Analyzer
PXI 2592
PXI 4551
PXI 4552
MXI-4
USB
Power for UUT
Notes: In this example wireless communication hybrid test system, the user is able to control PXI, VXI, and GPIB from a high performance PC. The buses are interconnected through MXI-4 to control PXI, the VXI-USB to control VXI, and GPIB. This allows users to take advantage of existing and specialized instrumentation with the GPIB power supply and VXI RF signal analyzer, but also integrate the newer PXI instrumentation.

## Slide 40: Hybrid ATE Summary
Use the five layer architecture
  Understand interfaces
  Carefully select or build components
Keep PC and PXI in the center
  Best PC interface connectivity
  Best instrumentation connectivity
Streamlines system transition and maintenance
Maximizes return on investment in existing software and hardware
PASS
FAIL
UUT
UUT
UUT
UUT
Notes: In summary, hybrid ATE systems allow developers to create test systems that streamline for system maintenance and transition and allow users to maximize investments in existing hardware and software. By using a five layer architecture, system developers create a system that can handle interconnecting multiple buses and extend and grow with needs. It is important to understand the various interfaces to interconnect buses and to carefully select components within the system. When designing the system, keeping the PC and PXI in the center provides the best connectivity options to PC interfaces and instrumentation.

## Slide 41: Questions?
Notes: <number>
<footer>
<date/time>
Def. push everyone to the web for additional information (free eval, white paper etc)– here, you can ask if you missed anything, if they need more information, follow-up from the engineer, a customer education course etc…
© National Instruments Corporation Acquire, Analyze, and Present with LabVIEW Seminar