## Slide 1: Increasing Test System Connectivity and Productivity with Measurement and Control Services

## Slide 2: Outline
Hybrid ATE Systems Overview
Measurement and Control Services
Configuration
Diagnostics
Drivers
Demonstration
Benefits
Summary

## Slide 3: Hybrid ATE Systems Overview
A hybrid system combines components from multiple ATE platforms
  Streamlines system transition and maintenance
  Protects investment in existing software and hardware
  Allows easy integration of advances in ATE system development
Layered architecture is important
Multiple hybrid topologies are available
Notes: Hybrid ATE systems provide developers with a long-term ATE system that can evolve with short commercial technology lifecycles. Hybrid ATE systems take advantage of a 5 layer architecture to increase reusability, connectivity, extensibility, and module replacement.
By following the layered architecture, you create a test framework that allows you to replace and/or add components without having to re-architect the system. By clearly defining the system, you can take advantage of multiple buses using a variety of hybrid topologies. This allows you to meet multiple needs – protect the investment in existing hardware and software while being able to integrate the latest technologies.

## Slide 4: Five Layer ATE Architecture
- TestStand, DIAdem
System Management
- LabVIEW, LabWindows/CVI, C++
Application
- VISA, LV PnP, IVI, MAX, DAQmx
Measurement and Control Services
- PXI, VXI, Desktop PC, GPIB
Computing
- Instruments, Data Acquisition, Vision, Motion
Device I/O
Notes: Moving from the bottom up, we’ll start with the actual hardware devices that you use to perform testing and automation. This layer includes the various instruments and data acquisition used in your system. Developers want to choose the devices that meet measurement needs and also scale with changing system needs. Oftentimes, the devices used will require multiple instrumentation buses. The computing layer above refers to the instrumentation buses used and the method and topologies that connect these buses. Users should choose a topology that meets timing and synchronization needs, allows them to protect investment in hardware, and add new components to benefit from advancing technologies. The measurement and control services is the layer that integrate the hardware with the software. It provides configuration utilities, soft front panels, and drivers with APIs to ease programming. With tight integration with the application layer, these APIs should appear as a seamless part of the application development environment. The application layer refers to the software used to create the test programs. For instance, developers might create a program to take a measurement with a DMM and another program to generate a signal. The system management layer allows users to call these programs, manage various user levels, log and manage data, and generate reports.

## Slide 5: Issues For System Developers
Longevity: Test platform lifecycle versus test system lifecycles forces mid-life upgrades
  Preserve equipment in hardware and software
  Streamline system maintenance
    Replacement
    Upgrades
Integration with latest technologies
  PXI
  PCI
Best System for
Measurement
Needs
Preserve
Investment in
Hardware and
Software
Streamline
System Upgrades
and Maintenance
Integrate Latest
Technologies
Notes: System developers want to design the best test system for their UUT measurement needs. A large part of creating the best test system is designing one with longevity - with the ability to preserve their investment in hardware and software as well as streamline the processes for maintenance and upgrades. In addition, a good test system provides the developer with the ability to build on top of their test system by integrating the latest technologies.

## Slide 6: Measurement and Control Services
Connectivity
  Seamless connection to numerous I/O devices
  Integration of various instrumentation platforms
Configuration and Diagnostics
  View and test both hardware and software components
Simplified Programming
  Tight integration with application development environments (ADEs)
  Provide high-level interfaces for simplified system development
Notes: Measurement and control services play an important role by providing connectivity to the many types of hardware in the system, configuration and diagnostic tools as well as simplified programming. The measurement and controls services allow you to connect to multiple devices of different buses and integrate them into one system. In addition, they should enable you to view test hardware and software, configure them, and test them for diagnostic purposes. By providing tight integration with application layer through power application programming interfaces (APIs), developers should be able to easily program their instruments.

## Slide 7: Measurement and Control Services
Benefits
Separate hardware and software when debugging
Aid in replacement
Help in planning for longevity
Measurement and Control Services
Configuration
Manager
Measurement and Automation eXplorer
Application Development Environments
Diagnostic Tools
NI-Spy, GPIB Analyzer
Instrument Drivers
LabVIEW and CVI Plug and Play, IVI
APIs
NI-VISA, NI-488, NI-VXI, NI-DMM, IVI
Driver Engine
VISA, GPIB, VXI
Notes: The Measurement and Control Services Software plays a critical role in delivering the key benefits of a modular computer and networked-based measurement system. The components of this software – hardware drivers, flexible high-level application programming interfaces (APIs), and a configuration manager – must all integrate within the application development environments (ADEs) to attain maximum system performance and development productivity. The specific tasks of the Measurement and Control Services include integration of measurement devices, as well as local and distributed configuration and programming of the measurement devices.

## Slide 8: Measurement and Control Services
Configuration Managers
  Graphical, hierarchical view of system
  Test system software to connect, configure, and control hardware and software components
  Simple interface to confirm drivers and hardware are functioning properly
Diagnostic Tools
  Distinguish between hardware and software issues
  Trace application calls
  Provide return codes and parameters for each call
Notes: Configuration managers allow users to see the hardware in the system and verify in they are connected properly. This allows users to confirm proper installation etc before starting to program the system. In addition, users can also use the configuration manager to perform some initial configuration to simplify programming.
Diagnostic tools help the user to distinguish between hardware and software issues by tracing applications calls and providing the return codes in an interactive manner.

## Slide 9: Measurement and Automation eXplorer (MAX)
Configuration for hardware and software
View devices connected to your system
Create and edit channels, task, and interfaces
System diagnostics
Notes: Measurement & Automation Explorer (MAX) provides access to your National Instruments CAN, DAQ, FieldPoint, GPIB, IMAQ, IVI, Modular Instruments, Motion, NI Switch Executive, VI Logger, VISA, and VXI devices. With MAX, you can:
Configure your National Instruments hardware and software
Create and edit channels, tasks, interfaces, scales, and virtual instruments
Execute system diagnostics
View devices and instruments connected to your system
Update your National Instruments software

## Slide 10: Diagnostic Tools
NI-Spy
Monitor and capture application calls to NI-VISA, NI-488, NI-VXI, IVI class drivers, NI-Scope, NI-DMM, and NI-Switch
Displays return code and parameters for each call
Highlights failed calls
GPIB Analyzer
Requires GPIB+ card
Monitor, capture, and participate in bus activity
Capture and display data
  Data transfers
  Command transfers
  Control line transitions
Highlight specific transactions
Flexible pattern-search utility to locate bus patterns
Notes: NI-Spy and the GPIB analyzer provide two ways to monitor application calls for debugging purposes. By displaying the return codes and parameters, users can separate hardware and software issues.
NI Spy is a valuable troubleshooting utility program that ships with the Win 32 versions of NI-488.2, NI-VXI and NI-VISA. With this tool, you can capture all function calls that your application makes into the following APIs: NI-VISA, NI-488, NI-VXI, IVI class drivers, NI-Scope, NI-DMM, NI-Switch, and more.
For each call, you can see its return code and verify the parameters. Failed calls are highlighted in red to make them easy to locate during your development. Detailed information includes contents of data buffers, time stamps, process IDs, and thread IDs. You can quickly debug multithreaded test applications. You can also save this information to a file or print out a hard copy.

## Slide 11: Software Architecture
Driver
Software
(*.DLL)
Instrument
Driver VIs
NI-VISA
ADEs
Diagnostics Tools:
NI-Spy
GPIB Diagnostic Tool
Configuration Tools:
Measurement &
Automation Explorer
Interface
(PXI, VXI,
GPIB, computer based, etc.)
Notes: <number>
<footer>
<header>
<date/time>
Underneath and between the different hardware components are the software components that are the heart of your instrumentation system. The figure above shows the software architecture for Windows 2000/XP from the perspective of the computer.
The instrument is connected to the computer through a built-in connector such as RS-232 or an installed interface board such as GPIB or VXI/MXI. Driver-level software for instrument is in the form of a Dynamic Link Library (DLL). In the example shown in the figure above, LabVIEW is the high-level application software layer. LabVIEW includes built-in functions for GPIB, serial, VXI, and computer-based instruments that load and use the installed driver software.
As with all Windows device drivers, any DLLs you install for interface boards will also interact with the Windows Registry so that resources such as base addresses, interrupt levels, and DMA channels can be assigned. Configuration and diagnostic software tools are also available with National Instruments hardware.

## Slide 12: VISA (Virtual Instrument Software Architecture)
GPIB
VXI
Serial
PXI
VISA
Platform independent
Interface independent
VISA is the backbone of the IVI and Plug & Play Instrument Drivers
Must know SCPI command set to program directly with VISA
Provides bus and controller interchangeability
Notes: For many years, industry has moved toward purchasing instrumentation from a variety of vendors. This allows engineers to select the best possible equipment for their applications without being locked into a specific vendor. This trend required the definition of hardware standards to ensure the compatibility between different modules. This was one of the factors leading to the development of the VXI specification. But even with these improved hardware standards, a system was time consuming and expensive to put together. Successful integration of a multivendor system requires all hardware and software products work together, eliminating system-level compatibility issues for end-users. VISA is the underlying layer of function calls used in the LabVIEW instrument driver VIs to communicate with the driver software.

## Slide 13: Instrument Drivers or Direct I/O?
Direct I/O: Use I/O libraries with Read() and Write() functions to send commands directly to the instrument.
Instrument Drivers: Driver function calls are made directly from the application
More Control and (Possibly) Higher Throughput
Simpler and Faster Application Development
Instrument Driver
Application
Vendor API
VISA
Hardware Driver
Instrument
Application
Vendor API
VISA
Hardware Driver
Instrument
Notes: <number>
<footer>
<header>
<date/time>
Users can choose between direct I/O and instrument drivers to communicate with their instruments.
Direct I/O uses I/O libraries with Read() and Write() functions to send SCPI Commands directly to the instrument. This requires the users to learn the operations of the specific I/O library and the SCPI language of the instruments. This makes programming more difficult, and users should use direct I/O when they need functionality not provided through the instrument driver or when the system requires extra control or the absolute highest throughput.
Instrument drivers provide an extra layer to simplify instrument programming. Instrument drivers are very helpful for people who are unfamiliar with their instrument and have less programming experience. Users benefit from a built-in hierarchy for the functions, visual programming panels, and context help. Users can call the instrument driver functions from the application development environment.

## Slide 14: Using Direct I/O
Use I/O libraries with Read() and Write() functions to send commands directly to the instrument.
Use direct I/O if:
  You have extensive instrument programming experience or access to programming experts
  You need to use instrument features not supported by the available drivers
  You need the absolute maximum in system throughput
  You need to control the exact configuration of the instruments in your system
  You have a large volume of legacy code
Notes: <number>
<footer>
<header>
<date/time>
Direct I/O is the choice when the assistance in programming the instrument provided by instrument drivers is either unnecessary or unavailable due to the choice in programming environment.
Very rarely, the performance of an instrument driver can be a limiting factor. This is pretty rare because modern PC processors are much faster than the fastest I/O bus, so the processing time of turning a driver command into SCPI direct I/O to the instrument is usually not a critical performance factor. Instrument drivers can actually improve performance for novice programmers by using the instrument in the most efficient way.
Direct I/O typically gives more flexibility than drivers. The full SCPI command set of the instrument is available, whereas drivers sometimes have less than complete coverage and do not permit every possible legal SCPI command, such as concatenating multiple SCPI measurement commands into one I/O transaction, which would amortize I/O latency across multiple commands rather than incur the latency cost with each command.

## Slide 15: Instrument Drivers
Provide a high-level, easy-to-use programming model
Access to instrument capabilities through an intuitive application programming interface (API)
Based on open standards like VISA, Plug & Play, and IVI
Use an instrument driver if
  It works in the desired Application Development Environment
  It supports the majority of instrument features you want to use
  You want instrument commands that are organized in a hierarchical structure - IntelliSense
  You want to quickly start using an unfamiliar instrument
Notes: <number>
<footer>
<header>
<date/time>
Since modern development environments can provide a lot of contextual help and assistance for using instrument driver software, the programming experience is usually better with instrument drivers than with direct I/O.
Instrument drivers are the best choice for programmers who need and can take advantage of that extra assistance, meaning they have not memorized the SCPI syntax of the instrument and they are in a programming environment that can turn the software information provided by a driver into concrete help and assistance like IntelliSense or visual panels.
They should be based on open standards like VISA, Plug& Play and IVI to give the system maximum flexibility to meet upgrade and replacement needs in the future.

## Slide 16: Instrument Drivers
Plug and Play Drivers (LabVIEW and CVI)
  Use VISA for bus and controller interchangeability
  Include native LabVIEW or CVI source code
  Widely available
IVI (Interchangeable Virtual Instrument)
  Standard instrument driver programming interfaces for common classes of instruments
  Instrument interchangeability
  Consistent API
Notes: There are two common classes on instrument drivers – Plug & Play and IVI.
VISA-based Instrument Drivers insulate the driver from the underlying bus -NI-VISA supports GPIB, Serial, Ethernet, USB, PXI, VXI.
LabVIEW or LabWindows/CVI Plug & Play Drivers use VISA for bus interchangeability and include native LabVIEW or CVI source code.
Certified LabVIEW or CVI PnP Drivers are similar in style, organization, and API to help eases instrument replacement.
The goal of IVI is to reduce the overall cost of test and increase test system longevity by defining standard instrument driver programming interfaces to common classes of instruments. It provides a common API for a class of instruments (like DMM, Scope, etc) so that instrument interchangeability is possible.

## Slide 17: Instrument Driver Considerations
ADE support
Instrument functionality coverage
Vendor reliability & support (documentation, online, phone)
Programmers experience
Performance (speed)
Complexity (API, instrument, task)
Based on open standards (VISA, VXI P&P, IVI)
Notes: When evaluating which instrument drivers to use, there are some considerations to factor in. Users should ensure that it supports the various ADEs that might be used as well as provides good coverage of the instrument functions needed. Another evaluation point is the reliability and support for the driver – if the vendor provides additional resources like documentation as well as online and phone support. Users will also want to factor in which instrument driver best supports the programming experience and performance and complexity needs of the user.
The user should also look for an instrument driver that is based on an on open standard like VISA, VXI Plug&Play or IVI to maximize the flexibility of the test system.

## Slide 18: Planning for Replacement Needs
Plug and Play Drivers
Controller replacement
  Use a VISA based driver
Instrument replacement
  Encapsulate instrument driver calls
  Develop separate VIs or functions for controlling each instrument
  Modify only these VIs or functions when replacing an instrument
IVI
Instrument replacement
  Avoid using instrument-specific features
  Replace with an instrument of similar capabilities
Notes: Use Plug & Play and IVI drivers to help plan for the test system longevity needs. These drivers help make controller and instrument interchangeability simpler and possible.
With Plug & Play drivers, bus and controller interchangeability is easy and seamless when using a VISA based driver. For instrument drivers, users should encapsulate instrument driver calls and develop separate VIs for controlling each instrument.
With IVI, instrument replacement is one of the direct benefits of using IVI drivers. For instrument interchangeability to work, users should avoid using instrument-specific features and replace instruments with ones of similar capabilities.

## Slide 19: Demo: Wireless Communications Test System
3D Power Spectrum, Occupied Bandwidth, Auto Find (LabVIEW)
TestStand
MAX, VXI ResMan, VISA, IVI and PnP Drivers
PCI (NI-8350), PXI MXI-4, VXI-USB, GPIB
2.7 GHz PXI RF Signal Analyzer, 8.5 GHz VXI RF Signal Analyzer, PXI DMM, PXI Switch, GPIB Power Supply
Notes: For a wireless communications system, you can see how the layers work together to integrate the buses for this test application. Through the architecture the user can integrate VXI and GPIB instruments with some newer PXI instruments. This allows the user to take advantage of existing hardware and software and still incorporate newer technologies for the price/performance benefits.

## Slide 20: Demo: Wireless Communications Test System
MAX sees all devices in the system
IVI driver for GPIB power supply allows instrument replacement
Plug&Play driver for VXI RFSA allows controller replacement
Configuration Manager: MAX
ADE: LabVIEW
Diagnostic Tools: NI-Spy
VXI RFSA:
LV Plug&Play Instrument Driver
PXI RFSA, DMM, and Switch:
NI-DMM, NI-Switch, and NI-RFSA
GPIB Power Supply:
IVI Instrument Driver
Notes: The developer uses MAX to survey the whole system and see all of the hardware on the system – VXI, GPIB, and PXI instruments. Through MAX and VXI ResMan, the user can run some initial diagnostics to make sure the instruments are properly installed. From there if additional analysis is needed, the user can trace application calls using NI-Spy. To program the instruments in the application development environment, the developer uses the Plug&Play driver created for the VXI instrument. By using a VISA based Plug&Play driver, if the VXI control method were changed (like from the VXI-USB to MXI-2), no software changes would be required. For the PXI instrumentation, the developer can use the NI-DMM, NI-Switch, and NI-RFSA drivers provided to talk to the instrumentation. For the power supply IVI can be used so that instrument replacement is pretty simple.

## Slide 21: Hybrid ATE Summary
Use the five layer architecture
  Streamlines system transition and maintenance
  Maximizes return on investment in existing software and hardware
Measurement and control services provide connectivity to various buses and configuration and diagnostic tools
Use instrument drivers over direct I/O unless functionality is not supported or maximum control is needed
Use instrument drivers based on VISA, Plug&Play or IVI for longevity needs
PASS
FAIL
UUT
UUT
UUT
UUT
Notes: To summarize, when designing hybrid test systems, it is important to use the layered architecture to streamline maintenance and maximize investments.
Measurement and control services provide developers connectivity to the various buses available as well as configuration and diagnostic tools to interact with will of their instruments. Typically, developers should use instrument drivers over direct I/O unless there is a specific, required functionality that is not available with the instrument driver. Using instrument drivers based on VISA, Plug&Play, and IVI is best when planning for longevity needs.

## Slide 22: Questions?
Notes: <number>
<footer>
<header>
<date/time>
© National Instruments Corporation Acquire, Analyze, and Present with LabVIEW Seminar