## Slide 2: Lower Your Cost of Development Throughout the Design Cycle
John Limroth
NI Consulting Services

## Slide 3: Control Design Cycle: The “V Diagram”
System Testing
System Definition
Targeting
Rapid Prototyping
Hardware-in-the-Loop Testing
Notes: In this presentation we will discuss the role of simulation software, real-time systems and data acquisition in dynamic test applications. Traditional testing is referred to as “static” testing where functionality of components is tested by providing known inputs and measuring outputs. Today there is more pressure to get products to market faster and reduce design cycle times. This has led to a need for “dynamic” testing where components are tested while in use with the entire system – either real or simulated. Because of cost and safety concerns, simulating the rest of the the system with real-time hardware is preferred to testing components in the actual real system.
The diagram shown on this slide is the “V Diagram” that is often used to describe the development cycle. Originally developed to encapsulate the design process of software applications, many different versions of this diagram can be found to describe different product design cycles. Here we have shown one example of such a diagram representing the design cycle of embedded control applications common to automotive, aerospace and defense applications.
In this diagram the general progression in time of the development stages is shown from left to right. Note however that this is often an iterative process and the actual development will not proceed linearly through these steps. The goal of rapid development is to make this cycle as efficient as possible by minimizing the iterations required for a design. If the x-axis of the diagram is thought of as time, the goal is to narrow the “V” as much as possible and thereby reduce development time.
The y-axis of this diagram can be thought of as the level at which the system components are considered. Early on in the development, the requirements of the overall system must be considered. As the system is divided into sub-systems and components, the process becomes very low-level down to the point of loading code onto individual processors. Afterwards components are integrated and tested together until such time that the entire system can enter final production testing. Therefore the top of the diagram represents the high-level system view and the bottom of the diagram represents a very low-level view.

## Slide 4: V Diagram – 1. System Definition
Specify requirements of control system based on needs. All functionality and performance requirements should be included.
Notes: We will now examine each of the steps of the diagram in detail, including the tools often used be engineers to complete each task. In the “System Definition” step, the needs and requirements of the system are often documented using word processing software, spreadsheets, etc.

## Slide 5: V Diagram – 1. System Definition
ECU Design
Engine Model
Notes: For each step we will also show an example diagram to illustrate conceptually how the tasks are carried out.
This diagram illustrates a greatly simplified view of a design of an Electronic Control Unit (ECU) for control of an automobile engine. Here you see the general representation of a feedback loop to represent the many signals communicated to and from the ECU to the engine. The system definition often includes a block diagram representation (more specific than the one shown here) to represent the required functionality of the ECU design.

## Slide 6: V Diagram – 2. Rapid Prototyping
Develop all algorithms needed to meet requirements and implement prototype controller. Test input/output characteristics and validate prototype with real system.
Tools
  Simulation software
  Real-time system with I/O for prototyping
  Data acquisition software and hardware
Notes: Often early on in the design process it is necessary to develop prototype controllers to test basic ideas and concepts in an actual system. For example an automotive controller may need to be tested in an actual vehicle after the algorithms have been developed and simulated in software.
As the design is developed, simulation software is often used to simulate both the control design as well as the rest of the actual system. In order to test these systems, the simulated design must be run on a real-time system to provide the prototype that can be used with an actual system.
To develop accurate software models for simulation, data acquisition systems may be used to measure parameters of the actual physical systems. In addition, data acquisition systems are used to help analyze prototype controllers tested in the actual system.

## Slide 7: V Diagram – 2. Rapid Prototyping
ECU Design
RT
Real Engine
Notes: This diagram shows conceptually the rapid prototyping process applied to the engine ECU design example. In this case the engine design must run on a real-time system to provide the prototype. Now the simulated engine may be replaced with an actual automobile engine that is interfaced to the control prototype for testing purposes.

## Slide 8: V Diagram – 3. Targeting
Generate code for target processor from validated control algorithms. Coding may be done by hand or by using automatic code generation tools.
Tools
  Automatic code generation
Notes: After a design has been prototyped and verified, the actual code must be deployed on the final production target processor. This is often a time consuming task since often simulation software tools are designed to provide a very high-level block diagram representation and target processors require C source code for use with a compiler specific to that target. Traditionally this has been done by hand, but now many automatic code generation tools have been created in an attempt to automate the process.

## Slide 9: V Diagram – 3. Targeting
ECU Design
Engine Model
Real ECU
Notes: This diagram represents the transition from the ECU design to the actual code to be run on a production ECU.

## Slide 10: V Diagram – 4. Hardware-in-the-Loop Testing
Test and validate actual controller against a simulated system on real-time hardware.
Tools
  Simulation software
  Real-time system with I/O for prototyping
  Data acquisition software and hardware
Notes: The idea of HIL testing is similar in concept to rapid control prototyping in that part of the system is simulated while connected to the rest of the real system. In this case the real portion is the actual controller and it’s associated hardware and the simulated system is the rest of the system being controlled. Often it is impractical or even impossible to test the controller with the real physical system. For example in today’s environment of rapid development the controlled system may not even be fully realized at the time that the controller needs to be tested.
For these reasons simulation software and real-time systems are required to simulate the physical system for HIL testing of the controller. In addition data acquisition may be used to characterize the physical system and take measurements during testing of the controller with the simulated system.

## Slide 11: V Diagram – 4. Hardware-in-the-Loop Testing
Real ECU
Engine Model
RT
Notes: In this diagram the simulated ECU design has been replaced by the actual ECU. In order to dynamically test the ECU, the engine signals and dynamics must be simulated with a real-time system.

## Slide 12: V Diagram – 5. System Testing
Test and validate controller with actual system. Verify all system requirements and then proceed to production testing.
Tools
  Data acquisition software and hardware
Notes: Finally when all the individual components and subsystems have been tested and validated, they must be combined to form the complete system. The overall system must also be tested and validated against the original design requirements.

## Slide 13: V Diagram – 5. System Testing
Real Engine
Real ECU
Notes: This diagram represents the final system: the actual ECU controlling the real automobile engine.

## Slide 14: Example: Missile Flight Control Design
Test controller in actual missile
Define missile flight control requirements
Generate code for controller
Test prototype controller with real flight data
Test controller with simulated missile
Notes: The previous slides outlined the individual steps of the design process for an automotive engine ECU design. The same steps are used in the design process of many different industries including automotive, aerospace and defense. Here a second example illustrates how the same process applies to the design of a missile flight control system. This example highlights the need for HIL testing since testing an actual missile in flight leads to the obvious problems of cost and safety as well as logistical problems such as instrumentation.

## Slide 15: Example: Vehicle Active Suspension Design
Test microcontroller in actual vehicle
Define active suspension requirements
Generate code for microcontroller
Test prototype suspension controller in actual vehicle
Test microcontroller with simulated vehicle suspension
Notes: As a second automotive application, we will consider the design of active suspension system for an automobile. Typically this system involves a traditional passive suspension system augmented with an electro-mechanic actuator and an “active” control system.

## Slide 16: Hardware-In-the-Loop Simulation
Develop model of simulated system
  Complex, non-linear systems require lookup tables based on emperical data
  Simple systems can use mathematical models
Implement simulation in real-time
  Must provide deterministic, real-time performance
  Real I/O required to interface to controller
Notes: We will now use the vehicle active suspension design example as a case study for HIL testing. Obviously an accurate dynamic model of the physical system is required to produce valid results from HIL testing. Depending on the complexity of the simulated system, various techniques are used to develop models. Complex systems often require look-up tables based on measured data acquired from parts of the physical system to account for non-linearities. For example engine dynomometer tests may be performed to characterize the complex dynamic characteristics of a combustion engine. Often in aerospace applications wind tunnel tests must be performed to model flight dynamics of aircraft. Simpler systems such as our automotive suspension can be modeled based on physical principles of the dynamics of the system.
Once the physical system has been accurately simulated in software, the system must be simulated in a real-time system for HIL testing. The simulated system must have time-response characteristics identical to the actual system for testing results to be valid. This places constraints on the simulation software and requires a real-time operating system or environment to run the software. In addition, the real-time system must provide all of the physical input and output signals of the real system that are connected to the controller.

## Slide 17: Active Vehicle Suspension Application
Must test control/actuator against simulated suspension system
Notes: To model the vehicle suspension system, we will develop a mathematical model of the suspension based on principles of dynamics. In this case we wish to test a single actuator/controller of the active suspension system. Assuming that there is one actuator/controller pair per wheel, we can use one quarter of the vehicle as a simple model of the dynamics associated with a single acutator/controller.
A free body diagram of the quarter-car model is shown on the slide. The body mass represents ¼ of the vehicle’s total mass (less the wheels, suspension, etc.). The spring and shock absorber are the physical connection from the wheel to the body of the vehicle. The performance of the active suspension system will be determined by evaluating the vertical motion of the vehicle body x(t) in response to the input of the road surface on the wheel u(t).

## Slide 18: Transfer Function Model
Resulting differential equation for suspension model:
Transfer function:
Notes: We know from Newton’s laws of motion that the mass times the acceleration is equal to the sum of all forces acting on the body mass. The acceleration can also be represented as the second derivative of position. The force of the spring is the spring stiffness k times the difference between road height u(t) and body position x(t). The force of the shock absorber is the damping coefficient b times the difference between the rate of change of u(t) and the rate of change of x(t). The resulting differential equation describes the vertical motion of the vehicle (at least one fourth of it) due to the verying road height.
By a process referred to as a Fourier transform, we can represent the differential equation in an algebraic form by replacing derivatives with “s.” This results in a transfer function which relates the output x(s) to the input u(s) as a ratio of two polynomials. Simulation software can accurately simulate the dynamic response of the suspension given the transfer function.
Note that parameters of the system such as m, b and k may not be known exactly when developing the simulation. Testing actual components such as the spring or shock absorber may help produce a more accurate simulation. In addition the input/output characteristics of the physical system can be tested and compared to the simulation to validate the model.

## Slide 19: HIL Simulation in LabVIEW Real-Time
Notes: Traditional real-time systems usually require compiled C code to run the simulation. This causes additional work because the resulting real-time simulation must be tested to verify that it performs identically to the non-real-time simulation software. Because LabVIEW can be used both on a PC and on real-time targets, it is possible to run the same exact software within out the need for an intermediate language.
This slide shows a simple example of the simulated passive suspension system. In this case the road height input is measure with an analog input and the resulting position of the vehicle body mass is provided by an analog output. To dynamically test the actuator/controller of the active suspension control system, hydraulic actuators could be used to simulate the road height and body mass position.

## Slide 20: NI Software and Hardware
LabVIEW Real-Time
  PID Control Toolset
    Advanced Control Tools
Real-Time PXI
  DAQ, CAN, 3rd party hardware
Real-Time PXI
LabVIEW Real-Time Development System

## Slide 21: LabVIEW Real-Time
Graphical environment – Rapid development
Deterministic real-time performance
Built-in tools for custom control systems
Notes: <number>
<footer>
<header>
<date/time>
As a quick refresher, when you meet RT customers, the points that you should always key in on are the following…
The graphical development of LabVIEW delivers faster development.
This application is then downloaded to an embedded hardware platform independent from the Windows machine.
This provides reliable real-time performance with the dedicated processor.
By delivering an integrated HW/SW solution, NI provides a scalable platform with faster development.

## Slide 22: PID Control Toolset
Control Technology
  PID Control Toolkit
  Fuzzy Logic Toolkit
  Advanced Control Tools New in LabVIEW Real-Time 6.1
Works with all RT hardware
Notes: <number>
<footer>
<header>
<date/time>
Today’s emerging control technologies are easily implemented in your LabVIEW software control applications. These technologies, such as PID and fuzzy logic, can help you develop successful control applications using LabVIEW. In addition, the interfaces to data acquisition hardware permit you to directly implement these strategies with your controlled process.
Currently, the PID Control Toolset include built-in tools for PID Control, Fuzzy Logic, as well as advanced control tools to build custom control algorithms. While these tools are included with the LabVIEW Real-Time Module, they can be used with LabVIEW on Windows with standard data acquisition or FieldPoint hardware to create non-time-critical control applications. However, using the toolset by itself will not deliver real-time performance.
This presentation assumes you have limited knowledge of control technologies and so will cover the basics and how to recognize when they can be sold into opportunities. In a lot of cases, knowing when to talk to customers about this product proves to be more vital than how the product works.

## Slide 23: Advanced Control Tools
Design custom control algorithms
  Anti-lock braking system
  Simulate complex environments for testing
Based on transfer functions and equations
Analogous to functions in common simulation packages
Notes: <number>
<footer>
<header>
<date/time>
G-Sim VIs were not optimized for real-time performance. These VIs were written specifically to be deterministic.

## Slide 24: Real-Time PXI Performance
Moore’s Law
Performance
1999
PXI-8176 RT 40 kHz
2000
2001
2002
2003
2004
2005
Leveraging Commercial Technology in Real-Time System
Notes: <number>
<footer>
<header>
<date/time>
Applying Moore’s Lay to real-time systems
As opposed to VME

## Slide 25: Modular Hardware I/O
Motion
Vibration
Pressure
Temperature
Commercial-off-the-shelf hardware
Built-in connectivity to various I/O types
Additional support for 3rd party hardware:
  MIL-STD-1553
  Reflective Memory
  Telemetry/IRIG B
CAN
Notes: <number>
<footer>
<header>
<date/time>
The flexibility of Virtual Instrumentation allows you to develop control applications with the I/O of your choice. Incorporate the I/O you need to achieve precise measurements. Use software and hardware technologies to integrate multiple I/O devices in your application.

## Slide 26: Application Examples
Automotive
  Power Train Control
  Hybrid electric vehicles
Aerospace
  Flight control systems
  Vehicle simulators
Biomedical
  Muscle stimulators
Electronics
  Printer paper feeders

## Slide 27: Traditional Development Time
System Testing
HIL Testing
Targeting
Rapid Prototyping
System Definition

## Slide 28: Development Time with NI Tools
System Testing
HIL Testing
Targeting
Rapid Prototyping
Traditional Development Time
System Definition
LabVIEW Real-Time and PXI
LabVIEW Real-Time and PXI