## Slide 1
TestStand™ Hands-On
Kit Farrar
TestStand Support Engineer
Thurs Aug 17
10:15-11:30 a.m., 12:00-1:15 p.m. 1:45-3:00 p.m., 3:30-4:45 p.m.
Exhibit Hall (3C)
Notes: This hands-on seminar is designed to provide an introduction to TestStand, and demonstrate how TestStand will help you design high-performance, flexible, and maintainable test systems that empower you to test more products, faster, and at a much lower cost.
The presentation includes an overview of test executives and a discussion of the TestStand software architecture, highlighting the key features of TestStand which will drastically improve your test development. Hands-on exercises compliment the slide presentation and teach you how to develop and run test sequences in TestStand.

## Slide 2: Agenda
TestStand features
Hands-on exercises
TestStand architecture overview
Advanced features and demonstrations

## Slide 3: Strategic Test Challenges
Org Silos
Time-to-Market
Quality
No Reuse
Internal
External
Tester per Product
Margins
Notes: TM1E-<number>
Hands-On Programming with TestStand
<header>
<date/time>
Take a look at some of the challenges you face today. If you are involved in building test systems or managing test resources, you face a variety of challenges, both external and internal.
Externally, today’s competitive environment forces you to increase quality and decrease your time-to-market. At the same time, prices and margins are a constant battle, and the cost of test is a key issue. In summary, your need for test is increasing, and you have to figure out how to test more in the future – but in less time and for less money.
Internally, you also face a number of challenges. Different departments work independently of each other, and re-use is almost non-existent. Each product ends up with its own unique tester, and the proliferation of different testers is very expensive to technically support.

## Slide 4: Why Use a Test Executive?
Eliminate duplicate effort
Reuse test code
Achieve better enterprise connectivity
Implement more intelligent, efficient testing
Notes: TM1E-<number>
Hands-On Programming with TestStand
<header>
<date/time>
A Test Executive provides a framework for your test system – a hub for your tests. Standardizing on a test executive provides advantages in code reuse, test development effort, enterprise connectivity, and testing efficiency.

## Slide 5: Eliminate Duplicate Effort
Measurements
Configuring instruments
Test strategies
Test reports
Operator Interfaces
Analyzing results
User management
UUT tracking
Archiving results
Test flow control
Calibration
Data acquisition
Different for every product tested
Similar for every product tested
Test Executive
Notes: TM1E-<number>
Hands-On Programming with TestStand
<header>
<date/time>
You can divide the tasks performed by any test system into two areas. One set of tasks – including calibration, instrument control, acquiring data, and analyzing results – is different for each product you test. However, there is another set of tasks that is very similar or perhaps exactly the same regardless of what you are testing. These tasks include the operator interface, sequencing and branching engine, and test reporting. It is this set of tasks, the things that do not depend on the product being tested, that a test executive handles. Thus, a test executive helps you eliminate duplicate coding – you do not have to start over for every test fixture.

## Slide 6: Reuse Test Code throughout the Product Lifecycle
R&D
Manufacturing
Service
LabVIEW™
LabWindows™/
CVI
Visual C++
LV Test Exec
3rd Party Test Exec
In-house Test Exec
VB
TestStand
Measurement Studio™
Notes: By standardizing on a unified approach to test software development, your organization can share code among departments as new product designs flow through the production lifecycle. By using the combined efforts of an organization, products get out the door faster, and departments communicate better, improving the overall manufacturing process.
Any test strategy that is shared throughout an organization is destined for success. To make this happen, the test executive software you choose must be flexible enough to scale to meet the needs of each of these groups and integrate with a variety of different systems. It must call tests written in a variety of testing programs to support the needs of different departments, and it must have entry points for customizations particular to each specific part of your organization.

## Slide 7
Enterprise Connectivity
Servers
UNIX
NT
Web Browser
Corporate
Database
Oracle
SQL Server
Sybase
Measurement & Automation System
Measurement Devices
Measurement
Clients
TestStand
LabVIEW, Measurement Studio
Notes: Enterprise Connectivity has become a buzzword for many of today’s fast-growing organizations, but what does it really mean? With enterprise connectivity, you share data throughout an organization and make intelligent, informed decisions based on that data. For test and measurement, it means seamlessly integrating your database, statistical control, and Web-based systems with your test software. You might, for example, do run-time process control and pass data to and from a server database with your test fixtures, permitting you to view real-time statistical data and make informed decisions based on it. You can even take this one step further and build intelligence into the test software itself so that it makes run-time decisions to improve efficiency or change testing strategies.
National Instruments TestStand provides this level of integration. It is built upon our LabVIEW and Measurement Studio measurement tools and provides a seamless path for data straight from the product you are testing to your entire organization.

## Slide 8: Implement Intelligent Testing
Test several UUT on a single test stand
Make intelligent decisions at run time
Keep track of complex data
Use test results throughout the organization
Notes: As computers and computer software become more and more sophisticated, it becomes increasingly beneficial to use these tools to improve your testing procedures. Intelligent testing involves optimizing use of hardware, finding potential errors in test routines, and making adjustments while testing to improve efficiency.
With TestStand, you can implement testers that keep track of large amounts of complex data, share it throughout your organization, and make intelligent decisions at run time to improve efficiency or change test strategies. The result – test your products faster, more accurately, and at less cost.

## Slide 9: Test System Architecture Overview
Test
modules
Test
Executive
Instrument
Drivers
Instrument I/O
Test Management
services
Test Programs
TestStand
LabVIEW
CVI
IVI/VISA
Notes: The software of a typical test system is made up of a set of modular components. These modular components include the test management services, or test executive, which manages and sequences test programs, the test programs, which communicate with hardware to make measurements and implement analysis algorithms, and the Instrument I/O, which is made up of drivers to communicate with the actual hardware.
National Instruments TestStand sits at the top layer of test software, sequencing together tests, logging results, and making decisions based on test data.
National Instruments LabVIEW and Measurement Studio (LabWindows/CVI) are the two most popular development environments for creating test programs. They include libraries for communicating with hardware and analyzing and displaying results.
Intelligent Virtual Instruments (IVI) is the new standard for instrument drivers. IVI drivers are high performance and support interchangeability of instruments. For example, a test system written with an IVI-compliant driver can interchange oscilloscopes without requiring reprogramming of test code.

## Slide 10: Test Executive Development
Special requirements
Enterprise data systems (database and SPC)
Proprietary or legacy hardware
Lower development costs
More stable product
Maintenance and support
Economy of scale
Build?
Buy?
Notes: Most test executives in use today on production lines come from custom, in-house development groups. Many companies now realize that these custom-built test executives are very difficult and expensive to support and maintain. Often, companies are trapped when key developers involved in these custom projects leave or move on to other projects. In addition, in-house development teams sometimes spend millions of dollars designing and porting test management software frameworks to different operating systems and platforms instead of focusing their resources on testing products. Therefore, rather than build a system themselves, these companies now look to buy an off-the-shelf, “shrink-wrapped” product with standard technical support, training, and continuous upgrades and improvements.
Off-the-shelf products provide a more cost-effective solution but may lack specific features that are important in various systems. Manufacturing organizations each have their own operators with varying skill levels, and their own internal databases and tracking systems based on various formats, their own products with varying testing processes and execution models. They cannot ignore these specialized requirements.
For more information on the Build Versus Buy Comparison, download the white paper “Build Versus Buy: A Financial Comparison” from the TestStand Web page at ni.com/teststand

## Slide 11: Test Executive Development Costs
Custom operator interface
Execution engine
Interface to test languages
Result evaluation
User management
Reports (ASCII, HTML)
Database integration
Offline SPC analysis
Serial number scanning
Sequence loading
Test limit loading
Revision control
Development environment
Development Effort
Custom Test Exec
Development Time
TestStand
TestStand
Standard Features
Test Exec
Requirements
Notes: TM1E-<number>
Hands-On Programming with TestStand
<header>
<date/time>
Building a custom test executive can be daunting. Consider the operator interface, sequence development environment, database integration, and interface to test development languages; these are just a few elements that you must develop.
TestStand’s set of off-the-shelf features fulfills a large percentage of typical test executive specifications. Because each organization has different requirements for operator interface, reporting, and so on, TestStand really provides the core features and development framework. And because its architecture is specifically designed for customization, it has tools for providing the additional features needed to complete your specifications. The bottom line: TestStand saves you time and money by providing the core functionality you would otherwise have to design, code, maintain, and support yourself.

## Slide 12: TestStand Features
High-speed parallel sequence execution engine (multithreaded)
Advanced sequencing, looping, and branching
Call tests written most popular test languages
  LabVIEW, Measurement Studio, any style DLL
Automatic report generation (ASCII, HTML)
Logging results to a Database
Modular and customizable
Notes: Because it is a new product, TestStand is built around the latest software technologies, including Multithreading and ActiveX. The TestStand flexible framework gives the test developer the opportunity to customize almost every aspect of its execution and development environment. Designed based on six years of user feedback in the test executive business, TestStand has the features and flexibility you need.

## Slide 13: TestStand Hands-On
Let’s take a test drive

## Slide 14: Hands-On Exercise One
Creating steps in the sequence editor

## Slide 15: A Powerful Test Executive Engine
TestStand Engine
Multithreaded sequencing
Branching
Looping
Limit checking
Data allocation
Multilevel user access (login)
Focused on execution speed, flexibility, and long-term support/compatibility
Notes: The TestStand architecture is built around the TestStand Engine. The Engine handles such test executive tasks as sequencing, branching, looping, limit checking, data allocation, and user management. Optimized for speed it provides maximum flexibility and long-term compatibility.

## Slide 16: Compatibility with Many Test Languages
TestStand Engine
LV
LW/
CVI
DLL
VB
VC++
Delphi
Execute test programs
Step into test programs
Generate test program templates
Notes: In any test executive, it is important to use code from all of the leading test development languages. This gives test developers the freedom to develop tests in the environment they feel most comfortable and most productive. You also can make use of existing test code.
TestStand uses structures called adapters to communicate with different programming environments. A different adapter is used for each type of test program that you can call. Currently, TestStand ships with adapters for National Instruments LabVIEW and LabWindows/CVI, any standard C DLL, and any ActiveX server DLL. The DLL and ActiveX server adapters permit test development in Microsoft Visual Basic and Visual C++, Borland C++ and Delphi, or any programming environment that can create a DLL or ActiveX server.
TestStand achieves especially tight integration with the two leading test development environments – LabVIEW and LabWindows/CVI. With these adapters, you can step directly into LabVIEW or LabWindows/CVI code from a TestStand sequence for detailed debugging. In addition, you also can generate LabVIEW or LabWindows/CVI code directly from the TestStand Sequence editor for faster, more consistent test development.

## Slide 17: Interfacing with the Engine
ActiveX
Server
Custom Operator Interface
TestStand Engine
LV
LW/
CVI
DLL
VB
VC++
Samples in Source:
CVI
LV
VB
ActiveX
Client
Application Programming Interface
Notes: The most common component of any off-the-shelf test executive that is modified is the operator interface. If the operator interface is tightly coupled with the sequence execution engine, then changes to it may affect the engine. This presents a problem for maintainability and upgradeability; often, changes to the operator interface are lost when upgrading to a newer version of an off-the-shelf test executive.
TestStand prevents such headaches by completely separating the operator interfaces from the execution engine and the sequence development environment. In fact, in TestStand, the operator interface is a completely separate application.
The TestStand Engine is actually an ActiveX server. This means that it can export an application programming interface (API), or a set of functions, to use with any ActiveX client program that acts as an operator interface. For instance, one of these functions is GetSequenceFile. When called from an operator interface program, this opens a sequence file.
TestStand ships with three operator interfaces, provided in source code for you to modify in whichever language you are most comfortable.

## Slide 18: TestStand Variables & Flow Control
Share data between tests/sequences
Define expressions
  “loop until x > 1000”
  “if y=10, skip Step3”
Access/change variable information at run-time from other programming environments
Allows intelligent run-time decision making
Sequence A
Step 1
Step 2
Seq A
Locals
Notes: The TestStand engine is designed for advanced, intelligent sequencing. Paramount to this is providing a flexible framework for data sharing between steps of a sequence and different sequences. This shared data is accessible within TestStand sequences and even within the test code itself. TestStand also permits you to define expressions to operate on this shared data so that you can make complex comparisons at run-time. Making such comparisons is what gives you the ability to design an intelligent test station – one that can analyze data during testing and automatically adjust parameters to improve efficiency.

## Slide 19: TestStand Debugging
Allows debugging of test code in other environments
Communicates with test code environment through ActiveX automation
Allows direct debugging from the TestStand sequence (into C, Visual Basic, or LabVIEW code )
Notes: In any test system, problems within test code inevitably arise. Debugging an individual test step within its development environment is often inadequate; to fully reproduce a problem, all test steps must be executed in the same manner as in an actual test. Therefore, it is important to debug test code from the test executive environment. Because TestStand uses an ActiveX interface to communicate with test development environments, it supports direct debugging of test code from within the application. For example, you can step into a LabVIEW virtual instrument from a TestStand sequence, and TestStand automatically launches LabVIEW and permits you to single step through the VI’s source code.

## Slide 20: Hands-On Exercise Two
Variables, expressions, and debugging

## Slide 21: Advanced Features
Full customization
Database connectivity
Product family testing
Multithreaded execution
Distributed execution

## Slide 22: Configurable Development – Step Types
Results
Properties
Algorithms
Measurement
Hi Limit Low Limit
If (HL > MEAS > LL)
Then Result = PASS
Numeric Value Test
Arrays, numbers,
strings, etc
Limits, file locations,
UUT info, etc
Custom
Algorithms
User-Specified
Notes: With TestStand, you not only customize the execution of tests, but you also customize the sequence development itself by plugging in user-defined components and tools specific to your development environment. One example of this is the ability to design custom step types that return
user-defined data of any type. These step types also can have user-defined properties and make complex comparisons. By creating a custom step type, you avoid having to recreate this functionality in each test you build.

## Slide 23: Database Connectivity
TestStand can automatically log results to any ODBC database
Parameters can load at run-time from database
Database interaction can be customized via TestStand database step types
  No database programming required!
Notes: One of the most important functions of a test executive is logging results. Most companies at some point put test data in some sort of a local or networked database. TestStand directly integrates with any standard Open database connectivity (ODBC) database by handling direct data logging to the database. In addition, TestStand can query a database for certain test parameters at run-time. You can customize all of this to your specific requirements – without any low-level database programming!

## Slide 24: Configurable Execution – Process Models
Execution Engine
Process Model
Identify UUT
Generate Report
Load Limits
Update Database
Initialize
Shutdown
Call User Seq
Notes: Every test executive follows some sort of process model – it might scan a serial number, turn on certain instruments, run tests, and generate a test report. TestStand provides entry points in the execution model that you can replace with your own routines. You can replace the default identify unit under test (UUT) Callback with your own routine for reading a bar code.
For an even greater level of flexibility, TestStand gives you the ability to edit the process model itself, which is in the form of a TestStand sequence.

## Slide 25: Product Family Testing – Dynamic Limit and Step Loading
TestStand
Model A
Model B
Alimits.TXT
Blimits.TXT
Product.SEQ
1. Scan bar code to determine model
2. Upload appropriate limits
to sequence file
TestStand
Notes: It is often necessary to test several different products or different models of the same product on a single tester. TestStand makes this easy by allowing you to store limits and other pertinent parameters in a file and load them at run-time after you have determined the particular model type. In addition, with TestStand you can run subsequences dynamically, so that a sequence can determine run-time.

## Slide 26: Multithreaded Execution
Production
Test
Notes: With multithreading technology, you can execute multiple sequences in parallel to better use hardware and achieve more efficient testing. When multiple sequences are executed concurrently in TestStand, each sequence is run in its own thread. It is also possible to debug or abort one thread without affecting others that are executing.
For more information on TestStand multithreading, download Application Note 136: “Using Multithreading to Increase Test Throughput” from the TestStand Web page at ni.com/teststand

## Slide 27: Distributed Execution
UUT
UUT
UUT
Notes: TestStand distributed architecture permits you to run tests on remote machines. Using this client-server model, you can have a single computer sequencing through a series of tests and archiving results while each test is run on a different networked machine. With distributed architecture, you decrease test time and improve efficiency of a line by creating tests that pass information to each other over a network.

## Slide 28: Optional Hands-On Exercise
Using templates to create code modules