## Slide 1: Understanding and Performing System Calibration
Bob Conyne
Signal Conditioning Software Group Manager
Thurs Aug 17
10:15-11:30 a.m., 12:00-1:15 p.m.,
1:45-3:00 p.m., 3:30-4:45 p.m.
Exhibit (3D)
Notes: Welcome to our presentation on system calibration. Today we will examine how system calibration can improve the accuracy of your measurements.

## Slide 2: System Calibration Agenda
Calibration defined
Component vs. system calibration
Improving accuracy via system calibration
Hands-on system calibration
Notes: Specifically, we will address:
An overview of calibration
Comparison of component and system calibration
Using system calibration to improve accuracy
Hands-on system calibration exercise

## Slide 3: Calibration
The process of determining and adjusting
an instrument’s measurement uncertainty
Notes: Calibration is about accuracy – figuring out what it is, and making adjustments to improve it.

## Slide 4: Two Types of Calibration
Component calibration
  Consider each component as individual units
System calibration
  Consider entire system as a unit
  Compensates for other system errors
Notes: There are different levels of calibration.
Component calibration – consider each device as a separate unit.
Common examples of component calibration are internal calibration and external calibration.
System calibration – consider the entire system as a unit
With this, you can compensate for other system errors (cables, sensor, differences in each unit of a multi-device system).

## Slide 5: Component Calibration
Calibration from the vendor or at a metrology lab
Determines each component’s uncertainty
  Ensure component meets published specifications
  Required for traceability
With calibrated components, you can:
  Calculate system’s absolute accuracy
  Replace devices without affecting accuracy
Notes: Component calibration
Calibrate each component separately.
Note – Your system may only have one component.
Determine the uncertainty of each component.
When each component is calibrated, you are now free to:
Swap in and out any calibrated components without changing your system accuracy.
Move your system to other environments without changing your system accuracy.

## Slide 6: System Calibration
Often referred to as “end-to-end” calibration
Reduces system measurement uncertainty
  Cables, sensor, environment
Apply adjustments in software
Notes: System calibration considers the entire system as a single unit.
Also called an “end-to-end” calibration.
Quantifies all of the measurement errors in your system, and compensates for them in software.
Therefore, it reduces the overall measurement uncertainty.
Does not replace component calibration, but compliments it.
You can no longer replace components without performing another system calibration.

## Slide 7: Performing System Calibration
Apply a traceable source
Source
Source Value
Measurement
Take measurements across your input range
Create a compensation function (or use a lookup table)
Apply this compensation to all future measurements
Y = AX2 + BX + C
Notes: How do you perform a system calibration?
Apply a traceable source that can generate signal values across your desired input range.
  The source should behave like your signal will
  Example – Thermocouple calibrator
Record measurements for each known setting of the source
  Set the thermocouple calibrator to 100 degrees – measure 101 degrees.
  Set the thermocouple calibrator to 200 degrees – measure 200.5 degrees.
  You continue for as many points as you need (typically 10).
Create a correction describing this behavior.
Apply this function to all future measurements.
Result – your system has a smaller measurement uncertainty!

## Slide 8: Why system calibration?
What if I change a component?
Does it take into account the transducer?
Does it take into account cabling?
Steady state vs. time-varying correction
Notes: Some common questions:
What if I change a component? – it depends
1) if, after factoring in that component’s case uncertainty, you are still within the limits of your total acceptable uncertainty ...no need to recalibrate
2) if that component’s uncertainty could cause your total uncertainty to exceed your threshold...you must recalibrate
Does it take into account the transducer? – maybe. If you have the transducer and you can realistically exercise it across all expected values, then yes. Otherwise, you will have to use some sort of calibrator in place of the sensor.
Does it take into account cabling? – yes!
What is the best compensation strategy? – it depends
Table lookup – works best when your input signal bandwidth is very narrow. For example, if you know a priori that you expect a temperature measurement to be very close to 150 °C, you can take lots of measurements around that temperature so you can create a table that provides very precise measurements across a small range – say, 149 to 151 °C.
Polynomial – works best when signal bandwidth is very wide, such as when a temperature could have any value from 0 to 1000 °C. In this case, you would want to take measurements at a few key data points and characterize the compensation with a polynomial equation.
Steady state vs. time-varying – System calibration takes into account known system errors. Random noise cannot be accounted for with a system calibration.

## Slide 9: Why system calibration? (cont’d)
What is the best compensation strategy?
  Table lookup
    Useful when measuring only a few discrete values (e.g., 50 C and 400 C)
    Generally faster than using polynomial compensation
  Polynomial
    Useful when taking measurements across a wide range of values (0 C – 800 C)
    Usually 2nd-order and 3rd-order polynomials are sufficient

## Slide 10: Hands On Exercises - Overview
Hardware:
  PCI-MIO E-Series data acquisition board
  SCXI-1000 4-slot chassis
  SCXI-1112 8-channel thermocouple module with TC input jacks and onboard calibration reference
  J-type thermocouple simulator (0 – 500 F)
Software:
  LabVIEW 6i

## Slide 11: Hands-on #1 Component Cal
Create a virtual channel
Open Component_Cal.vi
Perform E-series self-calibrate
Perform SCXI calibrate
Acquire and present data
Notes: In this hands-on we’re going to perform a component calibration by calibrating the individual pieces of the system. We will be using Component_Cal.vi to examine the results of our calibration.

## Slide 12: Hands-on #2 System Cal
Open System_Cal.vi
Configure SCXI module
Acquire system cal data – create lookup table
Take data
Apply adjustments
Present data
Notes: In this hands-on we’ll use the system calibration utility to perform a system calibration. Note that we do a component calibration first.

## Slide 13: Summary
Calibration overview
Component calibration – traceability
System calibration – accuracy
Hands-on using software calibration tools
Questions?
Notes: Remember:
Component calibration is about traceability – it really has nothing to do with your specific measurement system.
System calibration is about accuracy – this can greatly reduce the uncertainty in your measurements.
Calibration tools – using software tools like the system calibration utility provides a straightforward means of calibrating across the measurement.

## Slide 14: For More Information…
Application notes
Manual calibration procedures
National Instruments calibration services
Tutorials
Third party calibration houses
ni.com/calibration
Notes: If you need more information, please visit our Web site.
We have various documents to help you, including:
Calibration procedures
Application notes
Tutorials
Contact information for metrology labs
Thank you for attending!