## Slide 1
Publishing Data Over the Web
Ryan Wright
LabVIEW™ Product Manager
Wed Aug 16
10:15-11:30 a.m., 12:00-1:15 p.m., 1:45-3:00 p.m., 3:30-4:45 p.m.
Exhibit (3E)
Notes: Welcome to NIWeek 2000. We are glad that you could attend this year.
Since the advent of the computer network, and more recently, the Internet, these technologies have grown largely in the business arena and have been confined to the IS domain. However, as software advances in its ability to harness networking and Internet technologies, measurement and automation systems are reaching the next level and further improving the efficiency of organizations throughout the world.

## Slide 2: Why Publish Data?
R&D
Manufacturing
Service
Customer
Increase productivity and quality
Notes: One of the ideas that is prevalent in the business community today is the idea of sharing data from one department to the other. For example, a typical business will export its sales bookings directly to the manufacturing which is responsible for automatic inventory handling and, of course, production. The same concept applies to an enterprise employing measurement and automation systems. National Instruments software has been used extensively in R&D facilities by design engineers for development and design verification. With products like TestStand, software has made its way to the manufacturing floor in areas such as production test. Information sharing between these two distinct departments and across an enterprise can bring about more efficient and productive departmental interactions to reduce time to market and improve quality of products. For example, if manufacturing sees that production yields are low, they can share that information with R&D to explore alternate designs or product components for better yields.
The whole goal of sharing information across an enterprise is to improve product quality and increase productivity. This concept of information sharing even extends beyond the boundary of the typical enterprise as businesses increasingly interact with other companies. Data sharing between enterprises can greatly enhance the productivity of all parties involved.

## Slide 3: Why Use the Web?
The Web enables information sharing
Notes: The key to this sharing of data between departments and entire enterprises is the computer network and more generally the Web. Internet technologies are ubiquitous today and development continues at an ever increasing pace. The enabling technology for information sharing is really much more than the physical medium that networks computers and systems together. Today, Ethernet is everywhere, permeating all industries and types of companies. However, it is really the software that unifies the different departments and organizations and makes it possible to share the data over the physical transmission media.

## Slide 4: Types of Information Sharing
Reports and Results
Data
Streaming
Measurement and Automation System
Information
Sharing
Notes: There are really two distinct types of information sharing within an organization. As pictured in this slide, they are reporting and gathering results and streaming data. In this presentation, we will discuss how they differ from one another and also look at some different methods for sharing both types of information.

## Slide 5: Reports and Results
Processed data
Template
Rigid
Reports and Results
Data
Streaming
Measurement and Automation System
Information
Sharing
Notes: Reports and results generally consist of compilations of processed data. Often, this data is presented by populating some sort of a template so that all data results have the same general format. This makes reporting and posting results somewhat rigid and static in nature. Generally, this means that in order to see different types of results, you must not only acquire new data, but you must also create a new type of report or template and populate it with the new data you wish to examine.

## Slide 6: Data Streaming
Raw, unprocessed data
Flexible
Reports and Results
Data
Streaming
Measurement and Automation System
Information
Sharing
Notes: Data streaming is inherently more flexible and dynamic than publishing reports and results. This is because data streaming implies that the information exchanged is the raw, unprocessed data that has been collected. It is up to the user to determine how and when to analyze the data to extract meaningful information. If additional information stemming from a particular set of data is required, then the user can simply develop a new method of processing the data and simply apply it to the same data set.

## Slide 7: Fundamental Technologies
Ethernet
Browsers
DataSocket™
Notes: Let’s examine some of the fundamental technologies that greatly enhance and simplify the information sharing process. First, we will talk about Ethernet – one of the most common physical media for data exchange today. Web browsers are nearly universal so naturally they play a significant role in information exchange. They have especially become more useful with the development of intranets or Local Area Networks where they serve as a common, shared interface for users on the network. DataSocket is a data sharing protocol developed by National Instruments for simplified data exchange in measurement and automation applications.

## Slide 8: Ethernet
High speed
Long distance
Widespread
Notes: Ethernet has long been a communication infrastructure for business and information technology applications. Until recently, most viewed it only as an information network. But its widespread adoption in corporate offices and manufacturing floors has earned it the reputation of being a viable solution for control and device data transmission.
Ethernet is a high-speed networking interface that can operate over a variety of media. The most common variations have been 10Base2, or thin wire Ethernet, where the communication signals are carried through a flexible coaxial cable, and 10BaseT, or twisted pair Ethernet, where the signal is carried through a cable consisting of a pair of twisted wires. The "10" in the designation indicates that the interface operates at 10 Mbits/s. One significant benefit of Ethernet is that it can span long distances – from 100 meters (twisted pair) to more than 2 km (fiber optic) and message latencies of under 5 ms. If you need to monitor and control a system over a long distance, Ethernet is an optimal choice.

## Slide 9: Browsers
Good for reports and results
Multi-platform
Literally everywhere
Free
Notes: We have already discussed how Web browsers have permeated the corporate arena because they are so universal and readily available. They are available for most common platforms today and are even available free of charge to the user. Naturally they have become a common interface for both intranet and Internet applications. The Web browser is an ideal tool for accessing and displaying reports and results.

## Slide 10: DataSocket
Optimized for data streaming
Language independent
URL-based
Three actors
  Publishers
  Subscribers
  DataSocket server
Notes: HO2C– <number>
Publishing Data Over the Web
<header>
<date/time>
DataSocket simplifies streaming data between different applications on one computer or between a host of computers on a network or across the Web. Although a variety of different technologies exist today to share data between applications, such as TCP/IP and DDE, most of these tools are not targeted specifically for streaming data like DataSocket.
DataSocket applications require three participants – a publisher, the DataSocket Server, and a subscriber. A publishing application uses the DataSocket API to write data to the DataSocket Server. The publisher writes the data to an identifier, or tag, formatted like a uniform resource locator (URL), which looks like a Web address. A subscribing application then uses the same DataSocket API to read data from that URL on the server. Both the publishing and the subscribing applications are “clients” of the DataSocket Server. These three participants can reside on the same machine or they can run on different computers. The ability to run these DataSocket components on separate machines improves performance and provides security by isolating network connections from your measurement and automation application. The DataSocket Server can broadcast live measurement data at high rates across your network or across the Internet to several remote clients concurrently. It simplifies your measurement application by automatically managing the connections to clients. Furthermore, the only factor limiting the number of clients you can have in your system is your network bandwidth.
Another major advantage of DataSocket is that it is language independent. This means that you use a variety of programming languages to create both publishing and subscribing applications. You can program DataSocket applications with LabVIEW, LabWindows™/CVI, Visual Basic, or simply use a standard Web browser.
Another benefit of DataSocket is that it can not only connect to URLs created by DataSocket clients, but it can also directly connect to files using FTP or HTTP.

## Slide 11: Reports and Results
Reports and Results
Data
Streaming
Measurement and Automation System
Information
Sharing
Notes: Now, let’s take a look at a number of reporting examples using various National Instruments products.

## Slide 12: HTML Reports
Processed data
Images, tables, bulleted lists, links
Readily available
Notes: HTML reports are especially beneficial because they can be viewed inside a Web browser. We have already discussed how prevalent browsers are today and how they make an excellent tool for viewing reports. A typical HTML report consists not only of data, but often contains images of measurement and automation application user interfaces, additional graphics, bulleted lists, tables, and even hyperlinks to other HTML pages. Another key benefit of HTML reports is that they can be posted to a Web server and then anyone can view the results at will. This means that you do not have to worry about the actual distribution of the reports – the interested parties simply visit a dedicated Web page and have access to the information they require.

## Slide 13: HTML Reports in LabVIEW
Notes: Let’s generate an HTML report by using LabVIEW’s built in report generation tools. In LabVIEW 6i, we have built on the existing NIReports framework so that you can not only create printed and text-based reports, but now you can create reports directly in HTML format. After we have generated our HTML report we will view it using Internet Explorer.

## Slide 14: HTML Reports in TestStand™
Notes: A nice feature of National Instruments TestStand is that it also contains the ability to present test results in HTML format with literally a click of a check box. We are going to create a test in LabVIEW that we will call in a TestStand sequence. Once we have completed our test sequence, we will compile the test results into an HTML report.

## Slide 15: Web Publishing Tool
Similar to HTML report
Text rich
Image of front panel
Notes: The new Web Publishing tool in LabVIEW 6i creates a very simple HTML report for you through a dialog window that lets you publish text in conjunction with an image of your VI’s front panel. Let’s take a look at how it works.

## Slide 16: Web Publishing Tool in LabVIEW
Notes: In this example, we will develop a simple VI and then use the Web Publishing Tool to publish the front panel and append text to the image of the front panel to create a simple HTML report quickly.

## Slide 17: Data Streaming
Reports and Results
Data
Streaming
Measurement and Automation System
Information
Sharing
Notes: We have already looked at some examples of how to generate reports and results. Let’s move now to streaming data and examine several different samples.

## Slide 18: Web Servers
Publish HTML documents and UI images
Cross-platform
Security
Notes: One tool that is particularly useful is a Web server. Web servers are beneficial because they present data in a format that is available on most of the common computing platforms. This means that you can publish data on a Web server that is running on Linux, for example, and a client machine running Mac OS has the ability to display the data. Web-based data sharing offers significant flexibility when it comes to computing platforms. Modern tools make embedding animation, graphics, and even sound into a Web page an almost trivial task. Plus, you can present simple to complex data using the hierarchical nature of hyper-text. Web servers also easily manage a large number of clients.
Some of National Instruments software development environments have built-in Web servers. In this case, little or no programming is required to publish application data on the Web. Generally Web servers also provide security features to selectively block or grant access to various client machines. Let’s take a look then at one such application that has a built-in Web server.

## Slide 19: Web Server in LabVIEW
Notes: HO2C– <number>
Publishing Data Over the Web
<header>
<date/time>
LabVIEW has a built-in Web Server that is functionally very similar to the Web Publishing Tool. Just like the Web Publishing Tool, the Web Server exports images of a VI front panel. One nice feature of the Web Server that makes it stream data as opposed to simply publish a static report is is ability to publish images of front panels that update periodically to display the current state of a VI front panel at user-definable intervals of time.

## Slide 20: DataSocket Revisited
Little or no programming required
Optimized for data streaming
URL-based
Notes: We have already discussed how DataSocket is designed for streaming data across the network or the Web. The nice thing about it is that is is quite painless to integrate DataSocket into your measurement and automation applications. We will now take a look at how you can publish and subscribe to your data with just a few mouse clicks as well as develop some simple applications that programmatically make use of DataSocket to stream data.

## Slide 21: DataSocket in LabVIEW
Notes: The first thing that we will do is develop a simple LabVIEW VI that publishes live data to the DataSocket server. We will do this simply by right clicking on a front panel object and choosing to publish the data. Then, we will open another VI and subscribe to the same live data. All this is done with just a few mouse clicks.

## Slide 22: DataSocket in LabVIEW…Again
Notes: Let’s go back to the previous example now and instead of using shortcut menus to publish and subscribe to our live data, we will programmatically integrate DataSocket into our application. Whether you use DataSocket programmatically or through menus, it is quite painless and requires little or not programming to stream data to the Web so you can publish your data quickly.

## Slide 23: DataSocket in Visual Basic
Notes: Let’s build upon our previous example by using our same VI to publish data from LabVIEW. Let’s create a subscribing application now in Visual Basic using National Instruments Measurement Studio ActiveX controls. Once again, we will subscribe to our data simply by selecting a few options in property pages.

## Slide 24: DataSocket in Visual Basic…Again
Notes: Let’s modify our previous example slightly now by subscribing to our data in Visual Basic programmatically rather than through property pages.

## Slide 25: DataSocket in a Browser
Notes: We can create another type of subscribing application by using Measurement Studio™ tools for Visual Basic and Visual Basic’s ActiveX control generation capabilities to embed a graph inside of a Web browser to view live data.

## Slide 26: Internet Toolkit
FTP
E-mail
CGI
Notes: Both LabVIEW and Measurement Studio have add-on tools for incorporating more advanced Web functionality into your measurement and automation applications. Not only do they allow you to publish user interfaces over the Web, but they add more sophisticated technologies, such as FTP, E-mail, and CGI capabilities.

## Slide 27: E-mail and FTP in LabVIEW
Notes: Let’s take a look at the Internet Toolkit in LabVIEW now by sending e-mail and using FTP to transfer a data file.

## Slide 28: Conclusion
Increase productivity through information sharing
Reports and results (processed data)
  HTML reports
  Web documentation
Data streaming (unprocessed data)
  Web server
  DataSocket
  Internet toolkit
Notes: The whole thrust behind information sharing is to make you and your organization more productive and efficient so you can decrease product time to market and produce higher quality products. Information is typically shared in two ways – through reports and results and through streaming data. Today, we have examined several examples of each type of information sharing and have shown you how to incorporate them into your measurement and automation applications. We hope that you will use what you learned today in your own applications to take your measurement and automation applications to the next level and boost your organization’s productivity.