## Slide 1: LabVIEW for Real-Time Control in Measurement and Automation
National Instruments LabVIEW RT and the RT Series Hardware
Notes: Using LabVIEW RT and a real-time RT Series data acquisition board, engineers and scientists can develop real-time and reliable data acquisition and control applications for measurement and automation quickly and easily. Real-time computer-based data acquisition and control applications are developed with the industry standard technologies of Windows, LabVIEW, and plug-in data acquisition boards. Real-time applications are created when customizable, complete LabVIEW RT programs are run on the independent processor of the RT Series plug-in data acquisition board.

## Slide 2: Agenda
Definitions
Real-time in measurement and automation
LabVIEW RT
Video

## Slide 3: Real-Time Definitions
Real-time does NOT mean real fast
Hard real-time - deadlines can not be missed
  Flight control
  Engine testing
Soft real-time - missed deadline acceptable
  Temperature logging
  Banking
More soft real-time applications than hard
Notes: Hard real-time systems have deadlines that must be met at ALL times and the system must behave deterministically. Events are prioritized and trigger responses in known manners. Failure to meet preconditions and deadlines means incorrect data is collected and the test is invalid. Or, failure to meet a deadline can have catastrophic effects like loss of hardware or human life. Hard real-time systems need determinism, not necessarily speed. They must also be stable and reliable. An example of a hard real-time application could be an engine dynamometer. In this type of application, failure to do the real-time control will yield bad data on engine performance, and can potentially damage equipment.
Soft real-time systems also require that conditions and deadlines be met. However, a soft real-time system will still function properly and yield usable data even if a small number of deadlines are missed. For example, logging temperature to disk once a second to look for a general temperature trend over a 10 minute period is a soft real-time system. If you fail to log one temperature in the 10 minute period, you will still see a general trend and still have a successful logging system.

## Slide 4: Real-Time Applications
Trending
Data reduction
Interrupt and response
Deterministic control
Notes: Real-time data acquisition applications can be divided into two board classifications - real-time data collection and real-time stimulus and response.
Real-time data collection is accomplished today using modern DAQ boards that have advanced on-board circuitry to bring in data continuously and in real-time. Examples include the National Instruments MITE controller chip that allows scatter-gather PCI bus mastering to allow for high bandwidth data transfer from DAQ board to the host PC. This real-time data collection frees up the host computer for analysis and display.
Modern computers can do a lot of processing. Therefore, trending and data reduction applications such as temperature monitoring and thermocouple linearization can be accomplished in real-time on a desktop computer system. Spectrum analysis applications like FFTs can also be executed in real time. As long as you can process and view the data at acceptable rates to the human eye, you are maintaining real time for your user interface.
In an interrupt and response type application, a user defined response is generated based on a process input. For example, if a pressure level gets too high, shut down the process. In deterministic control applications such as PID controllers, the ability to acquire, process, and respond continuously at precise time intervals is the real-time need. On most systems with plug-in DAQ boards, this decision step is when Windows is involved in the data analysis and limit your real-time performance.

## Slide 5: Typical Real-Time Applications
Hardware
LabVIEW RT
WindowsNT
WindowsNT
LabVIEW RT
Hardware
Milliseconds Microseconds
Mechanical Test
Telecom Test
Motion Control
Hydraulic Control
Business/POS
Medical
Network Control
H/W Loop
Simulation
Dynamic Signal Analysis
Industrial Automation
Engine Test
Internet
1000 100 10 1 100 50 10 1
Notes: It is the time constraint of when you must respond to events that dictates what tools you can use for your measurement and automation application. Windows can respond in real time within a few hundred milliseconds and as such can solve many real-time applications today. Products like LabVIEW RT or systems built with real-time operating systems can solve applications with faster real-time constraints. For very fast real-time responses, you must use dedicated hardware programmed with DSPs (digital signal processors), FPGAs (field programmable gate arrays), or custom ASICs.
As computer processors continue to increase in performance, more real-time applications can be solved with Windows or LabVIEW RT.

## Slide 6: Real-Time Challenges
Windows does not guarantee hard real-time
There are many real-time target platforms
Software integration is difficult
  Fixed or very limited programmability
  Closed and proprietary software development tools
Different development environments
  Real-time vs. non-real-time
  Time consuming
  Costly
Notes: Why can you not use Windows for all your real-time applications? Although many real-time applications are solved with Windows, you are not guaranteed your real-time response due to device driver scheduling and internal Windows functions like memory management. Also, some engineers are cautious of using Windows for fear the PC will crash or hang.
Because Windows is not suitable for higher speed real-time applications, engineers doing measurement and automation look to separate real-time controllers. Controllers come in a variety of hardware platforms and have the same variety in software development tools. Some controllers have fixed or limited programmability, while others are more programmable but have closed or proprietary development systems. Since these development environments are usually not the same measurement and automation application development environments used for the rest of the systems, integration of the real-time pieces can be difficult. Separate development environments mean more languages to learn, more development and debugging time, and more money spent.

## Slide 7: Industry Standards Come Together
+
Independent Real-Time
Processor
Notes: As the leader in computer-based measurement and automation, National Instruments now extends their industry-standard data acquisition hardware and LabVIEW development software to simplify the development and deployment of real-time applications. With National Instruments LabVIEW RT and the RT Series hardware, users can develop hard real-time applications using standard LabVIEW measurement and automation software, the industry-standard Microsoft Windows platform, and high performance off-the-shelf data acquisition hardware.
When LabVIEW and DAQ are combined with a real-time processor placed on an intelligent RT Series DAQ board, a LabVIEW RT application is created that provides deterministic, real-time behavior. You can now achieve real-time performance without leaving your standard measurement and automation tools.

## Slide 8: Industry Standards Come Together

## Slide 9: LabVIEW RT System Architecture
Host PC running
Windows NT/98/95
RT Series Board
RT Engine
RT Development
System
DAQ Daughter
Board
Processor
Board
RT Hardware Target
LabVIEW RT
Notes: A LabVIEW RT System consists of LabVIEW RT applications and a real-time hardware target. LabVIEW RT generates embedded LabVIEW code that run real-time on the hardware target. The first hardware targets are intelligent, processor-based RT Series DAQ boards that plug into a host computer. LabVIEW RT consists of two components – the RT Development System and the RT Engine. The primary functions of the RT Development System are to program and debug LabVIEW RT code, download programs to the National Instruments RT Series hardware, and provide a user interface. The RT Development System is a Windows NT/2000/9X application that runs on the host computer. The RT Engine runs on the processor of the RT Series hardware and executes embedded LabVIEW RT programs in real-time.
The National Instruments RT Series DAQ boards consist of two components – a processor board and a DAQ daughter card. Like a PC, the National Instruments RT Series processor board includes a CPU, standard PC chipset, BIOS, and RAM. Unlike a PC, the processor board does not have a disk drive, monitor, keyboard, mouse, or other standard PC I/O devices such as a serial or parallel port. Because the National Instruments RT Series board has no user interface and no disk drives, it must work in conjunction with a host computer for application development, debugging, data logging, user interaction, and so on. The National Instruments RT Series boards are available in two different plug-in platforms – PCI and PXI (CompactPCI eXtensions for Instrumentation).

## Slide 10: Development Steps
Step 1. Develop
Step 2. Download
Step 4. Deploy
Step 3. Debug
Target Hardware
Windows PC
Notes: Developing aLabVIEW RT real-time measurement and automation application is almost identical to developing a standard LabVIEW for Windows measurement and automation application.
Step 1. Develop your LabVIEW application
Step 2. Download the application automatically at run time, or with a pull down menu selection
Step 3. Debugging in LabVIEW RT is identical to LabVIEW. All debugging features like breakpoints, single stepping, and probes are supported to simplify development. Communication between the RT Development System and the embedded RT Engine take place automatically.
Step 4. Deploy the application. Most real-time applications developed with LabVIEW RT use LabVIEW RT as a distributed part of a larger measurement and automation system. In this architecture, a host computer will run a host LabVIEW program that provides a user interface, controls other hardware that is not time-critical, saves data to disk, and accesses the network. Real-time tasks are distributed to embedded LabVIEW RT applications running on the real-time hardware targets. Communication between the embedded LabVIEW RT applications and the host LabVIEW main application is through direct RT Series shared memory access, TCP/IP, or VI Server function calls.

## Slide 11: Standard LabVIEW Programming
Notes: A benefit to using LabVIEW RT is that is based on the same graphical programming paradigm of LabVIEW and NI-DAQ. Therefore, existing LabVIEW and DAQ users will now be able to create and deploy real-time applications without an in-depth knowledge of real-time programming.
LabVIEW RT applications are seamlessly embedded into real-time hardware targets automatically at run time, or with a simple menu selection. Rather than use a proprietary, text-based, hard-to-use development environment, LabVIEW RT gives you simple graphical programming, coupled with proven DAQ technologies, for a complete integrated solution. Using LabVIEW RT, you have the flexibility to create and download complete, customized graphical programs to your hardware target like a National Instruments RT Series real-time DAQ board, instead of being restricted to limited-functionality canned routines.

## Slide 12: Embedded Real-Time Performance
Notes: Embedding LabVIEW RT into an independent processor guarantees real-time operation from the host PC. An embedded LabVIEW RT application is not affected by host PC problems such as a crash providing reliability. A LabVIEW RT application will also survive a soft reboot.

## Slide 13: RT Series Real-Time DAQ Board
7030/6040E - 12 bit MIO
7030/6030E - 16 bit MIO
7030/6533 - 32 channel high speed DIO
486/133 MHz
8M DRAM for user programs
PCI
cPCI/PXI
Notes: The first hardware target for LabVIEW RT is a line of processor-based plug-in data acquisition boards called the RT Series. The RT Engine running on the independent processor on the RT Series board utilizes a Win32-compatible real-time operating system to ensure real-time deterministic performance. Also, this separate processor adds a degree of reliability to your measurement and automation system because LabVIEW RT applications continue to run even if the host PC crashes.
The three classes of RT Series real-time DAQ boards are the 16-bit multi-function I/O, 12-bit multifunction I/O, and the high-speed digital I/O board.

## Slide 14: Typical LabVIEW RT Applications
Notes: LabVIEW RT is used when you need real-time and reliable performance in your measurement and automation system. Some applications that these products are used for are engine simulation and control, engine testing with dynamometers, hydraulic servo control, control design and test, chemical process control, vibration testing, tablet pressing, aircraft fuel control, real-time torque control, machine condition monitoring and control, battery testing, flutter suppression of aircraft wings, fuel cell test, and semiconductor tool positioning.

## Slide 15: LabVIEW RT and RT Series DAQ
Familiar industry standard tools
  Windows
  LabVIEW
  Data acquisition
Real-time and reliability
  Independent processor
Flexibility and integration
  Complete programmability
Notes: National Instruments LabVIEW RT gets real-time performance by creating real-time and reliable applications that run on an independent processor. Embedded applications can survive host PC crashes. You have complete programming freedom to create highly flexible applications that are tightly integrated with real-time measurement hardware. This integration provides the highest degree of productivity and allows you to create scalable and portable solutions with faster development times and at lower system costs. Productivity is also increased because LabVIEW RT and the RT Series real-time DAQ boards uses industry standard technologies for development like Windows, LabVIEW, and plug-in data acquisition boards. Users are able to embed complete LabVIEW RT programs into the processors of the RT Series boards providing reliable, real-time performance.

## Slide 16: LabVIEW RT in Action
Video
Inverted pendulum
  Classic control problem