## Slide 1: LabVIEW™ for Real-Time Control in Measurement and Automation National Instruments LabVIEW Real-Time and RT Series Hardware
Notes: Using National Instruments LabVIEW Real-Time and RT Series hardware targets, engineers and scientists can quickly and easily develop real-time, reliable data acquisition and control applications for measurement and automation. Engineers and scientists create applications in the easy-to-use graphical environment of LabVIEW and run the applications on the RT Series hardware targets. Because each RT Series hardware target has a dedicated processor running a real-time operating system, the LabVIEW Real-Time application runs independently and reliably.

## Slide 2: Agenda
Real-time definitions and applications
Real-time challenges
Real-time in measurement and automation
LabVIEW Real-Time
RT Series hardware
Typical real-time applications

## Slide 3: Real-Time Definitions
Real-time does NOT mean real fast
Hard real-time–deadlines cannot be missed
  Flight control
  Engine testing
Soft real-time–missed deadline acceptable
  Temperature logging
More soft than hard real-time applications
Notes: One of the most common misconceptions about real-time is that it improves the overall performance of your system. While this is true in some cases, the true mark of a real-time system is the ability to respond to an event within a given period of time.
Real-time applications span over a wide spectrum in terms of performance. Hard real-time systems have deadlines that must be met at ALL times and the system must behave deterministically where events are prioritized and responded to within a known amount of time. Failure to meet preconditions and deadlines means incorrect data is collected and the test is invalid. Worst yet, failure to meet a deadline can have catastrophic effects. Hard real-time systems need determinism, not necessarily speed. The determinism gives the system stability and reliability. An example of a hard real-time application could be an engine dynamometer. In this type of application, failure to perform real-time control yields bad data on engine performance, and can potentially damage equipment.
Soft real-time systems also require that conditions and deadlines be met; however, a soft real-time system still functions properly and yields usable data even if a small number of deadlines are missed. For example, logging temperature to disk once a second to look for a general temperature trend over a 10 minute period is a soft real-time system. If you fail to log one temperature in the 10 minute period, you still see a general trend and still have a successful logging system.

## Slide 4: Real-Time Applications
Data collection
  Trending
  Data reduction
Stimulus and response
  Interrupt and response
  Deterministic control
Notes: Real-time measurement and automation applications can be divided into two broad classifications—real-time data collection and real-time stimulus and response.
Real-time data collection is accomplished today using modern data acquisition (DAQ) boards that have advanced onboard circuitry to acquire data continuously and in real time. Examples include the National Instruments DAQ boards with the MITE™ controller chip that uses scatter-gather PCI bus mastering for high bandwidth data transfer from the board to the computer. Because of this real-time data collection, the computer can perform analysis routines such as linearization for trending or a Fast Fourier Transform for data reduction. While the native operating system of the computer still introduces some unpredictable behavior, these systems are often sufficient for most applications. But for more stringent applications, the system must be ported to a real-time operating system.
In a stimulus and response type application, a user-defined response is generated based on a process input. For example, if a pressure level exceeds a certain pounds per square inch (psi), the system must recognize this and shut down the process. Determinism is needed in such a case to guarantee the shut down of the system within a certain time when the psi level is exceeded.
In deterministic control applications such as PID controllers, the ability to acquire, process information, and respond continuously at precise time intervals requires real-time performance. On most systems with plug-in DAQ boards, this information processing involves the general-purpose operating system of the computer which affects the real-time performance.

## Slide 5: Real-Time Challenges
Windows does not guarantee hard real-time performance
Many real-time hardware platforms exist
Software integration is difficult
  Fixed or very limited programmability
  Closed and proprietary software development tools
Different development environments
  Real-time vs. non-real-time
  Time consuming
  Costly
Notes: Although some real-time applications are solved with Windows, you are not guaranteed a real-time response because device driver scheduling and internal Windows functions like memory management. Also, some engineers are cautious of using Windows for fear the computer will fail or hang. Because Windows is not suitable for higher speed real-time applications, engineers doing measurement and automation look to dedicated real-time systems.
Real-time systems come in a variety of hardware platforms and require certain software development environments to program them. Some real-time systems have fixed or limited programmability, while others are more programmable but have closed or proprietary development systems. Because these development environments focus only on developing for a specific real-time hardware, integrating a real-time component into a larger measurement and automation system is difficult, if not impossible. In addition, working with multiple development environments mean more languages to learn, more development and debugging time, and more money spent.

## Slide 6: Industry Standards Come Together
+
Independent Real-Time Operating System and Processor
Notes: As the leader in computer-based measurement and automation, National Instruments now extends their industry-standard LabVIEW development software, data acquisition hardware and PXI (CompactPCI eXtensions for Instrumentation) platform to simplify the development and deployment of real-time applications. With these three technologies combined with an independent real-time operating system and processor, you can create complete powerful embedded measurement and automation systems that are easy to develop and maintain.
LabVIEW is a dataflow programming language that enables you to quickly and easily develop applications by graphically creating and debugging your applications. It reduces development time and facilitates maintenance with the industry standard development environment.
National Instruments is the leader in data acquisition hardware. With boards that range from analog acquisition at rates of 1.25 MSamples/s for high-speed measurements to counter/timer boards that are precise to 75 part per billion for encoder reading, you can develop a measurement and automation solution to fit your unique application requirements.
The PXI™ platform provides a modular architecture to the entire system in a rugged, dependable form factor. With the front-loaded modules, you can quickly and easily build and modify a large real-time system while the high-speed backplane synchronizes the hardware to perform more complex routines.

## Slide 7: Industry Standards Come Together
Notes: National Instruments LabVIEW Real-Time (RT) and RT Series hardware combines these technologies so users get the flexibility of a standard development environment, high-quality data acquisition hardware and the real-time performance of a dedicated processor.

## Slide 8: LabVIEW Real-Time System Architecture
Host computer running
Windows 2000/NT/9x
RT Engine
RT Development
System
DAQ Daughter
Board
Processor
Board
RT Series DAQ Boards
LabVIEW Real-Time
Notes: A LabVIEW Real-Time system consists of a LabVIEW Real-Time application and an RT Series hardware target. You create the real-time application with LabVIEW Real-Time on the host computer with its familiar Windows environment. With a simple pull-down menu, you generate and embed LabVIEW code that runs in real-time on the dedicated processor of an RT Series hardware target.
LabVIEW Real-Time consists of two components – the RT Development System and the RT Engine. The primary functions of the RT Development System include programming and debugging LabVIEW Real-Time code, downloading programs to the RT Series hardware, and providing a default user interface for the application. The RT Development System is a Windows 2000/ NT/ 9X application that runs on the host computer. The RT Engine runs on the processor of the RT Series hardware and executes embedded LabVIEW Real-Time programs.
The first RT Series hardware targets we discuss are the RT Series DAQ boards. The RT Series DAQ boards are available in two different plug-in platforms, PCI and PXI. They consist of two components, a processor board and a DAQ daughter card, and are plugged into the host computer used to program them. The processor board includes a CPU, standard PC chipset, BIOS, and RAM and runs a real-time operating system independent of the host computer. Once the code is downloaded to the board, it can operate independently or communicate with the host through the PCI or PXI bus.

## Slide 9: LabVIEW Real-Time System Architecture
Host computer running
Windows 2000/NT/9x
RT Engine
RT Development
System
PXI DAQ
Boards
Processor
RT Series PXI System
LabVIEW Real-Time
Notes: Another line of RT Series hardware targets are the RT Series PXI controllers. The PXI platform combines the speed and performance of the PCI bus in a rugged, modular package. Each PXI system is composed of a PXI chassis with a controller and front-loaded data acquisition boards.
The RT Series PXI controller includes a dedicated high-speed processor, RAM, hard drive, Ethernet port, two serial ports, GPIB port, and runs a real-time operating system. You can plug various PXI data acquisition boards into the PXI chassis to create a custom real-time solution.
With a host computer running LabVIEW Real-Time, you can download a custom application to the RT Engine on the RT Series PXI system through the Ethernet link. Once the program is downloaded, the RT Series PXI system run independently from the host computer or communicate with any other system through Ethernet.

## Slide 10: Development Steps
Step 1. Develop
Step 2. Download
Step 4. Deploy
Step 3. Debug
RT Series Hardware Target
Windows PC
Notes: Developing a LabVIEW Real-Time measurement and automation application is almost identical to developing a standard LabVIEW for Windows measurement and automation application.
Step 1. Develop your LabVIEW application.
Step 2. Download the application automatically at run time, or with a pull-down menu selection.
Step 3. Debugging in LabVIEW Real-Time is identical to LabVIEW. All debugging features such as breakpoints, single stepping, and probes are available to simplify development. Communication between the RT Development System and the embedded RT Engine takes place in the background automatically.
Step 4. Deploy the application.
Some deployed systems are dedicated systems that can run independently. In other cases, the deployed application is actually part of a larger measurement and automation application. You can achieve communication between the embedded LabVIEW Real-Time applications and the host LabVIEW application can be achieved through RT Series shared memory (only available on the RT Series DAQ boards), TCP/IP, or VI Server function calls. The host LabVIEW application can then provide a user interface, control other hardware that is not time-critical, save data to disk, and access the network.

## Slide 11: Standard LabVIEW Programming
Notes: LabVIEW Real-Time is based on the LabVIEW graphical programming paradigm. With it, users can quickly develop applications with function blocks that are wired together in a format very analogous to engineering flow-charts. It reduces development time with the simple-to-use development environment that includes graphical debugging tools such as breakpoints, single stepping, probes, and highlight execution.
There are some features in the LabVIEW programming environment that are unavailable when LabVIEW Real-Time is targeted to an RT Series hardware target. ActiveX is a feature that is only compatible with Windows operating systems. Virtual Instrument Software Architecture (VISA), which is a standard I/O library commonly used to control standalone instruments, is not supported as well. Dialog boxes that are used to prompt the operator work under the RT development system but must be disabled when a system is fully deployed. In addition, file management functions are not supported on the RT Series DAQ board since it has no static memory.

## Slide 12: Standard LabVIEW Programming
Notes: With built-in data acquisition libraries you can quickly program the hardware to acquire data as single points or buffers. With the tight integration between the hardware and software, you can synchronize the hardware timing circuitry with the software for even greater determinism in your control loop.
You can use other built-in libraries in LabVIEW Real-Time to provide signal processing, Fast Fourier Transforms, digital filtering, PID and fuzzy logic control. Instead of building analysis routines from scratch, you can take these existing function blocks to build highly sophisticated applications.
Once you are done creating the application, a simple pull-down menu downloads the program to the RT Series hardware target. The dedicated processor then executes the application in real-time independently so that if the host computer fails, the program continues to run smoothly.

## Slide 13: Embedded Real-Time Performance
Notes: Embedding LabVIEW Real-Time into an independent processor guarantees real-time operation. An embedded LabVIEW Real-Time application is not affected by host computer problems such as crashes, providing reliability. A LabVIEW Real-Time application also survives a soft reboot on the RT Series DAQ boards and because the RT Series PXI system has its own dedicated power supply, it continues to work even in the event of a host computer shut down.

## Slide 14: RT Series Real-Time DAQ Board
7030/6040E–12-bit multifunction I/O
7030/6030E–16-bit multifunction I/O
7030/6533–32 channel, high speed digital I/O
486/133 MHz
8 MB DRAM for user programs
PCI
cPCI/PXI
Notes: The RT Series DAQ board includes a 486/133 MHz process, 8 MB of user defined RAM, and 1 kB of shared memory for quick data transfer to the host computer. There are three variations of this board. There are two versions with multifunction I/O DAQ daughter boards with 12-bit resolution and 16-bit resolution. The other board includes a digital I/O daughter board with 32 high-speed TTL lines. With each variation, there exists a PCI board and PXI/CompactPCI version. These cards can be integrated into existing desktop measurement and automation solutions or PXI/CompactPCI measurement and automation solutions. You can even incorporate extra signal conditioning and increase your channel count with the RT Series DAQ board with National Instruments SCXI or SCC hardware.

## Slide 15: RT Series PXI Systems
All PXI DAQ/SCXI products
PXI/SCXI combo chassis
MXI™-3 supported
333 MHz processor
4 GB hard drive
256 MB RAM
2 serial ports
1 GPIB port
Built-in Ethernet port
Built-in Watchdog
PXI/cPCI compliant
Notes: The RT Series PXI systems are ideal for larger real-time systems. With the PXI platform, you can pick from a variety of data acquisition modules to create custom real-time solutions with the right channel count and type to fit your application. With the rugged modular technology, you can quickly develop and maintain the system over time.
The 333 MHz controller delivers higher determinism and faster loop rates, while the onboard serial and GPIB port on the controller allows you to connect other peripheral devices. With the PXI/SCXI combo chassis, you can easily integrate SCXI modules into the same box for an all-in-one solution. If you need to expand past the limitations of one chassis, the MXI-3 board allows you to control two chassis full of PXI equipment with one RT Series PXI controller.
With the Ethernet port, you can connect the RT Series PXI controller to any network and communicate with other networked devices. So in addition to turning off critical components in a system when the pressure level is exceeded, an e-mail can be sent to notify an operator.
The hard drive in the controller gives you the ability to log data to the system. With the file management functions in LabVIEW, you can save information in various formats on the hard drive that can later be post processed or transferred back to the host computer with the File Transfer Protocol (FTP).
The built-in watchdog on the RT Series PXI controller creates an even more robust system by notifying users when a failure has occurred. It can be configured to toggle a digital line, start another program, or reboot the RT Series PXI controller.

## Slide 16: Typical LabVIEW Real-Time Applications
Notes: You use LabVIEW Real-Time when you need real-time and reliable performance in your measurement and automation system. Some applications that these products are used for are:
engine testing with dynamometers,
control design and test,
vibration monitoring and testing,
machine condition monitoring and control,
fuel cell test, and
semiconductor tool positioning.
Click on the pictures to get more information about existing applications created with LabVIEW Real-Time. These case studies include an engine testing application in automotive, a remote critical control application in oil/gas, and a machine control application in metals manufacturing.

## Slide 17: LabVIEW Real-Time and RT Series Target Hardware
Familiar industry standard tools
  LabVIEW
  Data acquisition
  PXI/CompactPCI
Flexibility and integration
  Complete programmability
Real-time and reliability
  Independent processor
Notes: National Instruments LabVIEW Real-Time creates real-time and reliable applications that run on an independent processor. Embedded applications run independently and can survive host computer failures. You have complete programming freedom to create highly flexible applications that are tightly integrated with real-time measurement hardware. This integration provides the highest degree of productivity and allows you to create scalable and portable solutions with faster development times and at lower system costs. Productivity is also increased because LabVIEW Real-Time and the RT Series real-time DAQ boards uses industry-standard technologies for development such as LabVIEW, plug-in data acquisition boards, and the PXI platform. Users can embed complete LabVIEW Real-Time programs into the processors of the RT Series boards providing reliable, real-time performance.