## Slide 1: National Instruments Lookout

## Slide 2: Agenda
Industry Applications and Successes
Architecture
Device Connectivity
Distributed Logging/SQL/MES
Distributed Alarms,Events,Trends
Web Client
Other Features
Product Options
Summary
Notes: This modular seminar consists of presentations about PC automation technology and Lookout Automation software. It includes demonstrations and hands on exercises.
In the exercises that follow you will actually create an application from scratch, connecting to real I/O. The seminar is conducted by using either a Modbus PLC simulators or National Instruments FieldPoint distributed I/O.

## Slide 3: Industrial Automation Market
Continuous Control
Pulp & Paper
Oil & Gas
Refining
Water & Waste
Power
Discrete Control
Electronics
Automotive
Consumer Goods
Durable Goods
Telecom
Batch Control
Food
Beverage
Chemical
Semiconductor
Pharmaceutical
Notes: Continuous Process
In a continuous process, materials are passed in a continuous flow through processing equipment.
Discrete Process
In a discrete parts manufacturing process, products are classified into production lots that are based on common raw materials, production requirements, and production histories.
Batch Process
Unlike continuous processes, a batch processing is typified by relatively short production runs (a few hours or a few days). Batch processes are neither discrete nor continuous; however, they have characteristics of both.

## Slide 4: Lookout Successes
Water and Waste Water
  Sonoma County
  City of Sherman - 14,000 I/O, 6 servers, RTU’s
Chemicals
  Superior Micro Powders - FieldPoint modules
Notes: Lookout is used in these three industry types (continuous, batch and discrete)
Sonoma county has three networked Lookout installations each serving data to multiple clients.
City of Sherman uses 6 networked machines with Lookout 4.0 with 14,000 I/O points and 10 RTU’s connected to each server. (Continuous Process)
Superior Micro Powder, a chemical manufacturer uses Lookout 4.0 in a networked application with 5 banks of Fieldpoint modules. (Batch Process)

## Slide 5: Lookout Successes
Power Plant - Szeged, Hungary
Food and Beverage - Silocaf
Paper - Willamette
Hydro Electric - Army Core of Engineers
Oil and Gas - Panhandle Pipeline
Plastics - Mexico
Many other industries
Notes: Power Plant - Lookout and Fieldpoint is used to control a power plant in Hungary (Continuous Process)
Silocaf - Lookout is used to control their coffee processing plant (Batch Process)
Army Core of Engineers - Lookout is used to monitor 8 dams, the motors, turbines in the dams. (Continuous Process)
Panhandle pipeline - Lookout controls the pumping stations which contains compressors from 20,000 to 35,000 hp. (Continuous Process)
Thin film calendering - This large manufacturer of plastics in Mexico who makes more than 1000 combination of products uses Lookout for control (Discrete Process)
Lookout is used to monitor and control a wide variety of industrial applications including chemical and petrochemical plants, oil and gas pipelines, food processing plants, paper mills, pharmaceutical processes, water and wastewater plants, energy management systems, commercial building automation, and countless manufacturing applications.

## Slide 6: NI Solutions
Industrial Measurements
  Distributed I/O
  Data Acquisition and Signal Conditioning
  Machine Vision
  Motion Control
Networking & Connectivity
  OPC
  Ethernet
  Internet
PC Control
  LabVIEW RT and RT Series boards
Notes: NI offers solutions which range from Industrial Measurements, Networking and PC Control. These broad range of products cover a very broad base of industrial automation applications.
Lookout offers the best networking and connectivity in software. Combined with our industrial measurements hardware and third party hardware it covers a broad range of applications.

## Slide 7
Lookout
Engineering
Test/Quality
Maintenance
Windows NT
Business Systems
Internet/Ethernet
OPC
DeviceNet
FOUNDATON
Fieldbus
LAbVIEW
Real Time
Ethernet
Windows NT
OPC
Data Acquisition
PLC
N
N
N
N
Distributed I/O
N
N
N
N
Real Time
Motion Control
<date/time>
Vision
Enterprise Connectivity
Manufacturing
Notes: <number>
<footer>
<header>
<date/time>
Today, with its increasing power and networking capabilities, the PC is now used more and more to connect the factory floor with enterprise business systems.
This represents a fundamental shift in the use of PCs in industrial automation. The applications in today’s factories require connectivity not just from the PC up to the business system, but also from the PC down to the I/O and control systems. Because of its increases in performance and reliability, the PC is now able to take on tremendously versatile tasks that extend from direct control and data acquisition, to motion control and machine vision, to remote monitoring and control, to supervisory control, and, of course, HMI. We call this PC-centric view that exists today in the industry: PC Automation. National Instruments offers a suite of hardware and software products for use in PC Automation.
  Data Acquisition Cards -- NI-DAQ
  Distributed I/O -- FieldPoint
  FOUNDATION Fieldbus
  Industrial Communication PC Cards -- DeviceNet, Fieldbus,
  Profibus, Serial
  Motion -- Flex Motion and Value Motion
  Real Time -- LabVIEW Real Time
  Vision -- IMAQ

## Slide 8: Lookout Architecture
Objects
Driver is just
Another Object
Object Execution is Event Driven
Notes: <number>
<footer>
<header>
<date/time>
National Instruments Lookout is a full-featured object-based automation software system that delivers unparalleled power and ease-of-use in demanding industrial measurement and automation needs.
The technology behind Lookout’s ease-of-use is its object-based architecture and its underlying methodology for creating object-based applications. To define any application, no matter how basic or how complex, you simply create objects and connect them together – no programming, scripting or compiling required. Application development and modification are done completely on-line to ensure no interruption in controlled processes.
This object oriented approach shortens the learning curve, decreases development and extends system life cycle.
With the new networking capabilities you can configure Lookout servers and clients across a network as easily as configuring it in the same computer. Alarms, Events can be viewed and acknowledged from any computer in a network. Data can be logged and retrieved from any computer in a network.

## Slide 9: Device Connectivity
Every package includes drivers for all major protocols, PLCs --lowers up-front costs
Drivers are DLL-based objects --ensures data integrity
Automatic scan blocking --simplifies configuration
Serial port sharing --lowers telemetry costs
OPC, DDE, and general purpose ASCII and TCP/IP objects --ensures open connectivity
Exercise 1 & 2
Notes: <number>
<footer>
<header>
<date/time>
Whether you need to monitor and control applications with National Instruments FieldPoint, DAQ, SCXI, FOUNDATION Fieldbus, or a third party PLC or RTU, Lookout includes an impressive set of connectivity tools. These are not add-on toolkits for which you might expect to pay extra. Instead, every protocol driver is included with every Lookout server package. And all protocol drivers are Dynamic Link Library (DLL) object classes. This means that they feature the best performance and highest data integrity in the industry.
Automatic scan blocking simplifies configuration
One feature which makes connecting Lookout to devices extremely easy is its ability to automatically optimize the scanning of data blocks. The time savings that this feature brings to application development cannot be overstated. Many software packages require you to assign blocks of PLC registers for scanning. A package might, for example, poll one block of data registers for a specific viewing panel, another block of registers for historical collection, and yet another block for alarming. This not only artificially adds to the overall point count of the system, but it also requires you to map registers in the PLC unnecessarily and redefine scan blocks within the driver software every time you make a change.
In contrast, Lookout can use the same register value for alarming, viewing, and logging. This reduces your overall I/O point count.

## Slide 10: Distributed Logging
Log data to any computer in a network
Retrieve data from any computer in a network
Log data to a spread sheet file
Exercise 3
Notes: You can save historical data and retrieve it from any computer on a network that is running Lookout.
Lookout has two tools for capturing historical data and logging it to disk. One is Citadel, an event based logger that compresses historical data into binary files. The other is spread sheet object class where you can log data in csv ACSII files and open it up using a spread sheet software.
Citadel is an event-driven historical data logger and SQL data server. As an SQL server database, it makes all historical and real-time data immediately available through queries by any ODBC-compliant SQL client like (Access, FOXPro etc.) With Citadel finding data logged an year ago takes no longer than finding data logged yesterday. Also because of the event driven nature every single change of logged signal will be captured without filling the hard drive with unnecessary data.

## Slide 11: Distributed Trending
View trend lines from any computer in a network that is running Lookout
Web clients can also view trends from anywhere in the world
Plots citadel data in real time
Includes pan and zoom with instant scrolling
Includes cursor bar with value search
Exercise 4
Notes: With Lookout’s networking technology trends can be viewed from any computer in a network. Trends can also be viewed from anywhere in the world or by using a web browser and a Lookout web Client.
The Hypertrend object class plots historical data in real time, combining historical and real-time data in a single seamless trend graph. The trend plots the data in a graph of value vs. time.
Hypertrend features ease-of-use and flexibility. Use HyperTrend’s built in button bar to scroll back and forth in time or jump to a specific point. The built in pop up window shows the current value and tag nameof each trend line and enables quick searches for a break in trend line, a signal peak, valley or the violation of a specific value. You don’t have to specify complicated queries and wait for historical data to appear. It’s that fast.
You can define as many HyperTrend objects as desired and you can have as many analog and/or discrete values as you want in each HyperTrend object.

## Slide 12: Distributed Alarms and Events
Monitor and acknowledge alarms from any computer in a network
Complex Alarm/Event logic when necessary
Grouping and Filtering
Voice and Pager activation based on alarms
Permanent archiving
Easy reporting to spread sheet
Exercise 5
Notes: Alarms and Events can be viewed from anywhere in the network. Alarms can also be acknowledged from anywhere in the network. Configuring to see the alarms in any machine on the network is done in two easy steps from the menu Alarms>>Select Processes. Logging the Events allows a user to create an audit trail of who does what.
Lookout can trigger alarms and events when complex combination of events occur. With the unique alarming capabilities of Lookout, you can group and filter alarms and events in any manner you choose based on plant area/ priority/ Object/ User/Process or Description.
Alarm annunciation options in Lookout are very flexible. They include several alarm summary presentation options, the ability to play recorded voice messages, and the ability to dial out to pagers.
You can easily set options to save the alarm and event information in .csv ASCII format. You can open these files using any standard spread sheet software or even using a word processing software.

## Slide 13
Lookout
Engineering
Test/Quality
Maintenance
Business Systems
Internet/Ethernet
Intranet
Data Acquisition
PLC
N
N
N
N
Distributed I/O
N
N
N
N
Real Time
Motion Control
<date/time>
Vision
Networking
Manufacturing
Internet
Exercise 6
Notes: <number>
<footer>
<header>
<date/time>
Today, with its increasing power and networking capabilities, the PC is now used more and more to connect the factory floor with enterprise business systems. With Lookout’s networking technology it is very easy to connect to multiple servers on the plant floor and communicate to multiple clients on the business side. With Lookout Web Clients you can use Internet Explorer from anywhere in the world to not only monitor the process but also to control it.
To connect to Enterprise Database and get data from Lookout the most popular tool is Citadel’s ODBC server. Virtually any other database, spread sheet, MES program, preventive maintenance program etc. can directly retrieve live and historical data from Citadel using SQL.
For SQL reads and writes within the real-time environment of Lookout, you can use the SQL_Exec and DataTable objects. The DataTable object class enables you to query hundreds of records in a single select statement. The SQL Exec object class enables you to read, append, update and delete individual records in any ODBC (open database connectivity) - compliant SQL database. Together, these objects enable you to import recipes, batch data, order data, etc. to and from various servers such as MRP and MES systems.

## Slide 14: Other features
Security
  Password based user accounts
  Security over a network and also over web
  Advanced security based on IP addresses
  Action verification and event logging
  Security enabled for object and panel control
  Menu function security
  Automatic start/up window
SPC and other objects
Notes: You can set up any number of operator accounts and choose between 10 different access levels for each account. These user-defined security levels determine what display windows a user can view and what objects he or she can control. Once security information is set, the same security is applied across all the computers in the network and also across the web.
Read Only/Write Only/ Both Read and Write security can be set based on IP addresses.
You can assign distinct control and viewing security levels to control panels so that only authorized viewers can view or change sensitive information on those panels. At the system level, you can easily configure Lookout for automatic startup when the operating system is activated. It can be locked so that it cannot be closed, minimized or exited by operators once it is running. You can log on and off the screen by clicking on the screen, choosing a menu pull-down, or through a hot key sequence.
Lookout enables password protection for proprieteray applications so that others cannot modify or even examine your configuration.
Some of the objects that are not described in the presentation and are used for Batch Management, Sequential Control, Continuous Process Control are:
Batch Management: Recipe object (easy interface through a spread sheet), Datatable (Multiplexing different data sources into a single display template or to import and export large quantities of data), PID loop tuning, Alternator, Pulse Timer, Sample, Animator, Counter, Neutral Zone, Integral and so on.
Full fledged SPC capabilities like histogram, X chart, X bar R chart, pareto etc. allows you to take tighter control of your process.

## Slide 15: Lookout Product Options
LOOKOUT
DEV / RUN-TIME SERVERS
N
N
N
N
<date/time>
LOOKOUT
INTEGRATOR
LOOKOUT
CLIENTS
LOOKOUT
RUN-TIME
SERVERS
Distributed I/O
PLCs
Data Acquisition
RTUs
Lookout is object-based automation software that delivers unparalleled power and ease-of-use for demanding measurement and automation applications.
Notes: <number>
<footer>
<header>
<date/time>
Lookout Server Software
Lookout Server software is fully scalable and is available in either runtime-only or development/runtime configurations. Development/runtime systems enable you to create and run applications. Although you cannot create or modify an application on a runtime-only server system, you can do everything else that a development/runtime package can do including full process monitoring and control. Price for development server ranges from from $745 (50 I/O) to 5,995 (unlimited I/O). Price for runtime server ranges from $495 to $3,995.
Lookout Client Software
Client systems can be connected to any server over the network. Client software enables operators to monitor and control processes, execute batch operations, acknowledge alarms, make setpoint adjustments, print reports, view HyperTrends, etc., just like a runtime-only server system – except Client nodes do not include or support any I/O protocol driver object classes. Like runtime-only servers, they also do not enable application development. Price is $745 (unlimited I/O)
Lookout Integrator System
Integrator Systems are identical to Lookout development/runtime servers, except they cease operation every three hours and must be restarted. Integrator Systems are ideal for system integrators, engineers, OEMs, etc. who wish to have a copy of Lookout onsite for configuration, testing, and demonstration purposes. Price is $795 (unlimited I/O).

## Slide 16: Productivity Guarantee
National Instruments backs your productivity..
Try Lookout for three months..If you don’t find Lookout easier to use than other HMI/SCADA software in the market, we will refund your money back.

## Slide 17: Benefits
Event Driven High Performance
Total Cost of system Great Value
Full Set of drivers, OPC Multi-vendor
Server and Client capability hardware Integration
Object Based Network Easy to Use and Architecture Develop Applications
Notes: Event Driven : Because Lookout is event driven, it can easily scale and handle thousands of I/O points.
Lower Price: Lookout is priced lower than most HMI/SCADA software in the market. Also a large set of protocol drivers to talk to hardware is FREE to customers. This provides great value to customers.
Integration: Lookout is an OPC server and client. This ability makes it very easy for Lookout to integrate with any OPC compliant hardware or software in the market.
Object Based Network Architecture: The object based architecture makes it very easy to develop applications in a single computer or over a network.
Lookout takes very less time to learn and use. This means faster return on investment made because of lower training, application development and maintenance costs. Combined with the productivity guarantee Lookout is the best value software available in the market.

## Slide 18: Summary
Easy HMI/SCADA
  Object oriented, no programming or scripting
  Easy Networking, Logging, Alarming, Security,
Flexibility and Power
  Event-driven to poll I/O faster
  Extended functionality with LabVIEW
Connectivity
  OPC Server/Client
Notes: Easy HMI/SCADA: Very easy to learn and implement because of the object oriented approach that Lookout uses. Developing networked applications with logging, alarming, security is very easy in Lookout.
Flexibility: Because of the event driven approach Lookout can poll I/O faster. This also means that Lookout can poll larger number of I/O’s very easily and hence is easily scalable. To extend the power of Lookout and take advantage of National Instrument’s Motion and Vision applications you can interface with LabVIEW for Industrial Automation.
Connectivity: Lookout is an OPC server as well as an OPC client. This makes it possible to communicate with any standard OPC software or hardware available in the market.