## Slide 1: National Instruments
MXI-2: A New Generation of VXI Control
View or print this presentation from within PowerPoint to see the notes with each slide.

## Slide 2: Virtual Instrumentation
Virtual
Traditional
Acquisition
and
Control
Analysis
Presentation
Signals
Notes: The instrumentation industry is undergoing a variety of exciting changes as a result of the widespread acceptance and proliferation of PCs. These changes in instrumentation are occurring in both hardware and software areas. Millions of scientists and engineers around the world use PCs to automate their research, design, and manufacturing tasks. Increased performance and capability of PCs now rivals that of sophisticated workstations at a fraction of the cost. Easy to use but powerful software and application development environments allow you to develop more capable applications faster.
With the advent of the PC, a new term has become popular in the instrumentation community. The term “virtual instrument,” describes the combination of programmable instruments with general-purpose PCs.
Historically, architectural limitations have resulted in hard boundaries between vendor-defined instruments and user-defined functionality in an instrumentation system. The PC revolution has equipped users with powerful processing and display capabilities of their own. If you enhance the fixed capabilities of a traditional instrument with flexible user-defined capabilities of a computer, you have a virtual instrument. The computer can enhance instrument functionality in any of the three element areas - data acquisition, analysis, and/or presentation.

## Slide 3: VXI – An Open Architecture with Shared Processor Bus and Timing
<footer>
<date/time>
Register-Based Instrument
Computer Module
VXIbus Mainframe Backplane
Message-Based Instrument
P
R
O
C
E
S
S
O
R
B
U
S
T
i
m
i
n
g
488
port
PROCESSOR BUS
Timing
PROCESSOR BUS
Timing
A/D
D/A
DI/O
TI/O
PROCESSOR BUS
Timing
A/D
D/A
DI/O
TI/O
ROM
Notes: A traditional instrument consists of three major elements – acquisition, analysis, and presentation. A virtual instrument also has these same three elements, but differs in that they need not necessarily reside in the same box. In a VXI system, these components are distributed between the instrument and the system controller, inherently creating a virtual instrument. VXI instruments cannot be controlled or operated alone; VXI instruments must work together with VXI controllers to realize complete instrument functionality. At a minimum, the VXI instrument always handles the acquisition/stimulus and the VXI controller takes care of the data/status presentation.
VXI is an ideal virtual instrument architecture that has promised to change the way instruments and systems are built. The modern memory-mapped computer architecture of VXI, its high-speed parallel data bus, and its advanced triggering and timing buses provide a perfect framework for virtual instrumentation.

## Slide 4: VXI Hardware Strategy Three Strategic Thrusts
VXIplug&play compatibility
  VISA
Capitalize on the latest ASIC technology
  Higher performance
  Higher MTBF and reliability
Leverage PC market
  Intel microprocessors
  PCI local bus for high-performance expansion
Notes: National Instruments recognizes the trends in the desktop computer and the instrumentation industries and is positioning itself to deliver products which take full advantage of these developments. National Instruments strategy for the future has three basic thrusts. All of our VXI controllers are and will continue to be VXIplug&play compatible. VXIplug&play controller compatibility means that your systems will be open and that software written on these controllers can run on any VXIplug&play controller.
The second thrust in our strategy is to design and use ASICs where it makes sense. ASICs compress board functionality into a smaller package usually resulting in fewer components on the target board. Fewer components frees up valuable board “real-estate” so that this space can be used for other functionality. By designing a complete architecture, the ASICs can incorporate many high performance features that can be duplicated on many different products.
We have already discussed how PCs have become a popular choice for instrument control. Not only have PCs become predominant, but PCs have consistently increased performance while maintaining low prices.

## Slide 5: Strategic Thrust #1

## Slide 6: What is a VXIplug&play Controller?
Runs all VXIplug&play software
  VISA
  Instrument drivers
  Executable soft front panels
  VXIplug&play ADEs
    LabVIEW, LabWindows/CVI
VISA ships with the controller
Notes: The main objective of the VXIplug&play Systems Alliance is to increase ease of use for end users of VXI technology through open, multivendor VXI systems. The alliance members share a common vision for multivendor systems architecture, encompassing both hardware and software. This common vision enables the members to work together to define and implement standards for system-level issues beyond the scope of the VXIbus specifications.
VXIplug&play-compatible controllers and software are the foundation on which all VXIplug&play software executes. VXIplug&play controllers provide all of the necessary I/O software components required to run the gamut of VXIplug&play software including VISA, source code instrument drivers, executable soft front panels, and VXIplug&play application development environments (ADEs) such as LabVIEW or LabWindows/CVI. The bridge between the application software and the hardware is VISA. Because VISA is a core component of this software architecture, VISA is required to ship with the controller to be VXIplug&play compatible. If you choose a VXIplug&play controller solution, your software task will be simplified tremendously.

## Slide 7: VISA is the Key
Unifies the industry
  Superset of NI-488.2, NI-VXI, SICL, etc.
Makes “systems” open
  Multivendor controllers, multivendor software
Improves ease-of-use
  One library for all instrument types
Protects users
  Backward compatible with entire installed base
Positions for the future
  Object-oriented, distributed systems
Notes: As a step toward industry-wide software compatibility, the alliance developed one specification for I/O software – the Virtual Instrument System Architecture or VISA. The VISA specification, VPP-4.1, defines a next-generation I/O software standard not only for VXI, but also for GPIB and serial interfaces. With the VISA standard endorsed by over 38 of the largest instrumentation companies in the industry including Tektronix, Hewlett-Packard, and National Instruments, VISA unifies the industry to make software interoperable, reusable, and able to stand the test of time. Before VISA, there were many different commercial implementations of I/O software for VXI, GPIB, and serial interfaces; however, none of these /O software products were standardized or interoperable.
VISA unifies the industry by employing an architecture that works for GPIB, VXI/MXI, serial, and Ethernet interfaces. VISA also creates a framework for the large installed base by including backwards-compatible libraries for the installed base of users, while incorporating the latest technological advancements in the computer industry. The VISA architecture works not only with today’s single-processor systems, but also for tomorrow’s multiprocessor distributed systems. Because of its intuitive object-oriented design, VISA is easily extensible to other I/O interfaces as they become important.

## Slide 8: VXIplug&play Solutions
System Frameworks
Instrument Drivers
Soft Front Panels
I/O Interface Software
Install Disk
VXIplug&play
Install
VX4240
VISA
Notes: Along with modular hardware, modular reusable software is a key to success with VXI. VXIplug&play compatible instruments include standardized, ready-to-go instrument drivers written by the instrument vendor and delivered in source code to ease your programming task.
Modular, user-configurable software provides the foundation for the powerful new “virtual instrument” methodology for next-generation instrumentation. Tools that work with the VXI virtual instrument methodology, such as LabVIEW and LabWindows, give you access to all VXI’s capability and make it easy for you to integrate modular hardware functions with software functions that perform highly specialized analysis and presentation.
VXIplug&play standards solve many of the problems that now occur because of the lack of standardization at the system level. These standards make it possible for VXI vendors to ensure their products are compatible with the other components within a particular system environment. By standardizing all of the software components in a VXIplug&play system, you can create your own virtual instruments without worrying about being locked into a single vendor.

## Slide 9: Strategic Thrust #2

## Slide 10: ASIC Benefits
Reduces number of discrete board components
  Easier to manufacture boards
  Increases reliability
Requires less board “real estate”
  More capability in a smaller package
Lowers power consumption

## Slide 11: New NI ASICs
MITE
  High performance DMA controller
  Bus translator
  Incorporates MIGA
MANTIS
  Trigger, interrupt, and utility bus interface
  Incorporates TIC
Notes: National Instruments developed two new ASICs – the MITE and the MANTIS – to streamline the connection between popular computers and workstations to both the MXI and VXI buses. With the extensive knowledge gained from developing products on a wide variety of computer buses, National Instruments designed the MITE to connect directly to the most popular computers and workstations while achieving an unprecedented level of performance.
The MITE ArbitratioN Trigger Interrupt Support chip (MANTIS) is a custom ASIC developed by National Instruments to lower manufacturing costs, lower power consumption, increase timing and triggering capability, and simplify the design of many related products. The MANTIS, when combined with the MITE ASIC, forms the foundation for the all of National Instruments next generation controller products delivering cost-effective high performance control solutions.

## Slide 12: Relative ASIC Size

## Slide 13: MITE Features
High performance DMA controller
Bus translator
  VXI, MXI, PCI, other
Synchronous MXI protocol
  Breaks 20 Mbytes/s barrier
VME64
  Doubles VXIbus throughput
CPU
I/O
MXI
VXI
CPU
I/O
MXI
VXI
DMA
DMA
Notes: The MITE chip is a bus translator and sophisticated dual-channel DMA controller that has built-in interfaces for VXI, MXI, and PCI. MITE-based products achieve their impressive performance benchmarks by taking advantage of the MITE’s many features, including state-of-the-art hardware DMA capabilities, synchronous MXI transfers, and VME64. Designed with several computer bus architectures and operating systems in mind, the MITE uniquely combines conventional and advanced DMA transfer mechanisms with adaptable hardware and software features to maximize performance and increase flexibility on a wide variety of computer platforms.

## Slide 14
MITE
VXI
MXI
CPU
PCI
I/O
DRAM, EEPROM
Notes: The MITE was designed to be easily adaptable to a number of different computer buses. Several key features of different computer bus standards were incorporated into the MITE’s design including extensions for both synchronous and asynchronous buses. The MITE connects external buses through its four ports: the I/O port, CPU port, VXI port, and the MXI port. Each port incorporates dynamic bus sizing for transferring data to devices or other buses of unequal data path widths.
The CPU port – the primary connection to computer interface buses – provides a flexible, but high-speed interface to existing computers. The CPU port streamlines the data flow from the computer to the MXIbus by being able to initiate a transfer while at the same time waiting for a prior transfer to complete. This type of transfer is called write posting. A write posting buffer placed between the CPU port and the MXI port decouples the connection resulting in the most efficient transfer.
Although the MITE incorporates key features that allow it to easily interface to many popular computer buses; the MITE incorporates an interface to one bus standard entirely – the PCI bus. Because of PCI’s rigid technical requirements, the CPU port incorporates extensions that make if fully compatible with the PCI bus standard.

## Slide 15: MITE DMA
Two independent DMA controllers
  Simultaneous transfers to different ports
State-of-the-art DMA modes
  Continuous
  “Scatter-gather” or Link chaining
  Data packing, formatting on-the-fly
Built-in FIFOs decouple ports
Notes: The MITE can be conceptualized as a fast data-moving engine. Controlling external instrumentation from a remote computer usually expends valuable CPU time because the microprocessor shoulders the burden of transferring data and/or commands to and from devices. However, MITE-based VXI controllers free-up CPU processing time by moving the burden of data transfer to one of the MITE’s two on-chip DMA controllers. Instead of the host computer’s microprocessor transferring data to instrumentation or devices, application programs or I/O software drivers can use the MITE to execute data transfers. While the MITE transfers the data, the microprocessor can perform application-specific tasks, such as data presentation and analysis.
The MITE also decouples the buses it connects. Separate write posting buffers strategically placed between each interface maximize data flow by unimpeding the data channel. In all applications, throughput is paced by the slowest link. By decoupling the links, transfers do not stop when one interface is busy. Transfers along the link continue until the busy link is free.

## Slide 16: MANTIS: MITE ArbitratioN Trigger Interrupt Support
Arbitration
  Interrupts
  Triggering protocols
  VXI and MXI data buses
TIC timers and counters
  Source pulse trains on the VXI trigger lines
  Count the number of pulses on a trigger and interrupt the local microprocessor when the terminal count is reached
Built-in DRAM controller
Notes: Designed in tandem, the MANTIS and MITE provide a complete MXI and VXI chip set resulting in complementary and modular components for all MXI-2 products. When the MITE performs high-performance data transfers primarily using direct memory access (DMA), the MANTIS handles VXIbus and MXIbus-specific tasks, such as bus arbitration, along with interrupt, trigger, and utility bus control. The MANTIS hooks directly to the MITE through the MITE I/O port. The MANTIS provides the primary interface for all the devices that appear on the I/O bus, including optional DRAM. To facilitate DRAM expansion off of the I/O port, the MANTIS includes a built-in DRAM controller.
To simplify board design and increase the timing and control capabilities, the MANTIS incorporates the Trigger Interface Chip (TIC), a key component found on all National Instruments embedded VXI controller products being shipped. Thus, all of the MXI-2 products now have the same advanced timing and triggering capabilities featured on these embedded controllers.

## Slide 17: Strategic Thrust #3

## Slide 18: PC’s For VXI Control
PC’s use the latest technology
  High performance microprocessors
    Pentium
PCI local bus architecture
  High performance peripherals
    Video, Enhanced IDE, SCSI-3, etc.
Plentiful and easy to use software
Attractive cost/performance ratio
Notes: As time has shown, low-cost desktop personal computer manufacturers continually capitalize on standard technological advancements to deliver products that are not only low in cost but also high in performance. By using standard bus interfaces, such as PCI, desktop PCs compete with the most advanced computer workstations to provide a platform that works with the highest performance peripherals. General-purpose desktop computers and workstations incorporate the latest high-performance microprocessors and new local bus designs centered on the Peripheral Component Interface (PCI) bus to achieve cutting edge performance while maintaining low prices.

## Slide 19
Peripheral Component Interconnect

## Slide 20: Why PCI?
High performance
  132 Mbytes/s for 32 bit transfers
  Burst cycles transfer data one long word per clock
  64-bit interface already defined
Industry standard peripheral expansion
  Apple, DEC, IBM, Motorola, Sun, HP
  PCs
    Dell, Compaq, and so on
Notes: The PCI bus, developed by Intel in 1992, provides an industry-standard peripheral expansion architecture for computer bus design. Local bus designs gained popularity during the early 1990s because standard peripheral interface connections, such as the ISA bus, lacked the performance and capability of the latest microprocessors with which they were integrated. By tapping into the microprocessor local bus, local bus designs capitalized on the microprocessor technology to achieve a higher level of performance. Before PCI, there were several different local bus implementations – none of which were interoperable or standard. With the backing of the largest computer and component manufacturers, including IBM, Apple, Motorola, Intel, and DEC, the PCI bus is widely recognized as the standard architecture that will stand the test of time.
Common PCI implementations operate at 33 MHz clock frequency and a 32 bit data path, yielding a top throughput rate of 132 Mbytes/s. Furthermore, users can extend the PCI bus data path to 64 bits with little effort because the expansion mechanism has already been defined in the specification and is built into many PCI bridge chip sets. By doubling the data path size, the maximum throughput is also doubled, thus facilitating a smooth upgrade path for taking advantage of future technologies.

## Slide 21: Typical PC/PCI Architecture
CPU-PCI
Bridge
PCI-E/ISA
Bridge
Video
E-net
Disk
Slot
Slot
CPU
DRAM
Printer
Serial
Mouse
Kybd
Floppy
PCI
EISA/ISA
Slot
Slot
Slot
Notes: Virtually every Pentium or 80486 PC that supports PCI implements the architecture in this slide. The video and hard disk controllers have been put on PCI to achieve higher transfer rates. Sometimes ethernet is also added on the PCI bus. Usually one or two PCI slots are available for users. A PCI bridge chip links the PCI bus to the ISA or EISA bus. Slower devices remain on the E/ISA bus and several E/ISA slots are available for users.
PCI PC’s have an extended BIOS that configures the PCI devices during system boot.
The majority of the PCI PCs currently on the market use Intel’s PCI chip sets for the 486 and Pentium. The Intel chip sets provide the CPU to PCI bridge and the PCI to ISA/EISA bridge. Hard disk, ethernet and video are provided by other companies. The PCI chip sets for the 80486 are code named Saturn and Ares. Ares is a slightly cheaper version of the Saturn chip set. PCI chip sets for the Pentium are code named Mercury and Neptune. 60 and 66MHz Pentium systems use Mercury and 90MHz systems use Neptune.
Due to PCI’s loading and signal constraints most PCI based PCs will offer one or two available PCI slots for users. PCI cards are designed so they can share a bracket location with an ISA slot. Some PC’s take advantage of this and implement a shared slot that can accommodate either an ISA card or a PCI card (but not both at the same time).

## Slide 22: Three Types of VXI Controllers
1.
2.
3.
Notes: VXI system control can be divided into three basic types. The first type of VXI system consists of a VXI mainframe linked to an external controller via the GPIB. The controller talks across the GPIB to a GPIB-VXI interface module installed in the VXI mainframe, which transparently translates the GPIB protocol to and from the VXI Word Serial protocol.
The second configuration involves a custom VXI-based embedded CPU. The controller is a VXI module physically located in the VXI chassis, thus creating the smallest physical size for a VXI system. The embedded VXI controller connects directly to the VXI backplane.
The third configuration uses a high-speed MXIbus link from an external computer to control the VXI backplane. This configuration is functionally equivalent to the embedded method, except that it has the flexibility for use with a wide variety of computers and workstations. The external computer operates as though it is embedded directly in the mainframe.

## Slide 23: VXI Controller Outlook
Notes: Over the years, VXI controllers have improved in both performance and capability. Many of the early VXI systems used GPIB-VXI interface cards as the system controller. Although there are attractive programming benefits to using GPIB-VXI interface cards for VXI system control, data throughput rates realized using this approach are much slower than embedded VXI controllers or MXI. The maximum throughput rate of GPIB is around 1 Mbytes/s. Actual throughput rates are much slower for GPIB controlled VXI systems, less than 300 Kbytes/s, because of the software overhead required to translate IEEE-488 commands to VXIbus register reads and writes.
Embedded VXI controllers have historically been the highest performing VXI controllers for data throughput. Plugged into the VXI backplane, embedded VXI controllers directly access all of the VXI backplane signals. Today’s fastest embedded VXI controllers can transfer blocks of data across the VXIbus at roughly 10 Mbytes/s.
However, the trend for VXI system control clearly indicates that users want to capitalize on the desktop computer industry to use the latest high performance microprocessors and operating systems to control their systems. Embedded VXI controllers typically cost more because of the specialized VXI circuitry and packaging required to fit the VXI form-factor. In addition, embedded VXI controller technology typically lags that of desktop computers because of these design challenges.

## Slide 24: MXI Today
Open specification
VXIplug&play core technology
VXI-MXI conforms to VXI-6
MXI has been successful for the industry
  Mainframe-to-mainframe expansion
    De facto standard to extend VXI mainframes
  Desktop computer control of VXI mainframes
Notes: National Instruments developed the MXI specification as an open document in 1989. Since that time, MXI has become the defacto standard for extending VXI mainframes and for controlling VXI mainframes from a general purpose desktop computer. MXI is fully VXIplug&play-compatible and is listed in the core technologies, meaning that all VXIplug&play software will work on MXI controlled VXI systems.
With MXI, you can use desktop computers or workstations to control VXI systems just like GPIB-VXI controllers, but the actual data throughput rates are much faster. Like an embedded computer, MXI directly connects the remote computer to the VXIbus thereby yielding faster data rates than GPIB-VXI controllers for all forms of VXI communication including register accesses, message-based communication, and block data moves. A read or write cycle generated on a desktop computer is converted to a VXIbus cycle via the MXIbus in hardware – no additional software processing is involved. You also use the same I/O software drivers to program MXI that you use with embedded VXI controllers. Historically, MXI products offered block data throughput rates that peaked at approximately 5 Mbytes/s even though MXI offered a theoretical maximum of 20 Mbytes/s.

## Slide 25: What Would Make MXI Better?
Higher throughput
More reliable cables at a lower cost
Single Cable
  Combine INTX and MXI
Optional DRAM on the MXI cards

## Slide 26: Introducing MXI-2!
New products based on the MXI version 2.0
  New synchronous MXI protocol
Integrates custom ASICs
  DMA for high data throughput
  Triggers
New cable combines MXI and INTX
  Direct control over interrupts and triggers
  More flexible cable
  => Highest performance control link available
Notes: Although MXI works in much the same way as embedded VXI controllers, embedded VXI controllers have generally outpaced prior generation MXI controllers in one important benchmark – block data transfers. MXI-2 defines new extensions to the MXI specification and takes advantage of the latest desktop computer technology, primarily the Peripheral Computer Interface (PCI) bus, to increase sustained block data throughput rates up to 23 Mbytes/s. The result is that MXI-2 based VXI controllers boost data throughput to levels that exceed commercially available embedded VXI controllers, making the new generation MXI-2 controllers the highest performance VXI control solution available.
The most significant addition to the MXI specification is the synchronous MXI protocol. Synchronous MXI block data transfers lower the protocol overhead of typical data transfers, effectively increasing performance. You can use synchronous MXI to transfer data – either 8, 16, or 32 bits wide – to consecutive addresses or a single address. With a MXI-to-VXI interface kit, you can use synchronous MXI to send data from a computer’s local memory to the VXIbus for writes or from the VXIbus to the external computer’s local memory for reads.

## Slide 27
MXI-2 System Architecture
uP
Memory
MITE
MANTIS
DRAM
Computer Bus
MITE
MANTIS
DRAM
MANTIS
DTB
MXI
Host Computer
VXI Mainframe
CPU-MXI-2
VXI-MXI-2
VXIbus
Utility bus
DTB Arbitration
Interrupt bus
Trigger bus
D8, D16, D32
Word Serial
Trigger bus
Interrupt bus
Utility bus
Shared Memory
Word Serial (FHS,FDC)
Shared Memory
A16, A24, A32
D8, D16, D32, D64
DMA Block Transfers
A16, A24, A32
+ Synchronous MXI
+ DMA
Notes: The MITE and the MANTIS streamline board design through the versatility of their operating modes. The PCI-MXI-2 uses the MANTIS to provide complete access to VXI interrupts and VXI triggers and accommodates the optional DRAM on these boards. By using the MANTIS in its different modes, you can combine several MANTIS ASICs on a single board to provide a complete VXIbus interface as well as a functional extension to the MITE.
The MANTIS interfaces to the MITE through the MITE I/O port where the optional DRAM on the MXI-2 products resides. All MXI-2 products have DRAM SIMM sockets so that users can configure VXI systems with up to 64 MB of additional DRAM. The MANTIS incorporates all of the DRAM controller circuitry necessary to control and interface this DRAM. Thus, the PCI MXI-2 uses the same DRAM controller interface in the MANTIS as the VXI MXI-2.

## Slide 28
<footer>
<date/time>
Mainframe
0h
200000h
400000h
800000h
VXI A24
DIg #1
DIg #2
DIg #3
DIg #1
DIg #2
DIg #3
MXI-2
PC Memory
DIg #1
DIg #2
DIg #3
VXI-MXI-2
Intel
DMM
Notes: The MITE’s state-of-the-art DMA transfer capabilities include special modes tailored for VXI instrumentation. For instance, the MITE’s “scatter-gather” DMA mode can transfer data to and from different devices located in non-contiguous address space. For example, you can program the MITE-based MXI-2 products to acquire data from several VXI digitizers that have physically separate shared-memory address spaces. In the process of moving the data from the digitizers to the computer, the MITE can automatically consolidate the data into a single buffer at the destination. In this example, you set up the transfer once, then MITE transfers and consolidates the data, not the microprocessor. When the transfer is complete, the MITE can assert a local interrupt to let you know the transfer has finished. You can programmably transfer the data just once, for a snapshot of the acquisition, or continuously.
Using DMA and synchronous MXI boosts block data throughput between the controller and instruments that use shared memory, however, this combination is equally effective with instruments that employ a FIFO, exposing a single register address for data storage or retrieval. Register-based Digital Multimeters (DMM) typically implement one data register for storing measured values. To preserve a series of measurements, a DMM will usually buffer the readings in a first-in first-out (FIFO) so that you can extract readings on a first-in, first-out basis. By successively reading the data register FIFO, MXI-2 controllers can use DMA to transfer this data in block form across the VXI and MXI buses. DMA block transfers from a source single address execute without a great deal of software programming because the MITE performs the transfers.

## Slide 29: MXI-2 Products
PCI-MXI-2
  High performance
    33 Mbytes/s burst
    23 Mbytes/s sustained
AT-MXI-2
  2 to 4 times faster than current MXI product
VXI-MXI-2, VME-MXI-2
  VME64
All of these products have:
  DRAM expansion
  High MTBF

## Slide 30: PCI-MXI-2

## Slide 31
VXI-MXI-2

## Slide 32: DOS and Windows MXI-2 Kits

## Slide 33: MXI-2 DRAM Expansion
Notes: To increase performance and capability, all of the MXI-2 products use the MITE I/O port to add DRAM SIMM sockets for optional onboard memory. System developers can use this dual-ported DRAM on the MXI-2 products as shared memory on the VXIbus or as a dedicated data buffer. Continuous or high-performance data acquisition applications can take advantage of this feature for real-time or post-acquisition analysis. Using the optional onboard DRAM in this manner opens new doors for high-performance data acquisition by ensuring that data captured at high speeds is delivered to the host computer fast and efficiently without the loss of data.

## Slide 34: MXI-2 Key Features
High performance
  Synchronous MXI, VME64
DMA
Direct control of VXIbus
  Interrupts, Triggers, CLK10, and so on
Optional DRAM
Software standard
  Backward compatible with MXI-1
Notes: For instrument control, MXI complements all high-speed platforms well by harnessing this high-speed potential. MXI customers can use low-cost personal computers to control sophisticated VXI instrumentation without sacrificing performance or control. The introduction of synchronous MXI firmly entrenches MXI at the forefront of computer-based instrument control by increasing MXI performance to a new level and providing a framework for realizing performance enhancements well into the future. Current MXI-1 users can also capitalize on these performance benefits, because all of the software developed with MXI-1 technology using NI-VXI is completely backward compatible.

## Slide 35: Controller Block Transfer Performance
Notes: With MXI-2, you can achieve faster block transfer performance than all of the current VXI control solutions - even embedded VXI controllers.

## Slide 36: Elements of Virtual Instrumentation
VXI
Acquisition
and
Control
Analysis
Signal Processing
Digital Filtering
Statistics
Array Operations
Presentation
GUI
Hardcopy Output
File I/O
Signals
Notes: Looking at the VXI virtual instrument architecture, an important question arises – “Where does the analysis reside?” You can perform data analysis on a VXI controller, standalone DSP boards, or on the instrument itself. By designing data analysis capability into an instrument, the instrument designer defines a specific set of functionality. For some well-defined systems, this approach makes sense. However, as microprocessors continually improve in performance, VXI controllers become more powerful, and standard data analysis routines are delivered with application software packages, an opportunity arises to move more of the data analysis operations from the instrument to the controller so that the functionality is defined by the user, rather than the vendor. In particular, with MXI-2 you can take maximum advantage of general-purpose desktop computers with the latest, high-performance microprocessors to perform data analysis. Using this virtual instrument architecture, you can choose lower cost hardware with raw acquisition or stimulus capabilities and build the rest in software.
MXI-2 delivers on the promise of VXI. Faster, more capable sytems that take advantage of the latest computer and instrument technology. MXI-2 answers the question of where to put the analysis functions in the virtual instrument architecture. The answer is anywhere that you want. With MXI-2, you can take advantage of the most sophisticated instruments that perform analysis right on the card or simple instruments that rely on the controling computer for analysis. MXI-2 is a controller solution that gives you the best of both worlds.