## Slide 1
Plug and Play Sensors Forum

## Slide 2
Introduction – Problems and Community Solutions
    Mihir Ravel, National Instruments
Plug and Play Sensors Standards and Technology Update
    Kang Lee, Chairman of IEEE TC-9
    David Potter, Vice-Chair of IEEE P1451.4
Plug and Play Sensor Overview and Panel Introduction
Q & A
Agenda

## Slide 3
Panel Members
  John Kubler
  Gary Rendla
  Mark Lehmann
  Randy Baker
  Martin Armson
  John McNeight
  Joe Cheatham
  Kerby Hull
  B.J. Seif
  Jim Bishop
  Bob Clark
  Ed Herceg
  Joseph Pearson
Plug and Play Sensor Program
  Kistler
  Measurement Specialties
  Watlow
  Transducer Techniques
  Sensotec
  PCB Piezotronics
  Weed Instrument
  Lebow
  Wilcoxon
  Celesco
  Endevco
  Macro Sensors
  National Instruments

## Slide 4
World-wide
Plant-Wide
Factory-Floor
The Smart System Vision

## Slide 5
Many sensors
Many interfaces
Many networks
F18 Aircraft Static Fatigue Test System
“and this console is only one out of five total” - Phil Ellerbrock, Boeing Intellibus Team
…Reality

## Slide 6: Wide Range of Sensing Needs
Raw
Integration
Conditioning
Conversion
Processing
Communications
Raw
Housed
Industrial
Packaging

## Slide 7: Markets/Applications
Source: Intechno Consulting, 1999

## Slide 8: Plug and Play Sensors Lead to Smart Systems
Lower cost
  Reduced wiring
  Decreased setup time – ‘plug and play’ configuration
More reliable systems
  Self test
  Self diagnostics
  Distributed conversion and processing
Improved measurements
  Self calibration
  Increased quality and quantity of information
  Software reconfiguration
  Easier networking connectivity

## Slide 9: Smart Sensor – Market Drivers

## Slide 10: Smart Sensor – Market Restraints

## Slide 11: Today’s Starting Point
Very diverse sensing technologies
Broad range of industries and applications
Large installed base of legacy sensors
Variety of networks and networking standards

## Slide 12: Smart Sensor Technology Evolution
Ease of Configuration and Connectivity
Sensor Integration
(and Development)
Raw Transducer
Intelligent Networked Sensor
A/D
P
“Smart” Sensors
Sensor
Sensor
Legacy
Sensor
IEEE 1451.4 Sensors
TEDS
Lack of standards
  Proliferation of network technologies
Technological complexity, cost
  Networking, software
Environmental conditions of sensor
Installed base of legacy equipment

## Slide 13: Taking the Next Step
It takes a whole village to raise a child
Sensing System Suppliers
  Research community
  Sensor manufacturers
  Instrumentation (I/O, controllers, instruments, etc.)
  Network suppliers
  Software vendors
Consumers of Sensors
  End Users
  System Integrators
  OEMs (automotive, aerospace, consumer, medical, …)

## Slide 14: IEEE P1451.4 Smart Transducer Interface Standard
Started exploring of mixed-mode smart transducer concept in 1995 at NIST
Aim: develop simple, low-cost interface
  Take advantage of concept of Transducer Electronic Data Sheets (TEDS)
  Maintain analog signal output to accommodate installed base of legacy sensors and instrumentation
Status: finish draft this year; ballot beginning next year

## Slide 15: IEEE P1451.4 Standard for Plug and Play Sensors
Analog Signal
Voltage
Resistance
Bridge
Etc.
Transducer
Plug and Play Sensor
Digital (TEDS)
000101011111010101010010100…
Sensor manufacturer
Model number
Serial number
Measurement range
Transfer function
Calibration info
User Info
And more …
Transducer Electronic Data Sheet (TEDS)
Memory
(EEPROM)
Mixed-Mode
Interface
(Analog + Digital TEDS)
Standardized TEDS
Notes: A plug-and-play IEEE P1451.4 sensor provides a mixed-mode interface; that is, an interface that both preserves the traditional analog signal (whether a simple voltage, a current, an impedance, a bridge circuit, etc.) and adds a digital interface for transferring the TEDS information.
The TEDS can store information about the sensor such as the sensor’s manufacturer, model and serial number, physical measurement range, transfer function, calibration information, arbitrary user fields, and more.
The result is that a system supporting dot4 gains plug and play features of the sensor, including automatic uploading of all sensor information, automatic setup of measurement system software and hardware, and automatic use of calibration information stored in the sensor.

## Slide 16: IEEE P1451.4 – Mixed-Mode Interface
Bridge Sensor
Digital
TEDS
Analog
Digital I/O
Analog
Signal Output
+ Excitation
- Excitation
Data Acq. System
AMPLIFIER
SENSING
ELEMENT
CURRENT
ANALOG
SIGNAL
Pullup
Resistor
DIGITAL
I/O
-
5 V
TEDS
IEPE Sensor
Data Acq. System
Digital TEDS protocol uses proven 1-Wire® technology
  Power and communication on 2 wires (signal plus ground)
  Off-the-shelf EEPROMS from Maxim/Dallas Semiconductor
Defines 2 types of mixed-mode interfaces
Class 1 Sensor
  Sequential access of analog and TEDS on shared wires
Class 2 Sensor
  Parallel access of analog and TEDS; TEDS separate from sensor circuit

## Slide 17: IEEE P1451.4 – TEDS and Templates
Binary TEDS
<0011010101>
TEDS Software
Mfgr ID: 41
Model: 710LP
Standard Templates
Decoded Sensor Information
TEDS in sensor
Very Compact
- (usually < 256 bits)
Flexible
  IEPE Accelerometers
  IEPE Microphones
  IEPE Pressure
  Bridge Sensor
  RTD
  Thermistor
  Thermocouple
  Strain gauge
  AC LVDT/RVDT
  Voltage output
  Current output
  Resistance output
  Frequency output
IEPE Accel
IEPE Accel
RTD
Bridge Sensor
Templates
Serial Num: 0012113
Range: ±50g
Output: ±5V
Sensitivity: 98.7mV/g
Etc…
Transducer

## Slide 18
Bridge (mV/V) Load Cell
Manufacturer ID
21
Model ID
19
Version Letter
D
Serial Number
0008451
Calibration Date
Feb 10, 2001
Measurement range
 100 lbf
Electrical output
 3.01 mV/V
Bridge impedance
350 
Excitation, nominal
10 VDC
Excitation, min.
7 VDC
Excitation, max.
18 VDC
Response time
5 ms
Sensor Location
R32-1
Cal. record ID
543-01.23
IEPE Accelerometer
Manufacturer ID
43
Model ID
7115
Version Letter
B
Serial Number
00731F
Calibration Date
Jan 29, 2000
Sensitivity @ ref.
1.094E+03 mV/g
Reference freq.
100.0 Hz
Reference temp.
23 C
Measurement range
 50 g
Electrical output
 5 V
Quality factor
300 E-3
Temp. coefficient
-0.48 %/C
Direction (x,y,z)
x
Sensor Location
Strut 3A-p2
Calibration date
April 15, 2002
Basic TEDS
Standard and Extended TEDS
User Data
TEDS Examples
Example 1
Example 2

## Slide 19: Plug and Play Sensors
.
Analog Signal
(bridge, ICP, mV, etc.)
Sensor
IEEE P1451.4
Sensor manufacturer
Model number
Serial number
Measurement range
Transfer function
Calibration info
User Info (location)
And more …
TEDS
(EEPROM)
Transducer Electronic Data Sheet (TEDS)
Digital
(extra line, or switched w/ analog)
Smart TEDS Sensor
“Legacy” Sensor
Sensor
Analog Signal
Virtual TEDS
TEDS Database
WWW
Virtual TEDS file
Notes: A plug-and-play IEEE P1451.4 sensor provides a mixed-mode interface; that is, an interface that both preserves the traditional analog signal (whether a simple voltage, a current, an impedance, a bridge circuit, etc.) and adds a digital interface for transferring the TEDS information.
The TEDS can store information about the sensor such as the sensor’s manufacturer, model and serial number, physical measurement range, transfer function, calibration information, arbitrary user fields, and more.
The result is that a system supporting IEEE P1451.4 gains plug and play features of the sensor, including automatic uploading of all sensor information, automatic setup of measurement system software and hardware, and automatic use of calibration information stored in the sensor.
The Virtual TEDS initiative by National Instruments leverages the IEEE P1451.4 standard to provide the same information, found in an EEPROM, in a TEDS database via the Web.

## Slide 20
Panel Members
  John Kubler
  Gary Rendla
  Mark Lehmann
  Randy Baker
  Martin Armson
  John McNeight
  Joe Cheatham
  Kerby Hull
  B.J. Seif
  Jim Bishop
  Bob Clark
  Ed Herceg
  Joseph Pearson
Plug and Play Sensor Program
  Kistler
  Measurement Specialties
  Watlow
  Transducer Techniques
  Sensotec
  PCB Piezotronics
  Weed Instrument
  Lebow
  Wilcoxon
  Celesco
  Endevco
  Macro Sensors
  National Instruments

## Slide 21
IEEE
P1451.4
Collaboration
Backwards
Compatibility
Sensors
Measurement
Hardware
Programming
Software
Communicate
to End-Users
System
Integration
Web Based
Virtual TEDS database
NI Plug & Play Sensor
Partner Program
Multi-Vendor
Smart TEDS
Sensors
Development Kit
TEDS LabVIEW Library
Web Based
Plug and Play
Sensor Advisor
NI Alliance
Partners
Broad-Based Industry Adoption

## Slide 22
Accelerometers, Pressure & Force Sensors and Signal Conditioners for automotive, aerospace, manufacturing, etc.
Developed IEEE P1451.4 compatible charge output sensors
  use EEPROM (Dallas Semiconductor) in conjunction with the internal impedance converter
IEEE P1451.4 permits customizing of template to accommodate specific user requirements

## Slide 23
MEMS based sensors for pressure, acceleration, and force, plus LVDT, tilt, and ultrasonic sensors.
Plug and Play Sensor advantages
  Improved sensor data management
  Sensor inventory and calibration management

## Slide 24
Thermocouple temperature sensors
Heat treating application
Plug and Play Sensor capabilities facilitate the use of non-linear/non-standard sensors
Three times more stable

## Slide 25: Transducer Techniques Inc.
Sensor focus: load cells, force and torque sensors
Application focus: product development, product testing, force and torque measurement
Need for end users to search and find available Plug and Play Sensors

## Slide 26
Pressure, load, displacement, torque and vibration
Standard for P1451.4 sensors and signal conditioning makes Plug and Play Sensors universally appealing
Availability of general-purpose development tools will facilitate adoption by sensor manufacturers, system integrators, sensor users and sensor calibration facilities

## Slide 27
Digital communication enables transducer identification and specification
Walk-around data collection becomes automated and less prone to error
Automatic normalization of signal conditioning
Palm reader capabilities – portable download of information
Multi-channel cable management made easy

## Slide 28
Temperature sensors – RTDs and thermocouples
OEM and custom-engineered markets
Virtual TEDS address our installed base
  immediate payback
  where operating conditions make it impossible or impractical to use smart TEDS sensors

## Slide 29
Load cells – general purpose and fatigue resistant
Torque sensors – rotary and reaction
Applications for automotive, aerospace, test machine manufacturers, government and military
TEDS EEPROM includes model type, serial number, capacity, manufacturing data, etc.
Lebow® Products Inc.

## Slide 30
Vibration sensors for machine diagnostics
Programmable IC chip in Wilcoxon sensors
Accurate implementation of system set-up
End users and sensor vendors need a TEDS programming tool for development
W i l c o x o n
Notes: Wilcoxon has been manufacturing piezoelectric sensors for over 40 years. Wilcoxon’s piezoelectric accelerometers are in use worldwide gathering valuable information about the mechanical condition of large rotating machinery.
The National Instruments TEDS LabVIEW Library can be used to automate the programming of the Dallas chip in Wilcoxon’s IEEE 1451.4 based TEDS sensors. This allows Wilcoxon to speed up the programming of accelerometers at the time of manufacture.
The combination of the Plug & Play capabilities in the National Instruments inherent in LabVIEW with the TEDS programmability of Wilcoxon accelerometers, allows users to implement rapid, accurate, cost-effective system setup.

## Slide 31
Cable-extension position transducers
  Linear measurement from 40 mm to 40,000 mm
  Chosen for ease-of-use
Structural, fatigue, on-road, and flight test
Open industry standards will lead to better more competitive product offerings for end-users.
Celesco

## Slide 32
Accelerometers, pressure transducers,and high intensity microphones have been integrated with TEDS
  Piezoelectric, piezoresistive (bridge) and variable capacitance sensor technologies
  Aerospace and automotive applications
Plug and Play technology offers improved test configuration control resulting in reduced cycle time and ease of system calibration
TEDS implementation goal: a minimal increase in package dimensions with a nominal increase in cost

## Slide 33
LVDT position sensors and gaging probes
  Frictionless motion and precision dimension measurement
Plug and Play LVDT position sensors
  Virtual TEDS for AC LVDTs (175°C) - external S.C.
  Sensors for legacy and high temperature applications
  IEEE P1451.4 for DC LVDTs (85°C) - internal S.C.
  Both hardware TEDS and virtual TEDS available

## Slide 34
Panel Members
Questions
and
Answers