## Slide 1: Introduction to Real-Time Control
Greg Morrow
Software Engineer
Wed Aug 16
10:15 - 11:30 a.m., 1:45 - 3:00 p.m.
Red River (4B)

## Slide 2: What You Will Learn
What is real-time?
How does LabVIEW RT work?
How can LabVIEW RT create real-time control applications?

## Slide 3: Real-Time Definitions
Real-Time does NOT mean real fast
Hard real-time
  Flight control
  Engine testing
  Alarm monitoring
Soft real-time
  Internet servers
  Banking
More soft real-time apps than hard
Notes: Hard real-time systems have deadlines that must be met at ALL times, and the system must behave deterministically. These “hard” systems prioritize and trigger events in known manners. Failure to meet preconditions and deadlines collects incorrect data and invalidates program results. Or, more importantly, failure to meet a deadline can cause catastrophic loss of hardware or human life.
Hard real-time systems need determinism, not necessarily speed. They must also operate in a stable and reliable manner. For example, an engine dynamometer must operate in real-time to avoid bad data on engine performance, which can potentially damage equipment.
Soft real-time systems also must meet certain conditions and deadlines. However, a soft real-time system still functions properly and yields usable data even if it misses a small number of deadlines. For example, when logging temperature to disk once per second to look for a general temperature trend in a 10-minute period, you would still see a general trend and have a successful logging system even if you failed to log one of your measurements.

## Slide 4: Real-Time Applications
Real-time control
Interrupt and response
Data reduction
Data logging
Notes: We can divide real-time data acquisition applications into two broad classifications – real-time data collection and real-time stimulus and response.
Real-time data collection today uses modern DAQ boards that have advanced on-board circuitry to bring in data continuously and in real-time. Examples include the National Instruments MITE controller chip that allows scatter-gather PCI bus mastering for high bandwidth data transfer from DAQ board to the host PC. This real-time data collection frees up the host computer for analysis and display.
Modern computers can do a lot of processing. Therefore, trending and data reduction applications such as temperature monitoring and thermocouple linearization can be accomplished in real-time on a desktop computer system. Spectrum analysis applications like FFTs also can execute in real time. As long as you can process and view the data at acceptable rates to the human eye, you are maintaining real-time for your user interface.
In an interrupt and response type application, a user defined response is generated based on a process input. For example, if a pressure level gets too high, shut down the process. In deterministic control applications such as PID controllers, the ability to acquire, process, and respond continuously at precise time intervals is the real-time need. On most systems with plug-in DAQ boards, this decision step is when Windows is involved in the data analysis and this may limit your real-time performance.

## Slide 5: Real-Time Challenges
Windows not guaranteed hard real-time
Many real-time target platforms
Difficult software integration
  Fixed or very limited programmability
  Limited ability to network to the enterprise
Separate development environments
  Time consuming
  Costly
LabVIEW RT helps with these challenges
Notes: PR1A– <number>
Introduction to Real-Time Control
<header>
<date/time>
Although people use Windows to solve many real-time applications, they can’t guarantee their real-time response due to device driver scheduling and internal Windows functions like memory management. When determinism must occur at the millisecond or microsecond level, engineers explore alternative operating systems and independent real-time controllers.
Controllers come in a variety of hardware platforms and have the same variety in software development tools. Some controllers have fixed or limited programmability, while others are more programmable but have closed or proprietary development systems. Because these development environments are usually not the same measurement and automation application development environments used for the rest of the systems, integration of the real-time pieces can be difficult. Separate development environments mean more languages to learn, more development and debugging time, and more money spent. In addition, these controllers normally have difficulty networking to other systems in the enterprise.
With LabVIEW RT, you can preserve your Windows development skills and connectivity, and at the same time get the real-time control and deterministic behavior of a real-time operating system based independent controller.

## Slide 6: Typical Real-Time Applications
Windows NT
LabVIEW RT
Hardware
Milliseconds Microseconds
1000 100 10 1 100 50 10 1
Mechanical Test
Telecom Test
Motion Control
Hydraulic Control
Business/POS
Medical
Network Control
H/W Loop
Simulation
Dynamic Signal Analysis
Industrial Automation
Internet
Notes: The time constraint of when you must respond to events dictates what tools you can use for your real-time application. Because Windows can respond in real time within a few hundred milliseconds, it can solve many real-time applications today. Products like LabVIEW RT or systems built with other real-time operating systems can solve applications with faster real-time constraints. For very fast real-time responses, you must use dedicated hardware programmed with DSPs (digital signal processors), FPGAs (field programmable gate arrays), or custom ASICs.
As computer processors continue to increase in performance, more real-time applications can be solved with Windows or LabVIEW RT.

## Slide 7: LabVIEW RT Architecture
Host PC
Target RT Engine
Download
Application
Notes: LabVIEW RT consists of two components. The host development system runs on Windows and has the look, feel, and functionality of standard LabVIEW. The target RT engine runs on the embedded processor, employing a real-time operating system. The connection between the two pieces is handled transparently, so that applications can download from the host to the target and front panels on the host can update from the target. The target also can run LabVIEW applications without any host connection.

## Slide 8: LabVIEW RT Host System
User experience is exactly the same as LabVIEW for Windows
LabVIEW RT running on Windows transparently handles user interface interaction with the RT engine on the target
“Run” button automatically downloads to target
Users have full LabVIEW debugging capabilities
Notes: The LabVIEW RT development system is a superset of LabVIEW and looks almost identical to standard LabVIEW. All the normal LabVIEW editing features and controls and functions are available (with some extra RT-only VIs provided in VI.LIB.) When a virtual instrument runs, LabVIEW RT downloads the VI and its sub-VIs to the execution target and initiates execution there. While the VI is running, its front panel constantly updates with values sent from the embedded execution engine. LabVIEW RT provides full debugging capabilities, including breakpoints, probes, and execution highlighting from the Windows environment.

## Slide 9: Embedded Execution Engine
Runs on PXI controller or plug-in board
Executes LabVIEW diagrams
Contains multithreaded real-time operating system kernel
Runs independently from the host computer
Notes: The LabVIEW RT embedded execution engine runs on the RT Series hardware. Running a stripped-down version of LabVIEW, without LabVIEW’s editor, display mechanisms, and compiler, the execution engine: 1) listens for and services a connection to a LabVIEW RT host development system and 2) executes LabVIEW virtual instruments. The execution of virtual instruments can proceed in the absence of a host connection. The operating system on the embedded system is a preemptive multitasking, multithreaded, real-time kernel. The LabVIEW RT execution engine is the only application running on the embedded computer.

## Slide 10: LabVIEW RT and RT Series DAQ
RT Engine on
RT Series DAQ Board
LabVIEW RT Development
System on Win 2000/NT/9x
DAQ Daughter
Board
Processor
Board
Shared Memory
TCP/IP,
VI Server
Notes: PR1A– <number>
Introduction to Real-Time Control
<header>
<date/time>
A LabVIEW RT System consists of LabVIEW RT applications and a real-time hardware target. LabVIEW RT generates embedded LabVIEW code that runs real-time on the hardware target. Examples of a hardware target include the intelligent, processor-based RT Series DAQ boards that plug into a host computer. This hardware target runs the RT Engine and the VI applications the user creates for running in real-time.
The National Instruments RT Series DAQ boards consist of two components – a processor board and a DAQ daughter card. Like a PC, the National Instruments RT Series processor board includes a CPU, standard PC chipset, BIOS, and RAM. Unlike a PC, the processor board does not have a disk drive, monitor, keyboard, mouse, or other standard PC I/O devices such as a serial or parallel port. Because the National Instruments RT Series board has no user interface and no disk drives, it must work in conjunction with a host computer for application development, debugging, data logging, user interaction, and so on. The National Instruments RT Series boards are available in two different plug-in platforms – PCI and PXI (CompactPCI eXtensions for Instrumentation).
The three DAQ card models available with the intelligent card are the:
PCI/PXI 7030/6040E 12-bit multifunction I/O
PCI/PXI 7030/6030E 16-bit multifunction I/O
PCI/PXI 7030/6533 32-channel high speed DIO

## Slide 11
LabVIEW RT Development
System on Win 2000/NT/9x
Ethernet
RT Engine on
PXI controller
LabVIEW RT and the RT Series PXI Controller
TCP/IP,
VI Server
Notes: PR1A– <number>
Introduction to Real-Time Control
<header>
<date/time>
In March, we announced the LabVIEW RT engine running on the PXI controller. You develop on a Windows machine separate from the controller. You download the code and communicate with the RT application from the PC through Ethernet. The controller controls a chassis full of any combination of data acquisition, including signal conditioning and accessories, in real-time. In addition, the controller also supports the built-in serial ports, GPIB port, MXI-3, and data logging to the hard drive. This controller runs only the RT engine and user applications downloaded to it.
The RT controller is available as the PXI 8156B/333 RT, preinstalled with the RT engine and ready for configuration through the Remote System Configuration utility installed with LabVIEW RT software on your host machine. You can upgrade existing 8156B Windows controllers with the RT software, but this requires run-time licensing.
Note: The controller currently does not support : plug-in Ethernet, serial, CAN, RT Series DAQ, IMAQ, motion, and instruments.

## Slide 12: Benefits of LabVIEW RT
Deterministic, real-time execution of LabVIEW code
Reliable – still runs if PC crashes
Fully programmable with LabVIEW – no proprietary library calls
Notes: What are the benefits of LabVIEW RT? First and foremost, LabVIEW RT guarantees deterministic performance of programs written in LabVIEW. For many soft real-time and hard real-time applications, LabVIEW RT provides a simple, user-friendly environment from design to deployment. Once your application is deployed, it operates independently of the Windows host, or a Windows machine can monitor and control the application. From the point of view of application design and development, LabVIEW RT is identical to LabVIEW; therefore, it leverages all the integration benefits and ease-of-use of LabVIEW.

## Slide 13: Performance Benchmark
Typical control application
  Analog in
  PID computation
  Analog out
Optimized LabVIEW code
  The “Advanced RT Control” session discusses the optimizations and conditions for these benchmarks
Notes: To give some idea of the performance of LabVIEW RT running on the RT Series hardware, we chose a common control application and timed it on our plug-in board and our PXI controller. Using a PID control loop, each loop iteration consists of reading an analog input, performing the PID calculation, and outputting an analog value. Please note that the code for the benchmark is not exactly the same as the example provided with the PID toolkit. Some RT-specific optimizations have been made in the code.

## Slide 14: PID Performance of LabVIEW RT
Analog in, PID computation, analog out*
PXI 8156B, 333 MHz
  1 PID 10,200 Hz
  8 PID 5,350 Hz
PCI 7030/6040E (133 MHz 486)
  1 PID 2,360 Hz
  2 PID 2,025 Hz
  *Optimized LabVIEW code

## Slide 15: LabVIEW RT Demos

## Slide 16: Summary
Array of real-time applications
Reasons for a non-Windows OS
Architecture of LabVIEW RT