## Slide 1: How Does the Internet Work?
Dr. Guy Vachon
Section Manager
Wed Aug 16
10:15-11:30 a.m., 1:45-3:00 p.m.
Colorado (6A)

## Slide 2: Agenda
Ethernet and networking
  Networks, protocols, physical layers
  Determinism
  Addressing
  Firewalls

## Slide 3: Ethernet is Everywhere
Fast becoming de facto corporate standard
Low cost
Easy to install, use, and maintain
Well understood
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>
Ethernet has become the de-facto corporate information and manufacturing networking standard. This ubiquity of Ethernet provides many benefits, including:
Very high commercial volumes – built into the motherboard of many PCs and can cost less than $200.
De facto standard high-speed communication backbone.
Sharing information between business applications.
Existing in-house experience in network administration groups, which have capabilities to design, install, and maintain complex Ethernet infrastructures.

## Slide 4: Simple Ethernet Network
  Use a crossover cable to link two Ethernet devices
  Or better yet – use a hub
128.1.0.0
N
N
N
N
PC
Ethernet Device
X.X.X.X
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>
The simplest case of an Ethernet “network” is to connect two devices together. This may be desirable when only the speed of Ethernet is required. In this diagram, a single PC is “networked” to a single FieldPoint device.
When using unshielded twisted pair cable, you must use a special cable type known as a crossover cable (sometimes referred to as a null modem cable). Because the vast majority of Ethernet applications with unshielded twisted pair media connect devices to hubs (as shown on the next slide) and do not need this crossover cable, it is easy to forget that such cables are needed in this simple case.

## Slide 5: The OSI Model
Application
Transport
Network
Physical +
data link
OSI names
TELNET
FTP
SMTP
DNS
TCP
UDP
IP
ARPNET
Cellular
ATM
Ethernet
100VG
Protocol
What you do with it
Where bits pass
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>
Ethernet has only recently become the de facto network standard. Over the years there have been many communication “models” and “protocols” that evolved to transmit data from one system to the next. Some of these are ARPNET, SONET, ATM, Ethernet, and so on. Upon all of these communications models, the protocol TCP/IP has bubbled to the top.
In its simplest form, one can now think of the industry de facto architecture as TCP/IP within the open systems interconnection (OSI) model as shown above. TCP/IP has become the standard protocol for sending voice, data, and even video.

## Slide 6: The OSI Model
UDP
IP
ARPNET
Cellular
ATM
100VG
Protocol
Where bits pass
Application
Transport
Network
Physical +
data link
OSI names
TCP/IP
Ethernet
What you do with it
Pass data
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>

## Slide 7: What is Ethernet?
Based upon CSMA/CD – carrier sense multiple access with collision detection
A
B
C
To B
To B
To B
To B
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>
Many people use the word Ethernet to mean the entire communication process, when in fact it only defines the physical communication method.
Ethernet access is done using a method called carrier sense multiple access with collision detection (CSMA/CD). In this method, multiple devices, or nodes, can listen until no signals are present. If they think that no other device is transmitting, they can attempt a transmission. After transmission , each communicator checks to see if a collision occurred. If it did, they wait and attempt to retransmit after a pre-set delay.
A second fundamental component of Ethernet is the Topology:
Bus – the simplest, in that all devices are connected in succession on a single cable. All transmissions go to all the connected devices with each device selecting those transmissions it should receive. An easy identification at a customer site is by the cable type. Most all Coaxial mediums are Bus topology.
Star – all attached devices are wired directly to a central hub, which establishes, maintains, and breaks connections, in the event of an error. The advantage of a star is that it is easy to isolate problems in the network. Star topologies come with many different forms of transmission media, including 100BaseT (phone type connector), 10 BaseT, fiberoptic, and so on.

## Slide 8: What is Ethernet?
Topologies
  Bus
  Star
XCVR
XCVR
XCVR
HUB
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>

## Slide 9: Is Ethernet Deterministic?
The faster the net, the lower the collision rate
  shared net can remain deterministic up to 10% of bandwidth load
  switch based net can remain deterministic at higher bandwidth load
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>
Often, in a data acquisition-based discussion the first question that arises is the question of determinism. Determinism of Ethernet is very dependent upon the amount of activity on the network.
Based upon the definition, one can say that the faster one can make the network, the less collisions that will occur and the more deterministic the system can become. A rule of thumb is that with a shared network, one can remain deterministic up to 10% of the bandwidth load. A switched-based net can remain deterministic up to 30% of the bandwidth load. You will learn the difference between a shared and switched network later.

## Slide 10: Cable Types for Ethernet
Operational
characteristics
10BASE-T
100BASE-TX
fast Ethernet
10BASE-5
Thickwire
10BASE-2
Thinwire
10BASE-FL
Rate
10
Mbps
100
Mbps
10
Mbps
10
Mbps
10
Mbps
Maximum
segment length
100 m
100 m
500 m
185 m
2,000 m
Devices/segment
2
(12/hub,
typ.)
2
(12/hub)
100
30
2
(12/hub,
typ.)
Medium
UTP
UTP
Coaxial (thick)
Coaxial (thin)
Fiber optic
Topology
Star
Star
Bus
Bus
Star
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>
Besides the unshielded twisted pair media 10BASE-T and 100 BASE-TX, there are three other major media types in common use today – thick coaxial (Thickwire) for 10Base5 networks, thin coaxial (Thinwire) for 10Base2 networks, and fiber optic for 10Base-FL networks.
The coaxial media (Thickwire and Thinwire) options, unlike the unshielded twisted pair media, uses a bus, not a star, topology. With Thickwire, you can have up to 100 devices on each bus, and up to 500 m length on the bus. With Thinwire, you can have 30 devices on buses of up to 185 m length.
Fiber optic media in a 10Base-FL network provides a star topology similar to the unshielded twisted pair media, but extends the distance between devices to 2000 meters. Fiber optic, although more expensive, is invaluable in applications where electronic emissions and environmental hazards are a concern. For example, fiber optic cable may be used in inter-building applications where long distances or insulation from damage caused by lightning are concerns.
Hybrid topologies that mix different types of media in a network are not only possible but common. There are many devices available that either convert one media to another or work with multiple media types.

## Slide 11: Simple 10/100Base-T LAN
  A 10/100Base-T hub connects multiple devices
PC
N
N
N
N
10/100Base-T hub
(Multiport repeater)
Ethernet devices
N
N
N
N
128.2.0.1
128.2.0.2
128.2.0.3
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>
To make a company’s network infrastructure easier to manage, most companies use a Hub/repeater, which can be purchased at local computer outlets for under $100.
To connect more than two devices to a star topology with media such as 10Base-T or 100Base-TX, you need to use a hub. Simple hubs have multiple Ethernet ports and repeat incoming signals out all of the other ports. Thus, these simple hubs are often called “repeaters” or “multiport repeaters.” When connecting devices to a hub, you use normal (sometimes referred to as “straight-through”) UTP cable.
IP addressing using a hub would follow the same rules as a simple device as mentioned in the previous slide.

## Slide 12: Understanding an IP address
32-bit physical IP address
Logical machine name
WINIPCFG
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>
To understand the basics of networking Ethernet, one must understand the terminology. At a high level, each PC on a Windows-based network will have a logical name. To see all nodes, go to the Network Neighborhood.
Several parameters are needed by the Windows operating system to see other nodes on the network:
IP Address
Subnet
Gateway

## Slide 13: Understanding IP Address
Each device on the network must have a unique IP address (130.164.0.0)
  First octet defines network class
    0-127 Class A (Huge companies!)
    128-191 Class B
    192-223 Class C
    224-255 other
Class A
Class B
Class C
0
1
0
1
1
0
16
8
31
24
hostid
netid
netid
netid
hostid
hostid
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>
Each node on the network must have a unique IP address. Nodes on the same physical network must have the same Class and the same NetID values.
NetID numbers are assigned by the Network Information Center (NIC). From the company-assigned NetID one can format several networks. National Instruments assigned NetID is 130.164. From the above, this means we are a Class B network.
If assigned a Class A NetID allows for 126 networks with 16 M hosts each. If assigned a Class B NetID allows for 16,382 networks and 64 K hosts. If assigned a Class C NetID allows for 2 M networks and 254 hosts. Each machine, (FieldPoint I/O) on the net is also defined by a hostID.
From the NetID of 130.164 assigned to NI, NI can have 64K hosts/nodes. Through the use of subnets, many more hosts/nodes can be assigned. More on subnets later.

## Slide 14: Components Used In A Network
Hubs/repeaters
Bridges/switches
Routers/gateways
Firewalls
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>
To increase determinism, make the network easier to manage, and increase the number of available hostIDs, a company uses three common components: hubs/repeaters, bridges/switches, and routers/gateways.

## Slide 15: More Complex 10/100 Base-T LAN
10/100Base-T hubs
(Multiport repeaters)
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
To corporate
backbone
  With simple hubs, all devices see all traffic
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>
You can use hubs to extend the network by connecting hubs to each other. Different hubs have different methods for cabling to each other. Some hubs might have a combination of UTP and coax media – one common application is to use hubs with several UTP ports for the different devices and with one coax port that is used to connect all the hubs together. Many UTP hubs have a special port (the “uplink port”) for connecting to other hubs with normal, straight-through cable. However, you can also connect hubs to each other through the standard port using crossover cable. When connecting hubs together, the main rule is to read the manual!
Hubs/repeaters only allow the devices to share Ethernet. A network created with hubs/repeaters is termed a “shared Ethernet,” meaning that all devices on the network are contending for transmission of data onto this single network. This network is called the “collision domain,” because if any two devices start to talk at the same time they cause a collision. After detecting the collision, both devices “back off” by stopping transmission then waiting a random amount of time before retrying to send the data.

## Slide 16: LAN Using Switching Hubs
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
To corporate
backbone
Local traffic
Local traffic
Traffic routed to destination
Switching hub
Repeater hub
Switching hub
Segmented collision domain
Repeater hub
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>
In addition to the simple repeating hubs that simply provide connectivity for multiple devices to share an Ethernet “collision domain,” there are other, more sophisticated, devices that actually separate the network into different segments or subnets, each with its own collision domain. These devices, called “switches”, selectively filter network traffic to pass only those messages needed on each segment. This significantly increases throughput on each segment and on the overall network. As defined in slide 4, determinism increases to 30% of load for a switched network.
You can use bridges or switches that separate Ethernet segments into separate collision domains and can be used in the same manner as repeater hubs, although they are somewhat more expensive, and may be called “switching hubs.” Switching hubs inspect a message coming in on one port, identify the destination device, and send the message only out the port which will get it to the destination device. Some switching hubs filter corrupted messages.
As shown above, two repeater hubs from the previous slide are replaced by switching hubs. This separates the Ethernet into multiple collision domains. For example, the hub on the left is still a simple repeater hub, so any traffic on its ports are repeated out all the other ports, and the devices connected to it share the same total bandwidth. However, the hub on the right is a switching hub, and prevents the local traffic to the left hub from getting on the networks of the other hubs.
The hub on the top is also a switching hub. It filters traffic from the corporate network. PCs and devices are free to communicate simultaneously on their Ethernet ports because the switching hub has separated them into different collision domains.
Because you can easily use switching hubs in place of repeater hubs, switching hubs are a simple method of improving bandwidth and are generally appropriate as the network becomes more than about 35 percent loaded.
One note – switch only hubs do not divide the network into separate hostIDs.

## Slide 17: Subnet Mask
  Determines whether local machine routes message to gateway
  Reduces traffic on network
  e.g. 255.255.255.0
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>
The last basic element of networking is the concept of a Subnet, which addresses an extension of the IP address scheme that allows a site to use a single netId for multiple physical networks. Instead of having to ask NIC for a new netID, a company can assign bits from the hostID bytes to create new physical netIDs.
Routing outside the site continues as usual by dividing the IP address into a netID and a hostID via the class. Inside a site, the subnet mask is used to re-divide the IP address into a custom netID portion and hostID portion.
For example selecting a subnet mask of 255.255.255.0 would add two additional netID bits, allowing for four physical networks.
11111111 11111111 11111111 00000000
In effect, 8 bits of the Class B hostID have been used to extend the netId, creating an extended netID, or subnet ID. Each unique combination of bits in the part of the hostID where subnet mask bits are 1 specifies a different physical network.
In the slide above, gateway G1 is the entrance into the corporate network. Within the internal network is gateway G2. Instead of having a new netID, the submask 255.255.255.0 is used to barrow the upper byte of the hostID. This allows for 255 additional physical subnet based netIDs.

## Slide 18: Gateway/Router
  Network is divided into local sub-networks
N
N
N
N
N
N
N
N
Gateway G
Switching hub
130.164.0.1
130.164.0.2
130.164.0.3
130.164.0.4
130.164.0.6
130.164.0.5
Internet
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>
The next type of component used to build a network is the Gateway, which filters out network traffic by specific protocol. An IP gateway/router divides the network into different logical subnets by interpreting the content of the messages. A key difference in a gateway is that the netID changes on either side of the gateway.
Although the inspecting of messages can add small delays, the overall efficiency added to the network is much improved. Because they work at the protocol level, you must configure the Ethernet devices with knowledge about the routers/gateways. And, because they operate at the protocol level, they can connect Ethernet to other types of networks that work with the same protocol.
For example, to enter into the NI domain, one goes through our gateway at 130.164.0.0. To get between Europe and Japan, NI leases dedicated bandwidth. This allows use to use the same netID between each facility.

## Slide 19: FieldPoint™ Demonstration
Connection to a local FP-1600 system
Ethernet hub
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>
In the first demo, we demonstrate how to connect a computer to an FP-1600 on a local LAN network. Another option would be to connect to an FP-1600 without a network connection. In this case, we would need a crossover cable, which has a different pin-out from a regular straight though cable used to network connections – some pins are reversed, much like the difference between a regular RS-232 serial cable and a null modem cable.
In this demonstration, we acquire data from dual-channel FieldPoint modules, which are two channel I/O modules. A dual-channel base behaves much like a regular FieldPoint base, and it allows six dual-channel FieldPoint modules on one base. Each dual channel FieldPoint module is completely isolated from the rest, and there are two-channel discrete versions, as well as two-channel single ended or one-channel differential analog inputs and outputs. The two-channel modules give our customers more flexibility in choosing their system by allowing several different signal connections to coexist concurrently on a same FieldPoint module. In this case, we will be using discrete I/O.

## Slide 20: Networking Primer

## Slide 21: Firewalls
A program or device that sets up an invisible boundary between you and the Internet
  To prevent unauthorized access
  To protect privacy

## Slide 22: Dual-Host Gateway
Program that filters connections into your computer
  Typical model for stand-alone personal firewall
  Two machines exchanging information
Internet Service Provider

## Slide 23: Screened-Host Firewall System
Sets up a router
Filters connections coming in or out
Packets that are not for you do not come through
Your internal packets do not go out
X

## Slide 24: Demilitarized Zone Firewall
Sets up a buffer zone between the Internet and a computer
  Allows voluntary passage of data among consenting entities
X
X

## Slide 25: Thank You For Your Attention
Enjoy your visit to NIWeek 2000!!!