## Slide 1: Real-Time Dynamometer Control
Doug Norman
Product Engineer
Wed Aug 16
12:00-1:15 p.m
Lavaca (6B)
Notes: Goals of this session:
1. You will gain a basic understanding of how a dynamometer works.
2. You will learn software architecture ideas for running LabVIEW™ RT applications on a PXI controller.
3. You will see the components and workings of a specific dyno demo.
4. You will see examples of typical transducers (temperature, pressure, vibration, position) and specific SCXI modules used to interface these transducers.

## Slide 2: Overview
System schematic
  Generic – What is a dyno?
  Specific – What’s in this dyno?
Software architecture
  Host user interface
  RT control and measurement
Measurement and control hardware
  LabVIEW™ on PXI-8170
  LabVIEW RT on PXI-1011
Dyno demo

## Slide 3: What is a Dynamometer?
DAQ-STC
Load cell
SCXI signal conditioning
DAQ board
Dyno load
controller
Electric
dyno
Throttle
controller
Unit under
test
(engine)
Mag
pickup
LabVIEW
Thermocouple
Notes: What is a dynamometer?
Webster: Any of several devices for measuring the energy expended by a force.
zone.ni.com: An instrument that provides rotational resistance to a unit under test (UUT). Typically used to load engines and determine performance characteristics in the automotive industry. Dynamometers may either drive the UUT or absorb its energy, or both. A universal dynamometer both drives and absorbs power to the UUT.
In a pure sense, a dynamometer measures force, speed, or power. However, dynamometers are also used to test parts under load. In the diagram above the UUT is coupled to a dyno. One typical test is to measure engine speed and torque while a braking force is applied. From the speed and torque values, engine power can be calculated (Horsepower = torque x rpm / 5252). Another common test is to have a motor on one side, a braking force on the other, and the UUT in the middle – in this case the UUT might be something like a transmission or a CV joint.
The braking force can be supplied in many ways. Popular braking methods used in industry today include water brakes, eddy current, AC motor, and DC motor.

## Slide 4: Components, Measurements, and Transducers of this Dyno
Drive
motor
Strut
Accelerometers
Rollers
Tire &
wheel
Disk brakes
Encoder
(MPH)
Load cell
Master brake
cylinder
Variable frequency
drive
Current donut
VFD
Pedals
Brake
Gas
Brake actuator
Thermocouples
Notes: Measurements: Control:
wheel speed (encoder) drive motor (AO to VFD)
brake pressure master cylinder via brake actuator
temperatures
vibration (accelerometers)
current
brake pedal (linear potentiometer)
gas pedal (linear potentiometer)
Connection notes: The current donut requires additional circuitry to measure RMS current. All other components (linear pots, VFD, brake actuator, encoder, accelerometers, thermocouples) are directly wired to SCXI modules. Digital relays run the brake actuator – three were used to provide lockout safety.
Main Goal: To show that LabVIEW RT running on a PXI embedded controller can be used to run industrial dynamometers. This dyno uses a PID controller to run user defined profiles (speed vs time) with varying brake pressures.

## Slide 5: User Interface Software
Diagnostics
Dyno main
Information
Game
Start screen
Data log setup
Profiler setup
VI server
RT Host
Notes: The User interface software uses a state machine to handles menu selections.
Start Screen allows you to choose which application to run. This demo will be used at trade shows so it needs to run as a dyno while being informative and entertaining.
Diagnostics is a password protected interface where raw I/O can be tested.
Dyno Main is the main interface where the dynamometer runs showing profile updates and other monitored parameters. Prior to running, a speed vs. time profile can be chosen or drawn, and data logging can be configured. Notice that the Information screen can be accessed from here.
Information is an application that tells everything about the demo including all the NI hardware used, the cost of the hardware, LabVIEW RT, transducers, and general notes on building the demo.
Game is an interface where you can “drive” the demo. This allows users to try following a profile as the computer PID controller would. It also provides scoring – what’s a game without a score?
VI Server is an application that communicates data between LabVIEW RT running on the PXI controller and LabVIEW running on the host PC. This application runs parallel with the other chosen application.

## Slide 6: RT Acquisition and Control Software
Data logging
VI server
Host RT
Log data to
host
Game control
Dyno main
control
Control
state machine
Diagnostics
Notes: The acquisition and control software also uses a state machine architecture. Most RT application names mimic the host names. The difference is that the host side handles user input/output, the RT side performs the actual acquisition, control, and data logging. User inputs and control outputs are communicated between the host and RT using the VI Server.
Diagnostics is a DAQ application where individual parts of the dyno can be tested.
Dyno Main Control is a DAQ application that uses a PID controller to run speed vs. time profiles while monitoring temperatures, pressure, vibration, current, etc. This application also handles immediate data logging.
Data Logging handles immediate logging of current data if logging has been configured from the host side. Data is logged to the RT computer.
Log Data to Host sends data back to the host for long term storage and review. This application only runs when no dyno application is running.
Game Control is a DAQ application where user input directly controls the speed and braking. Here the computer still monitors and can intervene in the event the user really has no business being on the road.
VI Server is an application that communicates data between LabVIEW RT running on the PXI controller and LabVIEW running on the host PC. This application runs parallel with the chosen DAQ application.

## Slide 7: User Interface Hardware
PXI-1000B, 8-slot chassis
  PXI-8170 embedded controller
  PXI-8210 fast Ethernet LAN interface
INNOVA STS-4018-RT monitor
Notes: PXI-8170 Embedded Controller:
  700 MHz Intel Pentium III processor
  256 MB RAM
  1 serial, 1 parallel, 1 USB port
  1.44 MB floppy drive
  4 GB hard drive
  Super VGA with 2MB RAM
  PS2 keyboard and mouse connectors
PXI-8210 Fast Ethernet LAN Interface
  100BaseTX (100 Mb/s); 10BaseT (10Mb/s)
  RJ-45 connector with integrated LEDs
  Wide Ultra SCSI interface
  External 68-position shielded connector
INNOVA STS-4018-RT Monitor
  All metal 19” rack mount
  NEMA 4 front panel
  18.1 AM-TFT LCD Monitor
  www.innovaelec.com

## Slide 8: Measurement and Control Hardware
PXI-1011 (4 PXI slots, 8 SCXI slots)
  PXI-8156 embedded controller
  SCXI-1530 accelerometers
  SCXI-1124, 1325 analog outputs
  SCXI-1126, 1320 frequency input
  SCXI-1121, 1320 analog inputs
  SCXI-1112 thermocouples
  SCXI-1161 switch/relay
Notes: PXI-8156 Embedded Controller: 333 MHz, 32 MB RAM
SCXI-1530: 4-channel integrated circuit piezoelectric (ICP) analog input module used to read accelerometers – BNC direct connect
SCXI-1124, 1325: 6-channel, 12-bit, analog output used to control the variable frequency drive (VFD)
SCXI-1126, 1320: 8-channel isolated frequency input used to read an encoder for tire speed
SCXI-1121, 1320: 4-channel isolation amplifier with excitation, used to read brake fluid pressure, drive current, gas pedal, and brake pedal
SCXI-1112: 8-channel amplifier, used to read thermocouples for inner and outer brake pads, drive motor, and VFD
SCXI-1161: 8-channel switch relay, used to control the brake actuator bang-bang control system

## Slide 9: Demo – Tire Dynamometer

## Slide 10: Questions and Answers
Notes: Want to know more about Real-Time and LabVIEW RT?
Introduction to Real-Time Control
Wed Aug 16, 1:45-3:00 p.m. Red River (4B)
Greg Morrow, Software Engineer
Real-Time Programming with LabVIEW RT
Thurs Aug 17 10:15 a.m.-1:15 p.m. Exhibit (3G)
Thurs Aug 17 1:45-4:45 p.m. Exhibit (3G)
John Limroth, Software Engineer
Advanced Real-Time Programming Techniques
Thurs Aug 17 12:00-1:15 p.m. Hickory (9C)
Thurs Aug 17 3:30-4:45 p.m. Hickory (9C)
Joe Hays, LabVIEW RT Product Support Engineer