## Slide 1: A Practical Application of Wavelets for Measurement – Automotive Engine Knock Detection
Sam Shearman
Product Manager, Signal Processing and Analysis Software
Wed Aug 16
1:45-3:00 p.m.
Lavaca (6B)

## Slide 2: Presentation Overview
Measurement applications of signal processing and analysis
A practical application – engine knock
Wavelets and Fourier analysis
National Instruments software for wavelets
Notes: Most discussions of wavelets and other mathematical constructs are heavy on theory and math. A real-world application – Detection of engine knock from an audio or vibration signal – is a good example for this presentation. Although this application is somewhat specific, the same ideas apply to analysis of any signal in which you wish to detect transients.

## Slide 3: The Measurement Application
Acquire
Present
Analyze
Notes: Before we begin, we need to assign a broad perspective to the upcoming topic, relate why analysis and signal processing are important topics, and mention where National Instruments software fits in to the mix.
Three tasks common to most PC-based measurement applications include, acquisition, analysis, and presentation.
Where does National Instruments software fit in to the creation of Measurement Applications? With tools that focus on these three elements, National Instruments development software, LabVIEW™ and Measurement Studio™, speed up the creation and deployment of modern PC-based measurement systems. It is possible to balance the specific needs of measurement applications with the general-purpose functions necessary to create a custom application with these tools.

## Slide 4: Applications of Analysis to Measurement
Wide range of problems (simple to complex)
  Visualization
  Scaling to convert voltage to temperature
  Statistics for process optimization
  Frequency-domain analysis
  Digital filtering
Online and offline analysis
  Differentiates LabVIEW and Measurement Studio from other Numerical or Mathematical software
Notes: Measurement analysis includes many different tasks, ranging from simple to complex. This is important to mention because complex analysis perhaps makes analysis unnecessarily intimidating.
This is an interesting side note – It turns out that frequency-domain analysis and digital filtering are related. Applying the famous Fourier transform, the most widely-used frequency-domain analysis tool, to a signal is the same as applying a bank of digital filters to your signal, with each filter’s center frequency at one bin of your transform. This implementation isn’t practical for use on a computer—alternatives based on the Fast Fourier Transform are more popular.

## Slide 5: LabVIEW for Analysis
All versions of LabVIEW include basic tools
LabVIEW Full and Pro Editions include a general purpose analysis library
Extend LabVIEW Full and Pro with toolsets
  Sound and Vibration
  PID/Control
  System simulation
  Wavelet and Filter Bank Design Toolkit for LabVIEW – today’s topic
Notes: It is important to put today’s topic in perspective, relative to other analysis tools associated with LabVIEW.
All versions of LabVIEW include basic analysis tools – graphing, array manipulation, and basic statistics.
The Full and Professional editions of LabVIEW extend this functionality with an analysis library that includes components for work involving statistics, frequency-domain analysis, matrix algebra, differential equations, curve fitting, and many other topics.

## Slide 6: A Practical Application for Online Analysis – Engine Knock
Common sound emitted by combustion engines
Automobile manufacturers work to eliminate it
Notes: Engine knock results from improper ignition timing or a misbalanced air-to-fuel ratio. Knock occurs when the residual mixture of fuel and air ignite prior to the spark. This ignition creates a local pressure front that travels at supersonic speeds. This rapid rise in pressure causes an effect that Sir Harry Ricardo described early in the last century as the same as a metallic impact.
Automobile and engine manufacturers consider knock during engine design, test, and production. Knock detection is both manual and automatic – National Instruments knows of several engine manufacturing facilities in Mexico that employ technicians for knock detection. They listen for the sound of knock during engine run up tests.
Automatic knock detection schemes are found in some powertrain control modules (PCM) of modern production automobiles. These devices adjust engine and transmission parameters to optimize performance, reduce fuel consumption, and lower emissions. Another common function of these devices is knock control.
The graph shows an audio signal containing engine knock.

## Slide 7: Measurement Applications of Wavelets
Transient signal detection
  Engine knock
  Fractures
  Power-line events
  Any transient signal
Wideband noise removal
  Maintains sharp features
Data compression
Notes: Engine knock is definitely not the only potential application for wavelets in measurement!
The top graph shows the original 3600 time domain samples of an electrocardiogram (EKG) signal. The bottom graph shows the signal plotted accurately after a wavelet transform with just 900 points. It is important to note that the sharp peaks of the signal are still present. Such peaks would be attenuated with other common noise removal techniques such as low-pass filtering.

## Slide 8: Knock Among Noise
?
Value Closure
Piston Slap
Other ignition noise
Vibrations
Etc.
Engine Knock Noise
Knock Detection Scheme
Knock Present?
Signal
Noise
Notes: Using an indirect signal (vibration or sound, rather than pressure) makes knock detection difficult. The indirect signal contains not only knock, but other engine sounds such as valve closure, piston slap, other ignition noise, and vibration.
The problem is the classic measurement problem: How do I distinguish signal from noise?

## Slide 9: Detection of Engine Knock
Best gauge for engine knock – cylinder pressure
  Cylinder pressure sensors – Not appropriate for production vehicles
An alternative – look for acoustic or vibration caused by knock
  Accelerometers
  Microphones
Notes: Knock suppression requires a reliable knock indicator.
The best gauge for engine knock is perhaps cylinder pressure, using a cylinder pressure sensor. Unfortunately, cylinder pressure sensors are too expensive for production vehicles (typically several thousand dollars). Such sensors commonly are built into special spark plugs or installed in the engine block. Kistler Instrument Corp. is well known for a variety of cylinder pressure sensing devices.
A viable alternative is to fit an engine with an accelerometer or microphone to detect knock in sound or vibration. For instance, Delco Electronics, Bosch, and Harris all manufacture hardware for knock detection given an accelerometer signal.

## Slide 10: Current Knock Detection Schemes
Notes: The block diagram shows a simplified mechanism that a PCM might employ to suppress knock. This feedback mechanism requires reliable knock detection in order to adjust engine parameters. By adjusting engine parameters such as air-to-fuel ratio and spark timing, the PCM can reduce knock while optimizing engine performance.
In production vehicles such systems must decide on the presence of knock by examining signals from accelerometers or microphones.

## Slide 11: Frequency-Domain (Fourier) Approach
Analog
Signal
Conditioning
Sensor(s)
A/D
Bandpass
Filter
Rectify &
Integrate
Threshold
Filter Gain / Center Frequency
Set by RPM
Engine Timing controls
Integrator’s Start/Stop
Background Noise,
Component Age, and
Other Factors Set Threshold
?
Knock
Present?
Notes: One modern knock detection approach consists of
Analog filtering/signal conditioning – first stage of isolating knock from other engine noise
Analog to digital conversion
Bandpass filtering – second isolation stage
Rectifying/Integration – to determine knock intensity
Thresholding – Answers “Is knock noise present?” question with a yes/no answer
Parameters for these elements are dynamically set based on engine conditions, sensor age, and other factors. The gain and center frequency of the bandpass filter pass only a knock-representative frequency range. By setting the integrator’s start and stop based on crank-shaft angle, the detector only listens for knock during periods when knock is prevalent. A threshold level is specified based on on the fly measurements of engine background noise and component age.

## Slide 12: Issues with this Approach
Complexity
  Highly dependent on parameters
  Multi-stage system
Frequency-selective filters such as Bandpass (BPF) are not well suited to transient signals such as engine knock
Notes: One issue with this approach involves complexity. The current multi-stage system relies on a number of engine parameters to function.
Another issue involves the use of a frequency selective filter (bandpass). As we’ll explain in the upcoming slides, such filters are not well suited to analysis of transient signals, such as engine knock.

## Slide 13: What to Filter?
It is difficult to choose cutoff frequencies for the BPF to isolate knock –
No Knock
Time-Domain
Frequency-Domain
Knock
Notes: Another issue with this approach involves the bandpass filter stage. As stated on a previous slide, the PCM must set a bandpass filter center frequency so as to pass knock sound and block other noise.
The four graphs show how difficulty of this task. The upper-right graph shows the time-domain representation of a portion of a signal that does not contain knock noise. The lower-right graph shows another portion that contains knock noise. The upper and lower left column show graphs of the frequency-domain magnitude of the two signals on the right. The similarity of these two plots makes it difficult to distinguish between the two by bandpass filtering any subsection of the spectrum.

## Slide 14: Basis Functions
Filtering  Pattern matching
Basis functions  Patterns
Incoming
Signal
Comparison
(Scalar Product)
Filtered
Signal
Notes: An intuitive feel for the nature of filtering can lead to a better option for transient signal analysis.
Consider “standard” filters such as lowpass, highpass, bandpass, and bandstop. We normally consider such filters as frequency selective because they modify the frequency content of an input signal based on frequency. For instance, you can have a bandpass filter with low- and high-cutoff frequencies of 1000 Hz and 1200 Hz. Such a filter would ideally block frequency components below 1000 Hz and above 1200 Hz.
Another way of looking at such filters is as a pattern matching device. With this viewpoint, you consider a filter as a device that performs a comparison of an input signal with a set of basis functions. The output of such a filter is a signal that represents how similar the input signal is to a specific set of basis functions.
The basis functions for any frequency-selective filter is a set of sinusoids with varying frequency and phase. When you apply a filter to an input signal, you can think of the filter as running a set of comparisons over a range of frequencies. The output of each test is how similar the input signal is to the particular frequency of the basis function for that test. In this way, the filter performs a kind of pattern matching between the incoming signal and these basis functions. Mathematicians call this comparison a scalar product or an inner product.

## Slide 15: Basis Functions (notes page)
Notes: Continuing with our example, the basis functions for the bandpass filter mentioned above is a set of sinusoids with frequencies in the range of 1000 to 1200 Hz. Ideally, applying a bandpass filter with these cut-off frequencies is equivalent to comparing an input signal to a set of basis functions in that range.
Although this pattern matching idea is useful to understand filtering, it is not really practical for implementation. Implementation on a computer typically involves a series of multiplications and additions and is commonly referred to as a “MAC” operation for multiply and accumulate.

## Slide 16: Sinusoids as Basis Functions
Frequency-selective filters use sinusoids of varying frequency and phase as their basis
If filtering is pattern matching, are we using a good set of patterns?
Do the general characteristics of these sinusoids match our signal of interest?
Notes: Frequency-selective filters such as Bandpass, Bandstop, highpass, and lowpass use infinite-duration sinusoids as their basis.

## Slide 17: A Fundamental Problem with Frequency-Selective Filtering
Engine knock and other real world signals are not well localized in the frequency domain
Only infinite duration signals such as sinusoids are localized in the frequency domain
Notes: There is a fundamental resolution relationship between the time- and frequency-domain representations of signals. Specifically, a pure sine tone that has infinite time extent has excellent frequency-domain resolution – its magnitude appears as an impulse. Practical, real-world signals never have infinite duration. The frequency-domain view of a finite duration sine only approaches an ideal impulse as the duration of the sine increases.
At the opposite extreme, a pure impulse function in the time domain has no frequency-domain resolution – it’s magnitude is a constant value. An impulse in the time-domain is analogous to a transient signal such as engine knock – both have finite time and so have limited frequency-domain resolution.
By using sinusoids as basis functions for our frequency-selective filters, we assume that the signal that we are filtering also has infinite extent. This assumption is not valid for knock and other transient signals.

## Slide 18: Wavelets as Basis Functions
What we need is a finite-duration basis function
Incoming
Signal
Comparison
(Inner Product)
Filtered
Signal
Notes: Instead of choosing an infinite-duration basis function, why not choose one that has a similar finite duration to our signal of interest?
Wavelets are a type of finite-duration signal that we can use to replace sinusoids as basis functions for filtering.
Just as in frequency-domain filtering, where you must use a set of sinusoids to implement a filter, you must use a set of wavelets for your wavelet-based filter. Unlike frequency-selective filters, where you compare an input signal with a set of sinusoids of various frequencies, with a wavelet-based filter, you compare an input signal with a set of wavelets that vary in both duration (scale) and location in time. Another difference is that you are free to choose an entirely different basis function, as long as it is meets the requirements of being a wavelet.
The following bullets summarize some key differences between wavelets and frequency-selective filters:
Basis function for frequency-selective filter – sinusoid
Basis function for a wavelet-based filter – father wavelet
Parameters of basis function that are varied for frequency-selective filters – Frequency
Parameters of basis function that are varied for wavelet-based filters – scale, position in time
Selection of basis functions for use in a frequency-selective filter – sinusoid
Selection of basis functions for use in a wavelet-based filter – any valid wavelet

## Slide 19: What is a “Wavelet”?
Zero mean, localized in the time and frequency domains
Discrete or continuous
Bi-orthogonal, orthogonal, or non-orthogonal
Notes: Just like the Fourier Transform, there are continuous and discrete versions of wavelets. Because we are using a computer to deal with samples of a signal, the discrete version is more practical.
Orthogonal wavelet bases yield a concise representation of a signal and give you the ability to reconstruct the original signal given it’s wavelet transform. Use of a non-orthogonal wavelets can lead to a redundant representation. Representation here means the result of applying a wavelet transform – the numbers that your transform algorithm produces to represent a signal.
What exactly is orthogonal? To understand, you should consider what Fourier realized when he constructed his famous transform – that you can represent any function as the sum (perhaps infinite) of sinusoids. In this way of thinking, you can think of the sinusoids as axes on a graph and any particular signal as a point in the space defined by the axes. Orthogonal implies that the axes (remember, these are functions) are perpendicular and so any given point in this function space can be represented by a unique set of coordinates.
Bi-orthogonal wavelets allow for two different wavelets – one for analysis and one for reconstruction. Analysis is transformation of a signal into the wavelet domain and reconstruction is transformation from the wavelet domain back into the time domain. These operations are the same as using an FFT and an inverse FFT to transform a signal to and from the frequency domain. Although you have more freedom in designing a bi-orthogonal wavelet, such wavelets do not reproduce the signal energy exactly in the wavelet domain. This can introduce errors when reconstructing a signal.

## Slide 20: Wavelet Transform of Engine Knock
Knock noise is clear in the wavelet domain
No Knock
Time-Domain
Knock
Wavelet-Domain
Notes: In this figure, I have applied a wavelet filter to two sections of the time-domain (the same sections shown in the previous slide). The top figure is a knock-free section of signal and the bottom contains three distinct knocks. The knocks are evident as jumps in amplitude in the wavelet domain.

## Slide 21: Wavelets vs. Fourier Analysis
Fourier analysis assumes that any signal is actually the sum of sinusoids of various frequencies
  This assumption allows frequency-selective filters to divide a signal by frequency
Wavelet analysis looks at signals as a smooth background with details on top of it
  Resolution designates smooth versus detail
Notes: Wavelets are perhaps best understood in terms of Fourier Analysis.
Fourier analysis makes the assumption that any signal is actually the sum of sinusoids of various frequencies. For signals such as a square wave that contain discontinuities, this sum is infinite. The real world doesn’t allow infinite sums, so we must settle for partial sums. Unfortunately, any partial sum only approximates the original signal.
This limitation is important because the result of a Fourier Transform represents the magnitude and phase of the sinusoids that you would have to sum up to generate the input signal. Because it isn’t possible to have infinite resolution with your Fourier transform, the result only approximates the sinusoidal components of the input signal.

## Slide 22: Wavelet Filter Banks
2
2
2
2
Multiple Outputs?
Which Wavelet?
What does the output Mean?
Notes: The practical application of a wavelet to a signal with a PC is with a filter bank. Filter banks are a widely-used digital signal processing (DSP) tool that are normally used for application of standard (frequency-selective) filters. When used with wavelets, such filter banks are called Fast Wavelet Transforms (FWT) as a kind of comparison to the Fast Fourier Transform (FFT).
However, the implementation of a wavelet filter bank is different than that of a FFT. A wavelet filter bank consists of multiple stages. Each stage consists of highpass and lowpass filters that are derived from a mother wavelet. The highpass stage is equivalent to applying a narrow wavelet and the lowpass a wide wavelet. After applying the filters, you drop every other sample (decimate by 2). For further filtering, you can then feed these decimated signals into another set of highpass and lowpass filters. The process repeats until you’ve derived what you need from the filtered signal or you run out of samples.
A mother wavelet is a basis function for a family of functions (the functions that you form by stretching a the mother wavelet in time or shifting it in time).

## Slide 23: Filter Bank Output
The output of a wavelet filter bank is another time-domain signal
Wavelet filter banks have multiple outputs – you can pick and choose
  These outputs separate the smooth and detail features of the original signal
  Each output is a path – you can choose the detail or smooth component at any stage of the output
Notes: If you are familiar with the Discrete Fourier Transform, and its efficient implementation, the FFT, then you’ll likely know something about the complex-valued output of the transform. Specifically, with a real-valued input to an FFT the output is a complex number, with magnitude and phase components. Such real-valued inputs are what you get when you sample a real-world signal. Unfortunately, complex-valued signals often aren’t intuitive. The output of a wavelet-filter bank with a real-valued signal is also a real-valued signal, which some would argue is easier to interpret.
Wavelet filter banks also have multiple outputs which break up the input signal into smooth and detail features of the original signal. Each output is a path on the filter bank (see previous slide).
Each “level” contains smooth and detail features of a signal at a specific resolution. With a filter bank, each level has half the resolution of the previous. The number of levels to calculate is a parameter that you can set.

## Slide 24: Which Wavelet?
The filters for your wavelet filter bank are derived from a “mother wavelet”
You can choose a mother wavelet that fits the signal of interest
No automated procedure exists for wavelet selection – it is an interactive process
Notes: You are free to choose a particular mother wavelet, although some restrictions apply to what function (its basis functions must be orthogonal and it must be time-limited).

## Slide 25: National Instruments Wavelet and Filter Bank Design Toolkit
Notes: National Instruments’ Wavelet and Filter Bank Design Toolkit includes interactive filter design tools that allow you to specify a valid wavelet basis and immediately see the results of applying that basis. The tool works online with live data or offline with data from a file. It ships as both a standalone executable and with LabVIEW source code.
The Wavelet and Filter Bank Design Toolkit now is sold as a component of the Signal Processing Toolset for LabVIEW.

## Slide 26: Filter Bank Implementation in LabVIEW
Notes: After you’ve chosen an appropriate mother wavelet, you are left with a set of coefficients that you then can use in a filter bank. The Wavelet and Filter Bank Design Toolkit includes ready-to-use VIs to implement a filter bank.
Engine knock detection with a wavelet filter bank was implemented with several of these tools. The core of the detection algorithm is a set of analysis and synthesis filter banks, as shown in the figure. Each analysis filter bank divides the signal into smooth features and details, while each synthesis filter bank reconstructs a signal given a pair of smooth and detail features. Parameters allow multiple stages of each of these types of filter banks.
To extract knock, the algorithm zeros out the smooth features of each filter stage and reconstructs the original signal with this change. The reconstructed signal is nothing but details. The knock signal appears in this detail signal as peaks. There are several methods that might apply to detecting the knock given a detail signal. One such method is implemented in another section of code – it’s a simple threshold-based scheme that performs a pass-fail test for the presence of knock if a user-set variable is exceeded.

## Slide 27: Engine Knock / Transient Signal Detector Start Up Kit
Notes: The figure shows a new engine knock detector application, developed by Shie Qian, Dave Wilson, and Sam Shearman, Software Engineers at National Instruments. The application shows an example of applying analysis to a real-world problem. It applies a wavelet filter-bank to detect engine knock during an engine run-up test. Other techniques that involve FIR or IIR filtering were not appropriate, because the knock signal is wide band (covers a broad swath of the spectrum), so an ordinary filter wouldn’t really isolate the knock and allow for detection.
You can freely download this application from ni.com/automotive/autovi_exchange.htm, available in both LabVIEW 5.1 source code, and as a standalone (installable) application. To view/modify/execute the source code version, you need LabVIEW 5.1 (or higher), Signal Processing Toolset for LabVIEW, NI-DAQ 6.7 or higher. The executable version requires the LabVIEW Runtime Engine (5.1.1 or higher) and NI-DAQ 6.7 or higher.

## Slide 28: References
Engine Knock
  SAE Technical Paper Series (sae.org)
Wavelets
  The World According to Wavelets, Barbara Hubbard
Signal Processing (General)
  A Digital Signal Processing Primer, Ken Steiglitz
Signal Processing (for Measurement)
  LabVIEW Signal Processing, Chugani, Samant, & Cerna
Notes: Burke, Barbara, The World According to Wavelets, The Story of a Mathematical Technique in the Making, 2ed, Wellesley, MA: AK Peters, 1998, ISBN 1-56881-072-5.
Chugani, Mahesh, A. Samant, M. Cerna, LabVIEW Signal Processing, Upper Saddle River, NJ: Prentice Hall PTR, 1998, ISBN 0-13-972449-4.
Samimy, Bahman, and G. Rizzoni, “Engine Knock Analysis and Detection Using Time-Frequency Analysis,” SAE Paper # 960618.
Scholl, David, T. Barash, S. Russ, W. Stockhausen, “Spectrogram Analysis of Accelerometer-based Spark Knock Detection Waveforms,” SAE Paper #972020.
Steiglitz, Ken, A digital signal processing primer, with applications to digital audio and computer music, 1ed, Menlo Park, CA: Addison-Wesley Pub. Co., 1995, ISBN 0-8053-1684-1.
Puzinauskas, Paulius, “Examination of Methods Used to Characterize Engine Knock,” SAE Paper # 920808.
Wagner, John, J. Keane, R. Koseluk, and W. Whitlock, “Engine Knock Detection: Products, Tools, and Emerging Research,” SAE Paper # 980522.