## Slide 1: The Impact of New Bus Technologies
Michael Simon
Hardware Design Engineer
Thurs Aug 17
10:15-11:30 a.m., 1:45-3:00 p.m.
Red River (4B)

## Slide 2: Agenda
Emerging bus technologies
Comparing bus technologies
Applying bus technologies
Notes: This presentation addresses emerging bus technologies by providing an overview of their technical background and specifications. The busses are compared, with focus placed on comparing complimentary technologies, as well as examining new application opportunities, and their relative merits, through example scenarios.

## Slide 3: Agenda
Emerging bus technologies
Comparing bus technologies
Applying bus technologies
Notes: We begin by discussing these four bus technologies from a technical angle. Rather than treat the technical aspects of the different busses in detail at this point, we instead provide a cursory overview of the busses as they affect the main topic, which is their impact on measurement and automation systems. The appendices at the end of this presentation provide a more detailed treatment of the technical distinctions of these busses. If you are interested in a more substantial treatment of the technologies, some excellent resources are provided in the Acknowledgements section.

## Slide 4: Emerging Bus Technologies
Universal Serial Bus 2.0
IEEE-1394 (FireWire™)
CardBus
Ethernet
FireWire™ is a registered trademark of Apple Computer, Inc. in the U.S. and other countries
Notes: The four emerging bus technologies that we examine are Universal Serial Bus (USB) 2.0, IEEE-1394, CardBus, and Ethernet. The first two are serial busses growing within different segments of the electronics and computing industries. The third is a backplane bus with some similar properties and some distinguishing properties relative to the other busses being discussed. The fourth is not a new bus, but is the target of new applications which can benefit measurement and automation systems.

## Slide 5: Emerging Bus Technologies
USB 2.0
IEEE-1394
CardBus
Ethernet
Host
Hub
Hub
Hub
Node
Node
Node
Node
Node
Hub
Notes: The USB transmits at 1.5, 12, and 480 Mbps, based on the complexity of the target device. Slower devices are less complex and, therefore, less expensive. The USB handles communication between a single host – a computer in most cases – and a variety of nodes, which are peripherals with particular functions, and hubs, which repeat the USB signaling to allow more nodes to be connected to the host. More devices can be added to a USB by adding a hub to an available port: Up to 127 devices can be connected, with no more than five hubs between any given node and the host. A device with a hub and a node combined in one system is called a “compound device.”
The end-user plugs a USB device into an active host. The host immediately queries the device for its characteristics. Based on those characteristics, the host USB driver loads device-specific drivers to control the device. Those drivers complete the initialization process and setup any pipes, or communication channels, that applications may need to use. A device can have multiple interfaces that allow different applications to communicate with a device in different ways. The device connects to the host’s pipes through endpoints, which are unidirectional ports for data transfer. Each endpoint has certain characteristics that define its functionality.
The user must use caution when inserting or removing a USB device from the bus. Doing so interrupts the functioning of the host, and could cause USB devices to overflow, lose information, or confuse the host.

## Slide 6: Emerging Bus Technologies
USB 2.0
IEEE-1394
CardBus
Ethernet
Branch
Branch
Leaf
Leaf
Notes: IEEE-1394 – “FireWire” is Apple’s trademarked name for their implementation of IEEE-1394 – transmits at 100, 200, and 400 Mbps, based on the complexity of the devices communicating. IEEE-1394 is a peer-to-peer protocol, meaning that all devices communicate directly with each other, whether they are a simple peripheral or a computer. Up to 63 devices can be daisy-chained on a single IEEE-1394 bus; further, up to 1,023 busses can be connected together through repeaters. The maximum distance between two devices is 4.6 m over copper; fiber-optic-based repeaters can extend this distance to hundreds of meters.
The end-user plugs an IEEE-1394 device into an available port. This causes the neighbor device to reset the entire bus. Every device is identified and a root is chosen based on proximity to all other devices and certain priorities. Devices like computers may use the information distributed to load device-drivers for all devices on the bus with which it can communicate. IEEE-1394 devices communicate using the IEEE-1212 CSR standard, which grants each device a fixed register space and a large publicly accessible virtual memory space. Like USB, an IEEE-1394 device can have multiple independent functions.
Since software is minimally involved in bus configuration, inserting or removing a device should not effect operating system behavior considerably. However, since the entire bus must be reset, the user must use caution when inserting or removing devices, since an active transfer could be considerably delayed when the bus is modified.

## Slide 7: Emerging Bus Technologies
USB 2.0
IEEE-1394
CardBus
Ethernet
Main bus controller
CardBus controller
Main bus controller
Notes: CardBus transmits 32-bit words at 33 MHz, for a total transfer rate of 132MB/s = 1,056 Mbps. The CardBus handles communication between a bus controller, typically managed by a single host, and a fixed number of possible devices. The CardBus standard defines Type I, II, and III slots, which are based on the size of the slot. Typically, a bus controller will connect to two Type II slots, which can accommodate either two Type I or II devices or one Type III device. These slots are ubiquitous on notebook computers, and adapters can be bought for personal computers and PXI chassis, as well.
The user plugs a CardBus device into an available slot. This causes the operating system to call its Socket Services driver, which queries the device for configuration information. Once the device is identified, a device-specific driver will typically be loaded to handle further configuration and operation of the device. Since the device communicates synchronously with the host, there are no special types of packet signaling. Instead, CardBus uses the PCI signaling protocol, which uses I/O, memory, and configuration cycles to communicate. Single and bursted transactions are available.
This bus is hot-pluggable, but the host can be hung by removing an active device in the middle of a transfer, so care should be taken. And, as with the previous two busses being discussed, any change in bus state must be updated at the host. Therefore, changes should be avoided during high-bandwidth transfer or computationally intensive programs.

## Slide 8: Emerging Bus Technologies
USB 2.0
IEEE-1394
CardBus
Ethernet
Notes: Ethernet, which has been in existence for nearly 35 years, is a standard which defines a method and medium for communication between local area networks (LANs). The original Ethernet specification transmitted at 10 Mbps, with Fast Ethernet and Gigabit Ethernet now available at 100 and 1000 Mbps, respectively. Ethernet is a broadcast medium, such that any device can communicate to any other device on the network. The theoretical limit to the number of devices on a network is 2^32, but the network will become too congested over a couple hundred. The length of a network is limited only by the type of media used.
Ethernet uses CSMA/CD protocol, which means “Carrier Sense Multiple Access with Collision Detect.” That means that a device 1) listens for a clear line, 2) communicates over the shared bus to all devices, and 3) stops transmitting if it hears another device trying to transmit. This can be a very efficient form of communication, but when many devices are trying to use the ether, the result is a large number of collisions. Therefore, the size of a specific ether, or a “subnet” is limited by the type of traffic experienced on the bus.
The user plugs an Ethernet device into the network. This can be done through the cable, a hub or repeater, a bridge or switch, or through a router or gateway. Although Metcalf’s original Ethernet involved joining devices into a common “ether,” modern devices can use a much more complex topology...

## Slide 9: Example Ethernet Subnet
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
To router
Local traffic
Local traffic
Traffic routed to destination
Switch
Repeater/hub
Switch
Segmented collision domain
Repeater/hub
Notes: Modern networks rarely use coaxial cable to directly connect devices into the network. You are more likely to see unshielded twisted pair (UTP) cabling connecting computers and devices to a hub, which is a multi-ported repeater. The repeater or hub does some signal correction, but basically only repeats the signal, and does nothing intelligent with it. A bridge or switch understands the Ethernet standard, and will switch a packet to one or another device. It can also buffer data, and basically isolates a subnet from the rest of the network. The result is messages internal to that subnet will not cause collisions on the rest of the network. Finally, routers and gateways use the network level protocol to determine where and how to transmit a packet. They can also transmit over different media and networks. (i.e. from fiber to copper or from Star to Novell.)

## Slide 10: Emerging Bus Technologies
USB 2.0
IEEE-1394
CardBus
Ethernet
Notes: Since self-configuration/identification is not available through Ethernet, the user must configure their device, and surrounding devices, to recognize the new device. Presently, some dynamic address servers, like DHCP, automate this service using address broadcasting. The new version of Internet Internetworking Protocol, the IP behind TCP/IP, will provide some self-configuration services.
Since Ethernet only defines a standard data packet for simple intra-subnet routing, higher level protocols are necessary to make sense of the data. One option is a proprietary protocol, which some product vendors use. Another option is a standard, like TCP/IP. IP provides wide-scale addressing and datagram services, while TCP provides transaction security, reliable stream services, and connections. This makes it possible for two systems to create a “socket,” or a seamless data pipe.
Since there is no software detection for insertions and removals, there is no effect on the operating system when an idle device is removed from the Ether. However, all systems must be notified of its absence or they may attempt to communicate with the missing device, causing confusion. Further, removing an active device from the network can cause some confusion. However, most popular protocol stacks are sufficiently mature that such an event would not affect other system functioning.

## Slide 11: Agenda
Emerging bus technologies
Comparing bus technologies
Applying bus technologies
Notes: Now that we have some background in bus technologies, let’s see how they stack up.

## Slide 12: Comparing Bus Technologies

## Slide 13: Agenda
Emerging bus technologies
Comparing bus technologies
Applying bus technologies
Notes: The remainder of this presentation is a discussion of how the emerging bus technologies can be utilized in measurement and automation systems.

## Slide 14: Applying Bus Technologies
Our scenarios
  Laboratory bench
  Field technician
  Factory floor
  Remote station
Applications
Misapplications
Server
Computer
Person
Instrument / control
Notes: Four scenarios are considered in this discussion. Each of them is represented on one of the following slides in a graphical format. In the soft-copy of the slides, there are also textual explanations of the representations.
These graphs represent the different nodes of the systems being considered: Servers, Computers, Instruments and Controls, and People.
Servers are defined as central resources which provide file sharing and logging, and allow individuals to archive and access relevent data.
Computers are defined as single person workstations, which can connect to one or more instruments using appropriate measurement and automation software.
Instruments and Controls represent the instrument that measures and logs, the control that adjusts as well as clusters of sensors that do these things. It is an open set which defines anything that tests, measures, controls and automates.
People are self-defined.

## Slide 15: Laboratory Bench
Notes: A Laboratory Bench has several properties, including:
An individual performs non-automated tasks.
Computer needs some connectivity to central resources.
Sharing of instruments between individual benchtops is a plus.

## Slide 16: Field Technician
Notes: A Field Technician has certain properties, including:
Individual is physically isolated from central resources.
Individual performs automated and non-automated tasks.
Instruments must be mobile, but not necessarily portable.

## Slide 17: Factory Floor
Notes: A Factory Floor has many properties, including:
Individuals and clusters of individuals require connectivity to central resources.
Sensors and clusters of sensors provide feedback on automated measurements.
Individuals perform automated and non-automated routines.
Instruments does not need to be portable, but can be.

## Slide 18: Remote Station
Notes: A Remote Station has several properties, including:
Needs little or no human intervention
Instrument is isolated from computer network but not necessarily from infrastructure. (ex: An instrument placed in an inaccessible portion of a building, like a throughway or on a constant-operation machine.)
Measurements are automated and need control and feedback.
Rapid configuration is not a requirement, but high reliability is a requirement.

## Slide 19: Agenda
Emerging bus technologies
Comparing bus technologies
Applying bus technologies

## Slide 20: Related Presentations
AT1A – Wireless Communication for Distributed I/O and DAQ
PR1B – A Technical Survey of Industrial Networks
PR1C – How Does the Internet Work?

## Slide 21: Appendix & Reference Materials
Emerging bus technologies
  USB 2.0
  IEEE-1394
  CardBus
  Ethernet
Topical bus comparisons
Acknowledgements/references
Notes: To understand how these busses will affect the measurement and automation industry, we need to understand how these busses behave.

## Slide 22
Emerging Bus Technologies
USB 2.0
IEEE-1394
CardBus
Ethernet
OSI Reference Model
PHYSICAL
DATA LINK
NETWORK
TRANSPORT
SESSION
PRESENTATION
APPLICATION
Notes: The OSI reference model provides a useful framework for discussing communication protocols such as those that we are discussing today.
The model begins at the Physical layer – commonly referred to as the PHY – which provides a direct hardware interface to the transmission medium used for communication.
The Data Link provides a data serialization and packaging protocol, while the Network layer provides information about the network topology, the source, and the recipient.
The Transport layer provides high-level data encapsulation services as well as certain connection and security services for multiple data transactions.
The Session and Presentation layers provide services to and from the operating system or user layer interface to use the rest of the stack in a fashion that makes sense for the application
The Application layer provides the interface for the user to the rest of the network stack. This is what the user sees.

## Slide 23: Emerging Bus Technologies
USB 2.0
IEEE-1394
CardBus
Ethernet
What is it?
What does it look like?
How does it work?
How do I use it?
What’s next?
Notes: We will cover these busses by answering these five questions:
What is it?
What does it look like?
How does it work?
How do I use it?
What’s next?

## Slide 24: Historical Perspective
By the early 90s...
  Plug-and-pray
  Poor standardization
  Rarely/poorly hot-pluggable
  Resource confusion (I/O conflicts, IRQ conflicts, etc.)
PCI & PXI solved most of these problems for internal busses, but the external busses remained a cable jungle!
Notes: First, we will discuss the motivations behind some of these busses. Anyone involved with computer systems in the 80s and 90s is familiar with the “cable jungle” that developed behind the computer, connecting the CPU and various peripherals. Keyboard, mouse, monitor, modem, serial busses (like RS-232 and RS-485), parallel busses (like Centronics and SCSI), and other devices used different busses for communication. Configuring a device would require setting base addresses and interrupts, and summoning quite a bit of luck and savvy. Operating Systems (OSs) had to rely on user information and vendor drivers to utilize peripherals. In general, things were confusing, difficult to use, messy, and susceptible to random acts of failure.
Since then, PnP ISA has become a considerably more stable bus with more intelligent and fault-tolerant OSs. PCI and PXI have solved the internal jungle by providing a dependable and easily configurable internal interface. Under normal conditions, the user should only need to install a driver and plug a PCI board in – the OS should recognize the board immediately. However, the external cable jungle remains untamed.

## Slide 25: Historical Perspective
New External Bus Interface Desired...
  Fast, Easy Setup
  One Universal Connector
  Hot-pluggable and Bootable
  Dynamic topology (with room to grow!)
  Well-understood OS Management Strategy
  Capable of supplying power through the bus
New external bus interface desired...
  Fast, easy setup
  One universal connector
  Hot-pluggable and bootable
  Dynamic topology (with room to grow!)
  Well-understood OS management strategy
  Capable of supplying power through the bus
  and low-cost!
Notes: The 90s brought on an industry-wide desire for a way that devices could be connected cleanly to the computer externally with the following features:
one bus, one connector
a fast, easy setup routine
a dynamic topology
configuration without concern of conflicts
the stability and ease of PCI
dynamic topology
inexpensive to implement
We start with a couple of answers to that dilemma.

## Slide 26: USB 2.0 – What Is It?
Driven by industry leaders
  Intel, Microsoft, Compaq, NEC,
  Hewlett-Packard, Lucent, and Philips
Driven by consumer demand
  Keyboards, mice, speakers, removable media, scanners, printers, flash memory, joysticks, video cameras,
  adapters, microscope, modems, network adapters, MIDI controllers, extenders, gamepads, drawing pads, power backup, serial adapters, microphones, headsets, teleconferencing kits, PDA connectors, hard drives, Ethernet adapters, computer link, PCMCIA adapters, MP3 players, IrDA transceivers, solar power, ADB server,
  and Computer-Based Instruments
Notes: Universal Serial Bus (USB) was developed by a group of computer industry leaders. It is a standard held privately by the USB-Implementers Forum, an independent corporation responsible for overseeing the development and compliance of the USB standard. The promoters group started with Intel, Microsoft, Compaq and NEC, and now includes Hewlett-Packard, Lucent, and Philips.
With strong marketing power and considerable backing from the promoters, USB devices flourish, entering almost every area of the computer peripheral market.

## Slide 27: USB 2.0 – What Is It?
Low speed
10 kb/s - 100 kb/s
Human interface devices
Keyboards
Mouse
Game peripherals
Device configuration
Medium speed
500 kb/s - 10 Mb/s
Streaming data devices
ISDN
POTS
PBX
Audio
Low-resolution video
High speed
25 Mb/s - 500 MB/s
High-speed transfer
High-resolution video
High-density disk
USB 1.1
USB 2.0
USB 2.0
Notes: We will discuss the second version of the USB Specification, which specifies three speeds of operation – Low, Full, and High speeds. USB 1.0 offered Low and Full speeds. Low speed, specified as 1.5 Mbps transfer rate, provides a good communication medium for Human Interface Devices (HIDs), which require very little speed compared to devices which interact with other computers. Communication devices, like POTS and ISDN modems, can be found in full-speed implementations, specified for 12 Mbps throughput, as can streaming devices like audio speakers and low resolution video. USB 1.1 is a minor revision providing some specification bug fixes.
USB 2.0 is a superset of the 1.x specification and introduces high speed into the mix. High speed transmission, which operates at 480 Mbps, opens USB 2.0 up to the high speed data transfer market, with devices like high density media and high resolution video. Protocol additions to support high speed aside, the rest of the specification remains very similar to the original USB specification.

## Slide 28: USB 2.0 – What Does it Look Like?
Tiered star topology
  Hub – connects to up to N-1 nodes and hubs
  Node – connects to one hub
  Host – connects to root hub(s) and is upstream of all nodes
Distance of “hop” limited to 5 m, with a max of 5 hubs
Limited to 127 devices
Host
Hub
Hub
Hub
Node
Node
Node
Node
Node
Hub
Notes: USB uses a tiered star, or rooted tree, topology. The highest tier contains the host, which controls the rest of the tree. The host is typically connected to a hub, which divides a bus segment so several nodes can be connected to one segment. Every hub can connect to several nodes and hubs. Sometimes, one or more nodes will be packaged with a hub, to provide easier connectivity (for example, monitors with USB audio and control nodes, and an embedded USB hub). These devices are called compound devices. Regardless of how many devices are connected, the Host is always bus master. A hop between a hub and another hub or node is limited to 5 m, with a maximum of five hubs between the host and a given node. The bus is limited to a total of 127 devices, plus the host.

## Slide 29: USB 2.0 – What Does it Look Like?
Monitor w/ integrated USB
USB headset
USB mouse
USB modem
“A” conn
“B” conn
Notes: Here are some examples of USB devices and interfaces. The “A” connector plugs into an upstream port, such as the host or a hub. The “B” connector plugs into a downstream port, such as a device or a hub port.

## Slide 30: USB 2.0 – How Does it Work?
Maximum bandwidth
  Low-speed = 1.5 Mbps
  Full-speed = 12 Mbps
  High-speed = 480 Mbps
Host is always master
Asynchronous and Isochronous communication available
Pipes, Endpoints, and Frames
Notes: USB communicates with devices on the bus by sending the bits as an encoded sequence, at the rate determined by the destination node. Low speed devices communicate at 1.5 Mbps, full speed devices communicate at 12 Mbps, and High-speed devices communicate at 480 Mbps. The host, which is root of our topology, is always the bus master. That means that the host schedules and initiates all transactions.
We will discuss them in more detail later, but to provide a quick background, asynchronous and isochronous are two models for data transfer. Asynchronous transport does not guarantee that a transmission will be completed within any given time, but it does guarantee that the data will be transferred accurately. Isochronous transport guarantees that a transmission will be completed within a given amount of time, but it does not guarantee that the transmission will be received error-free.
The host and device view the transmission medium in different ways. The host sees the device through “pipes”, which are bundles of unidirectional transport links. An application will communicate with a device function through different pipes. Meanwhile, the device sees the host through endpoints, which are unidirectional data sources and sinks. Each endpoint has certain properties which determine how the endpoint communicates with the host. (Such properties include frequency of transmission, isochronous vs. asynchronous, size of transmissions, etc.)

## Slide 31: USB 2.0 – How Does it Work?
Power distribution
  Power supplied to a peripheral
    100 mA at 5 V during startup
    500 mA at 5 V after enumeration (if available)
    500 µA-2.5 mA at 5V during standby
  Peripheral can be bus-powered or self-powered
Identification and enumeration
Notes: USB also has the advantage of providing a power source to devices through the bus. A device is allowed to sink a certain amount of power, based on the configuration of the network. The different modes are shown in this slide. If a device requires more than the maximum available power, (500 mA at 5 V) it must provide its own power source. Hence, a self-powered device is one which has its own power source, whereas a bus-powered device uses the USB bus for its power supply.
One other critical feature of the USB is self-identification and enumeration. When a device is added to the network, it is queried for certain characterisitics by the host, and is assigned an address. The host then starts the driver for the device, and communicates the appropriate information to that driver. To make the USB devices hot-pluggable, USB device drivers must be able to load and unload dynamically. Note that the device-specific driver still communicates through the OS. USB driver to transfer data through the appropriate pipe.

## Slide 32: USB 2.0 – How Does it Work?
Bits
Packets
Transactions
Transfers
SETUP
IN
IN
STATUS
DATA1
SETUP
STALL
DATA
SYNC
PID
CRC
Notes: The USB transmission begins at the bit level, which is a bit-stuffed NRZI encoding scheme. This means that bits are encoded such that a transition must occur on the USB data lines once every seven bit-times. This method of encoding generates enough transitions to allow clock recovery by the device.
Bits form packets, which are the atomic transfer on the USB bus. A packet is composed of a synchronization sequence, followed by a packet identifier (a four bit code followed by its inverse) called the PID. The data payload and a CRC check follow the PID. The type of CRC check varies based on the type of transmission.
Packets form transactions, which relate a command or data. All transactions have a token packet. If a data payload is being transferred, a data packet follows. If the pipe is asynchronous, a handshake follows.
Based on the type of pipe transferring the data, the transfer can be from one transaction long to many transactions long. Control transfers are at least three transactions long, while an isochronous transfer is only one transaction long.

## Slide 33: USB 2.0 – How Does it Work?
Notes: This slide summarizes the various properties of the different types of endpoints available through the USB transport protocol. Their behavior differs based on transfer speed, as shown.

## Slide 34: USB 2.0 – How Do I Use It?
Requirements for USB 1.1
  USB compliant host
    ex: PCs (x86, Mac), Sun Enterprise
  USB compliant OS
    ex: Windows 98, Windows 2000, Windows ME, MacOS, Linux, Solaris, SunOS
  USB Peripheral
Requirements for USB 2.0
  USB Peripheral
  Host & OS: TBD
Notes: Using USB is very straightforward. The host system, including the host controller hardware and operating system, must be compatible with the USB specification for the desired USB peripheral. USB 1.0 and 2.0 are forward and backward compatible. However, functionality of a USB 2.0 device may be limited when connected to a USB 1.1 host.
The exact host and OS requirements necessary for USB 2.0 were not entirely certain at the time of publication.

## Slide 35: USB 2.0 – How Do I Use It?
Plug in...
  Driver installation may be necessary on first insertion if the device is not part of a “Class”
  Plugging in a new device disrupts the bus... Be cautious when inserting while high-bandwidth transfers are underway
... and use!
  Programs designed to use drivers should recognize device right away
Notes: Connecting a USB device to the host merely requires one to plug it in. A device-specific driver may be necessary if the device doesn’t follow a particular class specification, like audio or human interface. Note that inserting a new device adds a small but negligible amount of traffic to the bus. More importantly, though, it places a burden on the operating system to identify the device and load the correct driver, which could slow down active applications. Therefore, one should be cautious when inserting a new device into the USB when high-bandwidth transfers are underway.

## Slide 36: USB 2.0 – How Do I Use It?
Unplug...
  Removing an idle device from an idle bus
  Removing an idle device from an active bus
  Removing an active device from an active bus
Warning! Disconnection affects OS functionality!
  Drivers cannot typically avoid this
  Applications are often affected as well
Notes: Unplugging an idle device from an idle bus should have no effect on any other device. If the bus is active, a disconnection may result in increased host processing, which could interrupt other devices. However, less processing is necessary than with an insertion. However, if a device is actively transmitting when disconnecting, the result could be serious confusion on the part of the driver. This can result in a crash of the device-specific driver, the USB driver, and even the OS kernel.
Although drivers can be designed to minimize the impact of active removal, some impact is often unavoidable, due to the nature of the waiting constructs used in USB requests. Applications that rely on that driver, and sometimes on the core USB driver, can be affected by the ensuing confusion as well. Therefore, the user should use caution when removing an active device from the USB. If possible, the user should try to stop all activity from the device before disconnecting.

## Slide 37: USB 2.0 – What’s Next?
USB 2.0
  Specification release – April 2000
  Initial OEM system releases – October 2000
  Initial product releases – October 2000
  Initial OS support – September 2000 (?)
  Comprehensive OS support – 2H’01
USB 1.x
  More and better
  New classes, better OS support

## Slide 38: IEEE-1394 – What Is It?
Began in 1986 – “High performance serial bus”
Apple Computer, Inc.
  Patented and pioneered
  Owns the FireWire™ name
IEEE-1394 is a peer-to-peer computing bus
Driven and supported by industry leaders
  Apple, Sony, NEC, Microsoft, etc.
  Has become an important interface in the consumer electronics industry
Notes: The development of IEEE-1394 began with the search for a “High Performance Serial Bus” to replace the tangled mess of cables in all varieties of electronics. This was a more generalized approach to the same problem USB approached in the personal computer.
The research committee was formed in 1986 and tried many different busses, with varying success, to define the specifications of a high performance bus. They also wanted to include the newly-specified IEEE-1212 control and status register scheme in the new bus specifications. This would provide a specific format for addressing and control, and would keep new, incompatible busses from spawning off the first.
Apple Computer developed and pioneered much of the technology behind IEEE-1394, and coined the popular moniker “FireWire.” Since this is a trademark of Apple Computer, most implementers name their bus something different, but the standard is the same.
The specifications, incidentally, also define a serial backplane for use within computing systems. The focus of this discussion will be on the cable definition for external connectivity.

## Slide 39: IEEE-1394 – What Is It?
Low speed
10 kb/s - 100 kb/s
Human interface devices
Keyboards
Mouse
Game peripherals
Device configuration
Medium speed
500 kb/s - 10 Mb/s
Streaming data devices
ISDN
POTS
PBX
Audio
Low-resolution video
High speed
25 Mb/s - 500 MB/s
High-speed transfer
High-resolution video
High-density disk
IEEE-1394
Notes: 1394 provides high-speed throughput for consumer electronics and computer peripherals in the medium and high speed ranges listed. Maximum throughput varies between 100 Mbps and 400 Mbps. New specifications for 1394 raise that maximum throughput to 800 Mbps, and as high as 3200 Mbps over improved media.

## Slide 40: IEEE-1394 – What Does It Look Like?
Daisy chain topology
  Every node is either a branch or a leaf
  One node is selected to be the root (can be any node)
Automatic bus enumeration
Non-cyclic (no loops)
Distance of “hop” < 4.7m
  Fiber extension is available
  Limited to 63 devices per bus
  Bridges link multiple busses
Branch
Branch
Leaf
Leaf
Notes: An IEEE-1394 network consists of a daisy-chain topology. A single device can operate alone, with two devices, or with a chain of devices. Some devices have a singleport and are not intended to pass through the signals. Others have multiple ports for chaining several devices together. If a node is connected to a single device, it is a leaf. If it is connected to more than one device, it is a branch. The bus must be non-cyclic – there must be no loops in the bus. If there is, packets may hit a destination multiple times, resulting in incorrect operation. The enumeration process is capable of detecting such cyclic bus topologies and alerting the user.
The bus also needs an arbitration handler, called the root. Using a bus-identification and self-identification process, a root is chosen from among the different nodes. Any node can be root, even a leaf.
A single bus is limited to 63 devices. However, multiple busses can be chained to offer larger networks of 1394 devices.
A hop is limited in length to 4.7 m. However, this limitation is based on the copper cable specification. Devices converting to and from fiber optic cable can extend a 1394 bus hundreds of meters.

## Slide 41: IEEE-1394 – What Does It Look Like?
Notes: Here are some examples of devices with an IEEE-1394 port. Their functions depend not only on them, but also on what they are connected to.

## Slide 42: IEEE-1394 – How Does It Work?
Bandwidth
  Base rate = 24.576 Mbps
  Throughput
    100, 200, or 400 Mbps
    800 - 3200 Mbps with IEEE-1394b
All devices can be bus master
Asynchronous and isochronous communication available
Notes:   Bandwidth is calculated as Base rate = 24.576 Mbps (~25 Mbps)
    =18x 1.536 Mbps or 12x 2.048 Mbps (ISDN base rates)
  Backplane spec
    25, 50, or 100 Mbps
  Cable spec
    100, 200, or 400 Mbps
    800 - 3200 Mbps with IEEE-1394b
Any device can be bus master. It arbitrates for bus control, and can perform reads, writes, and locks on any other devices public address space
Asynchronous transmissions are available through normal packet requests following an arbitration process.
Isochronous transmissions are granted at the beginning of every cycle, which is 125 µs long. Once all devices have completed their isochronous transmissions, asynchronous transmissions can begin.

## Slide 43: IEEE-1394 – How Does It Work?
IEEE-1212 CSR
  Every 1394 device has an accessible memory space
  All 1394 devices can share information
Power distribution
  8-40VDC at 1.5Amax
  Chain never broken
Notes: From a logical level, IEEE-1394 follows the IEEE-1212 CSR standard, which defines a memory space and a register space. Those registers can be used to obtain configuration and status information. Raw data can be exchanged through the public address space. All told, the IEEE-1212 address space defines 256 busses, each of which is 256 terabytes long.
Power is available using the power and ground lines of the cable. Unlike the USB power distribution, the spec is very open about what kind of power is available. A low-power device could be powered from the bus, but this is not the point of this power supply. Its primary importance is so that devices which are not powered do not cut the bus into two isolated pieces. Instead every device must be able to power up its PHY off of bus power, even when it is disabled, so that transmissions can continue to be propagated down the bus.

## Slide 44: IEEE-1394 – How Does It Work?
IEEE-1394 is serial
  Two twisted pairs for signaling
    Strobe_RX / Data_TX
    Strobe_TX / Data_RX
  One twisted pair for power
Packets
  Header
  Data block (optional)
Notes: IEEE-1394 transfers data directly over copper without encoding it. However, the two twisted pairs define the synchronization clock using a strobing sequence which is synchronized to the clock. This mechanism is easier, and more resistant to skew, than the NRZI used for USB.
IEEE-1394 communicates using packets, which consist of a header and a data block. The header contains information consisting of a token which explains what type of header is being transferred and fields containing information about the transmission. This information varies on the type of packet. A SELF_ID packet is one quadlet (the term for a 32-bit word) describing the device. Alternatively, a data packet might be several thousand bytes, starting with a header consisting of several quadlets describing the source, destination, type of message, a CRC, and other transmission specific information.
Notably, all packets are quadlet aligned, and must be padded to completely fit an integral number of quadlets.

## Slide 45: IEEE-1394 – How Does It Work?
Subactions
  Asynchronous
  Isochronous
Transactions
  Read
  Write
  Lock
    Fetch & add
    Compare & swap
    Mask & swap
Asynchronous subactions
Isochronous subactions
Notes: A subaction is the atomic sequence by which is a packet is transmitted and acknowledged. It consists of a synchronization signal, the packet data, a gap to wait for acknowledgement, and another, longer gap, waiting for the next arbitration period. Note that isochronous transmissions have no acknowledgement gap; delivery is not guaranteed error-free, so no check is performed to see if the data is received.
These subactions are combined to generate basic atomic functions. These functions are called out in IEEE-1212, and provide basic services like read, write, and lock. Lock can be used to generate compound commands like Fetch & Add. Since asynchronous transactions can take a non-deterministic amount of time, any modification to a remote value which depends on its current value demands that the value be locked so that a read and write can both occur. These lock transactions provide this service.

## Slide 46: IEEE-1394 – How Does It Work?
Arbitration
  Asynchronous
    Fair
    Urgent
  Isochronous
    Cycle master
    Cycle timing
DMA
Identification and enumeration
Notes: Since IEEE-1394 is a peer-to-peer bus, there must be a dynamic system of arbitration. All devices must support fair arbitration for asynchronous packets. An arbitration cycle is defined as a period of time during which devices are given equal access to the bus. During any given arbitration cycle, if a device gains access to the bus, it will not try to capture the bus during that period again. At the end of the cycle, all devices are once again allowed to transmit. The exception to this rule is urgent arbitration, which gives a device priority over all other devices for 75% of the arbitration cycle.
Isochronous transfers also have a cycle. That cycle is reported by the Cycle Master, commonly the Root. At the beginning of a cycle, all Isochronous devices try to transfer with urgent priority. Once they have all transferred, fair asynchronous arbitration continues for the rest of the cycle.
One advantage of IEEE-1394 is the ability to perform native DMA transfers from device to device. Since all devices have identical address spaces – from the view of the bus, at least – they all have access to each other’s public address spaces and can read and write to and from them. This is much more efficient than the centralized, programmatic transfers performed by USB.
Self-identification occurs automatically when a device is plugged into the bus. It begins when every device chooses “parents” and “children” The “parent” closest to all the nodes becomes Root. Then, all devices choose addresses in the same step as they report their characteristics to the rest of the bus. Note that this is an invasive process, which causes the bus to reset.

## Slide 47: IEEE-1394 – How Do I Use It?
Requirements:
  Any IEEE-1394 based device
    All are peers and can communicate
    May not have anything useful to say
  Special Cases:
    PC’s (x86, Mac, etc.) offer more options for using IEEE-1394 devices, but require compatible OS. (Win98, Win2k, MacOS, Linux*, etc.)
    Consumer electronics devices have certain defined inter-operability. (See www.1394ta.com for details)
* Solid confirmation that IEEE-1394 support will be available with Linux Kernel 2.4.x was unavailable at printing time.
Notes: Depending on the device, all related IEEE-1394 devices should be able to communicate once bus enumeration and identification is complete. If a device has software to control its IEEE-1394 functionality, that software must be loaded for transactions to be carried out. There are now protocol stacks available for most major personal computing platforms and many consumer electronics.

## Slide 48: IEEE-1394 – How Do I Use It?
Just plug and use!
  Same rules as USB
  All devices will review identification of all devices
  Careful! Plugging in disturbs the entire bus!
Unplug!
  Unplugging has little effect on software layers
  However, unplugging will reset the network
  Careful! A portion of the network may temporarily be isolated when disconnecting a node
Notes: Plugging in the IEEE-1394 device will result in a bus reset and a fresh bus enumeration and identification sequence. Once this is done, all devices will know about the new device. However, this also means that an insertion, even if the chain is not broken, will result in a temporary halt to bus operations. Unplugging has the same results. Therefore, caution should be used when connecting or disconnecting a device. When designing your bus topology, consider what devices will need frequent connection and disconnection – they should be leafs instead of branches, to reduce downtime during a bus change.

## Slide 49: IEEE-1394 – What’s Next?
IEEE-1394b
  Defines 800-3,200 Mbps transfer rates
  Longer distances available (50-100 m)
    Copper up to 4.5 m at 1,600 Mbpsc
    Fiber up to 100 m at 3,200 Mbps
  New constant full-duplex protocol
    8B10B encoding with Hamming Distance 2
    Pipelined arbitration speeds signaling
Support for faster configuration process and network bridges for larger network lengths

## Slide 50: CardBus – What Is It?
Backplane for communication between computing devices, memory, and peripherals
History
  PCMCIA
  JEIDA
  PC Card standard
CardBus
  Plug and Play
  Portable
Notes: CardBus is a 32-bit backplane for communication between computing devices, memory modules and I/O peripherals.
The original portable modular backplane definition was developed by two groups – Personal Computer Memory Card International Association and the Japan Electronic Industry Development Association. The original specifications were written in 1986 to standardize the portable computer memory market, which was disparate at the time. Since then, it has become an excellent format for porting general peripherals to portable computing platforms. The PC Card Standard has taken over the old PCMCIA standard. It defines two types of devices: 16-bit PC Cards and 32-bit CardBus Cards. The 16-bit PC Card is basically the original PCMCIA standard. The CardBus is something different.
CardBus is a solution like USB and IEEE-1394, in that it provides a hot-pluggable platform with plug-and-play functionality. It is also highly portable in that notebook, palmtop, and handheld computing platforms are inherently human-portable devices.

## Slide 51: CardBus – What Is It?
32-bit, 33 MHz bus interface
Multiple functional form definitions
  I/O
  Memory
  Video
  Audio
Multiple physical form definitions
Notes: CardBus provides a 32-bit, 33MHz interface interface, using a multiplexed bus with synchronous, sideband control signals. A 4-bit control bus provides byte enable and control information.
CardBus has multiple functional definitions available. It can act as a addressable I/O space and as a cacheable memory space. (Or memory-mapped I/O space.) A high-level video protocol allows CardBus devices to provide video services. The CardBus connector also provides a channel for digital audio data to be transferred independent of the remainder of the bus.
CardBus also comes in several physical forms. Type I is a very slender card which has historically been used for memory storage in small devices. Type II is a half-height device, and typically is used for peripherals like modems, Ethernet cards, and other general-purpose peripherals. Type III cards are full height, and are designed to accommodate larger devices like hard drives. The typical implementation of a PC Card socket is large enough to accommodate two Type I or II cards, or 1 Type III card.

## Slide 52: CardBus – What Does It Look Like?
Parallel backplane
  68 pin parallel interface
  32 pin address/data bus
  15 pin synch control bus
Typical system supports multiple CardBus devices on one bus
Main bus controller
CardBus controller
Main bus controller
  First scenario – more likely for consumer electronics devices and Handheld devices
  Second Scenario – more likely for Notebooks and PCs
Notes: The topology of the CardBus is much simpler that that of the serial busses previously discussed. Typically, two CardBus sockets will be in a fixed topology with relation to the Host. The Host will typically have the arbitration circuitry, but all devices on a CardBus backplane can become master.
The backplane connects to the host system via a 68-pin interface. 32 pins are used for the multiplexed bus, with 15 pins available for synchronous control and other sideband signals. The remaining pins are for power and ground.
The backplane can be connected directly to the main peripheral interconnect. In many notebook computers, and PC’s with PC-Card adapter cards, a PCI-CardBus bridge connects the CardBus to the PCI bus. This isolates activities on the CardBus from the rest of the system, but it also introduces extra latencies and diminished throughput on the CardBus, since all requests must be processed through the bridge.

## Slide 53: CardBus – What Does It Look Like?
Standard PC-card connector
CardBus modem
CardBus Ethernet adapter
Notes: Here are some examples of devices that use the PC Card specification.

## Slide 54: CardBus – How Does It Work?
16-bit PC-Card : ISA :: 32-bit CardBus : PCI
  Few modifications to PCI interface necessary to implement signaling protocol
  Power management different
    Multiple voltage specifications available
    Support for multi-stage power management services
    Hot-pluggability and hot-unpluggability
  Support for 16-bit PC card in same slot desirable
  Often a PCI-CardBus bridge is used to manage the CardBus peripherals
Notes: Let’s use this analogy:
16-bit PC-Card is to ISA as 32-bit CardBus is to PCI.
32-bit CardBus differs very little from PCI in most forms,including signaling, commands, and even some of the configuration structures. The CardBus specification was designed with that similarity in mind. That way, manufacturers with custom ASIC solutions would not need to change them to accommodate CardBus.
Power Management for CardBus is different from PCI, however. First, hot-pluggability is supported on all levels, from physical to the OS level. Second, multiple power specifications are available. A device can request different voltages on power-up. However, those voltages will not necessarily always be provided. Additionally, multi-stage power management should be available from the host system, allowing the device to slow, or disable, its clock in response to decreased power modes.
One other difference between PCI and CardBus is that CardBus provides the option for 16-bit PC-Cards to be used in the same socket as a 32-bit CardBus card. This makes such CardBus sockets much more flexible.

## Slide 55: CardBus – How Does It Work?
Bus cycles
  I/O
  Memory
  Configuration
Configuration storage
  PCI configuration structures
  CardBus information structures
Notes: CardBus transmissions consist of bus cycles. A bus cycle is initiated by the bus master and terminated by the bus master or the bus target, using sideband control signals. (FRAME#, IRDY#, TRDY#, etc.) A bus cycle is either an I/O cycle (read or write to an address), a memory cycle (single or bursted reads or writes to a memory location), or a configuration cycle (single or bursted reads or writes to the target device’s configuration space.) Although it can take several clock edges to begin a transfer, bursted transfers can move up to four bytes every clock edge.
Self-configuration is made possible by a standard configuration space. The PCI configuration structures provide plug-and-play functionality, indicating product and vendor identification as well as making interrupt and I/O window configuration registers available. The CardBus Information Structure, or CIS, is an expansion of the PCI configuration space, which stores lower-level information about the CardBus device.

## Slide 56: CardBus – How Does It Work?
CardBus is a backplane
  As opposed to serial interfaces...
    There is a predetermined topology
    Control signals are synchronous
    Protocol does not offer Isochronous transport
  Some asynchronous signals available
    Power indications
    Digital audio stream
    Interrupts
DMA
Notes: As opposed to the serial busses that we have been looking at, CardBus is a backplane. As a result, even though CardBus shares some characteristics with our other busses, there are some fundamental differences. There is a predetermined topology with a backplane, for example. Busses must perform bus-identification to determine where target devices are. CardBus will have a predetermined number of slots in parallel, typically two, either of which are empty or not empty. (Emptiness can be determined using a set of connector pins which are connected together when a card is inserted to indicate that the slot is not empty.)
Control signals, which are transferred as asynchronous packets on other busses, can be transmitted synchronously with the message on CardBus. Additionally, with the exception of the option for streaming digital audio, CardBus has no isochronous transfer abilities. It depends on the operating system to schedule fairly and the bus controller chips provide the CardBus with adequate priority. A few asynchronous signals, such as power-level request, digital audio, and interrupts are sideband signals, asynchronous to the normal bus cycles.
CardBus also has direct hardware DMA. This is unavailable under USB, and can be implemented using a low-level protocol with IEEE-1394, but CardBus, like PCI devices, can directly access it’s hosts memory space.

## Slide 57: CardBus – How Does It Work?
Host software
  Socket services
  Device driver
Metaformat
  Basic compatibility
  Data recording
  Data organization
  System-specific services
Notes: On the operating system level, the host is expected to provide a set of low-level services called socket services. Socket services provide generic access to CardBus devices, and abstract the specific device driver away from the actual implementation of the socket and CardBus controller. The specific device driver acts as an intermediary between the application and the operating system’s socket services layer.
In order to provide generic services, the Metaformat definition defines how configuration and general functionality should occur. The four levels of the Metaformat definition begin with the very generic Basic Compatibility layer, which guarantees that devices can be generally configured by Socket Services in the same way. The remaining three layers define higher level protocols which allow similar classes of devices, such as data storage, to function in a compatible way. The System-Specific Services layer allows individual architectures to define how devices should function in their systems. There are, for example, some definitions for behavior in an x86 system.

## Slide 58: CardBus – How Do I Use It?
Configure socket services
Hot plugging
  Plug in...
    System disruption is minimal
    Socket services should load device driver stack autonomously of other OS device services
  Unplug...
    Often, system must be interrupted to verify validity of device removal
    Use caution when removing a device from an active bus
Notes: The first stage in using a CardBus device is to make sure Socket Services is configured. This should typically be linked to the CardBus controller hardware, and is activated in an Operating-System-dependant manner. Most Socket Services drivers are configured for hot-pluggable operation, but the user should check if uncertain.
Plugging in a device will result in minimal change to the CardBus, although the operating system will need to configure the new device, which can disrupt overall functionality on a highly-loaded system. If Socket Services is configured correctly, though, the driver stack should load automatically when the device is inserted. If this device has never been used in a system before, it may be necessary to provide proper driver software to use the device.
Removing an inactive device should not significantly effect the overall system performance. Particular implementations of socket services may react differently to the removal of a device, however. Some may prompt for user confirmation upon device removal. Removal of a device while it is actively utilizing the bus is not recommended. Although the system should be able to recover from such an action, removing an active can cause application layer confusion, “blue screens,” bizarre messages, etc.

## Slide 59: CardBus – What’s Next?
Better power management system
Investigations into faster transfer rates
  The current connector cannot support a 64 bit bus, since it only has 66 pins
  Operation at 66MHz is unlikely due to hostile environment
Modification in physical connector form is unlikely any time soon

## Slide 60: Ethernet – What Is It?
Ethernet is a physical/data link solution
History
  ALOHA
  Xerox
  DIX
Standards
  IEEE-802.x (i.e. IEEE-802.2, 802.3, 802.5)
  ISO-8802.x
Notes: The next bus technology to discuss is Ethernet. Ethernet has a colorful past, beginning with the ALOHA system developed at the University of Hawaii. This is a system of transceivers who can talk to, and listen to, a common transceiver but are blind to each other.
Robert Metcalf came up with the idea of a network connected by a common “Ether” in 1973, at Xerox PARC. The idea was patented in 1976, and was adopted by DEC and Intel for product implementation in 1980, resulting in the joint promotion of the DIX standard.
An enhancement o f the original Ethernet was adopted by IEEE project committee 802, and was standardized by the IEEE as standard 802.3 for Ethernet. The ISO later adopted those standards as 8802.
The Ethernet standard, based on the Ethernet II/ DIX standard, is called:
“IEEE-802.3: Local and Metropolitan Area Networks, Part 3: Carrier Sense Multiple Access with Collision Detection (CSMA/CD) Access Method and Physical Layer Specifications”

## Slide 61
Emerging Bus Technologies
USB 2.0
IEEE-1394
CardBus
Ethernet
OSI Reference Model
PHYSICAL
DATA LINK
NETWORK
TRANSPORT
SESSION
PRESENTATION
APPLICATION
Notes: Let’s go back to the OSI reference model for a moment:
When we examined USB, 1394, and CardBus, we found that the specifications outlined the first four stages of the protocol stack, leaving the remaining three open to later specification by OS and application developers.
Ethernet, however, only defines the first two layers. The next two must be provided by other sources, to fill the gap between the OS and the media. This source has been network developers and product developers, with such solutions as the Novell stack and TCP/IP.
Strictly speaking, though, “Ethernet” only defines the bottom two layers of the OSI model. The remainder must be filled in by third-party protocols.

## Slide 62: Ethernet – What Is It?
Ethernet is a physical/data link solution
History
  ALOHA
  Xerox
  DIX
Standards
  IEEE-802.x (i.e. IEEE-802.2, 802.3, 802.5)
  ISO-8802.x
Notes: Thus, the answer to the question “What is Ethernet?” is that it is a medium for transport, and a protocol for data encapsulation. TCP/IP, a popular network/transport protocol, will be discussed before the close of this section.

## Slide 63: Ethernet – What Does It Look Like?
Pieces
  Layer 1 repeaters/hubs
  Layer 2 bridges/switches
  Layer 3 routers/gateways
Topologies
  Bus
  Star
  Uprooted tree
  Ring
Notes: Robert Metcalf’s originally proposed “Ether” consisted of a terminated coaxial cable, interconnecting multiple transceiver nodes which are, in turn, connected to the computer via an interface bus. Beyond computers, which can be anywhere from simple workstations to mainframes or servers, there are three physical components to the network:
Repeaters and Hubs – repeat signal from one bus to another. May boost, retime, and reshape signals, but the data is not interpreted, filtered, or modified. A necessity for non-coax solutions
Bridges and Switches – these devices are like repeaters, but they can direct content based on low-level addressing. They can buffer packets to avoid bus contention. The reason behind this will be explained in a moment.
Routers and Gateways – these devices are high-level switches. They can observe the protocol being used, and can direct traffic appropriately between different networks, using different media. (Copper to fiber, for example.) The reason behind this, too, will shortly be obvious.

## Slide 64: Ethernet – What Does It Look Like?
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
To router
Local traffic
Local traffic
Traffic routed to destination
Switch
Repeater/hub
Switch
Segmented collision domain
Repeater/hub
Notes: The above diagram demonstrates the topology of the components described.

## Slide 65: Ethernet – How Does It Work?
CSMA/CD
  Carrier sense
  Multiple access
  Collision detect
Encoding
  Manchester  4B/5B  8B/10B  MLT3  PAM5
Theoretical bandwidth
  nbase-mt
  nbroad-mt
100base-T
10broad-36
1000base-LX
Notes: The ideas behind Ethernet of particular importance are defined in the name of the low-level protocol:
Carrier Sense: Is there anyone talking?
Multiple Access: Now I’m talking!
Collision Detect: Oops! Pardon me! Sorry about that.
Whenever a node wants to transfer data, it listens for a carrier. If it hears none, it communicates on the shared medium so that all devices can hear it. Since signals don’t travel infinitely fast, two transmitters might begin simultaneously. If they hear their transmission get garbled, they must back off and try again after an amount of time determined by a random distribution. (Roughly 2xn according to the IEEE specification). If they aren’t garbled in the first 64 bit times, they win the bus.
In order to allow device synchronization, the data is Manchester encoded. That is, the data is defined by either one or two transitions occurring every bit time. This can result in a lot of transitions. On higher speed busses, 4B/5B is used, which converts every four bit combination to a five-bit code. 8B/10B works in the same way. At very high-speed busses over copper, this is not adequate to safeguard the signals. They must use MLT3 or PAM5, which use three and five voltage levels, respectively, instead of two levels as used in binary
Theoretical bandwidth is the first number in the media type. For example, 100base-T is 100Mbps over twisted pair

## Slide 66: Ethernet – How Does It Work?
IEEE 802.3 packet
No provisions for power
No isochronous transfers
  All data is asynchronous, although some control information is passed synchronously
No self configuration!!
Notes: The data link specifications for Ethernet provide for a packet of minimum length of 60 bytes and maximum length of 1,500 bytes, including header and payload. The header contains information about the data link protocol, the source, destination, and size of the payload. There is also a checksum for the packet. This checksum is the only error checking available at this level.
Note that, as opposed to our other busses so far, there are not provisions for bus power or isochronous transfers. Additionally, there is no low-level self-configuration service through Ethernet. Any self-configuration is dependant on much higher-level protocols.

## Slide 67: Ethernet – How Does It Work?
An example TRANS/NET: TCP/IP
  IP = (Internet) internetworking protocol
    Addressing & routing
    Datagram & error detection
    IPv4 vs. IPv6
Type
Net ID
Host ID
32 Bits
ddd.ddd.ddd.ddd
Prefix
128 Bits
hhhh:hhhh:hhhh: ... :hhhh
Notes: As mentioned earlier, there are a variety of ways to complete the Ethernet stack. One popular protocol is TCP/IP, developed for the ARPAnet in the 60s and packaged with UNIX since then, resulting in widespread distribution and usage. We will use them as an example:
The network protocol is IP, which is the Internet Internetworking Protocol
IP provides addressing and routing services, allowing networks larger than 256 devices to exist. Level 3 routers and gateways use IP to determine whether a packet belongs in a network, or if it needs to be transferred out of the subnet.
All data is encapsulated into a Datagram, which is a simple data package with header, including identification and address information, and a payload. In the present version of IP, v4, there is no special security or configuration services provided by these datagrams. They are somewhat spartan to provide robust support to higher level protocols.
IPv6 will offer more support in its datagrams for configuration, identification, and security. It will also offer a 128-bit address, compared to the current 32-bit address. Consider this:
128 bit address = 3.4E38 addresses total
= 665E21unique addresses/square foot on earth

## Slide 68: Ethernet – How Does It Work?
TCP/IP (cont.)
  TCP = Transmission Control Protocol
    Reliable stream transport service
    Connections & segments
    Handshaking
  UDP = User Datagram Protocol
    Connectionless
    No handshaking or segments
Notes: Two transport protocols available with TCP/IP are TCP and UDP.
UDP provides raw datagram support for simple messages between two devices. It does not provide much support beyond IP.
TCP provides a reliable stream transport service, which provides support for segments. These are the building blocks foe peer-to-peer connections with guaranteed transaction completion and defined handshaking sequences. It is a more complex protocol, but offers better support for continuous session objects, like “sockets.”

## Slide 69: Ethernet – How Do I Use It?
Each device needs a NIC
  Some faster protocols will require a switch
  Computers need an OS with a protocol stack
  Devices must share lower-level protocols
  Computers may also need to share upper-level protocols
Each device must be configured
  Small networks can use static addressing
  Larger networks can use protocol-dependant dynamic addressing (ex. DHCP)
Notes: In order to use Ethernet, you need a Network Interface Controller. These typically integrate the transceiver, interface, and Media Access Control (MAC) logic into one module. Depending on the speed of the network you are using, you may need a high-level switch to avoid collisions with other NICs. Computers running a general purpose OS will need a protocol stack. Without any other hardware to intercede, all devices will need to share the same PHY-level media (copper, fiber, and so on). Some protocol stacks are flexible enough to work with other protocol stacks (NDIS, ODI). You must familiarize yourself with your OS to know whether this is possible.
Note that, unlike our previous busses, Ethernet devices must be configured manually, including selecting a device address (IP address if you are using TCP/IP) and becoming aware of other devices. Larger networks will often use a central server to provide dynamic addressing services.

## Slide 70: Ethernet – How Do I Use It?
Ethernet is not hot-pluggable
  Adding or removing a device from the bus will not update group information automatically
  For some busses, device addition or removal is intrusive; for others, it is not
    For some fiber media, ring topologies, changes are intrusive
    For most star and uprooted tree topologies, additions and removals do not effect an active bus, unless the removed device is an active party
Some auto-negotiation is available
Notes: Note that Ethernet is not hot-pluggable. Adding or removing a device will not update anyone’s “neighborhood” listing. The degree of “intrusive-ness” of a change in device status depends on the network type and topology.
Auto-negotiation is available for devices on multi-speed busses, but this is dependant on the NICs involved, and, on failure, slows everyone down to the slowest device.
With IP6, some network level auto-configuration will be available.

## Slide 71: Ethernet – What’s Next?
Current protocols:
Notes: This slide contains a summary of all available cabled Ethernet protocols, as well as improvements to existing specifications.

## Slide 72: Ethernet – What’s Next?
Future projects
  10 Gbps Ethernet (IEEE-802.3ae)
    Fiber only
    March 2002
  Power distribution (IEEE-802.3af)
    December 2001
  Numerous wireless programs
    Wireless Ethernet
    Bluetooth
Notes: 10 Gbps Ethernet is in discussion at the IEEE 802 committee. Significant PHY modifications will be necessary to achieve this speed, and it is not likely that there will be any way to transmit over copper.
Power distribution is being explored. This might require a change in PHY on high-speed cables. Some low-speed attachments might be able to use the cabling as it is now defined.
There are also numerous wireless protocols that utilize Ethernet and similar 802 protocols. There isn’t time for to discuss these protocols today, but those interested in wireless Ethernet might be interested in some of the “related presentations” suggested at the end of this presentation.

## Slide 73: Topical Comparisons
IEEE-1394 vs. USB 2.0
Ethernet – everywhere, somewhere, or nowhere?
Isochrony vs. asynchrony
What about traditional busses?
Notes: .
Based on feedback on numerous occasions, and on some of the inherent design questions generated by these busses, some questions have arisen that treat the issue of performing this comparison quite well.
The first is “Will USB 2.0 kill IEEE-1394?”
The second is “Why don’t you use Ethernet?” and the companion “Why are you using Ethernet?”
The third is “What’s the difference between these data transmission styles?” or “Why don’t you just use this mode for this device?”
And the fourth is “What’s wrong with the busses we have already?”
The discussion will begin, comparing IEEE-1394 and USB 2.0 and the ability to hold in the market. The next topic will be the appropriateness, and inappropriateness, of Ethernet in given applications. Next will be a comparison of the different data transmission styles, followed by a comparison of the discussed busses with some more “traditional” busses.

## Slide 74: IEEE-1394 vs. USB 2.0
Similarities
  General idea
  Speed
Distinctions
  Speed
  Protocol
    Topology
    DMA
  Cost
Notes: With the advent of USB 2.0, many have suggested that USB and IEEE-1394 will compete to the final disappearance of one from the market. This view is often justified by the similarities between the two busses. The general idea of both busses is very similar: A simple, serial line that can be connected between devices to allow easy data transfer and control. Both are hot-pluggable and auto-configuring. Further, version 2 brings USB up to the throughput speeds of the original 1394 specification, seemingly damaging IEEE-1394’s hold over high-speed serial communication niche.
However, you can distinguish busses by certain differences that remain inherent to the busses. First, the protocol behind 1394 is quite different than USBs. Where USB is an unrooted tree which relies on the host for all transactions, 1394 is a daisy chain that allows interoperation of any two compatible devices, even when an intermediary is disabled. All devices in the 1394 bus are peers and can transfer data over the bus, as masters, allowing multiple classes of devices by different vendors to seamlessly integrate. Additionally, 1394 maintains much of its ground to USB in the area of transaction latency. The monstrous transaction latencies experienced under USB 1.1 are diminished by a factor of 8 with USB 2.0, but the same structural limitations exist, since the host must plan and schedule all transactions on the bus. 1394 provides a natural, free-running arbitration mechanism which reduces these latencies significantly. And, in the area of cost, USB still holds a strong lead, since the complexity necessary for peripheral development and production remains less than that for 1394 devices, which must be autonomous computing machines.

## Slide 75: IEEE-1394 vs. USB 2.0
Complimentary
  Small, inexpensive products benefit from USB low- and full-speed definitions
  High-speed consumer electronics need peer-to-peer communication of IEEE-1394
  High-speed computer peripherals will likely be built on whichever platform is closest to its protocol and topology in form and function
  Both protocols will probably keep each other’s prices low to compete for design wins
Notes: The end result of this competition will bring out a wide variety of products using both busses. Products in the domains which are best facilitated by USB include small, low power, low speed peripherals and medium speed, low cost data transfer devices. High speed consumer electronics that depend on a peer-to-peer environment will continue to use IEEE-1394, as will computer peripherals which benefit from the global addressing scheme provided by IEEE-1212. High-speed data streaming devices will be able to go either way, and will probably be developed for whichever bus meets the desired topology.
And, of course, the natural result of the competition between the two busses is that the busses will keep each other’s prices down as component vendors compete for design wins and product vendors compete for consumer buys.

## Slide 76: Ethernet – Where Does It Go?
Computer-to-computer
  Data sharing
  Remote device usage
Computer-to-server
  Datalogging
  Centralized configuration and monitoring
Device-to-computer (or server)
  Distributed acquisition
  Web-enabled measurement
Notes: Ethernet has long been a fixture in many commercial and industrial environments. How does this effect the Measurement and Automation system? There are several situations in which Ethernet makes the M&A system work more efficiently.
Computer-to-Computer connectivity can be accomplished easily with Ethernet through an inexpensive level 1 hub. Up to eight or ten computers can be internetworked using a simple hub, which can be connected to a modem or router for external connectivity. Alternatively, a computer with an ethernet computer can create an Internet gateway for the other computers on the LAN. The same applies to instruments. A user at one computer can use remote access methods to use an instrument on another computer in any other subnet.
By connecting a computer to a central file server, powerful datalogging applications can be developed. (See presentation WS3A, “Building a Network-Based Data Logger” by Thomas Magruder) Additionally, for automated testing applications, centralized configuration and monitoring allows vast numbers of sensors and instruments to be easily synchronized to the same operating parameters.
Additionally, devices which can be directly connected to Ethernet provide the opportunity for distributed acquisition. This sort of system works well in environments with many test points and a few monitoring points. Additionally, as web-enabled devices become more prevalent, Ethernet will be the major medium for utilizing them.

## Slide 77: Ethernet – Where Does It NOT Go?
Real-time instrumentation
  Ethernet is non-deterministic past ~10% utilization for shared networks, ~50% for switched networks
  Ethernet-controlled real-time programmable instruments offer a way around this limit
Highly mobile applications
Single point-to-point applications
  Not an efficient use of Ethernet services
  Better to use a bus with point-to-point protocol
Notes: As advantageous as Ethernet is under many circumstances, the weight of the protocol makes it a less of attractive option, particularly when dealing with applications that need real-, or nearly-real-time feedback. Since the backoff time for a collision is represented in many MAC implementations as an exponential function of the number of collisions, an environment with many potential collisions makes real-time implementation difficult. A study by Schneider Automation finds that 10 percent utilization of an Ethernet makes it non-deterministic. A switched environment is better, remaining deterministic at up to 50 percent utilization. For true real-time control, an Ethernet-controlled, embedded real-time device offers superior performance.
Truly mobile applications are somewhat hostile to Ethernet, as the configuration requirements make moving from area to area difficult. However, with dynamic addressing server networks, and wireless Ethernet technologies gaining a foothold, Ethernet may become a highly mobile medium for measurement and automation.
Another poor application of Ethernet is to use it in a strictly point-to-point protocol. The mechanisms necessary to provide more widespread access are still present, with none of the benefits. The alternative is to create a proprietary protocol, which is good for a single manufacturer but causes customer problems when they want to network multiple instruments and systems together. A bus with a built-in point-to-point protocol, like RS-485, IEEE-1394, or USB, would be more efficient.

## Slide 78: Isochrony vs. Asynchrony
Who needs asynchrony?
  Non-deterministic remote/mobile acquisition
  Guaranteed delivery control applications
    Most applications involving data acquisition
    ex: Frequency analysis, waveform generation, etc.
Who needs isochrony?
  No one who needs guaranteed delivery!
  Time-sensitive PID applications
  Environment measurement for unlogged human observation
Notes: Another issue is the confusing question of what kind of transmission protocol you should be using. The transport level protocols available differ between the discussed busses.
Asynchronous transmissions are not synchronized specifically to either your source or destination device, hence “a-synchronous.” With that in mind, for cabled networks where latencies may exist, an asynchronous transport mechanism allows one to initiate a transaction, and then continue with other activities while the transaction is processed. There is no definite time of response, but the delivery is guaranteed or, at the worst, an error is reported that the transaction cannot be completed. This is adequate for most applications that are not time-sensitive but that do need the data to be delivered accurately and completely.
Isochronous transmissions, where isochronous means “equal in duration,” provide transaction time at guaranteed intervals to varying granularity. Isochronous applications include anything where data is streamed blindly, like video and audio transmissions. The down side is that isochronous protocols are lossy, which means that a failed or misinterpreted transaction cannot be retried without higher-level protocol assistance. However, the higher the level where the mechanism is implemented, the greater the potential error for the transfer interval. Some other examples where isochronous transfers can be used is in some PID applications and environmental monitoring applications.

## Slide 79: Isochrony vs. Asynchrony
Synchronous only
  Cardbus
Asynchronous only
  Ethernet
    Isochronous or synchronous transport could exist on proprietary networking schemes
Asynchronous and isochronous
  USB 2.0
  IEEE-1394
Notes: Our busses have varying degrees of support. CardBus is a strictly synchronous bus. A transaction is executed immediately upon request.
Ethernet only offers asynchronous support, although an isochronous protocol could be implemented using high-level drivers. However, the guaranteed period of transmit would have to take potential bus conflicts into account.
USB 2.0 and IEEE-1394 both offer asynchronous and isochronous transfer protocols. The IEEE-1394 protocol provides granularity of down to one-eighth of a millisecond, as does the high-speed definition of USB 2.0. The full- and low-speed definitions only allow one transmission per millisecond. Both busses come with the caveat that isochronous transmissions do not compete fairly with other transport mechanisms for bus time. Therefore, isochronous devices are capable of starving all non-isochronous devices on the bus. Which is, of course, the whole point.

## Slide 80: What About “Traditional Busses?”
ISA, PCI
  ISA is being phased out
  PCI remains the best mechanism for computer-based measurement and control
    Portability
    Slot replacement
Parallel port
  One of the first portable/slotless alternatives
  Obsolete by USB and IEEE-1394
Notes: What about “Traditional Busses?” The purpose of this presentation is to determine how to improve the design of measurement and automation systems using emerging bus technologies. Why might we need to phase out traditionally utilized busses, then?
Inside the bus, ISA and PCI remain popular and powerful. However, ISA has already been phased out of the personal computer development standard, forcing developers over to the PCI standard. PCI is still going strong as the best and fastest way to communicate with the computer. However, it lacks the portability of a cabled or removable device, which is a severe limit in flexibility. Further, many systems are going “slotless,” which makes them more compact but requires all add-ons to go outside the computer. External busses can cater to these systems. Therefore, PCI cannot apply to all peripherals under all conditions.
The parallel port was supposed to be an easy-to-use mechanism for portable and slotless device interaction. However, parallel port specifications come in many flavors, and implementations vary within those standards, making the configuration process frustrating for the user. The easy configurability of USB and IEEE-1394 take the place of the parallel port in terms of functionality, and new systems sometimes do not include a parallel port, instead relying on USB and Ethernet to handle printer communications.

## Slide 81: What About “Traditional Busses?”
RS-232, RS-485
  Vast serial networks exist and will remain
  New large LANs could be served by Ethernet
  New small LANs can use RS-485 or IEEE-1394
GPIB
  Most box instruments have GPIB
  HS-488 is very fast, highly supported
  SCPI offers easy (easier) migration to Ethernet
  GPIB controllers exist for all of these busses
Notes: Vast networks have already been developed based on the major serial bus protocols, recommended standards 232 and 485. These networks are still an efficient method for point-to-point communication. Newer larger LANs could use these protocols, or they could use Ethernet, which is designed for large network interconnections. Smaller LANs could use RS-485 or IEEE-1394 for communication. Very small networks could USB. This is a question of the composition and age of existing infrastructure.
One final bus of interest is GPIB. GPIB remains ubiquitous on boxed instruments. The HS-488 standard, developed by National Instruments, provides a very fast GPIB communication protocol for such instruments. Therefore, it is up to the users discretion, when dealing with boxed instruments, how they wish to build up their T&M system. Note that 1) SCPI provides a method of transporting the GPIB communication protocol over Ethernet, making porting to an Ethernet topology somewhat easier, and 2) GPIB controllers exist for all of the busses presented in this document, and many that are not. (Presently, GPIB controllers are available from National Instruments for ISA, EISA, PCI, PXI, PC-Card, NuBus, NEC, MicroChannel, Sun/SPARC, Ethernet, USB, IEEE-1394, PMC, EXM, PC/104, VME, Parallel Port, RS-232, RS-485, SCSI, and Fiber Optics.)

## Slide 82: Acknowledgements
Boggs, David R, and Robert M. Metcalf. (Xerox Palo Alto Research Center) “Ethernet: Distributed Packet Switching for Local Computer Networks.” Communications of the ACM, ACM, Inc. Vol. 19, No. 5, July 1976, pp 395-404. 1976.
“Ethernet FAQ.” LANs/ethernet-faq, comp.dcom.lans.ethernet. Public Domain, 1994.
“Gigabit Ethernet: Accelerating the Standard for Speed.” [White Paper] Gigabit Ethernet Alliance. 1998.
Gilbert, H. “Ethernet.” PCLT. 1995.
Halsall, Fred. Data Communications, Computer Networks, and Open Systems. Addison-Wesley Publishing Company. Harlow, England. Fourth Edition, 1996.
Jain, Raj. “IP Next Generation: IPv6.” Ohio State University, Columbus, OH.
Notes: All material is the property of the owner.
All trademarks are the property of their respective owners.

## Slide 83: Acknowledgements
Kaplan, Hadriel. “Fast Ethernet Training.” InterOperability Lab, UNH.
Lueker, Jon. “USB 2.0: Electrical Overview.” May 2000 USB 2.0 Developers Conference. Intel, CA. 2000.
“P1394: A High Performance Serial Bus.” High Performance Serial Bus Working Group. IEEE Standards Dept. Draft 8.0v2, 1995.
PC-Card Standard: Release 7.0. PCMCIA/JEIDA. 1999.
“TechFest Ethernet Technical Summary” TechFest.com. 1999.
Teener, Michael D. Johas. “IEEE 1394-1995: High Performance Serial Bus.” Zayante, Inc., Scotts Valley, CA. 1998.
Universal Serial Bus Specification. USB Promoters*. USB-IF. ver 2.0. 2000.
*USB Promoters are Compaq Computer Corporation,
Hewlett-Packard Company, Intel Corporation, Lucent Technologies Inc,
Microsoft Corporation, NEC Corporation, Koninklijke Philips Electronics N.V.