## Slide 1: Telephony Parametric Testing
Abhay Samant
Software Engineer
Thurs Aug 17
10:15-11:30 a.m.
Lavaca (6B)

## Slide 2: Outline
What is telephony?
Telephony technologies
Telephony test
  Media tests
  Parametric tests
Demos using LabVIEW™ and computer-based instruments
Notes: We can divide the area of telecommunications into four major segments, including telephony, wireless, datacom and broadcast. The end users, products and signals are different for each segment, but the underlying test methodology is very similar. In this presentation, we focus on one of these four segments, namely telephony. We talk about different telephony technologies such as POTS, T1 and ADSL. We describe the signals and data transmission rates associated with these technologies. We then talk about telephony testing which consists of parametric tests (which measure the characteristics of the signal), protocol tests (which analyze the information carried by the signals) and media tests (which analyze the communication channel). In this presentation, we mainly focus on parametric testing. In the latter part of the presentation, we have a number of demos which show how LabVIEW and computer-based instruments can be used for parametric testing of telephony signals

## Slide 3: What is Telephony?
“Plain old” telephone set technology
It is much more than that
  Analog data services
  ISDN
  Older digital services (T1/E1)
  ADSL
Twisted pair copper wire is the primary medium of communication
Notes: Telephony is one of the four big segments in the telecommunications market, the other three being broadcast, datacom and wireless. Most people refer to telephony as the technology associated with the “plain old” telephone set that sits on a desk. But in reality, telephony is much more than just voice. It also includes analog data services (faxes and modems), ISDN, older digital services (T1, E1), newer digital services (ADSL) and a host of other less important services.
Twisted pair copper wire is the primary medium of communication. Single-strand copper wire is twisted into color-coded pairs. Pairs of wires are then bound together into distribution cables, which in turn form “binder groups” within larger feeder cables. These cables may terminate at the main distribution frame in a central switching office or at a subscriber loop carrier cabinet where they are multiplexed into higher-bandwidth signals.
Optical fiber is becoming popular in telephony recently. Almost all long distance trunks between central offices now use single mode optical cable operating at either 1300 nm or 1500 nm. Optical cable is capable of carrying up to tens of Gbps of data and is also immune to noise and other problems that plague wireless, coaxial cable and twisted pair. Were is not for the cost of replacing metallic networks with fiber, a much larger percentage of the world would be fiber today instead of copper.

## Slide 4: Telephony Technologies
Plain old telephone system (POTS)
  90% of telephone lines in the world
  Changes in the central office
T1/E1
  T1 : transmission rate 1.544 Mbps
  ((24*8)+1)*8000 = 1.544 Mbps
Notes: POTS is the still the most popular means of communication for people at home and work. Recent surveys have shown that POTS lines still make up over 90% of the telephone lines in the world. POTS has not changed much this century. It relies on analog devices to convert sound waves to electrical signals, then transmitting them over a public switched telephone network (PSTN). The biggest change has come in the central office switches. The progression has been from telephone operators with patch panels, to mechanical relays and now to digital switches. Digital switches have greatly increased network speed and reliability.
T1 has historical significance and is still used as the first level in a hierarchy that multiplexes ever increasing number of channels. T1 develops a 1.544 Mbps pulsed digital signal by multiplexing 24 voice channels. Each channel is sampled at 8000 samples/s. Each sample is then converted to 8 bits using companded pulse code modulation (PCM). The 24 channels are then time division multiplexed. Each frame which corresponds to one sampling period contains 192 (24 * 8) plus one bit for frame synchronization. Since frames occur at 8000 times/sec, the system transmits at 1.544 Mbps. T1 was developed as an ANSI standard and is use mainly in the US and Canada. The rest of the world uses E1 which transmits at 2.048 Mbps and has 30 channels.

## Slide 5: Telephony Technologies (cont.)
DSL (digital subscriber line)
  Voice and high-speed data sent simultaneously over copper lines
ADSL
  Splits the phone line into two frequency ranges
  0-4 KHz is reserved for voice
  More bandwidth for downloading data
  Much faster than analog modems
Notes: DSL is a technology that exploits unused frequencies on copper telephone lines to transmit traffic typically at multi-megabit speeds. DSL allows voice and high-speed data to be sent simultaneously over the same line. You can use your phone and stay connected to the Internet at the same time.
ADSL is an asymmetric variation of DSL that offers differing upload and download speeds. Download speeds range from 256 Kbps to 8 Mbps and upload speeds range from 16 Kbps to 640 Kbps. It is good for general Internet access and for applications where downstream speed is most important, such as video-on-demand. ADSL works by splitting the phone line into two frequency ranges. The frequencies below 4 KHz are reserved for voice, and the range above that is used for data. This makes it possible to use the line for phone calls and Internet access at the same time.
Analog modems send their signals through PSTN. On the other hand, ADSL modems carry their signals on top of voice signal. At the central office, the line gets split. Voice calls are sent to the PSTN and the data transmission goes to the Internet. This method moves data off the phone companies lines and instead uses connections optimized for carrying Internet traffic.

## Slide 6: Communication System
Channel
Protocol
stack
Protocol
stack
Analog
Digital
Modem
Transmitter
Receiver
Notes: The figure shows a simplified model of a communication system. The upper section represents a transmitter and the lower section represents a receiver. Input to the transmitter is data from a device such as a computer or a compander, which converts voice data from a cellular phone into digital data. This device then sends the data through a protocol stack. In this figure, the protocol stack represents all the Open Systems Interconnection (OSI) layers other than the physical layer and the data layer. A modem then modulates the digital data using different digital communication tools. We can categorize this process as part of the link layer in the protocol stack. A transmission protocol defines the type of source encoding, modulation and error control coding. The output of the modem is usually a modulated analog signal.
The transmit hardware transmits the analog signal over a channel. There are different types of channels such as coaxial cable, twisted pair copper wires, wireless or fiber optics. The receiver hardware receives the analog signals from the channel. Once again, the modem demodulates the incoming data and converts it back to the digital domain. The data is then consumed by the device on the receiver side.

## Slide 7: Telephony Testing
Media tests
  Test the channel that transmits the data
  Voltage, current, capacitance, loss
Parametric test
  Test analog signals
  Pulse mask, amplitude, frequency
Protocol test
  Test the protocol that defines a particular standard
  Bit error rate test (BERT)
Notes: You may perform different types of tests at different points along a communication system. You can broadly classify these tests into three categories, namely media, parametric, and protocol.
Media tests looks at the physical and electrical characteristics of the channel that transmits data. In case of telephony, the channel consists of the twisted pair copper wires.
Parametric tests looks at the characteristics of the signals themselves (irrespective of media). There are a number of tests that are performed on these signals before they are transmitted over a channel. The ITU/ANSI specifications describe a number of these tests such as pulse mask, amplitude, frequency, jitter and wander measurements.
Protocol tests are usually performed on the digital data. They test the protocol that defines a particular standard. They look at the logical flow of information (messages, packets, frames, cells, etc). Bit error rate testing (BERT) is one such common protocol test.

## Slide 8: Media Tests
Electrical parameters of the channel
  DC Volts, AC Volts, current
Specialized telephony tests
  Load coil detect
  Time domain reflectometer
  Longitudinal balance
Notes: Media tests address the electrical parameters of the twisted pair itself. Media tests include basic measurements such as DC and AC voltage, current, resistance and capacitance.
There are specialized telephony tests such as:
  Load Coil Detect – Load coils are connected to twisted pair to equalize the capacitance of the line. Reducing capacitance reduces loss, so load coils effectively extend the range of POTS signals. Load coils also reduce the bandwidth of POTS signals to 4000 Hz. You must remove them if you need to install DSL service
  Longitudinal Balance is a test to determine the balance of AC impedance on each side of the pair with respect to the cable shield (or ground). If the resistance or capacitance to ground on either conductor is different, this creates an imbalance. Poorly balanced twisted pair permits noise to enter (or radiate) from a circuit.
  TDR is a measurement technique for locating changes in impedance on transmission lines. TDR works by transmitting a pulse on a line, then looking for reflections of the pulse in the time domain. The distance to “events” can be calculated by measuring the time between the launch pulse and its reflection, then converting time to distance based on the velocity of propagation of the line. TDR can locate events on telephone lines such as shorts, opens, load coils, bridge taps, water in cable, and splices.

## Slide 9: Parametric Tests
Transmission and impairment measurement set (TIMS)
  Loss
  Noise
Production tests
  Mask test
  Amplitude and frequency
  Jitter
Notes: TIMS measures signal quality parameters such as loss and noise.
Mask Tests – Regulatory bodies such as ITU and ANSI define masks (envelopes) within which a signal must always lie. It is a common practice to test a predefined number of pulses to ensure that they fall within the mask. The number of hits is defined as a count of the number of pulses that fall outside the mask. Amplitude test measures the peak value of a signal. Sometimes, we also measure the DC component in the signal. Frequency tests measure the frequency of a signal. Jitter test measures the short-term variations of significant instants of a digital signal from their ideal positions in time (reference points). Jitter amplitude is usually measured in unit intervals (UI), which is defined as the nominal bit rate of the transmission of one binary digit. Suppose the nominal bit rate of transmission is 2000 Kbps. The nominal time for the transmission of a binary digit is 1/2000 K = 500 ns. If jitter is present on the signal with a phase deviation of 1 ms peak to peak, then the amplitude could be expressed in UI as 1000/500 = 2 UI.

## Slide 10: Mask Testing
Define a mask
  Using numbers
  Using formula
  Continuous or segmented masks
Perform limit testing
Demo
  Demonstrate use of limit specification and limit testing VIs in LabVIEW 6i
Notes: LabVIEW 6i provides VIs that allow users to specify a limit (mask), then perform limit testing. The limit can be specified in terms of numbers or formula. The limit can be either continuous or segmented. The user can specify the limit as part of the initialization process, then perform limit testing continuously on blocks of data. The output from the limit testing is a Boolean which indicates if the limit testing passed or failed. The VI also returns an array which contains the input signal, a failure array which contains the data points at which limit testing failed and the upper and lower limit.
In the next demo, we will see how easy it is to specify limits and perform limit testing using LabVIEW 6i.

## Slide 11: Measurements
Amplitude measurements
  Averaged DC and RMS measurement
Frequency measurements
  Extract single tone information
  Harmonic distortion analysis
Demo
  Demonstrate application of frequency and phase detection VIs
Notes: LabVIEW 6i has a number of VIs that implement high level measurements on top of the Advanced Analysis library.
The Averaged DC RMS Measurement VI takes a signal in, applies a window to the signal, and averages the DC and RMS values calculated from the windowed signal with the previous DC and RMS values according to the averaging type input.
The Extract Single Tone Information VI takes a signal in, finds the single tone with the highest amplitude (or searches a specified frequency range) and returns the single tone frequency, amplitude and phase.
You can specify a particular frequency to search for or the VI will return the frequency at the first peak it found in the spectrum. The VI internally applies an optimized window and then performs spectrum analysis.
The next demo shows how to use this VI to measure frequency and phase of an input signal.
In a latter demo, we use this VI also to measure the frequency of T1 signal. The trick is that an AMI signal has zero energy at DC and 1/T (fundamental frequency). The peak is found at 1/2T. The trick to get the right frequency is to take the absolute value of the T1 signal and then feed it to the frequency measurement VI.

## Slide 12: T1 Testing – LabVIEW & 5911
Demonstrations
Notes: The example uses a National Instruments arbitrary waveform generator (NI 5411) to generate a T1 alternate mark inversion signal. (In the real world, the T1 signal would come from a device under test.)
The T1 signal goes to a “device under test” (an RC circuit). The output of the RC circuit goes to the analog input of a National Instruments 100 MHz Digitizer (NI 5911).
The 5911 digitizes the signal, and LabVIEW measures:
Pulse Mask
Amplitude
Frequency
A “Pulse Mask” is set of values over which a measurement is within limit. It is displayed as a “mask” on an oscilloscope screen.
Measuring the level and frequency of T1 signals is non-trivial. We use the Extract Single Tone Information VI to measure these values.

## Slide 13: ADSL Testing – LabVIEW & 5911
Demonstrations
Notes: This is an example to test ADSL modems. An ADSL modem sends signals to the telephone company between 26 and 138 kHz, and receives signals from 138 kHz up to 1.2 MHz.
This example uses the NI 5411 to generate an ADSL upstream signal. (In the real world, the ADSL signal would come from a device under test.)
The ARB is connected to a simulated “device under test.” The output of the device under test is connected to the input of the 5911. The 5911 samples at 12.5 MHz (it is not in the flexible resolution mode) and acquires the incoming signal from 0 Hz to 6.25 MHz.
The LabVIEW code analyzes the incoming data and calculates:
PSD (Power Spectral Density) in the POTS band (0 to 4 kHz) and between the POTS and ADSL band (4 to 26 kHz). This would be unwanted interference generated by the modem under test (it should be very low.)
PSD in the upstream band (26 to 138 kHz). This is the primary signal generated by the modem. The levels must be within spec.
PSD in the downstream band and up to the 5th harmonic of the downstream band (138 kHz to 6.25 MHz).
Noise in the same bands.
The measured levels are compared to minimum and maximum limits defined by the ANSI T1.413 standard. Go/No-Go lights for each test are on the right.

## Slide 14: Summary
What is telephony?
Telephony technologies
Telephony tests
  Media tests
  Parametric tests
Demos
Questions?