## Slide 1: Understanding Digital I/O
June Zhu
Product Support Engineer
Thurs Aug 17
12:00-1:15 p.m., 3:30-4:45 p.m.
Red River (4B)

## Slide 2: Overview
Digital basics
  What are TTL, CMOS, and non-TTL signals
  TTL output specifications
Digital operation modes at a glance
Applications of operation modes
Time stamping, an
advanced application
Notes: This presentation starts from the digital basics and cover some of the common signal types such as TTL, CMOS and non-TTL signals
A more involved discussion will pertain to common digital applications and possible solutions.

## Slide 3: Digital Basics
TTL signals
TTL output specifications
CMOS signals
Non-TTL signals

## Slide 4: What Is TTL?
TTL stands for transistor-transistor logic
One of the popular logic families
The standard
  0-0.8V: TTL low
  Above 2V: TTL high
In order for the signal to be true TTL, the rise and fall time must be 50 nSec or less
Notes: Rise time – The time for the signal to go from logic low to high.
Fall time – The time for the signal to go from logic high to low.

## Slide 5: TTL Output Specifications
TTL output specification
0.8
0.4
2.4
2.0
TTL Input Spec.
TTL Output Spec.
Noise Margin
5
Notes: The amount of current a device allows to flow into or out of it in order to guarantee an output of TTL low or high is referred to as sinking or sourcing.
Note the difference between the TTL input specification and the TTL output specification. This is called the noise margin.
The PCI-DIO-32HS, PXI-6533, and DAQCARD-6533 allow you to sink or source 24 mA.
The output channels of a 6527 devices are solid-state relays containing an LED and two MOSFETs connected to form a bi-directional switch. Depending on how the load is connected to the terminal, an output can switch (either source or sink) currents to up to 120 mA. For details, see the 652x User Manual.

## Slide 6: CMOS Signals
Another popular logic family in current use
Typically 2/3 of the supply voltage (Vcc) is considered logic high, 1/3 of the Vcc is considered logic low
CMOS can be TTL compatible
Notes: CMOS input usually switches at about half of the Vcc level, though you can purchase CMOS that has Schmitt trigger (hysteresis) input.
Unlike TTL, voltage supply levels for CMOS have a wider range. For example, the HC and AC families of CMOS have a range of +2 to +6 V, and the 4000B and 74C families of CMOS have a range of +3 to +15 V.

## Slide 7: Non-TTL Signals
Non-TTL signals
  Voltages that are higher than 5V or lower than –0.5V input
  Not all devices can support this

## Slide 8: Summary of Digital Input Signals
5
10/3
2.0
5/3
0.8
0
Logic high
Logic low
Logic high
Logic low
TTL threshold
Vcc= 5V
Non-TTL threshold
User defined
CMOS threshold

## Slide 9: Isolated Digital I/O For Non-TTL
Can be used with
higher voltages
Optically isolated
inputs
Contains a light
emitting diode
(LED), a resistor
for current limiting
Notes: One example of the isolated digital input circuitry is the 6527 device. It contains a light-emitting diode (LED) and resistor current limiting.
The maximum input voltage for this circuitry is + 28 VDC.

## Slide 10: Digital Operation Modes
What do I mean by digital operations modes
  Functionalities that are offered by digital devices
Why are digital operation modes important?
  Different applications require different operation modes

## Slide 11: Digital Operation Modes at a Glance
My Application | Mode to Use
Static digital I/O | Unstrobed operation
Timing between each point transferred is important | Pattern I/O
Trigger is necessary | Pattern I/O
Transfer at fastest speed, timing between points doesn’t need to be consistent. | Handshaking
Generate internal request every time a change occurs on one or more input lines and device will then capture new pattern | Change detection
Run a user-specified routine when a particular event occurs | Message generation
Notes: This slide gives a brief overview of the functions available according to your applications.
Note: For handshaking, triggering is not applicable because the board asserts a signal each time it is ready for transfer
In the slides that follow, we will pay more attention to some of these functions and the applications that use them.

## Slide 12: Applications of Operation Modes
Detailed applications of the operation modes
Explanation of operation mode specifics

## Slide 13: Application
Control or monitor relays

## Slide 14: Operation Mode
Unstrobed operation
  Sometimes refer to as static or immediate
  Upon a software command, one or more digital lines immediately updates (output) or returns (input) the states
Notes: Upon a software command, digital line or port immediately updates the digital line or port state or returns the current digital value of an input line or port, depending on the digital line or port direction

## Slide 15: Application
Acquire an image from a scanner
  Note – image information can be represented by digital data
  The scanner sends a pulse when it is ready to transfer data
  It expects the measurement device to accept data and output a pulse to acknowledge receiving the data
  The scanner will send another pulse when it has more data to transfer
  Process repeats until the entire image data is transferred

## Slide 16: Operation Mode
Handshaking operation
  Digital device Input pattern after receiving a digital pulse on its REQ line
  The digital device acknowledges receiving data by outputting on the ACK line
  Give you the ability to synchronize digital data transfer between your digital device and instrument
PC
REQ
ACK
Scanner
REQ
ACK
Image Data
DIO device

## Slide 17: Handshaking Protocols
Depending on the timing of the handshaking signals, you have different protocols
Notes: The timing of the handshaking signals defines the handshaking protocol.
The 6533 family devices, which include the PCI-DIO-32HS, PXI-6533, DAQCARD-6533, offer five handshaking modes. The protocol you select determines the timing of the ACK signals that the 6533 devices send to the peripheral device and of the REQ signals expected from the peripheral device.
With the exception of one protocol (8255 emulation), all handshaking modes allow you to define the polarity of the handshaking signals, so you may define whether the signal is active high or active low
Details of the timing of each protocol is included as an appendix to this presentation. The next slide covers one of the most common handshaking protocols in detail.

## Slide 18: Burst Mode
Fastest of all the handshaking modes
Only handshaking protocol that uses three control signals
  REQ – indicates when the peripheral device is ready to transfer
  ACK – indicates when the digital device is ready to transfer
  PCLK – shares a clock signal between the digtial device and the peripheral device
Notes: Burst mode is the fastest handshaking mode. It is a synchronous, or clocked, protocol. It uses the PCLK signal and the two handshaking lines, REQ and ACK.
The data transmitter and receiver share a clock signal over the PCLK line. You may use the internal clock as the source for the PCLK or provide your own clock for its source

## Slide 19: Burst Mode Cont.
A typical cycle
Polarity of the REQ and ACK signals are programmable
Notes: In every clock cycle, the 6533 device asserts the ACK signal if it is ready to perform a transfer. If the peripheral device also asserts the REQ signal, a transfer occurs on the rising clock edge. Either the 6533 device or the peripheral device can insert wait states into the protocol by de-asserting the ACK or REQ signal, respectively.
Every clock cycle in which both the ACK and REQ signals are high transfers one data point.
You may programmatically select the polarity of the REQ and ACK signal.

## Slide 20: Burst Mode (cont.)
A word of caution
  “Missing data” when using burst mode
  Even though burst mode is a synchronous, or clocked protocol, does not guarantee that data will be transferred on every PCLK edge
  Remember:
    REQ and ACK need to be both asserted for a point to transfer
    That REQ and ACK can drop anytime the peripheral device or the digital device is no longer ready
Notes: Note that just because the burst mode is a synchronous, or clocked protocol, does not mean that it guarantees data transfers on every PCLK edge.
PCLK is a continuously running clock, but REQ and ACK both need to be asserted in order for a point to transfer. Remember that REQ and ACK can drop any time the peripheral device or the 6533 is no longer ready.

## Slide 21: Handshaking Demo
To demonstrate the burst mode functionality of the digital device

## Slide 22: Application
Pattern verification
  Upon receiving a trigger, the circuit sends out a digital pattern of x frequency
  Capture the digital data at that rate
Circuit
Digital device
Digital data
Clock signal
(external or internal)

## Slide 23: Solution
Pattern I/O
  With handshaking, there is no guaranteed time interval between each transfer
  With pattern I/O, you can generate and retrieve patterns at a constant rate
  Two clocking options
    Internal clock
    External clock
Notes: With handshaking, data is transferred whenever both sides are ready, which means that there is no guaranteed interval between each transfer. Pattern I/O allows you to generate and retrieve patterns at a constant rate, satisfying those applications that require fixed intervals between transfers.

## Slide 24: Application – Time Stamping
Integrate the change detection feature of the digital and the event counting feature of the timing devices
Monitors changing digital events and records both the digital data along with time information when those changes occur
Notes: This application uses the combined feature of the change detection of 6533 and buffered event counting of the 6602 counter/timing device
When you timestamp a signal you not only store its value, but also the time when that value was latched into the hardware. This way, you have an accurate representation of all the events that happened in the hardware and their relative times. These information could be used later to recreate the events or for post-acquisition analysis.

## Slide 25: Change Detection
Monitor for transition on one or more input lines
Capture the new input pattern on entire port when the change occurs
Increase CPU and bus efficiency for control applications by eliminating constant polling
Notes: In change detection, the 6533 generates an internal request only when the input data changes. This feature increases CPU and bus efficiency for control applications because you can monitor activity on input lines without continuously polling, and without transferring unnecessary data during periods of inactivity.
You may specify the pattern mask, which selects the significant bits for change detection. The 6533 only monitors those significant bits for changes. However, after detecting a change the 6533 captures the values of all bits. After a change occurs, the 6533 takes from 50 to 150 ns to clock in the new data. Therefore, the resolution of change detection is 150 ns. Repeatedly changing data is also subject to the usual pattern generation rate limits, discussed earlier.

## Slide 26: Time Stamping Example
Post acquisition analysis
  Correlating digital and time data to perform pulse width measurements
01000
00001
10100
01101
11100
Monitored data
0.2
0.5
0.7
0.8
1
Time (sec)
0.5
1
0.8
0.7
Bit 0
Pulse width

## Slide 27: Other Digital Features (cont.)
Change notification
  Supported by the 652x family
  How it works:
    change occurs
    the 652x generates an interrupt
    NI-DAQ driver notifies your software
    does not report which line changed or the state of the line
    maximum rate of change notification is limited by software response time
Notes: The same idea applies to change notification that is supported by the 652x family. It reduces the number of reads your software must perform to monitor inputs. Instead of continuously reading the inputs, your software reacts only to transitions.
Similar to the change detection presented on the previous page, you can monitor changes on selected input lines or on all lines.
Unlike the change detection, you can monitor for rising edge (0-to-1), falling edges (1-to-0), or both. When the input change occurs matching your criteria, the 6527 generates an interrupt. The NI-DAQ driver then notifies your software using a DAQ event, message, or LabVIEW occurrence. The maximum rate of change notification is therefore limited by software response time and varies from system to system. When the 6527 notifies you of the changes, it does not report which line changed or whether the line rose or fell. After a change, you read the input lines to determine the current line states.
Change notification is considerably slower than change detection due to its software dependency.

## Slide 28: Software Consideration
With LabVIEW™ 6i, you can display the digital data in the digital waveform graph
Notes: With digital waveform graph, a new waveform graph type featured in LabVIEW 6i, you can specify the number of ports and the array of digital values and plot it on the graph for visual display.

## Slide 29: Summary
Questions?
Related Presentation or Workshops
For more information