## Slide 1: Integrating Measurement Applications with Databases Martin Svestka Industrial Automation Product Support Engineer Thurs Aug 17 12:00-1:15 p.m., 3:30-4:45 p.m. Colorado (6A)
Notes: Welcome to the National Instruments Integrating Measurement Applications with Databases presentation.
Software requirements
LabVIEW™ 6i + SQL Toolkit 5.0
CVI 5.5 + SQL Toolkit 2.0.5
TestStand™ 1.0.2
Lookout™ 4.0.1
MS Access 97 or 2000

## Slide 2: Agenda
Introduction
Database architectures
National Instruments database support
Advanced topics
Historical databases
Notes: Are you acquiring a large amount of data that you need to permanently store for later use?
This seminar addresses users with no database knowledge as well as users with previous or advanced database experience. It starts with database basics and finishes with advanced topics such as stored procedures. It targets both test and measurement systems and industrial automation systems.
The seminar contains several demonstrations that help you understand the respective topics.

## Slide 3: Introduction
Test executive example
Permanent data storage
Database
Referencing a database
Open database connectivity (ODBC)
Notes: The introduction answers two basic questions
What is a database?
Why use a database?
We start with a typical application example that is used in this presentation to demonstrate some database features or techniques.

## Slide 4: Test Executive Example
Computer board as a unit under test (UUT)
  Power supply test
  CPU test
  Memory test
Notes: Let’s set up an example that we can use in all of the demonstrations.
Assume we have a test executive that runs a test procedure for each manufactured computer. The procedure comprises of three tests
Power supply test (if result is a voltage within 4.95 to 5.05 it is OK)
CPU test
Memory test
We can log data to a table where each column represents an attribute that we want to store, such as timestamp, unit under test (UUT) number, result of the board testing, operator who performed the test, title of the test, measurements, and result of each single test.
We can read from the table that board number 101 passed all of the tests, however, board number 102 has the wrong power supply.

## Slide 5: Permanent Data Storage
Acquisition
Analysis
File
Server
Notes: Assume we have a typical test and measurement application. We acquire data we want to use later. For this purpose, we need to find a way to store our data permanently. The easiest way is to stream data to a file. We can use either spreadsheet file or a binary file. In both cases, we design the format of the files.
For example, we decide to use a spreadsheet file where first column is a timestamp, the second column UUT number, and so on.
The reason we store data is to reuse it later. We want to report all measurements that meet specific criteria. This operation can become quite complex if we need to search a file for specific values, group them together, aggregate their value, and so on.
Sometimes we want to update some values or delete some measurements. To delete a line, you recreate the file. The task becomes much more difficult if the file format is binary.
Since our measurements are important, we might want to provide them to other company departments for further analysis. In such a case, we provide a detailed description of a the format, or ideally, a function to manipulate the data, such as a driver or a server.
This solution is generally referred as a database.

## Slide 6: Database  Database Server
File
Server
Server
DB1
DB2
DB3
Notes: It is important to understand the difference between database and database server. People tend to put everything related into a single basket referred as a database. However, a database is just the place where data are stored usually as a set of files. The other important part of the whole system is the database server, which executes all requested operations from another applications.
The server manages multiple independent databases at the same time. There is always a way to reference a particular database. The method is database dependent and we explore this later in the presentation.

## Slide 7: How Do I Reference a Database?
It is database server specific
  dBase enter directory with *.dbf files
  MS Access enter *.mdb file
  Oracle enter service name
We need a wrapper with standardized interface
ODBC
Notes: PR2H-<number>
Integrating Measurement Applications with Databases
<header>
<date/time>
Before any data manipulation, you have to connect to your database. Each database server provides its own way to do this. Different database designs determine the connection.
For example if you want to open a dBase database you have to point the dBase server to a directory where the database files are stored. This directory contains all files with *.dbf extension that makes the database. Each file corresponds to a table.
If you want to connect to a MS Access database, you have to point the Access server to the respective *.mdb file. This file contains all database tables.
With Oracle, you provide a service name that translates all necessary details for connecting to a database.
This makes application development more difficult and database dependent. What we need is a standardized independent way to reference a database. This issue is solved with ODBC technology.

## Slide 8: What is ODBC?
= Open database connectivity
ODBC driver has a standardized interface
Driver is just a DLL
Do you have to know which DLL to connect to a database?
ODBC Administrator
ODBC
Driver
Application
DB
Server
ODBC
Admin
Notes: PR2H-<number>
Integrating Measurement Applications with Databases
<header>
<date/time>
Open database connectivity (ODBC) is a standard developed by the SQL Access Group – including representatives of Microsoft, Tandem, Oracle, Informix, and Digital Equipment Corporations. ODBC provides a uniform mechanism for accessing data in a database.
An important feature is that it wraps up database specific interfaces and exposes standardized ODBC interfaces. Because each database is different, there must be a different wrapper for it. The wrapper is referenced as an ODBC driver and it is basically a DLL.
Do you have to know which DLL to use for a particular database? No, not at all.
All drivers are managed by ODBC Administrator. Whenever a new driver is installed it is registered with ODBC Administrator and becomes available to you.

## Slide 9: ODBC Administrator
Lists all data source names
  Use DSN=data_source_name
Notes: ODBC Administrator is available from the control panel. Important tabs in the Administrator are Data Source Name tabs – User DSN, System DSN and File DSN. Please refer to the ODBC online help for more detail. We use the system DSN for our demonstrations.
Generally, each DSN corresponds to a database. Whenever you need to reference a database, you use the respective DSN. There are a couple of pre-configured entries, but it is likely that you need to create your own.
Steps to create the DSN used in this demonstration –
1) Start ODBC Administrator (Start >> Settings >> Control Panel >> ODBC)
2) Click on the Add button in the System DSN tab
3) Select Microsoft Access Driver (*.mdb) – comes w/Microsoft products
4) Specify NIWeek 2000 as the Data Source Name
5) Create a new *.mdb file
In every National Instruments product that supports database connectivity, you can reference any Data Source Name (database) with the following string
DSN=data_source_name

## Slide 10: How do I Talk to a Database?
Structured Query Language (SQL)
Powerful, difficult to learn, differences exist
Data definition statements
CREATE TABLE, DROP TABLE
Data manipulation statements
INSERT, UPDATE, DELETE, SELECT
Notes: Once you connect to a database, you can manipulate data. You can use an SQL language to do this. Structured query language (SQL) is standardized database data manipulation.
Unfortunately, you have to learn SQL and there is a chance that statements working for a one database server will not work for a different server. Each server uses SQL standard as a core, but implements additional functions and its own data types and syntax.
Whenever possible, National Instruments tries to offer an option that allows you to perform database operation without SQL knowledge.

## Slide 11: SQL Basics
INSERT INTO Test
(Date, UUT, PassTest, Operator, Test, Meas, Pass)
VALUES (‘3/30 15:34‘, 101, TRUE, ‘John Power‘, 5.01, TRUE)
SELECT * FROM Test
SELECT TmStamp, UUT, Operator FROM Test
WHERE Pass = TRUE
Notes: You are likely to use the INSERT statement since majority of test and measurement applications acquires data that need to be stored in a database. You are also likely to use the SELECT statement to retrieve data from a table.
Refer to the database SQL reference manual for more information.
Notes
Avoid using keywords as column names (date, max, user and so on)
Check for conflicts between table and column names (test)
Be careful about column order in Select * statement
Not all servers support Boolean
Put strings and date/time constants in single quotes

## Slide 12: LabVIEW
LV 5.x SQL Toolkit 5.x
  ODBC
(LV 6.x Database Toolkit 6.x)
  ODBC, ADO
  No SQL knowledge required
Always part of enterprise connectivity toolset
Demonstration
ni.com/labview/addons.htm
Notes: You need to install SQL toolkit for LabVIEW to access a database. The latest SQL toolkit version is 5.0 and this toolkit uses ODBC interface.
ADO is explained later in this course in advanced chapter. Now, we can think of it as another option to connect to a database as opposed to ODBC drivers.
Toolkits are not sold separately, but as a part of an enterprise connectivity toolset that includes SQL, SPC, and Internet toolkits.
The demonstration example shows how to create the test table from our computer test executive example. We use the database we created in the previous demonstration. It also shows how to insert a row into a table.

## Slide 13: LabVIEW SQL Toolkit 5.x
Database browser (Project menu)
SQL toolkit help (Help menu)
  Application examples
  Quick SQL reference
Notes: Database browser installs along with the SQL toolkit version 5.0 and is available from the Project menu. With database browser, you browse database tables, build queries and so on.
For more information on SQL toolkit, refer to SQL toolkit on-line help. Besides toolkit VIs description, you find useful examples and a Quick SQL reference guide.

## Slide 14: ADO – Active Data Object
ODBC
admin
ODBC
driver
Application
DB
ADO
(OLE DB)
provider
Server
Microsoft
DataLink
DSN=xxx
File name=yyy.UDL
Notes: In addition to ODBC data sources, you can also access data through any provider that complies with the Microsoft Active Data Object (ADO) standard.
As opposed to ODBC driver, you need to have ADO Provider.
As opposed to a data source name (DSN), you need to create a DataLink entry, which is basically a file.
Any ODBC DSN is referenced with “DSN=data_source_name”, any DataLink file is referenced by “File Name=filename.UDL”
The application is not trying to parse the string to find out which technology to use to connect to a database. An ADO interface is always used for connection. However, if you specify the DSN instead of the file name, the ADO talks to the database through ODBC.

## Slide 15: CVI
CVI 5.x - SQL Toolkit 2.0.5
  ADO (ODBC)
  No SQL Knowledge required
Load cvi_db.fp library
Demonstration
ni.com/mstudio/addon.htm
Notes: Install CVI SQL toolkit to access a database from CVI. The latest SQL toolkit version is 2.0.5 and this toolkit uses ADO interface.
SQL toolkit is an *.fp library that you load in the project before use.
You can use two methods to access database data – automatic SQL that does not require the SQL knowledge, or explicit SQL that allows you to execute SQL statements.

## Slide 16: Function Sequences
Automatic SQL
Explicit SQL
Notes: Use following rules to determine the best method to use
1) no SQL knowledge – automatic SQL
2) SQL knowledge – explicit SQL
non-SELECT statements - DBImmediateSQL() function
SELECT statement - DBActivateSQL(), DBBindColXXXX(),…

## Slide 17: TestStand
No additional toolkit required
  ADO (ODBC)
  No SQL knowledge required
Run create scripts to create tables
Use database viewer to select data
Demonstration
Notes: TestStand is a ready-to-run test executive that organizes, controls, and executes your automated prototype, validation, or production test systems. TestStand is completely customizable, so you can modify and enhance the program to match your specific needs.
While TestStand is running, it logs data directly to a database. You can use potentially any database server, but MS Access, Oracle server and SQL server have better support. The fixed data table format always comprises two tables that have predefined columns. To create those tables, you can run scripts that are present in the <TestStand>\Components\NI\Models\TestStandModel directory.
You do not need any other toolkit to log data to a database. It is based on the Microsoft ADO technology, so you can use both ADO and ODBC data sources.

## Slide 18: Lookout
No additional toolkit required
  ODBC
  SQL knowledge required
SQLExec, DataTable objects
Demonstration
Notes: Lookout is an object-based automation software. To develop an application, no matter how complicated, all you need to do is drag and drop objects and connect them. Lookout comes with two build-in objects, so no additional toolkit is required.
SqlExec and DataTable are objects Lookout uses to communicate with the ODBC driver. ODBC allows Lookout to connect to any database that supports ODBC. These objects connect to ODBC using the standard ODBC calls and query the database using SQL statements. The data, if any, is returned in the object data members.
Both objects provide similar SQL functions, they differ with data members. Generally, DataTable is more suitable from SELECT statements.

## Slide 19: Advanced Topics
Better database design
Security, database transactions, PL/SQL
Historical databases

## Slide 20: Database Design
Notes: Developers tend to put all of their data to a single table. However, a well designed database usually comes from multiple interconnected tables.
In our computer test example, we put all data into a single table. A better design is to split the table to two part to avoid duplicated value for the TmStamp, UUT, Operator, and Pass. The first table represents units under test (UUT), the second one tests. Each UUT passes three tests, so each row in the unit table owns three rows in the test table. The UUT column in that table is a pointer to the first one. This relationship is called master-detail, unit table as a master, test table as a detail.
You can still use SELECT statement to retrieve data from both tables at the same time. While the original single-table statement to select all test that passed was:
SELECT TmStamp, UUT, Operator FROM Test
WHERE Pass = TRUE
then the two-tables design requires the following select statement
SELECT Unit.TmStamp, Unit.UUT, Unit.Operator
FROM Unit, Test
WHERE Test.Pass = TRUE
AND Unit.UUT = Test.UUT
Unit
Test

## Slide 21: Security, Transactions, PL/SQL
Security (like NT)
Transactions (electronic money transfer)
PL/SQL – procedural extension of SQL
Example
Account B
Account A
$1000-500=500
$1000+500=1500
Notes: The majority of today’s computers are permanently logged on to the Internet. Enterprise computers are usually protected by a firewall, so nobody can access them directly. However, there are still ways to access a company intranet. One of the popular ways to launch a routine remotely is to use Trojan embedded in an e-mail message.
So far, we connected to our databases with full privileges. Well designed databases have access rights based on user account. We can compare this to a Windows NT design. When connecting to such a database, you have to specify a user ID and a password. You can use this feature from National Instruments products.
An important feature of advanced databases is database transaction. A transaction is a user-defined execution block that atomic – can be either executed completely or not executed at all. For example, when transferring $500 from a bank account A to an account B, money is first debited from account A and then credited to account B. If the operation failed in the middle, it must be rolled back otherwise $500 would be lost.
PL/SQL is a procedural extension of the SQL, introducing stored functions, procedures and packages. You can find LOOP, IF-THEN-ELSE, EXCEPTION, etc. statements in this extensions. You can use this feature from National Instruments products.
Refer to “Using Database Stored Procedures, Transactions, and Exceptions for Oracle 8.0.4.” on example program database (ni.com/support)

## Slide 22: Citadel – Historical Database
Only logs changes
Log dead band
Temperature
Time
Dead band
Notes: When monitoring or acquiring a signal, we usually store every sample. This can become a waste of database space if the signal does not change fast enough.
Particularly in industrial automation, the process variables such as temperature, level, flow, and so on, change slowly. Sometimes they appear to be constant. For example, if there are 100 signals we would like to store, samples every second each stored as a double (8B) require 70MB every day
60*60*24 * 100 * 8B = 69,120,000B
Citadel historical database logs data only when the value of a point changes, not at a timed interval. The logged data accurately reflects the actual behavior of the point logged because the same value of a point is not recorded repeatedly. With Citadel, disk use is exactly proportional to the amount of information recorded.
Because Citadel uses universal coordinated time (UCT) to time stamp the data, you do not need to compensate for data logged in different time zones.
You can exercise log dead band to avoid logging changes caused by a noise or small drifts. You think about your signal in terms of resolution instead of sampling rate. This technology makes sure that you do not miss any glitches while saving your disk space.
This database is only available for industrial automation products.

## Slide 23: Summary
National Instruments software development environments supports databases
Often, no SQL knowledge is necessary, but can be exercised
Notes: National Instruments products support permanent data storage in databases. Support is realized either by add-on toolkits, or it is directly integrated in the development environments.
All user levels are supported. Developers with no SQL knowledge can build applications that communicate with databases. On the other hand, SQL toolkits allow users to leverage off of the power of SQL and even PL/SQL.