## Slide 1: Measurement and Automation with Macintosh
Jeremy Wilden
Design Engineer
Fri Aug 18
12:00-1:15 p.m.
Red River (4B)

## Slide 2: New Products Supported in 2000
17 new plug-in boards in NI-DAQ 6.6
  With 31 boards in NI-DAQ 6.1
  Total of 48 boards in NI-DAQ 6.6
Overview of new products with demos
Remote and wireless measurement and automation
LabVIEW™ 6i and more!

## Slide 3: Overview of New Products

## Slide 4: New Multifunction I/O
Low cost 12-bit 6023E/6024E
  8/16 AI, 2 AO (6024 only)
  Up to 200 kS/s analog Input
High-resolution 16-bit 6052E
  8/16 AI, 2 AO
  Up to 333 kS/s analog Input
  Also in PXI via MXI™-3

## Slide 5: New Multifunction I/O
Low cost 16-bit 6034E/6035E
  8/16 AI, 2 AO (6035E only, 12-bit)
  Up to 200 kS/s analog input
Many E Series still supported

## Slide 6: New Timing I/O
Low-Cost TIO, 6601
  Four counters, 20 MHz (60 w/prescaling)
  Up to 32 Digital I/O
  Digital debouncing filters
High-Speed TIO, 6602
  Eight counters, 80 MHz (125 w/prescaling)
  Same DIO and filtering as 6601
  Also in PXI via MXI-3

## Slide 7: New Low Cost Digital I/O
Low cost DIO, 6503
  24 digital I/O
  Handshaking
  Unidirectional/bidirectional
  User defined power-up

## Slide 8: New Analog Output
Static AO, 6703
  16-bit voltage, 16 outputs, ±10 V
  8 digital I/O
Static AO, 6704
  16-bit voltage, 16 output, ±10 V
  16-bit current, 16 output, 0-20 mA
  8 digital I/O

## Slide 9: New Analog Output
Waveform generation
  12-bit
  Up to 1 MS/s
  Four channel, 6711
  Eight channel, 6713
  Eight digital I/O
  Two counters (same as E Series)
  Also in PXI via MXI-3

## Slide 10: DSA Instruments
Dynamic Signal Analyzers
PCI-4451
  Two analog inputs
  Two analog outputs (51.2 kS/s)
  16-bit, 204.8 kS/s
PCI-4452
  Four analog inputs
  16-bit, 204.8 kS/s

## Slide 11: DSA Features
High dynamic range (93 dB)
±10 mV to ±42.4 V range
AC/DC coupling
Differential inputs
DC to 95 kHz bandwidth
Fine-grained sampling rate control

## Slide 12: Remote and Wireless Measurement and Automation

## Slide 13: New PXI Modules with MXI-3
PXI-6052E
  16-bit AI/AO
PXI-6602
  Eight high-speed counters/timers
PXI-6704
  16 static analog outputs V & I
PXI-6711/6713
  4/8 waveform analog outputs

## Slide 14: MXI-3/PXI Benefits
Rugged, remote, isolated (fiber)
PXI backplane timing bus
200 m with optical fiber
10 m with copper
Software-transparent
Up to 200 meters!

## Slide 15: Wireless With Airport
Using VI server
  Most flexible
Using TCP/UDP
  Just data transfer
Using DataSocket™
Using LabVIEW™ Web server
  Most universal

## Slide 16: LabVIEW 6i

## Slide 17: New Features of LabVIEW 6i
LabVIEW 6i demo

## Slide 18: Other Surprise Topics