## Slide 1: National Instruments Solutions for Medical Device Manufacturing Hall T. Martin Market Development Director Gregory Swanson / Lee Globus MNovation, Inc. (mnovation.com) Fri Aug 18 12:00-1:15 p.m. San Jacinto (5B)
ni.com
Notes: Obtaining FDA certification for your medical devices and equipment tests is a challenging process. The solution encompasses processes, tools, and knowledge of system integration. This presentation describes the issues that face the manager seeking to certify the test process for a medical device and how virtual instrumentation tools address these needs.
Virtual instrumentation tools can help with certification processes. These tools include software validation, software release, and software build utilities. Other virtual instrumentation tools include configuration management and source code control. You need robust and modular solutions. This modularity promotes the use of templates, which leads to reuse of code modules. Remote control, distributed execution, and Internet access are also important.

## Slide 2: Market Size and Diversity
$70 billion spent in U.S. per year for medical device manufacturing
1,200 manufacturers in the U.S
Examples
  Neurology products – $3 billion
  Diagnostic imaging – $4 billion
  Anesthesia equipment – $500 million
  Patient-monitoring equipment – $1.6 billion
  Cardio-vascular – $6 billion
Notes: The market for medical device manufacturing continues to grow at a rapid pace. In the U.S. alone, $70 billion will be spent this year on medical device products. There are more than 1,200 manufacturers in the U.S. These devices range from neurology to diagnostic-imaging, to anesthesia equipment and patient-monitoring.

## Slide 3: Product Quality is the Driving Factor
Meeting the specification is the goal
Electronic and software specifications are rigorously set
Test plans are developed followed by code reviews
Version and configuration control are critical
Notes: To the medical device manufacturer, the quality of the product is of utmost importance. Meeting the set specification is paramount. The process for production and test is what drives this level of quality. Steps taken to ensure quality in the test process must be documented and demonstrated. Typically, a test for a medical device starts with electronic specifications, followed by requirement specifications. The results then go through a methodology review. Accuracy analysis and software hazard analysis takes place, then test plans are developed, followed by code development and code reviews. Throughout the code development, rigorous version controls are applied. It is a complex process.

## Slide 4: Examples
FDA # 21 CFR Part 820
  Quality system requirements
  Design controls
  Documents
  Identification
  Traceability
  Production processes
Notes: For medical device manufacturing, FDA #21 CFR Part 820 describes the requirements for validation and verification of medical devices. The document describes the overall process, procedures, and documentation requirements in detail. For details of the specification, go to the following Web site
http://www.fda.gov/cdrh/devadvice/part820.html#contents
The subparts of the FDA 820 specification include
  Subpart A - General provisions
  Subpart B - Quality system requirements
  Subpart C - Design controls
  Subpart D - Document controls
  Subpart E - Purchasing controls
  Subpart F - Identification and traceability
  Subpart G - Production and process controls
  Subpart H - Acceptance activities
  Subpart I - Nonconforming products
  Subpart J - Corrective and preventive action
  Subpart K - Labeling and packaging control
  Subpart L - Handling, storage, distribution, and installation
  Subpart M - Records
  Subpart O - Statistical technique mil std 2167

## Slide 5: Validation Programs
ISO-9000 varies widely
FDA – audits more rigorously
  Human accountability – tracking who approves what
  Traceability of materials – could lead to recalls
Notes: There are many quality assurance programs available. ISO-9001 is one example. In general, these programs vary widely in their scope and rigor.
The FDA validation process is much more rigorous than ISO-9001 and differs from other quality programs in two ways. First, key steps require individual accountability. Second, the user’s materials are traceable. If a material is determined defective, the products using that material may be recalled at great expense to the manufacturer.

## Slide 6: Device Types
Minor – no patient risk (thermometer)
Moderate – potential risk of minor harm (dialysis machine)
Major – support life systems (heart/lung machine)
Notes: The amount of validation and verification also depends on the type of device under test. There are three main categories – minor, moderate, and major. Minor devices incur no patient risk. Thermometers are an example of this category. Moderate devices pose a potential risk of minor harm. A dialysis machine is an example. A major device is one that provides life support. A heart/lung support machine is an example. The validation and verification requirements from minor to major become more stringent.

## Slide 7: Validation and Verification Elements
Process is key
Tools are important
Notes: The two elements to validation and verification in the FDA standard are processes and tools. The process of designing and building a test system for a medical device requires a rigorous procedure throughout the development of the product and the test set, and even carries through into production.
Key tools provide validation and verification of the test code and results. We will look at the elements of the process and the tools needed.

## Slide 8: Typical Process – Simplified
Typical test process development includes the following steps
  Concept – form overall test strategy
  Requirements – ascertain detailed requirements
  Coding – develop test programs
  Verification – verify coding meets the specification
  Validation – verify coding meets intended use
  Installation – install test code
  Training – train operators
  Maintenance – provide ongoing maintenance
Notes: This is a typical validation process. It follows a standard test development process, with the addition of verification and validation. Verification establishes that the test code meets the specification. Validation verifies that test code meets the intended use.

## Slide 9: Process Overview
<-----Configuration Management-------->
Test planning
Req. review
Design/implement
Review
Checkout
Review/approve
Release/install
Maintenance
Test strategy
Test
requirements spec
Test
req.
Cal.
req.
Checkout plan
Checkout report
Project
approval
Notes: This slide provides a graphical overview of the test development process including validation and verification.

## Slide 10: Configuration Management
Revision control
Version control
Metrics
Project build
Issue/change management tracking
Document control
Code/project auditing
Verifiable loading at run-time
Notes: The key requirement for test software in a validation environment is configuration management. The key elements include version control, which shows snapshot status of development files. Revision control shows development files in progress. Metrics shows statistics of software modules. Project build performs build up of the project with the software modules. Issue/change management tracks open issues and software request changes or CARS. Document control tracks changes that affect documents. Code/project auditing gives development snapshot across various hardware, operating system, and network platforms.

## Slide 11: Project Management
What is it?
  Tracks software modules for a specific test project
  Tracks test cases by software unit
  Manages loading and execution of software modules
  Provides metrics on software unit by size, memory usage, and other parameters
Notes: In addition to configuration management, there is also project management. This tracks software modules for a particular test project. A good project management tool provides test cases by individual units. Loading and executing the software modules may be important to control. Finally, metrics on the software units such as size, memory usage, and other properties may be useful to know.
An example of this type of package is the OverVIEW/UTool/Metrics toolset from MNovation, which you can be find at the following Web site
mnovation.com/products/products.htm

## Slide 12: Requirements for Configuration Management Tools
Multi-user
Ease of use
Source code control/issue tracking
Web-enabled
Notes: A good configuration management tool handles multi-user environments. Since multiple users access the data, the configuration management tool must track who has “checked out” the software, the modifications made, and then “check in” the software module before another user can take it.
Ease of use is an issue in working with any software tool. Most packages need to control not only the source code, but also the “open issues” associated with the code changes. Finally, the move to Web-based applications drives many vendors to provide “Web-enabled” tools.

## Slide 13: Configuration Management Packages
PVCS by Merant
Microsoft Visual Source Safe
Source Integrity by MKS
Clear Case by Rational
Notes: This slide lists some configuration management tools available today. The goal of this presentation is to inform – not to persuade users to use one package or another. To find out more about these packages go to the following Web sites.
1. PVCS – Merant
merant.com/pvcs/
Provides many of the basic features of a standard configuration management tool.
2. Microsoft – Visual Source Safe
http://msdn.microsoft.com/ssafe/?RLD=195
In addition to the standard configuration management tools, the program sets access control for various users at different levels, controls changes with check out, merge, and diff tools, and controls promotion status (beta, alpha, released).
3. MKS – Morten Kern Systems
mks.com
Offers a package focused on UNIX/Windows interfacing capability.
4. Rational – Clear Case – high-end system
rational.com/products/clearcase/index.jtmpl
This is a high-end package that gathers requirements and estimates tasks. Has a module for calculating resource needed. Provides a “release management” function. Can perform validation on unit, subsystem, and system level.

## Slide 14: Other Factors Affecting Validation
Test strategy
Team composition
Notes: There are other factors that affect validation. Some device manufacturers want to move through FDA certification quickly to achieve a “first-to-market” strategy. These device manufacturers perform more extensive and exhaustive testing to avoid delays in the FDA submission process.
Another factor is the make-up of the test team. If the team includes external personnel such as consultants or outside partners, then their work is treated differently under validation rules.

## Slide 15: Software Issues for Medical Device Testing
Performance – reliability, meeting specification, quality
Development tools – speed of development, debugging features
Integration
Cost – not a factor
Notes: Medical device testers feel that the over riding issues with software for test applications are reliability and meeting the specification. Quality is important. Robust development tools, such as debugging features and code control are also important. Integration of tools is useful and cost is typically not a major factor.

## Slide 16: Validation Adds to Test Development Time
Validation adds 2X to 10X onto standard process
4X over non-validation is typical
Notes: For those who come from a non-validation test environment, the development time and resources increase anywhere from 2X to 10X when performing validation. The typical increase is around 4X but this depends on the type of device, the test strategy, and the performance of the tools.

## Slide 17: Other Issues in Validation
Other practices to follow
  Data retention
  Control
  Discipline
Notes: Other issues in validation include following good practices on retaining data, providing controls for test development, and establishing discipline in the team.

## Slide 18: Rigorous Testing Environment
FDA Factors
  Verification and validation (V&V) requirements increase time needed for software development and test
Time-to-market
  Competitive market forces decrease allowable development time
Notes: The test development landscape in the medical device industry is challenging. Like most industries, there are competitive market forces that continue to shrink the overall product development cycles. This causes reduced time for test development.
Unlike some industries, medical device manufacturers have additional requirements related to validation and verification. These requirements dramatically increase the time for development test systems.
Productivity tools are essential in reducing the time needed for development and testing of software.

## Slide 19: FDA Factors – Auditability
Test development process
  Consistent
  Training
Documentation
  Defined checkpoints in process
  Proof of process
Notes: Some of the primary FDA factors include are auditability, predictability, traceability, and validation.
The primary components of audit concern in the product testing environment relate to the test development process and the documentation supporting the process.

## Slide 20: FDA Factors - Predictability / Traceability
Requirements
Design
Implementation
Unit
TEST
Unit
TEST
Unit
TEST
Unit
TEST
Unit
TEST
Unit
TEST
Unit
TEST
Unit
TEST
Unit
TEST
Unit
TEST
Unit
TEST
Unit
TEST
Unit
TEST
Notes: One common example of traceability deals with how requirements for a given test application are tracked from design through implementation. Throughout the entire cycle, you must trace specific items from the end product, which is implemented back through to the original requirements.
This is most obviously accomplished with the proper supporting documentation, but should also be part of the software development process.
One aspect of predictability relates to having a firm grasp of how the software behaves. A good example of achieving this is with clearly defined software modules (VIs) and applying unit tests (UTs) to each module.
These unit tests serve as proof of the predicted behavior by exercising the VIs against known and expected test results. They also serve as a traceable link back to the requirements as you can create the tests to prove that the functions of the modules meets all requirements. We discuss this in regard to validation next.

## Slide 21: FDA Factors – Validation
Validate functions against requirements and design
Verify proper code use
  Development
  Run-time
Notes: Validation is another component of FDA factors. You can characterize validation in two ways. The first is the validation that the software code functionally meets the intended design and necessary requirements.
This is typically a time consuming process as the various test cases used (plan) must be thought of, implemented, reviewed, and agreed on. Once this validation plan is approved, there needs to be a method to exercise the plan and have traceable proof that the code exercises as expected and meets the intended design and requirements.
Another important component of validation is verifying that the proper code is implemented. Both in the development process and, most importantly, in the release product, it is essential to verify that the code implemented is actually the intended set.

## Slide 22: Time-to-Market
Automation of process items
  Documentation
  Configuration
Multi-developer environment
Configuration management
Re-usability
Project status visibility
Third party development
Notes: Not unlike other software development areas, there are many ways to address some of the time-to-market pressures. Any sort of automation is helpful from an efficiency standpoint. Because of the FDA-related requirements, it is important to discuss tools that help automate the processes related to documentation and software configuration.
Team development helps speed up project development. The necessity for utilities such as configuration management are essential to keeping control of the project in a multi-developer environment.
A popular concept with any type of software development is re-usability. There are obvious benefits to re-using previously developed code. In a rigorous testing environment where validation is essential, it is also imperative to have a method of validating the re-usable code against different application requirements.
Another dimension of improving overall development time is having an understanding of where the project stands. Therefore, it is essential to have utilities and information that provide the complete project status to judge workloads and time to completion.

## Slide 23: How is this Achieved?
V&V Activities
Goal of addressing FDA and time-to-market factors is achieved
through an efficient process and use of appropriate tools
Design
Code
Non-regulated development environment
Project Time
Integration
Design
Integration
Code
Regulated development environment
Project Time
Notes: Juggling the opposing forces of time-to-market and the FDA factors mentioned is challenging.
The goal of addressing FDA and time-to-market factors is achieved through an efficient process and use of appropriate tools.
As we know, LabVIEW™ is an effective tool for software development. It reduces the coding time compared to other languages in numerous applications.
The tools we review from MNovation assist with the validation factors that tend to add time to a project.

## Slide 24: Tools Make the Process
Project time
Design
Develop
Functional
testing
Project
implementation
Project time
Design
Develop
Unit
testing
Project
implementation
Notes: Another dimension of these tools relates to how they play into or help shape the given process. In other words, the process and the tools are not necessarily mutually exclusive.
An example of this is when one client used the unit testing utility (UTool) from MNovation to re-architect the process to shrink the total application development time.
The previous process involved waiting until all code was completely designed and developed before beginning the functional testing.
With the new process, utilizing unit testing instead of functional testing, the testing begins at the time each individual VI is completed. This pushes the validation stage into the development phase and dramatically reduces the overall development cycle time.

## Slide 25: Unit Testing Advantages
Offers finer granularity which improves quality of entire system
Reduces overall development time
  Re-use validated code
  Testing to begins during implementation
Makes regression analysis possible
  Reduces irrelevant testing on upgrades
  Only necessary components are re-tested
Notes: Unit testing of software has many advantages related to improving the quality and reducing development time of the system. We can apply the same analogies of a modular software design to a modular testing strategy.
The ability to have test cases for each module in the system dramatically improves the test coverage of the system resulting in a higher-quality product. Once tested, users can share the module and re-use it with other development projects, which helps reduce the development and testing cycles.
The modular unit testing begins as soon as the code modules are completed, which dramatically reduces the overall development time as the implementation and formal testing phases overlap.
Another advantage is that future upgrades to the system have far less testing requirements as only the necessary modules (those that have changed or those that are new) need to be re-tested.
LabVIEW lends itself to a modular software design and the UTool from MNovation is a valuable unit testing environment for LabVIEW-based systems.

## Slide 26: Complexity and Third Party Acceptance
Test
Standards
Metrics
Notes: Another component of the tools we examine relates to how you can use them to manage the complexity of a given application and the issues that relate to using outside resources for development.
The UTool (unit testing) and Metrics tools can serve as a means to quickly judge the quality of code as it is developed. This can be essential when dealing with outside vendors. Since it is unlikely that the vendors have the same development process, the tools become the means by which you analyze and control quality.
Another aspect to the Metrics is that it can quickly help analyze and optimize a large software project by giving information about some of the key characteristics of each VI in the project.

## Slide 27: Features of Toolset
At-a-Glance project management
  Documentation
  Test/regression
  Standards compliance
  Quality
  Issue tracking
Notes: Some of the key features of the toolset we review include the following. A critical aspect of this toolset is the ability to give at-a-glance project status information for some of the key aspects of the application.
Documentation
Unit testing and regression
Compliance with standards
Quality (Metrics)
Issue tracking

## Slide 28: Features of Toolset (continued)
Automation
  Code analysis
  Code link management
  Multi-developer environment
  Test case capture
  VI setup properties
Notes: Automation makes the process more efficient. Some aspects of the toolset that provide automation involve the following.
Code analysis
Code link management (verification)
Multi-developer support
Capturing test cases
VI setup properties

## Slide 29: Toolset Architecture
OverVIEWTM
Control links
Project status
Edit documentation
Issue tracking
VI setup
MetricsTM
Code Analysis
UToolTM
Unit Testing
Regression analysis
Cfg. mgmt. interface
Notes: The toolset is structured as four products
1. OverVIEW
2. Metrics
3. UTool
4. LaunchPad
OverVIEW is the project management framework that coordinates most of the project status and automation aspects. When linked with Metrics, UTool, and other future add-ons, it becomes a comprehensive vehicle in which to control, optimize, and automate project development.
Following the development of a given project, LaunchPad is the engine that verifies the code utilized in production matches what the OverVIEW project file configured.

## Slide 30: Development Environment
Configuration
management
OverVIEW
project file
Check in/out
Structure/links
Notes: A typical project involves numerous code modules (VIs). These are typically managed by a configuration management tool such as Visual Source Safe, MKS, ClearCase, and so on.
The CM tool manages the version of each software module, which is part of the verification process. However, this does not complete the picture. Without a tool to capture how the project links together, the verification process is suspect.
The project file managed by OverVIEW ties the complete application together as it understands and manages the links of each VI within the project.

## Slide 31: Manufacturing Environment
LaunchPad
engine
OverVIEW
project file
Application
Notes: Once the development is complete, use the resulting OverVIEW project file in conjunction with LaunchPad to properly verify the code during every use on the production test platform.

## Slide 32: Demo of Toolset
OverVIEW
Metrics
UTool
LaunchPad
mnovation.com
Notes: The toolset from MNovation, Inc. reviewed here involves the following items.
OverVIEW Project configuration and status
Metrics Complexity management and code analysis
UTool Unit testing and validation
LaunchPad Run-time load engine for verification of code used in conjunction with OverVIEW

## Slide 33: Conclusion
Solution = test tools with configuration management features
Rigorous controls and procedures are important
Expanded resources include validation/verification at 4X
Notes: In choosing test tools for validation testing, performance for reliable test development is the first criteria. Configuration management is also an important requirement.
Strict test coding and documentation procedures are required for the test development process.
Finally, you must allocate additional time and resources. A 4X increase is a starting point for calculating the time required.