## Slide 1: Avionics, Instruments and Engine Test
Doug Shepard
Business Development Manager
Fri Aug18
3:30-4:45 p.m.
San Jacinto (5B)

## Slide 2: Applications
Development
Design verification
Manufacturing
Maintenance

## Slide 3: T&M System Anatomy
Controller
Stimulus and measurement instruments
Programmable power supply
  Test applications
Fixturing
  Receiver or panel
    Generic signal interface
  Adapter
    Signal connections
    UUT-specific test hardware

## Slide 4: Common Signal Types
Measure or simulate
Power
  14/28 V DC
  115 V AC, 400 Hz
  0 – 100 mA DC current
Voltage – mV to 28 V
Pressure
Strain/load
Displacement
Angle
Acceleration
Discretes
  14/28 V DC
Synchro
RF
  NAV radio
  Transponder
  Radar
Video
  RGB
  NTSC

## Slide 5: Common Interfaces
Switches
  Many configurations (SPST, 6PDT, etc.)
Data busses
  ARINC-429
  MIL-STD-1553
  Commercial standard data bus (CSDB)
    RS-232
    RS-422/485

## Slide 6: Traditional Approaches
Automated systems
  UNIX
    ATLAS test executive
  GPIB and VME/VXI instruments
Bench test fixtures
  Specific purpose
  Manual procedures

## Slide 7: PC-Based Approach
Compared to traditional automated systems, provides
  Lower initial cost
  Smaller footprint
  Increased flexibility
  Improved upgrade path
  Improved performance

## Slide 8: PC-based Technologies
CompactPCI™/PXI
  Instruments
  Data acquisition
SCXI Signal Conditioning
  Amplifier, filter, sensor excitation, bridge completion, etc.
Software
  OS – Windows NT/2000
  Programming tools – C/C++, LabVIEW™, VB
  TestStand™ test executive

## Slide 9: PXI Starts with Compact PCI
PCI electrical specification
Eurocard mechanical specifications
Latest connector technologies
PCI
Eurocard packaging
IEC connectors
CompactPCI
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>
A brief overview of PXI.

## Slide 10: PXI Adds Instrumentation Features
Electrical
Trigger bus
Star trigger
Local bus
System reference clock
Compatible with 3U CompactPCI devices
Mechanical
Defined slot locations
Cooling
Environmental testing
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>
PXI adds instrumentation hardware features to CompactPCI, similar to the way that VXI supplements the VMEbus standard.
PXI includes the most-used features of VXI without adding other costly features unneeded for most test and measurement applications.

## Slide 11: PXI-Based System Architecture
Modules
Modules
CompactPCI
Notes: PXI and CompactPCI modules and systems are interoperable. Many functions can be implemented without leaving the PXI form factor.
A PXI system can be used to control VXI, VME, and GPIB systems. This allows existing or specialized instruments to be easily integrated, and eliminates the need for an industrial computer.

## Slide 12: cPCI/PXI-Compatible Instruments
General-purpose
Oscilloscope
DMM
RS-232/485
Counter/timer
Data acquisition
Discrete digital I/O
Arbitrary waveform generator
Serial protocol analyzer
Switches
Digital waveform I/O
Motion control
Image acquisition
IEEE 1149.1 boundary scan
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>
A solid and growing base of core instruments are already available in the PXI form factor.

## Slide 13: cPCI/PXI-Compatible Instruments
Specialized
Mil-STD-1553
ARINC-429
Synchro/resolver to digital
GPS
Time code generation/translation
  IRIG A, IRIG B, XR3, 2137 or NASA 36
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>
Several of the specialized instruments associated with aerospace applications are also available in either PXI or CompactPCI form.

## Slide 14: Available I/O Interfaces
8170 Embedded PC
USB
RS-232 (Com1)
Printer
Optional Plug-in cards
10/100BaseT Ethernet
Ultra SCSI
MXI-2 (VXI/VME) controller
GPIB (IEEE-488) controller
Notes: Mkt1– <number>
Expanding Your Business with Marketing
<header>
<date/time>
A broad variety of industry-standard data and instrument control buss interfaces are also available.

## Slide 15: PXI-based System Architecture
Modules
Modules
CompactPCI
SCXI
Notes: PXI and CompactPCI modules and systems are interoperable. Many functions can be implemented without leaving the PXI form factor.
A PXI system can be used to control VXI, VME, and GPIB systems. This allows existing or specialized instruments to be easily integrated, and eliminates the need for an industrial computer.

## Slide 16: SCXI Signal Conditioning
Strain gage
Load cell
Thermocouple
AC and DC LVDT
RVDT
Resolver
Accelerometer
Resistance
Frequency
mV - 250 V
4 - 20 mA
Switch
Relay driver

## Slide 17: PXI-Based System Architecture
SCXI
MXI-2
GPIB
Notes: PXI and CompactPCI modules and systems are interoperable. Many functions can be implemented without leaving the PXI form factor.
A PXI system can be used to control VXI, VME, and GPIB systems. This allows existing or specialized instruments to be easily integrated, and eliminates the need for an industrial computer.

## Slide 18: Implementation Strategies
Use specialized instruments
  Minimize engineering investment
  Minimize support costs
or
Use generic instruments
  Minimize purchase cost
  Customize fixturing to provide specific features

## Slide 19: Implementation Options
Only one option in some cases
Programmable power supply
RF I/O
  PC-based equivalent does not exist
  Use traditional instruments (GPIB, VXI)

## Slide 20: Programmable Power Supplies
Provide power for fixture and unit under test
Available from third parties
  Elgar/Sorensen
  California Instruments
  American Reliance
  Xantrex
  NH Research
  Kepco
GPIB or RS-232 control

## Slide 21: Example- ATC Transponder Test
Discretes
Analog
IFR
ATC-
1400A
GPIB
Power
supply
Unit
under
test
Windows PC
Fixture panel
CSDB (Serial)
DC power
RF
UUT
cables

## Slide 22: Implementation Options
Some signal types offer a choice of interfaces
Switches
Discretes
Voltages

## Slide 23: Example – Programmable Switch
Three components
Control logic
Relay driver
Relay

## Slide 24: Three Implementations
PXI or SCXI switch modules
  All components on PC board
  Incremental cost per switch – $30 - $90
Relays in fixture
  Control logic and relay driver on PC board
  Incremental cost per switch – $21 - $29
Relays and drivers in fixture
  Only control logic on PC board
  Incremental cost per switch – $5 - $8

## Slide 25: Other Considerations
Fixture-related costs
  Engineering development
  Component purchase
  Assembly and test labor
  Ongoing repair and support
Business plan
  Core competencies
Third party suppliers