## Slide 1: Maximizing Productivity with Application Development Environments

## Slide 2: Outline
Hybrid ATE Systems Overview
Five Layer ATE Architecture
Designing Test Programs
ADE Factors
ADE Categories
System Benefits
Demonstration
Summary

## Slide 3: Hybrid ATE Systems Overview
A hybrid system combines components from multiple ATE platforms
  Streamlines system transition and maintenance
  Protects investment in existing software and hardware
  Allows easy integration of advances in ATE system development
Layered architecture is important
Multiple hybrid topologies
Notes: Hybrid ATE systems provide developers with a long-term ATE system that can evolve with short commercial technology lifecycles. Hybrid ATE systems take advantage of a 5 layer architecture to increase reusability, connectivity, extensibility, and module replacement.
By following the layered architecture, you create a test framework that allows you to replace and/or add components without having to re-architect the system. By clearly defining the system, you can take advantage of multiple buses using a variety of hybrid topologies. This allows you to meet multiple needs – protect the investment in existing hardware and software while being able to integrate the latest technologies.

## Slide 4: Five Layer ATE Architecture
- TestStand, DIAdem
System Management
- LabVIEW, LabWIndows/CVI, C++
Application
- VISA, LV PnP, IVI, MAX, DAQmx
Measurement and Control Services
- PXI, VXI, Desktop PC, GPIB
Computing
- Instruments, Data Acquisition, Vision, Motion
Device I/O
Notes: Moving from the bottom up, we’ll start with the actual hardware devices that you use to perform testing and automation. This layer includes the various instruments and data acquisition used in your system. Developers want to choose the devices that meet measurement needs and also scale with changing system needs. Oftentimes, the devices used will require multiple instrumentation buses. The computing layer above refers to the instrumentation buses used and the method and topologies that connect these buses. Users should choose a topology that meets timing and synchronization needs, allows them to protect investment in hardware, and add new components to benefit from advancing technologies. The measurement and control services is the layer that integrate the hardware with the software. It provides configuration utilities, soft front panels, and drivers with APIs to ease programming. With tight integration with the application layer, these APIs should appear as a seamless part of the application development environment. The application layer refers to the software used to create the test programs. For instance, developers might create a program to take a measurement with a DMM and another program to generate a signal. The system management layer allows users to call these programs, manage various user levels, log and manage data, and generate reports.

## Slide 5: Designing Test Programs
Plan for ATE needs with modular test code
  Separate UUT level and system level tasks
  Reuse code for other test systems
  Simplify replacement of instruments
Keep applications and tests independent of ATE bus
  Avoid direct ATE bus level calls in tests
  Use test-oriented abstractions
    Create GenerateWfm.vi instead of AWG4321_Start.vi
Take advantage of the ADEs available
  Legacy test code
  Newer ADEs
Notes: When designing a test program, it is important to create modular test code to maximize reusability. Developers should separate UUT level and system level tasks so that the programs can be easily reused for other test systems and to simplify replacement of instruments.
Applications and test should be kept independent of the ATE bus by avoiding direct ATE bus level calls in tests. Using test-oriented abstractions should help to simplify maintenance of software when replacing instruments.
Developers should take advantage of all the ADEs available. With modular test programs, developers can use legacy test code for some program and write others in newer ADEs.

## Slide 6: Key Requirements for ADE’s
Open architecture
Flexible
Platform independence
History of innovation
Ease of use
Technical support
Driver availability
Stability
Availability of experienced programmers
Notes: There are many requirements for ADEs that developers should look for. Some of the more important ones include an open architecture that is flexible and offers platform independence. This provides users with a application development environment that scales with their needs. In addition, users should also look for a ADE that has a history of innovation so that there is confidence in the product and continued support. Developers should also look for ADEs that are not only easy to use but also provide technical support if needed. A key factor is the availability of instrument drivers in the ADE. Having many instrument drivers to choose from can greatly simplify programming.

## Slide 7: ADE Factors
Productivity
Development
  Example code
  Code generation
  Tools for remote connectivity
Deployment
  Application and distribution kit builders
Maintenance
Modification
Scalability
Supports multiple user types
Accommodates a variety of measurement hardware
Supports various measurement and control applications
Adjusts to expanding system
Notes: Productivity and scalability are also two factors to consider in an ADE. An ADE should provide tools to improve and speed up code development as well as deployment. For instance, providing example code or code generation can quicken development. Tools to simplify maintenance and keeping track of modifications are important for up-keep of test code.
The ADE should also be able to support multiple users and support the various types of hardware.

## Slide 8: ADE Factors
Integration with Measurement and Control Services
Simplified configuration programming
  Create and edit channels
  Identify and configure remote interfaces
Alias names
Integration with instrument drivers
Integrated Measurement Functionality
Incorporated measurement data types
Statistical and analysis functions
Signal processing
Control algorithms
Digital filtering
Octave and order analysis
Notes: A key factor is that the ADE integrate with the measurement and control services layer well. If these two layers are integrated, the user benefits from simplified programming and thus quicker development. By applying the configuration of devices and creation and editing of channels in the measurement control services layer to the ADE layer, developers will be able to easily develop test programs.
The ADE should also provide integrated measurement functionality meaning that it incorporates the measurement data types required as well as any statistical analysis and processing functions needed. Provision of additional algorithms and functions like digital filtering and octave and order analysis are useful as well.

## Slide 9: ADE Factors
Project Management Tools
Revision history
File consolidation through libraries
  Portability
  Save disk space
File hierarchy
Code comparison
Source Control
Adequate tools for your test system development
  Documentation of revision changes
  Revision tracking
Availability or integration with third party software
Notes: For larger applications or ones that will be maintained over time, it is important that the ADE provide tools to help manage the product. Things like revision history, file hierarchy and consolidation, and code comparison allow users to keep track of the code properly. For source control, the ADE should provide tools to keep track of revision changes and by whom. If the set of tools is not complete, it should also provide integration with 3rd party software.

## Slide 10: ADE Categories
Graphical Development Environment: LabVIEW
  High productivity
  Intuitive user interface
  Optimized to T&M
Textual Development Environment: LabWindows/CVI
  ANSI C standard
  Stable API with backward compatibility as a priority
Microsoft Visual Studio Toolkit: Measurement Studio
  Staying current Microsoft technology
  T&M specific tools for Microsoft languages
Notes: There are three main types of application development environments.
Graphical environments like LabVIEW provide users with high productivity and intuitive user interfaces due to its graphical nature. There are graphical ADEs that are optimized for test and measurement to simplify code development.
Text-based environments like LabWindows/CVI should be based on the ANSI C standard and provide a stable application programming interface with backwards compatibility as a prioirity.
The last category, Visual Studio Toolkits, enable developers to apply Microsoft technology to test and measurement. Toolkits like Measurement Studio provide specific test and measurement tools, functions, and user interface controls.

## Slide 11: LabVIEW
Graphical Programming for Virtual Instrumentation
  Front panel graphical user interfaces
  Graphical block diagram source code
  Compiler for optimized execution
Platform Independent
Standalone executables for easy distribution
Notes: <number>
<footer>
<header>
<date/time>
Since LabVIEW first became available in 1986, graphical programming has grown from an alternative to programming methodology to a de facto industry standard. With LabVIEW, you quickly design your user interface and graphically assemble your program as a block diagram. The development paradigm is ideal for measurement and instrumentation system developers. LabVIEW users have reported saving hours, days, and even months of development time compared to the software tools they used previously.
LabVIEW gives you the flexibility of a powerful programming language without the associated difficulty and complexity. LabVIEW makes all instrumentation system developers more productive, regardless of their programming background. LabVIEW also has an extremely broad user base with applications in test and measurement, data acquisition and control, process monitoring, factory automation, and laboratory automation.

## Slide 12: LabVIEW
Acquire
  Interactive assistants
  Code generation
Analyze
  Over 450 built in functions for analyzing measurements and processing signals
Present
  User interface design
  Web publishing
  Software connectivity
  Connectivity to thousands of devices
  Report generation
  Data management
Notes: LabVIEW simplifies the process of acquiring, analyzing, and presenting data. To simplify acquisition, LabVIEW not only provides connectivity to thousands of devices but also interactive assistants and code generation. For analysis, LabVIEW gives users over 450 built in functions. To ease presentation, users can take advantage of tools for interface design, web publishing, report generation, data management, and web publishing.

## Slide 13: LabWindows/CVI
Proven
  ANSI C development environment for test and measurement
  History of Innovation beginning in 1987
Optimized for test and measurement
  T&M Libraries
    Analysis
    User Interface
    Instrument Control
    Multithreading
    ….
  100’s of source code instrument drivers
Complete ANSI C Development Environment
Notes: <number>
<footer>
<header>
<date/time>
LabWindows/CVI is a proven test and measurement ANSI C development environment that increases the productivity of engineers and scientists. LabWindows/CVI streamlines development with hardware configuration assistants, comprehensive debugging tools, and interactive execution to run functions at design time. Built-in measurement libraries enable rapid development of complex applications such as multithreading and ActiveX server/client programs. The flexibility of LabWindows/CVI optimizes the data acquisition, analysis, and presentation of test and measurement applications.

## Slide 14: Measurement Studio
Integrated measurement classes for Visual Studio .NET
Reusable acquisition tasks
Code-generating designers
Sophisticated advanced analysis libraries
Rich object-oriented hardware APIs
Highly extensible C++ and .NET class libraries
Wizards and data networking
Native user interface controls
Notes: <number>
<footer>
<header>
<date/time>
What is NI Measurement Studio? Measurement Studio is an integrated suite of native classes and controls for measurement and automation applications in Visual Studio .NET. Measurement Studio dramatically reduces application development time with wizards, simplified data networking, and .NET user interface controls. New code designers interactively define reusable acquisition tasks and automatically generate code. Advanced analysis libraries and rich object-oriented hardware APIs, such as data acquisition and instrument control, enable the development of sophisticated measurement applications. The highly extensible C++ and .NET class libraries in Measurement Studio for Visual Studio .NET deliver unparalleled flexibility to scientists and engineers.
In the following slides, we continue our discussion of the actual development environment of Measurement Studio.
© National Instruments Corporation 19 Acquire, Analyze, and Present with NI Measurement Studio Seminar

## Slide 15: Application Development Summary
Prioritize ADE requirements
  Open and flexible
  Platform independence
  Driver availability
  Technical support
Three ADE Categories
  Graphical ADE
  Textual ADE
  Visual Studio toolkit
Notes: When considering application development environments, developers have three main categories to choose from, graphical ADEs, text-based ADEs, and Visual Studio toolkits. One the main things developers should do when choosing an ADE is to prioritize the requirements and look for an ADE that is open and flexible, that is not tied to just one hardware platform, provides instrument drivers for your system, and gives you access to technical support.

## Slide 16: System Benefits
Maintain investment in software
Modular Test Programs
  Reuse test programs and legacy code
  Simplify maintenance and replacement of instruments
Incorporation of new software
  Increase productivity
  Minimize development time
  Simplify building new test programs
Notes: When designing a test system, it is important that developers wisely architect the test programs to maximize the investment in software. Creating modular test programs can simplify maintenance and also allows users to reuse test programs and legacy code. In addition, developers can still incorporate new software and take advantage of new ADEs to increase productivity and minimize development time.

## Slide 17: Demo: Wireless Communications Test System
3D Power Spectrum, Occupied Bandwidth, Auto Find (LabVIEW)
TestStand
MAX, VXI ResMan, VISA, IVI and PnP Drivers
PCI (NI-8350), PXI MXI-4, VXI-USB, GPIB
2.7 GHz PXI RF Signal Analyzer, 8.5 GHz VXI RF Signal Analyzer, PXI DMM, PXI Switch, GPIB Power Supply
Notes: For a wireless communications system, you can see how the layers work together to integrate the buses for this test application. Through the architecture the user can integrate VXI and GPIB instruments with some newer PXI instruments. This allows the user to take advantage of existing hardware and software and still incorporate newer technologies for the price/performance benefits.

## Slide 18: Demo: Wireless Communications Test System
System Management Software
CVI
LabVIEW
3D Power Spectrum, Occupied Bandwidth, Auto Find
GPIB power supply control
Etc…
Etc…
Notes: By designing this system with modular test programs, developers can easily maintain and scale the code as needed. The system management software will call individual modular test programs to execute the actual test sequence. This system contained an individual test program to perform a specific function like finding the 3D power spectrum, determining the occupied bandwidth, and performing an auto find to see what frequency the signal was coming in at. There is also a CVI program to communicate with the GPIB power supply. If additional test programs needed to be added to the system, they could, and the user could also integrate any legacy code if needed.

## Slide 19: Hybrid ATE Summary
Use the five layer architecture
  Streamlines system transition and maintenance
  Maximizes return on investment in existing software and hardware
  Carefully select or build components
Use ADEs that are
  Open and flexible
  Provide platform independence
  Have instrument drivers available
Build modular test programs
  Separate application and UUT level tasks
  Keep applications and tests independent of ATE bus
PASS
FAIL
UUT
UUT
UUT
UUT
Notes: To summarize, when designing hybrid test systems, it is important to use the layered architecture to streamline maintenance and maximize investments. It is important to carefully select the components used, including the application development environment used. When choosing ADEs, developers should look for an ADE that is open, flexible, that does not tie the system to just one hardware platform, and that has instrument drivers for the instruments used in the system. A key part of the test program layer is to create modular test programs that separate application and UUT level tasks and that keep the test independent of the ATE bus.

## Slide 20: Questions?
Notes: <number>
<footer>
<header>
<date/time>
Def. push everyone to the web for additional information (free eval, white paper etc)– here, you can ask if you missed anything, if they need more information, follow-up from the engineer, a customer education course etc…
© National Instruments Corporation Acquire, Analyze, and Present with LabVIEW Seminar