## Slide 1: Introduction to Measurement Studio™
<date/time>
Chris Mathews
Measurement Studio Product Support Engineer
Wed Aug 16
10:15 a.m.-1:15 p.m., 1:45-4:45 p.m.
Exhibit (3H)
Notes: National Instruments delivers the tools you need to turn your compiler into a measurement-ready development environment. National Instruments Measurement Studio integrates with industry standard environments such as Microsoft Visual Basic and Visual C++, and LabWindows™/CVI to give you flexibility in your development efforts. Measurement Studio leverages the proven software strengths of National Instruments to deliver tools for power users as well as novices – you never run out of functions.

## Slide 2: Agenda
Measurement Studio overview
  What is Measurement Studio?
  Benefits
LabWindows/CVI – a complete C environment
Visual C++ tools
Visual Basic tools
Conclusion
Notes:   National Instruments Measurement Studio is the most productive set of tools for creating measurement and automation applications using standard text-based programming environments. Measurement Studio reduces time-to-market and production cost with proven software tools for adding acquisition, analysis, and presentation to your applications. You have the flexibility to choose which environment best suits your application. By integrating with Microsoft, we bring you all of the measurement functions you need so you do not need to learn a new way to program.
  National Instruments LabWindows/CVI, a component of Measurement Studio, is the premier text-based development environment for creating measurement and automation applications. LabWindows/CVI includes:
    Simplified integrated development environment
    Instrumentation libraries
    Multithreading, ActiveX automation, file I/O
    DAQ, IVI, VISA, GPIB, VXI, Serial
    DataSocket, TCP, DDE
    Analysis, Signal Processing
    Productivity Tools
    IVI Class Wizard
    ActiveX Automation Wizard
    Localization Wizard
    DLL and Distribution Kit Creation
National Instruments tools for Visual Basic Tools (formerly known as ComponentWorks™) is a collection of instrumentation and test programming tools in ActiveX control format. The ActiveX controls are used in compatible control containers to add instrumentation specific functionality to general purpose programming environments including Visual Basic.

## Slide 3: What is Measurement Studio?
Measurement hardware
Windows
Visual Basic Visual C++
Internet
Visualization
Analysis
Acquisition
LabWindows/CVI
Measurement Studio
Measurement Components
Notes: Measurement Studio is a complete solution that includes ANSI C, Visual Basic, and Visual C++ tools for value added acquisition, analysis, visualization, and Internet capabilities to the standard compiler. These tools consist of our recently upgraded LabWindows/CVI, Visual Basic tools, and a new add-in for Visual C++ to deliver the measurement tools for data acquisition, analysis, and visualization that programmers need to turn everyday compilers into a measurement-ready development environment.
National Instruments is the leader in virtual instrumentation systems and Measurement Studio builds on more than 12 years of software development for measurement and automation applications. By leveraging our expertise in software and hardware, Measurement Studio provides the best development tools for engineers and scientists to complete their jobs quickly, with better quality, and more cost effectively than ever before.

## Slide 4: Measurement Studio
Productivity
  Spans the gap in instrumentation functions
  Streamlines development
Integration
  Alliance with Microsoft through the Visual Studio Integration Program (VSIP)
  Fully integrated tools for Visual C++ and Visual Basic
Flexibility
  Select the programming environment that best suits your application
  Powerful enough for an expert, simple enough for a novice
Notes: After pinpointing the gap that exists between standard software development tools and what is needed for virtual instrumentation, National Instruments developed solutions to bridge the gap. Measurement Studio delivers functions specifically targeted at test, measurement, and automation applications. For faster application development, we developed a suite of rapid development tools. This means you can write programs quickly and easily and modify them as future needs dictate. By creating applications faster and easier, you lower application development costs and decrease time-to-market.
In today’s fast-paced engineering world, organizations need to design and implement test strategies for shorter development cycles and higher volume production runs. With tighter test system production schedules, test engineers want to use proven pre-existing code modules to build test systems quickly. Rather than develop code from scratch for each test system, engineers focus on code reusability for faster, more reliable software development on the production floor.
Now you can choose the best tool for the job. Measurement Studio provides all of the tools in the compiler that suit your application development needs.

## Slide 5: LabWindows/CVI
ANSI C
Standard Language
Compiler
Editor
Debugger
Open System
Built-in
instrumentation
libraries
I/O (GPIB, VXI, DAQ, Serial, IMAQ, etc)
Analysis
DataSocket ActiveX
TCP
GUI
Productivity tools
for faster development
Code
Generation Tools
Interactive
Execution
Standard ANSI C language
  Open, powerful
  Multithreaded
Notes: LabWindows/CVI provides measurement application development in an integrated ANSI C development environment. It includes a 32-bit compiler and linker and advanced editing and debugging tools. You can incorporate code from multiple developers by generating DLLs to use in other environments.
LabWindows/CVI comes with a comprehensive suite of libraries targeted at measurement applications, from instrument control to data analysis and graphing – everything you need is right at your fingertips.
For rapid application development, LabWindows/CVI includes CodeBuilder™ and interactive function panels. These two powerful code generation tools mean you can develop your application with minimal programming. It is like having your own personal C expert help you with your application!

## Slide 6: User Interface Editor
Drop-and-drag editor
Instrumentation controls
Custom menus
Quick to build – simple to change
Notes: The User Interface Editor in LabWindows/CVI is a graphical drop-and-drag editor for building the graphical interface to your C programs. Creating the interface for your program requires no source code. You select each control for your interface from the “Create” menu and place it on the front panel. The controls and indicators, such as numeric controls, text boxes, command buttons, graphs, and binary switches, are divided into different sections under the Create menu. The numeric control palette illustrated above shows all the controls available for getting numeric data to and from your C program.
In addition to controls and indicators designed to emulate conventional instrument controls, there is also a range of Windows-like controls available including pull-down menus, ring controls, and tabbed dialogs.
Once created, the user interface is stored in its own file (suffixed .uir for user interface resource). You can store it in an ASCII format suitable for use with source control tools. Although you normally create these panels with absolutely no coding, it is also possible to programmatically create and modify front panel objects.

## Slide 7: Callback Functions
Event-driven programming made easy
User interface
resource file (.uir)
Source file (.c)
control 1
indicator
control 2
function 1
function 2
function 3
timer
mouse
click
key
press
data
timer
tick
Notes: Each control on the user interface links to a particular function in the C source file (this method is similar to the events used in Visual Basic). When you operate a control, the function is automatically called to process the events. Writing programs in this way is referred to as using callback functions – each control calls back to the C source code to a particular function.
Two common methodologies exist for developing event-driven programs. Using callback functions is a simple, object-oriented approach for developing user interface control code – each control on the user interface has a corresponding C function that processes the events generated by that control. The second method involves using an event-loop. LabWindows for DOS uses this method. Event-loops require more programming. You must build a mechanism to recognize which control on the user interface generated the event, and then decide where to pass the control in your program.
With LabWindows/CVI, you can build your programs using event-loops or callback functions. This presentation will concentrate on the callback function methodology.

## Slide 8: Function Panels
You can
  Interactively execute code
  Quickly test hardware operation
  Experiment with library functions
  Generate code
  Call up function help
Without
  Typing C source syntax
  Compiling programs
  Linking to libraries
You can create your own
function panels for code you want to reuse!
Notes: LabWindows/CVI not only has the tools required to build standard ANSI C programs from scratch, it also adds interactive code execution and generation tools called function panels that simplify your development efforts. Function panels feature:
• On-line help to teach you how the function operates
• Automatic code generation capabilities
• Interactive execution capabilities so you can experiment with functions
Function panels provide the key to interactive programming in LabWindows/CVI. With a function panel, you can interactively execute any function in the LabWindows/CVI libraries. Before you write a single line of C source code, you can experiment with any of the library functions to learn how they operate and which are best for your application.
The slide above shows a function panel for the AI_VRead function from the data acquisition library. AI_VRead reads an analog input voltage from a plug-in data acquisition board. Each control on the function panel represents an argument or parameter to the AI_VRead function. As you input values into the controls, LabWindows/CVI automatically constructs the C syntax for calling the function at the bottom of the function panel. You can run this function interactively or pasted into your C program.
The function panel mechanism is simple, yet powerful and can be layered into your custom libraries to make them easy to access.

## Slide 9: A Complete ANSI C Editor/Debugger
Flexible editor
  Color-coded source
  Difference finder
  Source code tags
Powerful debugger
  Multithreaded debugging
  Dynamic breakpoints
  Conditional breakpoints
  DataTips
  Variable/watch windows
  Run-time memory checking
  Use LabWindows/CVI to debug DLLs
Notes: LabWindows/CVI includes a number of shortcut keys and utilities aimed specifically at programmers. You can open header files referenced in your program with a single keystroke, automatically match left and right parentheses or brackets in a function, or compare two files for differences. You also have multiple ways of highlighting code, searching for function definitions in your program, or finding function panels quickly. Use color coding to differentiate commands, constructs, comments, and definitions.
The Source window is a full function source code editors – you are free to type in ANSI C source code directly from the keyboard. Choose from standard cut, copy, paste, find, and replace commands. Of course, each of these commands can operate on a single file, or multiple source files, when finding or replacing text.
In addition, the editing tools can navigate around large source files in many ways. You can split the window in half to view two areas of the same file. Or, you can set tags on particular lines of source code.
Much of the editing and debugging features of LabWindows/CVI are reflected in the far left-hand column of the Source window. For example, the green squares represent tags in the source code and the red diamonds and the yellow, hollow square represent different types of breakpoints in the source code.

## Slide 10: Instrument Drivers
Let you concentrate on the measurement task, instead of low level I/O
Make programs
  Simpler to update or modify
  Better structured
  Easier to read
Take advantage of more than 700 instrument drivers available at ni.com/idnet
Notes: Instrument drivers are key to test productivity. Test programmers use them to focus on the test problem at hand, rather than the minute details of low-level instrument communication.
Instrument drivers help make test programs more maintainable in the long term. An instrument driver contains all of the I/O within its own library, separate from the test code, protecting you during hardware changes and upgrades. You can read and maintain test code much easier when the instrument command strings are not littered throughout the test code. In addition, when you come to upgrade your instrumentation, it is much easier to upgrade your test code because all of the code specific to that particular instrument is self-contained within the instrument driver.
The current LabWindows/CVI library runs to more than 700 instrument drivers available FREE on the Web. As test developers know, instrument drivers play a key role in test development productivity.

## Slide 11: Multithreading
Keep time critical tasks from being greatly affected by UI
Keep UI responsive while performing background task
  Printing in background
Improve performance on multiprocessor machines
Logical separation of independent program parts
Word
Processor
T
I
M
E
Process
UI
Printing
Program
Thread 1
Thread 2
Notes: Multiple threads executing in the same program is called multithreading. Multithreaded programs require support from the operating system. Windows 2000/NT/9x all support multithreading.
The green box represents a single process. Each blue box represents a single thread of execution. From the user perspective, the UI responds to the user input at the same time the program is printing. On multiprocessor machines or a fast machine, the user may not see a degradation of UI responsiveness while a print operation runs.

## Slide 12: Multithreading Support
Simplified multithreading libraries
Can debug multithreaded applications directly in the environment
  Can step into each thread one at a time
  Color codes threads while debugging for easier differentiation
Notes: Only a few applications today are actually multithreaded, largely because multithreaded applications are difficult to develop. The latest version of LabWindows/CVI solves this problem by simplifying and taking advantage of the multithreaded capabilities of today’s Windows operating systems. The LabWindows/CVI multithreading libraries work well with the LabWindows/CVI event-driven model.
The LabWindows/CVI multithreading technology is built into the environment. LabWindows/CVI gives you a high-level multithreading library for building fast, flexible measurement and automation applications. To easily write a multithreaded program, you call a single function to run a function in a separate thread, and then receive an event when the function completes.

## Slide 13: Other LabWindows/CVI Functions
ActiveX automation
DataSocket
UIR localization
Covert UIR to code
Windows SDK
Distribution packager
Notes: There are many functions that make LabWindows/CVI a great tool for creating Windows applications. It comes with a full Windows Standard Development Kit for creating any Windows application. It also comes with DataSocket so you can easily transfer your live measurements across the Web. LabWindows/CVI has a localization utility to make your application ready for the worldwide marketplace. You can even convert your user interface into code so you can compile your application into a single executable. Finally, LabWindows/CVI provides a distribution packager that can make sharing your application easy and professional.

## Slide 14: Measurement Studio Tools for Visual C++
Compiler integration
Intellisense
ClassWizard
  Visa
  GPIB
  Analysis
UI Controls
Utility Classes
Data Object
Application wizard
Measurement classes
  Acquisition
  Analysis
User interface through ActiveX
Utility classes
Data objects
Notes: The tools for Visual C++ inside the Measurement Studio package are the first and only C++ tools designed specifically for the needs of the Visual C++ measurement and automation programmer. Measurement Studio incorporates many years of development time from LabWindows/CVI and provides you with a C++ interface native in the C++ environment.
National Instruments joined Microsoft through the VSIP program to provide complete integration. You do not need any tools outside of the compiler to create your application. Just use the new measurement wizard and the functions are integrated into your project and ready to use.

## Slide 15: Application Wizard
Built on standard MFC application wizard
Adds measurement functions
  ActiveX controls
  C++ classes
Finds drivers on your computer and adds them to project
Converts CVI project to Visual C++ project
Notes: The application wizards helps you start your applications by asking a few questions, then generating a code skeleton for you. The wizard adds measurement functions, such as measurement specific ActiveX controls to the resource toolbox, and includes measurement class libraries and instrument drivers found on your machine. The wizard is built on top of the standard MFC applications wizard so programmers do not need to learn anything new.

## Slide 16: User Interface
Custom wrapped ActiveX controls for simplified use with Visual C++
Front Panel Objects
  Knobs, switches, sliders
  2-D graphing and charting
Advanced visualization
  3-D graph
Notes: Measurement Studio delivers custom wrapped ActiveX controls to simplify Visual C++ user interface development. With objects such as knobs, switches, sliders, 2-D graphing and charting, and 3D visualization, any application can have a professional look that mimics real-life instruments for intuitive operation.

## Slide 17: Compiler Integration
Classes integrated into Class Wizard
Function syntax help integrated in IntelliSense
Notes: Intellisense and ClassWizard, along with other functions, fully integrate with Visual C++. You do not need to learn anything new to use these helpful tools. They function exactly like the built-in MFC classes. Just start typing and Visual C++ helps you fill in your code syntactically correct, and the ClassWizard works with our tools to eliminate the tedious tasks of creating and headers and source files, constructors and destructors, and much more.

## Slide 18: Instrument I/O
Classes for GPIB™ and VISA
Notes: To integrate the computer with measurement components, you need highly productive software development tools. These tools acquire and analyze data with high-speed I/O services for user-defined instrument systems.
Measurement Studio C++ classes for GPIB and VISA offer a unified interface for data collection. Coupled with the IVI class drivers, you can acquire data from a variety of instruments easily with native C++ class interfaces. You can incorporate an NI-DAQ dynamic link library (DLL) for Microsoft Visual C++ into your measurement and automation application.

## Slide 19: Analysis Classes
Notes: After collecting data, engineers and scientists use a variety of signal processing and data analysis tools to extract information for their measurement and automation work. Applications involving research and development, engineering and validation, manufacturing, and service require tools such as curve fitting, spectral analysis, statistics, and visualization. National Instruments Measurement Studio provides a variety of signal processing and data analysis tools for application development.

## Slide 20: DataSocket™ Classes
DataSocket functions exposed through C++ classes
Use to easily pass live measurement data across networks, the Internet, and to other applications or Web pages
Notes: Whether you pass data between applications or pass data across the Internet, National Instruments software makes moving measurement data easy.
DataSocket simplifies live data exchange between different applications on one computer or between computers connected by a network. Although a variety of different technologies exist today to share data between applications, including TCP/IP, DDE, and others, most of these tools are not targeted for live data transfer. DataSocket, however, implements an easy-to-use, high-performance programming tool that is designed specifically for sharing and publishing live data in measurement and automation applications.

## Slide 21: Data Objects
Represent a common format for exchanging information between the data acquisition, analysis, and visualization portions of your application
  CNiComplex – for use with complex data types
  CNiVector/CNiMatrix – encapsulates vector and matrix data
  CNiString – simplifies passing strings
Notes: The data object classes in Measurement Studio are the glue that bind Visual C++ tools together. They provide a simple mechanism for transferring your measurement data from the acquisition classes to the analysis classes and then to your user interface controls. You use the data objects to interface your measurement needs to provide a simple standard interface upon which you can build.

## Slide 22: Measurement Studio Tools for Visual Basic
Measurement and automation ActiveX controls
Analysis
UI
DAQ
Network
GPIB
Serial
Notes: SC1B-<number>
Introduction to Measurement Studio
<header>
<date/time>
Measurement Studio contains numerous libraries of controls that add different instrumentation and measurement tools to compatible environments.
The user interface library supplies measurement-specific, optimized controls including graphs, strip charts, knobs, meters, slides, buttons, switches, and so on. You can customize each control to fit your application with features such as multiple axes, plots, and cursors; time and log scales; and custom images.
The data acquisition controls support the full range of NI-DAQ functions: analog input, analog output, digital I/O, and counter/timer applications.
The instrumentation controls include GPIB (IEEE-488.2), Serial (RS-232/485) and VISA – the Virtual Instrument Software Architecture, a comprehensive package for configuring, programming and troubleshooting instrumentation systems comprised of VXI™, VME, PXI™, GPIB, and Serial interfaces. In addition to providing basic read/write operations, the controls add productivity tools including an interactive tester and automatic parsing tools. For instrument driver development, the Visual Basic tools in Measurement Studio contain the “instrument driver factory”. You can find more than 700 instrument drivers with modifiable source code on the instrument driver network on the Web.
The analysis library includes controls for array and matrix manipulation, statistics, digital signal processing, and other advanced analysis functions. For network connectivity, the tools include DataSocket to add support for data exchange between applications and systems on a network.

## Slide 23: User Interface
Controls for virtual instrumentation front panels
Advanced controls for visualization
Notes: The standard Visual Basic user interface objects were not designed for the performance and function requirements of high-speed measurement and automation systems. The Visual Basic tools graphical user interface (GUI) controls give the application an instrumentation look and feel without sacrificing performance. The interface controls consist of switches, knobs, graphs, and so on, that aid in creating a virtual instrumentation application.
The optimized graph control delivers speed and reliability. The 2-D graph can display multiple plots and use customizable cursors and axes to highlight relevant data. The 3-D graph includes features such as lighting and contours to help visualize the dataset to gain a better understanding of the relationship between data points.

## Slide 24: Analysis
Instrumentation class analysis controls
1-D arrays – arithmetic operations on arrays
Matrix – vector and matrix operations
Complex – arithmetic operations on complex scalars or arrays
Signal processing – generating signals and analyzing data in the frequency and time domain
Statistics – basic statistics functions
Notes: CWArray
1-D and 2-D array functions contain functions that manipulate one- and two-dimensional arrays.
Multi-dimensional array functions contain functions that perform operations on a whole array.
Multi-dimensional element functions contain functions that perform operations on each element in an array of any dimension.
CWComplex
Complex numbers contain functions that perform scalar complex arithmetic.
Multi-dimensional complex numbers contain functions that perform arithmetic on complex arrays of any dimension.
CWDSP
Signal generation contain functions that initialize arrays with pre-defined patterns.
Frequency domain processing contain functions that perform transformations between the time domain and the frequency domain and perform analysis in the frequency domain.
Time Domain Processing contains functions that perform direct time domain analysis of signals.
IIR Digital Filters contains functions that perform Infinite Impulse Response (IIR) digital filtering on signals by mapping analog specifications into digital specifications. This object contains Butterworth, Chebyshev, Inverse Chebyshev, and elliptic filters.
FIR Digital Filters contains functions that design Finite Impulse Response (FIR) filters. These functions do not actually perform the digital filtering. This object contains window and equi-ripple FIR filters.
Windows contains functions that create windows frequently used to smooth data and reduce the truncation effects in data acquisition applications.
Measurement contains functions that perform spectrum analysis using real units, such as Hz and seconds.
CWStat
Statistics contain functions that use various common methods such as Mean and Base Deviation to describe a set of data.
Probability Distributions contain functions that operate as cumulative distribution functions from various probability distributions and functions that operate as corresponding inverse functions.
Analysis of Variance contains functions that perform one-way, two-way, and three-way analysis of variance in different statistical models.
Nonparametric Statistics contains a function that analyzes data without assuming that the data is normally distributed.
Curve Fitting contains functions that perform curve fitting using least square fit techniques, such as linear, exponential, polynomial, and general least square linear fit.
Interpolation contains functions that take a set of points at which a function is known and estimate the value that the function takes at some specific intermediate point.
CWMatrix
Methods for vector and matrix operations; vectors and matrices are represented by 1D and 2D arrays respectively

## Slide 25: IVI Controls
Provides simplified application programmer interface (API) for control of IVI class instruments
Provides complete user interface for the instrument, or becomes invisible so you have complete programmatic control
Create applications that are truly instrument interchangeable
Notes: With interchangeable virtual instrumentation (IVI), test engineers can build high-performance hardware-independent test systems by changing the instrumentation hardware without changing any code. The IVI drivers also deliver a high-performance state caching engine and can simulate an instrument when hardware is unavailable.
The new IVI controls simplify and enhance the control of instruments with IVI class-compliant instrument drivers. The new digital multimeter (DMM) and scope controls support the IVIDmm and IVIScope classes. A new tool control provides application helper functions and low-level instrument attributes. The new IVI controls have built-in user interfaces and support instrument configuration through interactive property pages.

## Slide 26: Data Acquisition
Full NI-DAQ functions in ActiveX controls
  Analog input
  Analog output
  High speed waveform
Simple interactive property page interface
  Digital I/O
  Counter/timer
Notes: The tools for Visual Basic DAQ components along with National Instruments DAQ boards perform analog, digital, and timing I/O operations. With the DAQ components, you can easily configure acquisition routines and handle tasks such as transferring buffers from the hardware to the computer with no low-level programming required.

## Slide 27: DataSocket and Binding
DataSocket
  ActiveX control for network distribution of data
  Supports DSTP, OPC, FTP, HTTP, and file connections
UI Binding
  Requires no
  programming to
  pass data
  between
  applications
Notes: Because Measurement Studio tools for Visual Basic consists of ActiveX controls, you can build dynamic virtual instrument Web pages that interactively view data across the Internet. You can add routines from the tools for Visual Basic analysis libraries to analyze data you acquire from the Web directly into your Web browser and display the results.

## Slide 28: For More Information
Online seminar
  ni.com/webevents – video demonstration
NI Developer Zone
  http://zone.ni.com
Application notes
User solutions
White papers
Free evaluation software
  for an in-depth look at Measurement Studio
  ni.com/mstudio
Notes: If you would like to find out more, there are many sources of information available. Be sure to check out the contents of your seminar CD because it contains a great deal of useful technical information, including white papers, customer solutions, and application notes.
Evaluation software gives you a chance to take an in-depth look at National Instruments software before you buy.
For the latest information, check our Web site ni.com The site is constantly kept up-to-date with product data and other valuable information.
If you still have questions, feel free to talk to us after the seminar or call your local National Instruments sales office.