## Slide 1: Designing a Motion Control Project
Joseph Ting
Motion Support Engineer
Wed Aug 16
10:15 a.m.-1:15 p.m., 1:45-4:45 p.m.
Exhibit (3I)

## Slide 2
Designing a Motion Project
Step-by-step feature demo
Application – Drilling a circular hole
Notes: Often times, motion control is a core part of building a machine. More and more, machine builders are discovering the benefits of using off-the-shelf components and leveraging the PC architecture for the motion and numerical control of their machines.
In a traditional machine, much of the design effort is spent on proprietary hardware. When building an open architecture machine using motion control, systems integrators are now forced to spend a tremendous amount of time and money developing custom application software. Thus, software productivity becomes an important factor of building the motion component of a machine.
Using LabVIEW™ and an open architecture FlexMotion™ controller from NI, the user can create an application 10X faster than traditional methods. We guide you step-by-step through creating a simple motion project in a very short time.
For this application, imagine you are interested in drilling a hole, roughly 5 inches in diameter, in a block of wood or metal. This would be one task of a machine that manufactures car parts, a subwoofer box, or furniture.

## Slide 3
Motion Components
Motion software
Motion controller
Motor drive
Motors, feedback, mechanical fixturing
Notes: This slide illustrates the components of a motion control system.
Motors, feedback devices, and mechanical fixturing greatly vary from application to application. For example, if you are building a semiconductor wafer handler, your motors, feedback, and fixture are totally different than if you were building a biotech test tube sampler or a computer controlled lathe. Selection and integration of these hardware components require your specific vertical market expertise.
Regardless of your system or machine, users can solve all their drive, motion controller, and software needs using off-the-shelf components from National Instruments.
The drive drives current through your motor, modulating the signal as necessary for different sizes and types of stepper and servo motors.
The motion controller is specialized hardware designed to intelligently command and output any trajectories. It handles features such as limit switches, breakpoints, encoder feedback, and more. (There are too many hardware features to list.)
You send high level commands to your controller such as “Load Target Position” and “Start” with the motion software. It is also where you can create an interactive user interface.
We discuss and demonstrate the productivity features of NI-Motion™ software that you can use for ANY motion control project.

## Slide 4
Configuration
One-time process
Control any motor
Virtual stage
Notes: To control any motor, nearly every setting you can think of is software configurable – stepper output mode, inhibit polarities, rising/falling edge/level position triggers, PID parameters, and more.
Configuration for your mechanical system is often a one-time process using an easy-to-use, interactive interface, Measurement & Automation Explorer (MAX). There are hundreds of parameters you can optionally configure to optimize your system. Then, within your application, call “Initialize” and all the parameters you have configured are set.
In addition, you can run diagnostics and test individual axes of motion using this program. These diagnostics include a 2-axis virtual stage. This is useful for our demonstration, because with it everyone in the audience can see real world motors in motion. It traces the path as well.

## Slide 5
Simple 3-Icon Demo
Initialize
  Calls default configuration from MAX
Load Target Position
  Default mode is absolute position mode
Start Motion
Notes: Now let’s return to our application. Using the NI-Motion software and controller, a basic point-to-point move involves only three commands.
First, Initialize the board. This configures all motion parameters to a known state and energizes the motors.
Next, load the target position to which you want to move.
Finally, command the board to Start Motion.
Note that, after you run this program, LabVIEW completes immediately while the motor is still moving. This is because the motion board has a real time trajectory generator and onboard intelligence to complete the commanded move.
It follows a trapezoidal velocity profile using your default velocity and acceleration parameters, arriving exactly at the commanded target position.

## Slide 6
Set Velocity, Acceleration,
and Monitor
Load velocity
  Counts/second
  RPM
Load Acceleration
  Counts/S2
  RPS/s
Plot position while move not complete
Notes: For our next step in the simple point-to-point move, we add a Velocity and Acceleration control. Setting each of these parameters requires one function call.
As shown, users can load velocity and acceleration using two different units, depending on their personal preference. With counts/s and counts/s2 users can easily specify a low level, precise value. RPM and RPS/s are higher level real-world units. Users can also benefit from moving at speeds below 1 count/s (because they are floating point parameters).
Once the move begins, we can plot the current position of the moving axis while the move is not complete. This requires two commands, “Check Move Complete” and “Read Position.” We use a LabVIEW whileloop to poll our motion board.
Experiment with different values of velocity and acceleration. Specifically, set a very low acceleration to see and hear the motor ramping up and down in speed. Also notice how quickly you can communicate with the board, thanks to the fast bus speed of our controller. You would not achieve this monitoring performance with a RS-232 controller.

## Slide 7
Add Another Axis
Duplicate all commands (Copy/Paste)
Start Motion twice
Notes: In only a few minutes, you have seen how to make a simple point-to-point move on one axis. We can set the trapezoidal profile values, and monitor the move until it was completed.
Now let’s introduce a second axis by simply copying and pasting the block diagram of one move. Also, we create separate copies of the position, velocity, and acceleration controls in order to set independent values.
If we set velocity and acceleration to be equal on both axes, but with different target positions, users see that the motion starts on both axes (roughly) at the same time. However, one axis completes its move before the other one does.
If we were moving a two axis stage or positioner, this is not acceptable to perform vectored moves. We would have to resolve our desired vectored move into component vectors, in terms of velocity and acceleration.
Even then, the move does not truly start and end at the same time, because the LabVIEW code is in a basic race condition and may be off by several milliseconds.

## Slide 8
Coordinate the Axes
Vector space
Position (x,y,z) =
Velocity = d /dt
Accleration = d /dt2
V
V
V
Notes: This graph illustrates the problem of no interpolation vs. linear interpolation, also called using a vector space.
The National Instruments motion interface supports onboard calculations of vectored information, causing motion on two (or three) axes to start and stop at exactly the same time (within microseconds).
To use a vector space, first configure the vector space (X,Y,and Z axes). These can be in any order, and any axis can be disabled for a 2D VS instead of a 3D VS.
Next, replace the individual “Read Position” functions with a “Read Vector Space Position.”
Users do not have to change Load Velocity, Load Acceleration, and Start Motion; and will intelligently operate on the vector instead of an individual axis.

## Slide 9
Move in an Arc
Load Circular Arc
  Radius
  Start angle
  Travel angle
Notes: Keeping in mind that our original goal was to move in a circular pattern, we now introduce the circular interpolation mode of the NI-Motion controller.
This is similar to linear interpolation in that it operates on a vector space; however instead of loading an (x,y,z) coordinate, you specify three parameters of a circular arc.
In the slide, radius corresponds to label #6, start angle is #4, and travel angle is #2. Using these three parameters you can define any circular arc.
Start angle must be between 0-360°, but the travel angle can be outside of this range for multiple arcs or reverse movement.

## Slide 10
Move in Two Arcs
Wait for Move Complete (LabVIEW level)
Load Another Arc
Notes: Recall that we are drilling a circular hole. In order to prevent an uneven cut, we should avoid dropping the drill bit at the edge of the path. This may cause splintering. So, we would like the profile to follow two arcs are shown above.
In the LabVIEW code, just add another “Load Circular Arc” command and another “Start” command. We also have replaced the while loop with a high level function called “Wait for Move Complete.” This is a blocking function that suspends itself until the move is complete.
Now, you can use the 2-axis position plot (virtual stage) to monitor your profile and ensure that the six parameters you have chosen for the two arcs are correct.

## Slide 11
Blend the Two Arcs
Blend Motion
Notes: To further reduce the risk of splintering, it would be nice to move smoothly through the two arcs instead of stopping motion after the first arc and then starting a new motion.
With blending, users can superimpose two trajectories between two independent moves, so that you can move from point A to B to C without stopping motion at B.
The charts in the slide illustrate a velocity profile with and without blending. In our code, we replace the “Start Motion” with a “Blend Motion.” Also, we replace the “Wait for Move Complete” with a “Wait for Blend Complete.”

## Slide 12
Conclusion
Using NI-Motion is EASY
NI-Motion is POWERFUL
Creating an application with NI-Motion is FAST
Notes: In a few short steps, we can create a motion profile that would take significant hardware effort in a traditional, proprietary system.
In a real machine, we could continue to increase the performance and functionality of this task. For instance, you could download all the code to the controller and have it execute onboard. Then, you could have it wait on a digital trigger. You could also have it stored in non-volatile flash ROM and automatically run after a power cycle. You could also run two of these tasks in parallel on a 4-axis controller, using the onboard, real-time, multithreaded operating system.
Designing a motion project with National Instruments motion control is easy, powerful, and fast.