## Slide 1: Real Time Programming with LabVIEW™ RT
John Limroth
Software Engineer
Thurs Aug 17
10:15-1:15 p.m., 1:45-4:45 p.m.
Exhibit (3G)

## Slide 2: Agenda
LabVIEW RT basics
Current RT hardware targets
Using LabVIEW RT
Advanced programming techniques
Software/hardware watchdogs
Application builder
Notes: LabVIEW RT Hands-on
<header>
<date/time>
Welcome to LabVIEW RT Hands-on session. The purpose of this course is to familiarize you with the important aspects of the product. While we might only be using the RT Series PXI systems, most of these exercises would work with the RT Series DAQ devices as well.
This three hour session begins by covering some basic principles and terms with real time systems and how LabVIEW RT fits into these systems. We then look at the current RT Series hardware targets that are supported and how to install/configure them. This is followed by some basic exercises using LabVIEW RT. Then we cover some advanced programming techniques to help you create more efficient real-time programs. After that, we look at how to create software and hardware watchdogs and finally we use the Application Builder to build executables.

## Slide 3: What is Real-time?
Real-time does NOT mean real fast!
Requires deterministic response
Windows does NOT guarantee determinism
Notes: LabVIEW RT Hands-on
<header>
<date/time>
To fully understand LabVIEW RT, we need to first focus on real-time and what it means in the control engineering industry. We briefly cover this topic. To find out more, please attend the “Introduction to Real-time” course by Greg Morrow.
What is a real-time application? The most essential component of real-time applications is deterministic responses. It does not mean that the application has to run real fast; instead, the application must respond to an event within a given interval. A good analogy to describe the need for a real-time system is driving a car. When you are driving, your eyes feed information to your brain and then your hands react to the information by steering the car. If you saw an accident on the side of the road, it might draw your attention away from the road and you could veer off course or get into an accident. With a real-time system, this would not have happened. A real-time system would constantly monitor the road at a given interval and only look at the accident if it had time between these intervals.
The drawback to Windows 9x/NT/2000 is that the operating system doesn’t deliver guaranteed determinism. It has too many software drivers that assert interrupts which distract the processor from the real-time operation.

## Slide 4: RT Hardware Architecture
P
Win OS
Motherboard
LabVIEW
P
RTOS embedded LabVIEW
Target motherboard
A/D
A/D
A/D
DAQ board
A/D
DAQ board
TCP/IP
connection
Notes: LabVIEW RT Hands-on
<header>
<date/time>
National Instruments LabVIEW RT is a software package that helps deliver real-time determinism with our RT Series hardware. To understand some of the features in the software, it is important to first understand the basic hardware architecture behind the RT Series hardware. To develop an understanding of the hardware, we show how LabVIEW RT enhances an existing LabVIEW/DAQ solution on a Windows 9x/NT/2000 operating system.
In the existing LabVIEW/DAQ on a Windows 9x/NT/2000 system, there is a computer running with the Windows OS and a DAQ board connected through a PCI bus. A real-time environment is added to this system with a second computer. With the RT Series DAQ boards, this is the PXI/PCI-7030 board; with the RT series PXI system, this is the PXI-8156B controller. Generally, this is an embedded computer without the monitor, keyboard, and mouse connections. Both embedded computers have a processor dedicated to running the Phar Lap real-time operating system. The data acquisition card(s) can then be connected to the real-time embedded computer for real-time performance. With the RT Series DAQ boards, one standard DAQ board is permanently connected to the 7030 board. With the RT Series PXI systems, multiple DAQ boards can be inserted to interact with the PXI-8156B controller. With the development environment on the Windows OS computer, code is downloaded from via a TCP/IP connection. In the case of the RT Series DAQ boards, this TCP/IP connection is emulated through the PCI bus, while the RT Series PXI systems can be connected through an actual Ethernet hub.

## Slide 5: LabVIEW RT Software
LabVIEW RT adds two extra components to regular LabVIEW
The RT Development System
  Part of it runs on host PC
  Programming and debugging LabVIEW code
The RT Engine
  Runs on target
  Executes embedded code
  Independent of host PC
Notes: LabVIEW RT Hands-on
<header>
<date/time>
To understand the software, we first consider the fundamental differences between LabVIEW RT and LabVIEW. LabVIEW RT adds two components to normal LabVIEW—the RT Development System and the RT Engine...
The primary functions of the RT Development System are to program and debug LabVIEW RT code, download programs to the RT Series hardware, and provide a default user interface for the embedded program. The RT Development System is a Windows 2000/NT/9x application that runs on the host computer. Programming with the RT Development System is almost the same as programming in the regular LabVIEW environment. The only difference is that the instead of downloading the code to the host computer and running it there, LabVIEW RT code is downloaded to the RT Series hardware and run. All the same debugging tools are still available including single stepping and probes.
The RT Engine runs on the processor of the RT Series hardware and executes embedded LabVIEW RT programs in real time. The RT Engine runs on the embedded processor of the RT Series hardware target. The RT Engine runs LabVIEW RT code in real time with the aid of the RTOS. Embedded LabVIEW RT applications run completely independent of the host computer and even survives a host PC failure. When the RT Development System runs code, it is downloaded to the RT Engine which then runs the program in real-time.

## Slide 6: Software Architecture
Three separate instances of LabVIEW
Notes: LabVIEW RT Hands-on
<header>
<date/time>
When you breakdown the software architecture even further, you see that there are actually three instances of LabVIEW RT. An instance consists of an executable being run on a processor. The first instance of LabVIEW RT (Instance A) is regular LabVIEW. This LabVIEW executable runs on the host PC and the VI code is also run on the host PC. The second instance of LabVIEW RT (Instance B) actually works with the third instance of LabVIEW RT (Instance C) to create one environment (the RT Development System). The second instance consists of an executable that runs on the host PC as well, but the VI code is not run on the host PC processor; instead, it is downloaded to the target processor and run by the third instance of LabVIEW RT. The third instance of LabVIEW RT consists of the emblview.exe (the embedded version of LabVIEW.exe) running on the target processor with the real-time OS. Instance B maintains the default user interface and all the debugging features while Instance C actually runs the code on the embedded processor. Instance B and C communicate in the background with TCP/IP and VI server so data can be sent between the VI and the front panel.
With the third executable running on the RT Engine itself, we can achieve real-time deterministic control independent of Windows OS even with Instance B connected to it. To obtain higher performance deterministic control, we can even detach Instance B and allow Instance C to run completely embedded. This would represent the RT Engine that we described earlier.

## Slide 7: Software Architecture
VI Server
TCP/IP
Peek/poke
RT development system
front panel
RT engine (diagram)
User Interface Thread
RT data acquisition
daughter card
DAQ VIs
RT engine (diagram)
RT data acquisition
daughter card
DAQ VIs
(Instance C)
Host LabVIEW application
on Windows PC
DAQ VIs
Plug-in
DAQ
board
(Instance A)
High-performance application
Target
Host PC
Application
development
(Instance B)
(Instance C)
Notes: LabVIEW RT Hands-on
<header>
<date/time>
Now let’s discuss both ideas together to see how the instances relate to the RT Development System and RT Engine. With the RT Development System, you can see that it is a combination of Instance B and Instance C. The communication between the two is done through a user interface thread in the background and doesn’t need to be programmed by the user. Therefore, the user can not control the priority that default user interface thread occupies or how efficient it behaves.
With the high-performance application, you launch everything in the RT Development System and then disconnect from the engine with the “Exit without closing RT Engines”. This leaves the RT Engine running by itself which is composed of Instance C. Then you can re-launch LabVIEW in regular host mode which won’t interfere with the RT Engine. You can then run a program that communicated to the embedded program on the RT Engine through the three forms of communication: VI Server, TCP/IP, and Peeks/Pokes. With this method, you replace the user interface thread with more efficient calls to transfer information between the embedded program on the RT Engine and the host PC application. In addition, you can add regular data acquisition components to Instance A of the system to perform non-real-time measurements.

## Slide 8: Agenda
LabVIEW RT basics
Current RT hardware targets
Using LabVIEW RT
Advanced programming techniques
Software/hardware watchdogs
Application Builder
Notes: LabVIEW RT Hands-on
<header>
<date/time>

## Slide 9: RT Series DAQ Devices
Hardware
  Processor
    486 133 MHz AMD chip
  Memory
    8 MB of DRAM for LabVIEW executable and NI-DAQ.dll
    1 kB of SRAM for shared memory
  Two user-defined LEDs
Notes: The RT Series DAQ devices consist of two boards permanently joined together. The first is the RT Series intelligent card (7030) that plugs into a PCI or PXI slot in your normal desktop computer running a Windows OS. The 7030 cards have the same basic components as regular motherboards, such as an embedded microprocessor (486 133 MHz AMD processor) and RAM (8 MB of DRAM). The RTOS, embedded LabVIEW executable (emblview.exe), and user program all run on the embedded microprocessor. The DRAM contains the emblview.exe as well as the NI-DAQ.dll and the user’s program.
There is also 1 kB of SRAM that is available for the user to peek and poke to the host PC. This 1 kB of SRAM is on the intelligent card, but is memory mapped by the host PC making it a quick and deterministic method of transferring data. There is no hard drive on the intelligent card which makes streaming to disk difficult. But, it can be done by transferring data back through the shared memory to the host program where it is then streamed to the host PC hard drive.
On these intelligent cards, there are also two LED’s that are useful for debugging purposes. They can be used as heartbeats.

## Slide 10: RT Series DAQ Devices
Form Factors
  Single product based on DAQ devices
    7030/6040E : 16 channel, 12-bit resolution, 250 kS/s
    7030/6030E : 16 channel, 16-bit resolution, 100 kS/s
    7030/6533 : 32 high-speed digital lines
  Single PCI slot
  Double PXI slot
  All SCXI and accessories supported
Notes: Currently, the different RT Series DAQ devices all use the same RT Series Intelligent Card (7030). This Intelligent card is permanently joined with one of our reliable data acquisition cards. The only thing connected to the RT daughter card is the RT intelligent card. So the only device that is capable of real-time performance is the RT daughter card. The list below shows that the flexibility of the available cards fits most applications. The PCI RT devices take one PCI slot while the PXI RT devices take two slots. All SCXI accessories are supported including the PXI/SCXI combo chassis.
7030/6040E (MIO-16E-4), 8/16 12-bit 250 kS/s AI, 2 AO, 8 DIG, 2 CNTR
7030/6030E (MIO-16XE-10), 8/16 16-bit 100 kS/s AI, 2 AO, 8 DIG, 2 CNTR
7030/6533 (DIO-32HS), 32 High speed DIG
Note: This card does not make everything in the desktop a real-time solution. If you purchase two 7030/6040E cards and use them together, you do not get one 32 input channel / 4 output channel real-time system. The cards would work independently from one another and would create 2 real-time systems each with 16 input channels and 2 output channels.

## Slide 11: Installing the RT Series DAQ Card
Installed and seen in MAX
RT intelligent card has one device number
Daughter card has separate device number
No test panels
Notes: LabVIEW RT Hands-on
<header>
<date/time>
The RT Series DAQ devices are easy to install and configure. After you have installed the necessary NI-DAQ driver (6.5.2 and later) you can insert the RT card in the desktop computer. The RT card appears just like normal DAQ cards in Measurement and Automation eXplorer (MAX). The RT Intelligent Card (PXI/PCI-7030) has a different device number than the RT Daughter Card. The RT Intelligent Card device number is used to perform computer operations such as TCP/IP or accessing the shared memory. The RT Daughter Card device number can be seen by double-clicking on the RT Intelligent Card. This device number is used to perform data acquisition.
Due to the present architecture of the RT Series DAQ devices, Test Panels do not currently work. To actually access the RT Daughter Card, you have to download a LabVIEW RT program to it. The quickest way to test the RT Series DAQ device is to run a quick test in LabVIEW RT with one of the simple examples.

## Slide 12: RT PXI Controller
General description
  Connected through Ethernet
  Pre-loaded RTOS and software
  Available with LV RT 5.1.2 and NI-DAQ™ 6.7
  PXI-8156B (233 or 333 MHz) must be configured
Communication
  Default user interface thread
  VI Server
  TCP/IP
Notes: With LabVIEW RT 5.1.2 and NI-DAQ 6.7, you can download LabVIEW RT code to the PXI-8156B/333MHz RT controller. The communication with the RT Series PXI controller is done through Ethernet. An RT Series PXI system must have the Ethernet connected to either a local subnet or through the direct CAT-5 cable to another computer to be configured. The PXI-8156B/333MHz RT arrives with the RTOS preloaded along with the other necessary LabVIEW RT software. The controller has been completely configured minus the IP address which varies from system to system.
You can also add the RT capabilities to a regular PXI-8156B controller. You can setup the regular PXI-8156B controller with an RTOS only hard drive but that would require formatting the hard drive. As another option, you can setup the controller to boot off a floppy disk into RT and maintain your Windows OS. In either situation you need to purchase a LabVIEW RT Runtime License for each regular PXI-8156B controller you reconfigure for RT.
The communication with the RT Series PXI controller can still be implemented through the default user interface, VI Server and TCP/IP. The only method not available is the shared memory.

## Slide 13: RT PXI Hardware
Supported hardware
  All PXI chassis without monitors
  All of regular NI-DAQ
  MXI-3
Configure your own system
Notes: With the support of the PXI Controller as an RT Series hardware target, came the ability to use our entire suite of PXI NI-DAQ hardware. All the PXI Chassis are supported, except the PXI-1020 and PXI-1025. Our PXI/SCXI combo chassis allow users to easily incorporate signal conditioning into the application. If you choose to use the PXI-1011, you need to modify the pxisys.ini file in the “National Instruments\Remote System Explorer\Install\Pxi” folder before configuring the PXI system. (It is setup for the PXI-1010 by default.) In addition to the chassis,all the regular NI-DAQ cards are supported. With the addition of MXI-3 we can even expand our system to fill two chassis with PXI NI-DAQ cards.
With the additional processing power of the Pentium processor in the controller, we can create faster, larger, and more customized real-time systems with the PXI platform.

## Slide 14: Remote System Explorer
Configures system
Installs or upgrades software
Creates utility disks
Lists installed software or hardware
Notes: The Remote System Explorer is a software that is bundled with LabVIEW RT 5.1.2. This allows users to see and configure their embedded PXI systems. With this utility, you can configure the IP address, the subnet that it belongs to, specify a gateway, or have the DHCP server assign all of this programmatically.
The Remote System Explorer also offers the option to create a boot disk that is used to configure the system. Other disks can also be created such as:
An Uninstall Disk—uninstalls all the RT software from the PXI controller
An IP Reset Disk—resets the IP of the PCI controller to 0.0.0.0
A Launch Settings Disk—disables any user programs that have been configured start at boot up.
A Format Hard Drive Disk—this formats the hard drive on the controller and instead installs just RT on it.
The user can also use this tool to install software on the controller and view the devices that are installed in that PXI chassis.

## Slide 15: Installation Procedure
Ensure the system is ready to be configured
  Must reside on same subnet
  Run the uninstall disk if questionable
Reboot system with floppy installed
  IP = 0.0.0.0
  Serial number is from Ethernet chip set
Create boot floppy (RT system specific)
Notes: LabVIEW RT Hands-on
<header>
<date/time>
To install RT on the system, it must be on the same subnet. The PXI system broadcasts messages on a network and the host computer with the Remote System Explorer must be on the same subnet to understand these messages. After it has been configured, the PXI system can be on another subnet connected through a gateway. The installation process has three basic steps.
Step 1. Create the boot floppy and insert it into the PXI system and turn it on or reboot it.
Step 2. Assign IP settings. You can configure the IP address manually or use the DHCP server to assign the IP Settings. To avoid problems with the dynamic allocation of IP addresses, work with your system administrator to configure the IP address manually.
Step 3. Install the software. You can install the software using the install script.
The system reboots by itself after steps 2 and 3. After this, it should be ready to run. When the system is rebooting, it will not show up on the Remote System Explorer window. You can press F5 to refresh the window.

## Slide 16: Installation Procedure (cont.)
RT system is ready
Reboot system
Upgrade/download software
  Choose install script
  Verify software versions
Reboot system
Assign IP address, name, password, etc
  Password is optional

## Slide 17: Exercise 1 – Configuring a PXI Controller

## Slide 18: File Structure
Viewable through Windows OS
Ph_exec.exe and ni-rt.ini in root directory
Embedded PXI File Structure (c:\ni-rt\)
  \system\ includes emblview.exe, ni-daq.dll, etc
  \startup\ includes boot up executables
Notes: The file structure installed by Remote System Explorer on the RT Series PXI Controller can be examined either with a standard FTP program or by rebooting the controller into the Windows OS. The ph_exec.exe and ni-rt.ini files are installed in the root directory (c:\) when the PXI controller is configured. The ph_exec.exe is the basic component of the RTOS. A directory (c:\ni-rt\) is created with two folders: system and startup. The system directory includes the emblview.exe as well as all the DLL’s. The startup directory includes any LabVIEW executables that the user has selected to run when the PXI system is booted up.

## Slide 19: Useful Tools in MAX
Remote DAQ Configuration
  Sets the properties of the remote DAQ boards
  Also available through Remote System Explorer
Remote Device Access
  RDA Server enabled on RT Series PXI controller
  Allows user to test the board with test panels
Notes: LabVIEW RT Hands-on
<header>
<date/time>
In addition to the FTP utility, there are two other helpful tools in MAX: Remote DAQ Configuration and Remote Device Access. Both tools treat the RT Series PXI controller as remote computers and ignore the fact that they are running an RTOS.
Remote DAQ Configuration allows the user to completely configure the settings of a DAQ board in the RT Series controller. These are the same settings as in the property pages for normal data acquisition devices except the user can not run the test panels or test the resources.
On the RT Series PXI controller, the RDA server is automatically enabled. This allows the user to connect to any device in the RT Series PXI system from the host machine and run the test panels on a that DAQ device. This is a great utility for verifying the function of the board.

## Slide 20: Exercise 2 – Troubleshooting RT Series PXI controller

## Slide 21: Agenda
LabVIEW RT Basics
Current RT hardware targets
Using LabVIEW RT
Advanced programming techniques
Software/hardware watchdogs
Application Builder
Notes: LabVIEW RT Hands-on
<header>
<date/time>

## Slide 22: Embedding a VI – Step 1
Select target platform
Host
RT intelligent card
PXI controller on network
Notes: LabVIEW RT Hands-on
<header>
<date/time>
We should begin by understanding the most common action in LabVIEW—how to embed a VI. When you start up LabVIEW RT, a prompt asks you to choose between the host PC development environment and the embedded PC development environment(s). As we discussed earlier, choosing the host PC development environment leads you straight into normal LabVIEW. Choosing one of the embedded PC development environments starts up the RT Development System with the specified RT Series hardware target and host PC. If you don’t see this prompt, you may need to make a change in your preferences under Edit>>Preferences>>Miscellaneous>>Prompt for Target Execution.
Notice that there is a reset button with the RT Series DAQ devices. This clears the RAM on the board and reload the emblview.exe and ni-daq.dll. This isn’t necessary on the RT Series PXI controller because everything there is loaded in static memory (hard drive). With the RT Series PXI controller, you only need to supply a password if you configure your system with a password.

## Slide 23: Embedding a VI – Step 2
Download code on target
Notes: LabVIEW RT Hands-on
<header>
<date/time>
After you have developed a program, you can simply click on the run button to download the code to the embedded processor. A popup window appears that shows the progress of the download. Notice that on the bottom left corner of the main window, the current hardware target is listed. Under the Operate menu there is also an option to download the application. This differs from the run button in that it only downloads the program and doesn’t run it. After the program is downloaded, it can be run multiple times without having to download it again. If you exit LabVIEW without closing the RT Engine and restart LabVIEW with the same RT Series hardware target, the program will still be downloaded. Whenever a change is made to the program though, it needs to be downloaded again. After the code is downloaded, it is switched to run mode. To make changes to the code, it must be switched to edit mode (ctrl+m).

## Slide 24: Embedding a VI – Step 3
Exit without closing RT Engine
Notes: LabVIEW RT Hands-on
<header>
<date/time>
Finally, you need to close out the RT Development System and leave the RT Engine running. This leaves all the programs you opened and ran still downloaded and running. This step is not necessary if you are developing the program and want to debug the code. The only drawback to skipping this step is that the performance of the embedded program suffers since the default user interface thread is eating up processor time.

## Slide 25: Exercise 3 – Download a VI

## Slide 26: Shared Memory
Incremental read/write – high-level continuous transfer of array of singles
Read/write VIs – incorporates a flag (8-bit word) to make reading and writing more efficient
Low-level peeks and pokes – basic building blocks for other levels
Notes: LabVIEW RT Hands-on
<header>
<date/time>
If you choose to fully embed the real-time program with just the RT Engine but want to maintain some form of user interface, you can use the shared memory on the RT Series DAQ devices. This is the most deterministic method of transferring data to and from the board. There are three separate layers of protocol with shared memory, but they all consist of the same basic functions.
The highest layer consists of two VI’s: RT incremental single read.vi and RT incremental single write.vi. These transfer arrays of data in smaller packets over time. The second layer consists of VI’s that actually create flags in the shared memory along with the data memory block. They use this flag to determine when new data is there and when to fetch new data. This is only efficient when transferring data larger than 1 byte and when the data doesn’t change frequently.
The lowest layer makes very basic register level calls. There are two sets of these, one with error clusters and one without. These VI’s are the building blocks for the other layers.

## Slide 27: VI Server
Similar to normal VI Server
Different machine name that corresponds to RT Series Intelligent Card device number (DAQ::1)
Requirements
  VI must be loaded in memory
  LabVIEW RT must be running on target
Notes: LabVIEW RT Hands-on
<header>
<date/time>
VI server can also be used to communicate between the host PC and embedded target in the same way that it is used to communicate between two instances of LabVIEW on two computers. Just like normal VI server, a computer name is needed. With the RT Series DAQ device, this computer name is dependent on the device number of the RT Intelligent Card such as DAQ::1. With the PXI controller, just the IP address is necessary.
The subtle differences in VI Server with LabVIEW RT is that the VI must be loaded into dynamic memory with the RT Series DAQ devices because there is no hard drive to reference. On the other hand, with the PXI system, the user can save VI’s on the controller and access those instead. Also, the LabVIEW executable must be running on the target. We talk about how to overcome these challenges next.

## Slide 28: Download Application
Loads VI into dynamic memory without running it
VI is now ready to run (Download bar will not appear)
Notes: LabVIEW RT Hands-on
<header>
<date/time>
Loading the program into dynamic memory (DRAM) is relatively simple. The Operate>>Download Application completes this process. This can also be done by running the program once. On the host PC side, a strictly typed refnum or virtual instrument refnum is needed. For a deeper understanding of these topics, you can look at the online documentation.

## Slide 29: LabVIEW RT Running on Target
Important aspect of VI Server
Exit without closing RT Engine VIs
  Keeps LabVIEW RT open
  Closes user interface
Notes: LabVIEW RT Hands-on
<header>
<date/time>
To perform VI Server, you must find a way to keep LabVIEW open on the target. From the previous slides, we know how to download a program to RAM. To keep the program running on the target, you have to use the Exit without closing RT Engine VIs option. This keeps the embedded LabVIEW program running and the VI remains in memory.

## Slide 30: Exercise 4 – Using VI Server

## Slide 31: TCP/IP with LabVIEW RT
Similar to regular LabVIEW
Requires different machine names to correspond to Intelligent DAQ Cards (DAQ::1)
Used to communicate large chunks of data
Not deterministic
Notes: LabVIEW RT Hands-on
<header>
<date/time>
TCP/IP can also be used with LabVIEW RT. Once again, using TCP/IP in LabVIEW RT is very similar to using it between two regular LabVIEW applications. The subtle difference is the machine name where it is DAQ::1 for the RT Series DAQ device or the IP address of the RT Series PXI system. TCP/IP is ideal for transferring larger chunks of data but this hinders the determinism of the system. The user must keep these TCP/IP operations on a separate thread with a lower priority to maintain determinism in the time critical thread.

## Slide 32: Exercise 5 – Using TCP/IP

## Slide 33: Agenda
LabVIEW RT basics
Current RT hardware targets
Using LabVIEW RT
Advanced programming techniques
Software/hardware watchdogs
Application Builder
Notes: LabVIEW RT Hands-on
<header>
<date/time>

## Slide 34: Programming Tips – Timing
Keep unnecessary computations outside of the time-critical loop
Keep configuration VIs outside of the loop
Sleep mode helps maintain loop rates while allowing other loops to share time
Notes: With all real-time systems, there is an amount of error. This error is called the jitter in the system. Jitter is a measure of how inconsistent the system is by calculating the difference between an individual loop interval and the ideal loop interval. We focus on how to reduce this jitter and improve the loop rates of the program as well.
In terms of programming, creating efficient code usually results in a more stable real-time program. Avoid having unnecessary computations inside the time-critical loop. You want the least amount of CPU time to be taken while running your real-time code.
Keep your configuration VIs outside of the loop. This is basic good programming practice, but for a LabVIEW RT program, this is even more critical.
Timing your loops is critical as well. When you set a thread for time-critical priority, it’s important that you allow the loop to “Sleep” so that other CPU tasks are allowed to take place. You do this using the Wait Until Next msMultiple.vi function. We cover this further when talking about priorities and multithreading.

## Slide 35: Programming Tips – Memory
Determinism
  Pre-allocate arrays
  Avoid shared resources
Performance
  Cast data to the proper type
  Inplaceness
  Global Variables
Notes: While increasing timing efficiency is very beneficial to a real-time program, there are other memory intensive operations that can induce jitter. In general, memory allocations within the time-critical loop are known to affect the deterministic properties of a LabVIEW RT program. Reducing the amount of memory used by an application also increases the performance of the program.
You must pre-allocate your arrays outside of the loop if you want to be deterministic. When you use the Build Array.vi inside of a loop, every time data is written to the array, a memory allocation is made. Shared resources such as the same subVI between threads can induce jitter. If one thread is using that subVI, it won’t allow the other thread to use that same subVI causing the second thread to wait and throw off timing. Making the subVI reentrant should solve this problem.
Try to cast data to the proper data type. Every time LabVIEW has to do a type conversion, either implicitly or explicitly, a copy of the data buffer is made in memory to retain the new data type after the conversion. Use the smallest data type possible and try to convert data being placed in an array before the array is built. A function’s output buffer reuses an input buffer if the output and the input have the same data type, representation, and in the case of arrays, the same structure and number of elements. This ability for a function to reuse buffers is called inplaceness. Use it to reduce the number of memory allocations in a program.. For each global variable used in a program, an extra copy is placed in memory on program start up. This causes extra memory allocation as well.

## Slide 36: Exercise 6 – Reducing the Jitter in a LabVIEW RT Program

## Slide 37: Single-Threaded LabVIEW
Computer
Thread
User Interface
Loop
Exec( )
Co-routines
Notes: LabVIEW RT Hands-on
<header>
<date/time>
Multithreading and priorities in LabVIEW RT are very crucial to maintaining a real-time system. A LabVIEW VI consists of an execution system, Exec(), that cooperatively multitasks the parts of a program. Portions of code that are independent of each other can therefore cooperatively share a processor to be more efficient. A cooperative system switches tasks at predefined locations that are explicitly compiled into the code. LabVIEW puts a possible cooperative switch at the end of each nested block diagram.
In contrast, “preemptive” multitasking is implemented between OS threads on a system that provide them. In preemptive multitasking, a task switch can happen between any two machine instructions and the program does not need to create any code to enable the switch.
In single-threaded LabVIEW configurations, LabVIEW uses only one OS thread to implement its entire system. Within that thread, layers of “cooperative” balancing are implemented – between clumps of LabVIEW code and the handling of user interface events (keyboard, mouse etc.)
*For those not familiar with threads, a thread is an independent sub-program which runs within a program or process. LabVIEW is a process, its threads run independently within it. Threads can access all of the address space of the owning process, so all global variables are shared. This sharing is a very powerful and useful thing, but it is also a source of very difficult to understand bugs and problems.

## Slide 38: Multithreaded LabVIEW
Exec( )
Thread
Computer
UI Loop
Exec()
Thread
Exec( )
Thread
Exec( )
Thread
Messages
Notes: LabVIEW RT Hands-on
<header>
<date/time>
Multithreaded LabVIEW split the program into a single UI thread (which still contains an Execution System) and multiple execution threads that use Exec() as their main thread procedure. The separate execution threads are swapped by the OS preemptively. Within themselves, they still perform LabVIEW-style cooperative multitasking.
The Exec() loops in multi-threaded LabVIEW never return (until LabVIEW quits running). When there is no code executing, they sleep while waiting for the OS to tell it to do something. Threads cost some system resources to allocate, but when they are asleep, they do not take processor cycles. So idle execution threads do not take performance away from the rest of the running system.

## Slide 39: LabVIEW RT – Target System
Exec( )
Thread
RT Computer
Communication
Loop
Exec()
Thread
Exec( )
Thread
Exec( )
Thread
Messages
TCP/IP
Notes: LabVIEW RT Hands-on
<header>
<date/time>
The split architecture of multithreaded LabVIEW that separated the user interface from its execution systems was ideal for LabVIEW RT. The architecture of the LabVIEW RT system on a RT Series hardware target is much the same as multithreaded LabVIEW, except here the role of the user interface thread is played by the “Communication” thread.
In the dedicated environment of the RT Series hardware target, no other applications are executing, no unused drivers or interrupts are active, and multithreading support has been specifically built to be quick and deterministic in switching threads.
Here we can see the default user interface thread interacting in a multi-threaded system. Had we left a program as a single-threaded system, it would have greatly effected the performance of our real-time system.

## Slide 40: LabVIEW RT – Deployed System
Host PC
RT Series
hardware target
Thread
Exec()
Thread
Exec()
Thread
Exec()
Thread
Communication
Exec()
-Shared
memory
-TCP/IP
-VI
server
Thread
Exec()
Thread
Exec()
UI Loop
Exec()
Thread
Thread
Exec()
Notes: LabVIEW RT Hands-on
<header>
<date/time>
Using one of several communication techniques, a “regular” LabVIEW application can work in conjunction with a LabVIEW RT application. In this case, the default user interface for the VIs running on the RT Series hardware target is closed. LabVIEW on the host PC can have normal LabVIEW panels and displays. You can use the “Call By Reference” feature of VI Server to implement distributed execution (this consists of running parts of an application on different computers). LabVIEW RT can perform all of the necessary VI Server activities to make the RT board a member of such a distributed execution system and run real-time VIs whose execution is coordinated by a different host LabVIEW.

## Slide 41: Understanding Priorities
Normal priority
  Allows the CPU to be shared
Time-critical priority
  100% of CPU time
  Sleep mode is very important
Subroutine priority
  Highest priority level
  Releases thread only when done
Notes: LabVIEW RT Hands-on
<header>
<date/time>
With the multithreading architecture of LabVIEW, setting priorities applies to an entire thread. With the user interface already occupying a thread, we must be careful in how we write our programs. In LabVIEW, events are prioritized with events with higher priority threads preempting lower priorities. This means that if a higher priority thread wakes up while a lower priority thread is executing, the higher priority thread will kick off the lower priority thread from the processor. Threads with the same priority are scheduled in a round-robin manner. This is true for everything except the time-critical priority which doesn’t release the thread unless you program a sleep mode into the thread.
It is important not to run time-critical tasks on the normal priority thread. However, if your VI priority is set to time-critical priority without a sleep mode, the user interface thread may be starved of processor time causing your front panel to appear locked up. Adding a wait time to the diagram insures determinism by putting your block diagram “to sleep” and allowing the user interface thread to update the front panel.
Note: The only way to achieve “hard real-time” determinism is to have the VI priority set to time-critical.
Subroutine Priority is actually the highest priority level. When you give a VI subroutine priority, it takes control of the thread in which it is running. No other VI can run within this thread. If you give a sub VI subroutine priority in your time-critical thread, no other tasks are performed within that thread. If the time-critical thread has a user interface component, then no updates are made to the UI while the sub-VI is running. This priority level can be used to allow a VI to run most efficiently.

## Slide 42: Exercise 7 – Understanding Priorities

## Slide 43: Agenda
LabVIEW RT basics
Current RT hardware targets
Using LabVIEW RT
Advanced programming techniques
Software/hardware watchdogs
Application Builder
Notes: LabVIEW RT Hands-on
<header>
<date/time>

## Slide 44: Watchdogs
Hardware or software mechanism that checks the status of the embedded system
Increases the system’s robustness
Generally requires a low overhead
Notes: LabVIEW RT Hands-on
<header>
<date/time>
Watchdogs are important in real-time systems. They can be implemented with software or hardware. The purpose of the watchdog is to alert the user that the embedded system has malfunctioned. This can be used to restart the system if necessary or shut down the peripheral system as well. There is no standard method of creating a watchdog, but the simplest method with the lowest overhead is usually the best.

## Slide 45: Software Watchdog
Software watchdog can use the shared memory
One side writes a value that is constantly changing
Both host PC and embedded PC can implement watchdogs
Host
PC
1K
Embedded
PC
(?)
(?)
Notes: LabVIEW RT Hands-on
<header>
<date/time>
The software watchdog can be created through the shared memory on the RT Series DAQ devices. The easiest way to perform this is to write a constantly changing value such as the iterator in a while loop to one location in the shared memory. Then the host PC can read this value to verify if the value has changed since the last iteration. This can be reversed as well so that the embedded system knows when the host PC has shut down.

## Slide 46: Hardware Watchdog
Embedded
PC
(?)
External
System 1
External
System 2
(?)
CTR/DIO
Digital/counter lines can be used to trigger other systems
Notes: LabVIEW RT Hands-on
<header>
<date/time>
The digital/ counter lines can be used to create a watchdog as well. Since these are not analog values, a different method must be implemented where one side can continually toggle a line while the other side reads it. This method of a hardware watchdog can be implemented with our RT Series DAQ devices and RT Series PXI system as long as the system has a DAQ board with a counter/timer or digital line.

## Slide 47: Built-in Hardware Watchdog API
Extra hardware counter/timer
Continuously counts down
Software continually resets the counter
Can be configured to take action
  Reset PXI System
  Set Occurrence
  Trigger
Notes: LabVIEW RT Hands-on
<header>
<date/time>
On the PXI-815xB controller, there is a built-in hardware watchdog timer. With LabVIEW RT 5.1.2, the watchdog API can be manipulated quite easily. It is simply a counter/timer that is continuously counting down. The software must periodically “whack” or acknowledge the watchdog to reset the timer to its initial count. If the software misses a “whack” and the counter reaches zero, then the hardware can be configured to take certain action. Currently with the hardware, this can either reset the chassis, trigger a PFI line or set a software occurrence.

## Slide 48: Exercise 8 – Implementing a Hardware Watchdog

## Slide 49: Agenda
LabVIEW RT basics
Current RT hardware targets
Using LabVIEW RT
Advanced programming techniques
Software/hardware watchdogs
Application Builder
Notes: LabVIEW RT Hands-on
<header>
<date/time>

## Slide 50: Application Builder
Usually targeted to host PC
Extra RT options
  Show RT target selection dialog
  Quit RT boot application after downloading
Notes: LabVIEW RT Hands-on
<header>
<date/time>
The LabVIEW RT Application Builder has some subtle differences from the regular LabVIEW Application Builder. In addition to creating normal LabVIEW executables with LabVIEW RT Application Builder, you can download these executables to any of the RT Series hardware targets. You can run Application Builder on the host or RT series PXI target. (Due to limited memory, you should avoid targeting the RT Series DAQ devices to run Application Builder.)
The tabs appear to be the same except there are two RT specific options under the “App Settings” tab. The first option allows the user to disable the hardware target selection device when it launches and the second quits the RT boot application after downloading. This second option is equivalent to opening the executable, targeting a RT Series hardware target and then using the “Exit without closing RT Engines”

## Slide 51: Targeting to the PXI Controller
Able to save executable to disk
Remove serpdrv
“App Settings” Tab is disabled
Notes: LabVIEW RT Hands-on
<header>
<date/time>
When you target to the RT Series PXI controller and run Application Builder, there are some more differences. If you are targeted to the RT Series PXI controller, you can save the executable to the PXI hard drive instead of the host PC hard drive. This allows you start the executable automatically on the PXI controller without any interaction on the side of the host PC.
Note: If you plan on using the serial port in the executable, you also need to remove serpdrv from the files since the PXI controller already has a different version that works for Phar Lap.
Finally, notice that the “App Settings” tab is disabled, since these applications are embedded and have no connection to the host computer, the options there are unimportant.

## Slide 52: Networked Preferences
Application Builder (when connected to TARGET)
  Default name “Startup.exe” (C:\ni-rt\startup)
  NETWORKED PREFERENCES->RT Target: Miscellaneous
    Install path
    Name must be 8.3
Notes: LabVIEW RT Hands-on
<header>
<date/time>
With the networked preferences on the RT Series PXI controller, you can configure the controller to automatically start up a LabVIEW RT executable at boot up. To do this you need to first save the executable to the controller. The default name of the startup application is Startup.exe, but can be changed. The name can be changed under the RT Target: Miscellaneous tab.

## Slide 53: Command Line Arguments
Used to alter execution
  Ex: c:\mybuiltapp.exe –target DAQ::1 –reset –quithost
 | RT Series DAQ device | RT Series PXI system
-target | DAQ::1 | 130.164.48.51
-reset | Resets device | not available
-quithost | Exits without closing RT Engines | Exits without closing RT Engines
Notes: LabVIEW RT Hands-on
<header>
<date/time>
You can also use command line arguments with LabVIEW RT executables to enhance their flexibility. These command line arguments can explicitly specify a certain target for the executable, reset the DAQ device, or disconnect from the target afterwards. These options can be combined to achieve a specific download sequence for your executable. The example command line “c:\mybuiltapp.exe –target DAQ::1 –reset –quithost“ would download mybuiltapp.exe to the RT Series DAQ device with device number 1 after resetting the RT Series DAQ device and then disconnects the host PC. You can use these command lines in batch files and place that batch file in the startup folder on your host PC to automate the application download process.

## Slide 54: Exercise 9 – Using Application Builder

## Slide 55: End of LabVIEW RT Hands-on Questions?