## Slide 1: Building an Integrated Measurement System
Darren Halla
Applications Engineer
Fri Aug 18
10:15 a.m.-1:15 p.m., 1:45-4:45 p.m.
Exhibit (3G)

## Slide 2: Course Agenda
I. Course overview
A. Goals/non-goals
B. System overview
C. Demo
BREAK
II. Theory/exercises
A. Configuration file VI’s
B. Synchronization
C. VI server
D. Multithreading
BREAK
III. System integration
A. State machine
B. Continuous display updates
C. Synchronization: semaphores/occurrences
Notes: The first session of this short course in system integration is an introduction to the tools used in the circuit test system to effectively combine data acquisition, signal conditioning, image acquisition, and motion control into an efficient unit. A complete description of the circuit test system will be provided, in addition to recommendations on effective software integration techniques.
The second session of this course covers the theory and specific software tools available to effectively integrate a system. Exercises detailing the usage of these tools are performed for added comprehension.
Finally, in the last segment, a demonstration of how these tools work together is given to tie together the information and theories presented in the class.

## Slide 3: Course Overview

## Slide 4: Goals For Course
    Basic LabVIEW instruction
    Basic data acquisition, motion, and image acquisition instruction
Non-Goals For Course
    Introduce some of the integration capabilities in LabVIEW™ by simultaneously performing DAQ, motion and IMAQ™ in an integrated measurement system
    Develop a working automated circuit test system
Notes: This course is designed as an introduction to the theories of software integration using National Instruments data acquisition, motion, and vision products. As this course is intended to delve into the theory behind software integration with LabVIEW, a basic familiarity with LabVIEW and National Instruments measurement products may be necessary to achieve the full benefit.

## Slide 5: Benefits of Software Synchronization Tools
Sharing resources through software synchronization tools requires less hardware
System portability and adaptability greatly increased with software tools such as Configuration File VI’s
Execution control can be manipulated through software to achieve optimum performance
Programmatic control of LabVIEW and VIs
Notes: Many benefits to system integration exist, including the protection of shared resources, such as an analog-to-digital converter, with synchronization tools. Also, with the Configuration File VIs, applications can be easily altered without major reconfiguration. Using tools such as multithreading, execution control can be manipulated to achieve the most effective performance.

## Slide 6
Integrating DAQ, IMAQ, and Motion
Project overview – circuit test system (CTS)
Issues encountered during integration:
  Coordination between system monitoring and functional circuit testing
  Timing of image acquisition and motion
  Portable configuration information
Notes: This presentation is in line with the theme that National Instruments data acquisition products provide you the ability to “measure anything and automate everything.” One engineering challenge while developing measurement and automation systems is to integrate different systems together in a complete solution.
To present the topic of integrating National Instruments measurement and automation products we developed a circuit testing demonstration. While developing this demonstration we ran into a few specific software integration issues which are the focus of this presentation. These issues are:
1. Coordination between system monitoring and functional circuit testing
2. Timing of image acquisition and motion
3. Portable configuration capability

## Slide 7: Circuit Test System (CTS)
Objective – verify circuit manufacturing through automated testing
Solution – integration of data acquisition (DAQ), signal conditioning (SCXI), image acquisition (IMAQ), and motion control into an automated test system
Notes: The objective of this demonstration is to test a unit under test (UUT) for manufacturing flaws. The three tests are to:
1. Verify chip placement
2. Verify FIFO chip functionality
3. Verify the gain setting of an operational amplifier
In addition to these tests the serial number of the UUT is read (using optical character recognition) and displayed.
This demonstration uses the SCXI signal conditioning modules to constantly monitor the vital signs of the system, such as:
  Ambient temperature
  Motor temperature
  DC Voltage
  DC power (DC power supplies for the stepper motor and camera as well as the two fans)

## Slide 8: Circuit Test System (CTS)
Camera
Motor
UUT
PC-based acquisitions
System vital signs
Notes: Here is the basic system. A stepper motor positions a plate of units under test. A camera continuously monitors the UUTs on the plate and at the appropriate time analyzes the image of the UUT for the presence of a specified chip. It also reads the serial number on the UUT. In addition, the data acquisition hardware tests the FIFO chip and verifies the gain of the operational amplifier.
As the above-described system is busy positioning and analyzing the circuit, the SCXI signal conditioning hardware continually monitors the system.

## Slide 9: Software Overview of System
Initialization, display & synchronization
Motion
DAQ
IMAQ
SCXI
DDS
(high)
(low)
(low)
(normal)
[DATA]
[DATA]
(Occurrence)
(Semaphore)
State machine

## Slide 10: Hardware Components
    PXI-8156B – Controller
    PXI-1010 – Chassis
    PXI-7314 – Open loop stepper
    PXI-1408 – IMAQ
    PXI-6533 – DIO
    PXI-6070E – MIO
Notes: PXI-8156B: Controller
- 233 MHz, 333 MHz processors, Up to 256 MB RAM
- 2 serial, 1 parallel, 1 USB port, 1.44 MB floppy drive
- 0BaseT Ethernet and GPIB (IEEE 488.2) interface
- 4 GB hard drive, minimum
- Super VGA with 2MB RAM
- PS/2 keyboard and mouse connectors
PXI-1010: Chassis
- Complete solution for demanding signal conditioning applications
- Combines computer, peripheral modules, and signal conditioning in a single chassis
- 8 slots for PXI and Compact PCI modules
- 4 slots for SCXI signal conditioning modules
- Integrated interface between PXI and SCXI backplanes
PXI-7314: Open Loop Stepper
- General-purpose stepper control
- Open and closed-loop versions
- Microstepping and robust motion I/O
- 3U Compact PCI motion controller
- Real-time motion control processor
PXI-1408: IMAQ
- Four video inputs for standard and nonstandard sources
- Monochrome and StillColor acquisition
- Variable scan rate (5 to 20 MHz); Four external trigger/digital I/O lines
- Onboard programmable region of interest
- Onboard pixel decimation

## Slide 11: Hardware Components (cont.)
    SCXI-1102 – 32-channel thermocouple amplifier
    SCXI-1121 – 4-channel isolation amp with excitation
    SCXI-1120 – 8-channel isolation amplifier
    SCXI-1303 – Terminal block
    SCXI-1321 – Terminal block
    SCXI-1327 – Terminal block
Notes: PXI-6533: DIO
- NI-DAQ driver with DAQ channel wizard for reduced configuration
- Available for PXI/CompactPCI systems
- 32 (5 V/TTL) digital I/O lines
- Pattern I/O up to 10 Mbytes/s; Handshaked I/O up to 64 Mbytes/s
- User defined power up state; start and stop triggering; pattern and change detection
PXI-6070E: MIO
- Available for PXI/CompactPCI systems
- Up to 16 analog inputs; 12-bit resolution; 1.25 MS/s sampling rate
- Two 12-bit analog outputs; 8 digital I/O lines; two 24-bit counters
- Calibration certificate included for NIST traceability
- NI-DAQ driver with DAQ channel wizard for reduced configuration
SCXI-1102: 32-Channel Thermocouple Amplifier
- For temperature measurement applications using thermocouples
- 32 channels, up to 333 kHz scanning rates
- 2 Hz lowpass filter on every channel
- Programmable instrumentation amplifier on every channel
- Overvoltage protection to +/- 42V
SCXI-1121: 4-Channel Isolation Amp with Excitation
- For RTDs, strain gauges, and thermistors with isolation
- 4 channels, up to 333 kHz scanning rates
- Gain Settings of 1 to 2,000 (per channel)
- 250 Vrms working isolation per channel
- 4 Hz or 10 kHz lowpass filter configurable on each channel
SCXI-1120: 8-Channel Isolation Amplifier
- For low-voltage, high-voltage, current inputs and thermocouples requiring isolation
- 8 channels, up to 333 kHz scanning rates
- Instrumentation amplifier on every channel
- 4 Hz and 10 kHz low-pass filter settings on each module
- 250 Vrms Isolation per channel

## Slide 12: Hardware Components (cont.)
    SCXI-1180 – Feedthrough panel (breadboard)
    SCXI-1180 – Feedthrough panel (breadboard)
    SCXI-1180 – Feedthrough panel (breadboard)
    Custom box – Houses motors, power supplies, wiring, UUT
    UUT – FIFO chips, Op amps, serial number
    light intensity sensor
Notes: SCXI-1303: Terminal Block
- Recommended for high-precision thermocouple temperature measurement applications
- Shielded for quick, convenient signal connections
- Mounts to front of SCXI module
- Recommended for use with the SCXI-1100/1102/1102B/1102C
- Isothermal construction minimizes errors caused by thermal gradients
SCXI-1321: Terminal Block
- Manual bridge offset nulling and software controllable shunt calibration
- For applications using strain gauges, RTDs, or thermistors
- Shielded for quick, convenient signal connections
- Mounts to front of SCXI module
- For use with the SCXI-1121
SCXI-1327: Terminal Block
- For measuring signal levels up to 250 V
- Shielded for quick, convenient signal connections
- Mounts to front of SCXI module
- For use with the SCXI-1120/1120D/1121
- Extend signal input range to 250 Vrms or 250 VDC; switch configurable per channel
SCXI-1180: Feedthrough Panel (3)
- Cables directly to breadkout connector or SCXI cable assembly
- Extends unconditioned I/O signals from plug-in data acquisition board to front of SCXI chassis
Custom Box:
Houses Motors, Power Supplies, Wiring, UUT
UUT:
FIFO Chips, Op Amps, Serial Number

## Slide 13: Software Tools
Development software – LabVIEW 6i
DAQ driver software – NI-DAQ™ 6.8
IMAQ driver software – NI-IMAQ 2.2
Vision software – IMAQ Vision 5.0
Motion control driver SW – Value Motion™ 5.0
Internet - distributed – NI DataSocket™

## Slide 14: Follow Good Software Development Practices
Top-down verses bottom-up
Define tasks for modularity
Determine the main data flow of the application
  Critical paths and priorities
Determine dependencies between modules
Standardized junctions for inter-module communication
Remember to design with the future in mind!
Notes: When developing large systems that require integrating various sub-systems following good software development practices is imperative.

## Slide 15: Demonstration
Circuit Test System

## Slide 16: Theory / Exercises

## Slide 17: How to Integrate Your System
Initialization
  configuration File VIs
Execution control
  state machine
Synchronization
  occurrences
  semaphores
VI server
Multithreading
DAQ
SCXI
Motion
IMAQ
Notes: Our system is made up of four main components: IMAQ, SCXI, DAQ, and Motion. To get each component working is only half the battle. Getting all four components to work together requires good knowledge of LabVIEW programming. As we learn how to integrate our system, we will focus on the following advanced LabVIEW programming topics: Configuration File VIs, State Machines, Occurrences, Semaphores, VI Server, and Multithreading. In this section we focus on the programming techniques we used to integrate our system. Later we will see where these techniques were applied in our system, but for now we will just focus on the techniques themselves.

## Slide 18: Initialization
Configuration File VIs
  Allow control over initial state of your system
  Create a platform-independent file
Notes: With any system, make sure you have a known initial state. The larger the system, the more parameters you have to configure at start up. You also want the ability to easily change your initial state in the event that the system changes (such as, you change the device numbers for your hardware). An easy way to accomplish this is with the Configuration file VIs in LabVIEW. The Configuration File VIs are found under the File I/O sub-palette. The Configuration File VIs allow you to create a platform independent file that can be read from (to set the state of your system), or written to (to record the current state of your system).

## Slide 19: Configuration File VIs
Can read or write keys to the file
Keys are put into sections
Key values can be Boolean, DBL, I32, U32, string, or path
Notes: The configuration file created is very similar to an INI file. You can create different sections for your file. For instance, in our system we have a section for DAQ, SCXI, IMAQ, and Motion. Within each section you create keys that can be either a Boolean, DBL, I32, U32, string, or path. In the example above we have written a configuration file that has a section titled DAQ, with an I32 key called Device that has a value of 1, and a string key called Channel that has a value of 0,1.

## Slide 20: Execution Control
State machine
  Allows control over the order of execution of your program
  Used often with a menu button interface
  Consists of:
    While loop
    Case structure
    Shift register
  Each “state” is a case in the case structure
  Shift register tells what “state” to go to next
Notes: Often, it is desirable to control the flow of your program in a non-linear manner. For instance, suppose you have a program with stages A (A is your default stage), B, C, and D. The program executes stage A if nothing else is happening, and stage B, C, or D based on a user input. After the user chooses stage B, we want the program to go back to stage A and wait for another user input. However, when the user chooses stage C, we want to execute stage C and then go directly to stage D without returning to stage A to wait for another user input. Sounds complicated? It can be done rather simply with a state machine. A state machine consists of a while loop, a case structure, and a shift register. The case structure consists of all the different states you want to have. In the case of our example we would have four. The shift register tells you what case to go to next. You learn how to build a simple state machine in the next exercise.

## Slide 21: State Machine
Notes: Above is an example of a simple state machine. The front panel consists of a Boolean cluster and a power button for the while loop. Before any buttons are pressed, the state machine is in the default state. In the default state, the state machine waits to see if one of the buttons has been pressed. When a button is pressed the state machine will go to the case of the case structure corresponding to that button. The value that is passed out of the case will tell the state machine where to go next. In the example above if the State 0 button or State 2 buttons are pushed case 0 or case 2 respectively will execute and the state machine will return to the default case (-1). However, if the State 1 button is pushed, case 1 will execute, case 2 will execute, and then the state machine will go back to the default state (-1).

## Slide 22: Exercise
State Machine

## Slide 23: Synchronization
Occurrence
  Allows part of your diagram to sleep until the occurrence is set
  Optimizes your system by eliminating the need to poll a variable in a while loop
  Software trigger
  Three VIs:
    Generate occurrence
    Wait on occurrence
    Set occurrence
Notes: Most often, everything doesn’t have to happen at once in your system. In fact, you may want a portion of your system to begin execution after a particular event. You can accomplish this in LabVIEW with the use of an occurrence. An occurrence is similar to a software trigger. It allows part of your diagram to sleep until the occurrence is set (triggered). The Occurrence palette can be found under Advanced>>Synchronization. You use Generate Occurrence to create the occurrence (similar to a refnum). Then you pass that to Wait on Occurrence, which will force the portion of your VI that Wait on Occurrence is in to pause until Set Occurrence triggers the occurrence. Using an occurrence frees up your system resources, because the portion of your diagram waiting on the occurrence will not be polled – it simply pauses until the occurrence is set. Without occurrences you would have to poll a local or global variable in a loop, thus occupying system resources. You learn how to use an occurrence in the next exercise.

## Slide 24: Exercise
Occurrence

## Slide 25: Synchronization
Semaphore (Mutex)
  Allows you to limit access to shared resources (global variable, hardware and so on)
  You define the number of tasks that can acquire the semaphore at a time
  Other tasks have to wait for semaphore to be released before they can execute
Notes: You will often have two or more portions of your code in your system that need to access the same resource. Two good examples of shared resources are global variables and external hardware. In either case, it is undesirable for either of those resources to be accessed in two places at the same time. To prevent this, you can use a semaphore in LabVIEW. The Semaphore sub-palette is located under Advanced>>Synchronization. You can define the number of tasks that can acquire the semaphore at a time. Let’s say we only let one task acquire the semaphore. Once a task has acquired the semaphore, any other task that tries to acquire the semaphore will be denied until the task that has the semaphore is done. Then the semaphore is released and a new task can acquire the semaphore. You learn how to use a semaphore in the next exercise.

## Slide 26: Exercise
Semaphore

## Slide 27: VI Server
  Allows programmatic access to LabVIEW objects
    Previously only available through menu items, preferences, and so on
  For instance, you can:
    Launch a VI
    Change VI properties options
    Get and set control values of a VI
    Customize printing
  Can be done locally or remotely
Notes: One of LabVIEW’s powerful features is VI Server, which allows you to control features of LabVIEW and VIs that are normally only available through menu items, preferences, and so on. For example, VI server allows you to launch a VI, change VI properties options (making the abort button visible, centering the front panel, and so on), Get and Set the values of controls on your front panel, or customize your printing, just to name a few. VI Server also includes built in TCP/IP functions so you can control LabVIEW and VIs on a remote machine. The VI server function is located in the Application Control palette.

## Slide 28: VI Server
Two types of LabVIEW objects
  LabVIEW application (one per application)
  LabVIEW VI (one per VI)
Basic steps
  Open a reference to either LabVIEW or a VI
  Get/set methods or properties
  Close the reference
Notes: VI Server gives you access to two different classes of objects: Application Class and Virtual Instrument Class. The Application Class gives you a reference to your LabVIEW application. The Virtual Instrument Class gives you access to a LabVIEW VI. The three basic steps for using VI Server are:
1) Open a reference to a class (application or VI)
2) Get/Set methods or properties allowed by that class
3) Close the reference

## Slide 29: VI Server
Properties
  Achieved with Property Node
  Can do multiple properties with one Property Node
  Executes top to bottom
  Some VI class properties
    Show abort button
    Front panel open
    Print at finish
Methods
  Achieved with Invoke Node
  Can only do one method per Invoke Node
  Gray terminals are optional
  Some VI class methods
    Run VI
    Get control value
    Set control value
    Save instrument
Notes: After you have chosen the class to open a reference to, you will get/set properties or methods for that class. Properties are modified with the Property Node. You can expand the property node to modify more than one property at a time. When using multiple properties in one node, the node will execute the priorities in a top to bottom order. Some examples of VI class properties are showing/hiding the abort button, opening/closing the front panel, and printing the VI when it is finished running.
Methods are modified with the Invoke Node. You can only invoke one method with each node. Some methods will have gray terminals. The gray terminals are optional. For instance, with the Run VI, if you don’t wire the Wait until done terminal the node will still execute with a default value. However, you can wire a value into Wait until done if you don’t want to use the default value. Some examples of methods are running the VI, getting the value of a control on the front panel, setting the value of a control n the front panel, and saving the VI.
Use the help window to show what each property or method does. You learn how to use VI Server in the next exercise.

## Slide 30: Exercise
VI Server

## Slide 31: Multithreading
Allows the CPU to process tasks separately within your LabVIEW program
Threads are grouped by Execution Systems
  User interface
  Standard
  Instrument I/O
  Data acquisition
  Other 1
  Other 2
CPU
LabVIEW
T
a
s
k
T
a
s
k
T
a
s
k
Notes: In a system it is usually desirable to have multiple tasks running in parallel. As in life, all tasks are not created equal, and it is desirable to have one task run more often than others. Multithreading allows you to break up your tasks, so they can be seen separately by your CPU, and assign each task a priority level. LabVIEW groups its threads into six different execution systems: User Interface, Standard, Instrument I/O, Data Acquisition, Other 1, and Other 2.

## Slide 32: Multithreading
Choose priority and execution system under VI Properties>>execution
Multithreading works best when VIs with different priorities are launched with VI Server
Notes: Priorities and Execution systems are set under VI Properties>>Execution, and are chosen on a VI-by-VI basis. To avoid any data dependencies that may be caused by having the VIs in the same while loop, or on the same diagram, you should have the two VIs running separately. You can launch the VIs with VI Server so they run simultaneously, yet separate from each other. Multithreading is most effective when implemented in this fashion with VI Server.

## Slide 33: Multithreading
Each execution system has four threads (except for user interface which has only one)
  Normal priority thread
  Above normal priority thread
  High priority thread
  Time critical priority thread
Background priority will only run if a thread is available
Subroutine priority borrows the thread of the calling VI
Notes: The User Interface Execution System is only allocated one thread. It is used to process user interface tasks such as mouse events, screen updates, attribute nodes, and so on. The other five Execution Systems (Standard, Data Acquisition, Instrument I/O, Other 1, and Other 2) each have four threads. Each of the four threads in an Execution System has a different priority: Normal, Above Normal, High, and Time Critical. You can also assign a task a Background or Subroutine Priority. In the case of a Background Priority no thread is assigned. The task only executes if a thread is available. In the case of a Subroutine Priority the task will borrow the thread of the calling VI.

## Slide 34: Exercise
Multithreading

## Slide 35: Summary
  Use Configuration File VIs to initialize your system
  Use a State Machine to control the order of your system’s execution
  Use an Occurrence to put part of your diagram to sleep
  Use a Semaphore to protect shared resources
  Use VI Server to programmatically control LabVIEW and your VIs
  Use Multithreading to split up tasks and assign priorities to those tasks

## Slide 36: Circuit Test System

## Slide 37: System Execution Flowchart
Initialization
Motion
Data acquisition
(FIFO, digital tests, etc.)
Image acquisition
(controls IMAQ VI)

## Slide 38: State Machine – Initialization
Notes: The heart of the application is a state machine. It executes in a fixed sequence:
Initialization  Motion  DAQ  IMAQ  Motion  DAQ, etc…
The initialization only happens once. There is no path back to this state until the application is restarted. It contains a sequence which handles the configuration of all the equipment used in the application.
If the sequence of states is fixed and you aren’t monitoring for user input, why not just use a sequence in a loop, rather than a state machine? You could make this application with a sequence, and it would work fine. However, a state machine has the advantage of cleanly storing data in shift registers instead of using numerous local variables, sequence locals, and shift registers. In addition, any changes you want to make to the flow of execution such as adding or deleting tests, adding conditions for tests, and so on, are much easier to implement with a state machine.

## Slide 39: State Machine – Motion
Notes: The motion state initiates a simple move of the UUT platform, then monitors for completion of the move. Notice the string constant in the lower right-hand corner which dictates that the “DAQ” section will always follow the motion. The DAQ operation is done before the imaging to allow time for the motion to dampen out and allow for a crisp image to be acquired. Notice how easy it would be to change the sequence to perform the IMAQ section next, if we decide to do that in a later version of the application.

## Slide 40: State Machine – Data Acquisition
Notes: The DAQ state acquires the semaphore from the continuous SCXI monitoring operation, performs its various tests, reinitializes the SCXI operation, and releases the semaphore. The loop only executes once unless there is an error in acquiring the semaphore.
This state always designates the IMAQ operation as the next state.

## Slide 41: State Machine – Image Acquisition
Notes: The IMAQ state controls the dynamically called IMAQ VI with a global variable and occurrence, as discussed earlier.

## Slide 42: Continuous Display Updates
Notes: Measurement data is updated continuously on the front panel of the application. You want to be able to see the latest measurements, regardless of what portion of the program is executing at the time.
We handle this by constructing a global variable update loop which operates in parallel with the main state machine. To minimize the effect of repeatedly reading the global variables on performance, we use a fairly slow 500 ms wait in the loop.

## Slide 43: System Execution Flowchart
Initialization
Motion
Data acquisition
(FIFO, digital tests, etc.)
Image acquisition
(controls IMAQ VI)
SCXI monitoring
(VI server)

## Slide 44: Synchronization – Semaphores
Notes: Besides ensuring that measurement events occur in the right sequence, we need to ensure that we don’t attempt to use the same resources for two different operations at once. This arises where we have a DAQ board which is used to take measurements on the UUT, and also to control a continuous SCXI monitoring operation. We need a way to ensure that the UUT measurements are not attempted while the monitoring operation is in progress.
To make this work, we will ensure that both operations periodically give up control of the board. Semaphores then allow each operation to check if the board is in use before starting. If the board is in use, the semaphore does not complete execution until the other process is complete.
The process goes something like this:
The UUT operation attempts to acquire the semaphore. SCXI monitoring is in progress, so the UUT waits until it completes and releases the semaphore. Then the UUT operation acquires the semaphore and executes.
Meanwhile, the SCXI monitoring operation attempts to reacquire the semaphore but must wait until the UUT operation completes and releases the semaphore. As a courtesy, the UUT operation reinitializes the board for the SCXI operation before returning control.
This process continues. Normally the SCXI monitor will acquire the semaphore with no problem, since it is operating continuously. It will occasionally have to wait, however, for the UUT operation to complete.

## Slide 45: Synchronization – Semaphores
Notes: This slide shows the dynamically launched SCXI monitoring VI. Once the semaphore is acquired it reads the SCXI configuration parameters from the main VI via global variables, then executes a monitoring cycle. It releases and reacquires the semaphore once for every measurement it takes, giving the UUT DAQ operation a chance to acquire the semaphore between cycles.

## Slide 46: System Execution Flowchart
Initialization
Motion
Data acquisition
(FIFO, digital tests, etc.)
Image acquisition
(controls IMAQ VI)
Image acquisition/processing
(VI server)

## Slide 47: Synchronization – Occurrences
Notes: To integrate the various functionalities into a single application, we need to provide a means of ensuring that certain operations are constrained to occur at specific times. One example for our application is the requirement that the motion of the unit under test (UUT) be complete before its image is acquired and analyzed.
This is accomplished with the use of occurrences and a global variable. The diagram above extracts an image and processes it to do the character recognition and chip detection. When it is done it sets an occurrence. The main state machine of the application has a “Wait on Occurrence” which does not finish execution until the dynamically called IMAQ VI sets its occurrence. Once that happens, the program is free to continue and move the next unit into position.
The IMAQ operation is started by a global variable, “Send”, rather than an occurrence. This is necessary due to the constraint that the image be continuously displayed while the application is running. In order to keep updating the display, we need to keep the IMAQ loop shown above running continuously. If we were to use an occurrence, the loop would stop until the occurrence was set and we would lose the display. Here the IMAQ case of the main state machine writes to the global variable to send the loop above into the True case. Otherwise, the loop just continues to execute through the (empty) False case, updating the display each time.

## Slide 48: Synchronization – Occurrences
Notes: The global variable which prompts the IMAQ VI to process an image is shown above, along with the “Wait on Occurrence”, which holds the state machine in the “IMAQ” state until the processing is complete.

## Slide 49: Integrated Measurement System
Portable, compact test set-up
Single software environment (LabVIEW)
Modifications, additions, and scaling are straightforward
Synchronization tools and multithreading facilitate control of complex systems

## Slide 50: Closing
Application integration involving several measurement techniques is easily achieved by utilizing National Instruments measurement hardware and software products.