## Slide 1: Multisim 3D NI ELVIS II How-to
Notes: <number>

## Slide 2: Why is this important?
3D Environment bridges the gap between theory to real-world prototype:
Learn/practice prototyping
Space to make mistakes
Design and connectivity check – verify circuit
Notes: <number>

## Slide 3: 1. Begin with Multisim 11.0
File » New » NI ELVIS II Schematic
Start » All Programs » National Instruments » Circuit Design Suite 11.0 » Multisim 11.0
Notes: <number>

## Slide 4: 2. Draw your circuit
( Ctrl + W ) to open component browser to select and drop components
Click source and destination to make wire connection between components
Notes: <number>

## Slide 5: 3. Launch the breadboard
From the menu
From the toolbar
Tools » Show Breadboard
Off the main menu, click on Show Breadboard Icon
Notes: <number>

## Slide 6: 4. Explore the 3D NI ELVIS II Environment
Notes: <number>

## Slide 7: a. Rotate the model
Press and hold the ( Left ) mouse button and move mouse
Notes: <number>

## Slide 8: b. Zoom in and out
Scroll DOWN to zoom out
Scroll UP to zoom in
Notes: <number>

## Slide 9: c. Panning
Hold down mouse-wheel and drag.
( Ctrl + Shift ) and drag.
Notes: <number>

## Slide 10: d. 3D NI ELVIS II default view
These arrows allow you to scroll through your components
Description of a component the cursor is hovering over
Components appear in the Place Component Bar ready to be placed
Notes: <number>

## Slide 11: e. Place component = Drag & Drop
1. Start here. Click component hold. Drag.
2. DROP here desired location
Notes: <number>

## Slide 12: f. Place component = Drag & Drop
RED sockets indicate where the component pin will be placed when mouse button is released
GREEN sockets indicate sockets are internally connected to the red socket on the same row
Tip: ( Ctrl + R ) rotates selected components by 90 degrees clockwise
Notes: <number>

## Slide 13: g. Wiring specifics
Click on the socket where you want to start and the destination socket to complete wiring.
Legitimate “target” pin turns green…you know where to connect.
Start with a signal source and…
Notes: <number>

## Slide 14: h. Changing wire colors
Click Breadboard Wire Color icon to change the wire color.
Notes: <number>

## Slide 15: h. Verification with DRC and Connectivity Check
Run the Design Rules and Connectivity Check to verify the circuit on breadboard with your schematic
Design Rule Errors – indicate connections on breadboard not on the schematic
Connectivity Errors – indicate component pins not connected to schematic nets
Notes: <number>

## Slide 16: 5. Back to the Schematic
GREEN components indicated component has been place in 3D environment
GREEN wire indicates correct connection has been made in 3D environment
Notes: <number>

## Slide 17: You have successfully explored the NI ELVIS 3D environment!!
Notes: <number>