## Slide 1: Lesson 6 Controlling the FPGA VI
Introduction
FPGA Interface Functions

## Slide 2: A. Introduction
Common host VI tasks:
  Data processing
  Perform operations not available on the FPGA target
  Log data
  Sequence multiple FPGA VIs
  Control the timing and sequencing of data transfer
  Control which components are visible on the front panel window for communication
Notes:   A. Introduction
  The external host program might provide a remote graphical user interface, log data, and post process data. The host program can run in Windows on a PC or PXI controller; or it can run on a real-time operating system (RTOS) on a PC, PXI controller, Compact Vision System, or CompactRIO controller. The RT host controller communicates with the CompactRIO RT processor over the network using shared variables or low-level protocols such as TCP/IP.
    The Host VI can perform the following tasks in this architecture:
    Perform more data processing than you can fit on the FPGA
    Perform operations not available on the FPGA target, such as floating-point arithmetic
    Provide a multi-tiered application with the FPGA target as a component of a larger system
    Log data
    Sequence multiple FPGA VIs
    Control the timing and sequencing of data transfer
    Control which components are visible on the front panel window because some controls and indicators might be more important for communication than others

## Slide 3: B. FPGA Interface Functions
  Establish and terminate communication with the FPGA VI
  Control the execution of the FPGA VI on the FPGA target
  Read and write data to the FPGA VI
  Wait for and acknowledge FPGA VI interrupts
  Read DMA FIFOs
Notes:   B. FPGA Interface Functions
  When you install the LabVIEW FPGA modules in LabVIEW, if you open a VI under the host in the project hierarchy, the FPGA Interface Functions palette is available, as shown above.
  Use the FPGA Interface functions to communicate with an FPGA VI from the host VI using the following operations:
    Establish and terminate communication with the FPGA VI
    Control the execution of the FPGA VI on the FPGA target
    Read and write data to the FPGA VI
    Wait for and acknowledge FPGA VI interrupts
    Read DMA FIFOs
  The FPGA Interface functions can return general LabVIEW error codes, specific FPGA interface error codes, or error codes specific to the FPGA target. Refer to the specific FPGA target documentation for a list of target-specific error codes.

## Slide 4: Open FPGA VI Reference
  Opens a reference to:
    Open the FPGA VI or bit file
    Selects an FPGA target
  Select VI and target in the shortcut menu
    Or, specify target with the resource name input
      Right-click and select Show Resource Name Input
  Must open a reference to the FPGA target before you can communicate between the host VI and the FPGA VI.
  Configure for Open or Open and Run
    Use free label to describe functionality
Notes:   Open FPGA VI Reference
  Opens a reference to the FPGA VI or bitfile and FPGA target you select in the shortcut menu or that you specify with the resource name input. You must open a reference to the FPGA target before you can communicate between the host VI and the FPGA VI.

## Slide 5: Read/Write Control
  Reads a value from or writes a value to a control or indicator in the FPGA VI on the FPGA target.
Notes:   Read/Write Control
  Reads a value from or writes a value to a control or indicator in the FPGA VI on the FPGA target.

## Slide 6: Invoke Method
  Invokes method or action from a host VI
  Methods:
    Run
    Abort
    Reset
    Wait on IRQ
    Acknowledge IRQ
    Download
    Read and write DMA FIFOs
Notes: Invoke Method
Invokes an FPGA Interface method or action from a host VI on an FPGA VI. Use methods to download, abort, reset, and run the FPGA VI on the FPGA target, wait for and acknowledge FPGA VI interrupts, read DMA FIFOs, and write to DMA FIFOs. The methods you can choose from depend on the target hardware and the FPGA VI. You must wire the FPGA VI Reference In input to view the available methods in the shortcut menu.

## Slide 7: Close FPGA VI Reference
  Stops and resets the FPGA
  Right-click and select Close from the shortcut menu to close the reference without resetting
  Default is Close and Reset if Last Reference, which closes the reference, stops the FPGA VI, and resets the FPGA
  Use free label to describe functionality
Notes: Close FPGA VI Reference
Stops and resets the FPGA VI running on the FPGA target and closes the reference to the VI. Right-click the Close FPGA VI Reference function on the block diagram and select Close to close the reference without resetting the FPGA VI running on the FPGA target. The default is Close and Reset if Last Reference, which closes the reference, stops the FPGA VI, and resets the FPGA VI running on the FPGA target.

## Slide 8: Exercise 6-1 Creating an FPGA Interface
Create a host VI for the custom trigger.

## Slide 9: Summary
  FPGA host interface functions control and communicate with the FPGA VI
  Expose only necessary controls and indicators on the FPGA VI
Notes: In this lesson, you have learned how to use the FPGA interface VIs to control and communicate with your FPGA VI. Remember that you need to display just the necessary controls and indicators on your FPGA VI, because extra front panel objects might take additional space. In the next lessons, you will learn more advanced topics like synchronization between the host and the FPGA VI, as well as different mechanisms to transfer information between them.

## Slide 10: Quiz
You communicate with the FPGA VI is by using which of the following:
  Array functions
  NI-DAQmx VIs
  FPGA Interface Vis
  TCP/IP VIs
Which of the following are used for reading the values of controls/indicators on the FPGA VI:
  Open FPGA VI Reference
  Read/Write Control
  Invoke Method
Notes: FPGA Interface VIs
Read/Write Control